## Slide 1: MW-level Gyro-klystron for Driving a Harmonic Lineariser for an X-ray FEL
Liang Zhang1, Laurence Nix1, Li Wang2, Wenlong He3, and A.W. Cross1
on behalf of research teams of
1Department of Physics, SUPA, University of Strathclyde, Glasgow, G4 0NG, UK
2 University of Electronic Science & Technology of China, Chengdu, 610054, China
3 Shenzhen University, Shenzhen, 518060, China

## Slide 2: Outlines
Motivation
Principles of Gyroklystron
Design of the interaction circuit
Design of other components
  MIG gun
  Input coupler and input window
  Output launcher and transmission line
  Collector design
List of specifications

## Slide 3: Motivation
XLS injector works at C-band (~6 GHz)
36GHz linearizer system is the baseline design, while other frequencies are also under consideration
*Courtesy by Massimo
linearizer system

## Slide 4: Linearizer
*Courtesy by A. Castilla, and Sergey V. Kuzikov
Linearizer is used to generate shorter electron bunches.
Ka-band Traveling Wave Structure
SLED-II Compressor, power ratio ~ 7@1us
15MW@30cm, more power at shorter length
Microwave source
Phase shifter

## Slide 5: The requirements
Optional driving source:
  Multiple-beam klystron
  Gyroklystron
Source type | Amplifier | Amplifier
Harmonic number | 6 | 8
Output frequency | 36 GHz | 48 GHz
Output power | 3.0 MW | 2.0 MW
Pulse repetition rate / Duration | 1000 Hz / 1.5 us | 1000 Hz / 1.5 us
Bandwidth | ~100MHz | ~100MHz
The 36 GHz 3MW source can also be used to a Ka-band Microwave undulator.
L. Zhang, et. al, Journal of Synchrotron Radiation, vol. 26, pp. 11-17, 2019.

## Slide 6: Gyro-klystron
Bunching in azimuthal direction. Interacting with TE modes.
Lower axial velocity due to the beam alpha results in larger cavity size.
Operating frequency determined by the external magnetic field.
Open output cavity, high power capability.
Schematic of a 4-cavity gyroklystron
*Courtesy by M. S. Chauhan

## Slide 7: Linear gain theory
The operating mode (output cavity) is TE02;
Competing modes: TE11 & TE01
Output power (kW) | 3200
Beam voltage (kV) | 150
Beam current (A) | 50
Magnetic field (T) | 1.5
Frequency (GHz) | 36
Drive power (W) | 400
Gain linear & sat (dB) | 48 & 39
Efficiency | 42%
Bandwidth (MHz) | 190
TE02
TE11
TE01
1st harmonic
2nd harmonic
Based on Electron Cyclotron Maser instability,
near the waveguide cutoff frequency.

## Slide 8: Cavity Simulation
Three-cavity structure
Selected set-up is a 3-cavity cylindrical arrangement with TE01-TE01-TE02 cavity sequence
The normalized coupling coefficient as the function of the normalized size of beam radius
Structure | Freq. (GHz) | Q
Cavity 1 | 35.25 | 52.6
Cavity 2 | 34.58 | 23.5
Cavity 3 | 35.79 | 78.6
0
1
2
3
4
0
0.2
0.4
0.6
0.8
1
Normalized cavity structure
Normalized coupling coefficient
Input cavity
Bunching cavity
Output cavity
Normalized Beam guiding centre

## Slide 9: Nonlinear model
Interaction efficiency
The normalized motion equation ignoring the axial momentum of the helical electron beam due to the frequency being close to cut-off.
Beam-wave interaction
Fast and quickly estimate the interaction efficiency, and to determine the initial parameters.
L. Wang et al., IET Microw., Antennas Propag., vol. 12, no. 11, pp. 1752–1757, Sep. 2018.

## Slide 10: Nonlinear simulation model
L. Wang et al., IET Microw., Antennas Propag., vol. 12, no. 11, pp. 1752–1757, Sep. 2018.
0
5
10
15
20
0
0.1
0.2
0.3
0.4
0.5
0.6
z
(mm)
E-field amplitude
Efficiency curve
Efficiency
Input cavity
Intermediate cavity
Output cavity
The input signal slightly modulates the beam. The interaction efficiency is ~1E-5.
The intermediate cavity enhances the bunching. The efficiency is ~0.5%.
Major energy exchange in output cavity. The interaction efficiency can be ~40%.

## Slide 11: Particle-in-Cell simulations
Peak power: 3.2 MW
Frequency
36 GHz
Electron phase space

## Slide 12: Magnetron Injection Gun
Beam trajectories
Solenoid system, superconducting magnet
Conservation of angular momentum:
Spread in the guiding center:
L. Zhang, et. al, IEEE Transactions on Electron Devices, vol. 67, no. 11, pp. 5151-5157, Nov. 2020.
synthesis method developed by Wes Lawson. Further optimization of the cathode and anode by Parameterized geometry.

## Slide 13: MIG-type e-gun
PARAMETERS | EGUN | MAGIC | CST
Velocity ratio α | 1.32 | 1.32 | 1.32
Velocity ratio spread Δα (%) | 7.99 | 5.74 | 7.12
Transverse velocity spread Δβt (%) | 3.06 | 2.17 | 2.78
Guiding centre radius Rg0 (mm) | 2.36 | 2.42 | 2.41
Modulating anode voltage Vm (kV) | 43.2 | 46.6 | 45.45

## Slide 14: Input coupler & window
Beam tunnel
Coaxial coupler
Electron
beam
Pillbox window
-30dB reflection over the required bandwidth with the ceramic disk. Lower reflection can be achieved without step.
Step for brazing.

## Slide 15: Collector Simulations
τ=1.5μs, f=1000Hz, U=150kV, I=50A, η=40%;
Electron beam power 7.5MW;
Output microwave power 3MW;
Power in the spent beam 4.5MW;
Average spent beam power, microwave on: 6.75kW;
Average spent beam power, microwave off: 11.25kW
Collector structure optimized for higher average power capability with fins added for cooling to lower the temperature on the collector.
Output Window
The temperature of window <40℃
Temperature rise < 100 degree
Cooling channel

## Slide 16: Output coupling – solution 1
120 cm
60 cm
Output from axial direction.
Output mode is TE02 in circular waveguide, can be converted to TE01 mode with a waveguide taper.
Electron gun
Collector
Superconducting
magnet
Input window & coupler
Interaction circuit
Output window

## Slide 17: TE01/02 transmission line
Transmission line system is composed by:
Waveguide taper (conversion between TE01 to TE02)
Straight waveguide (low loss ~0.02 dB/meter)
Miter bend (Major reflection source)
Pure TE01 mode
Miter bend structure:
Hybrid TE0n modes
The taper section is used to convert from pure TE01 into a mixture of higher order TE0n modes, which helps to locate the wave energy more centrally. And to reduce the loss.
Taper angle (degree) | TE02 content
4 | 4%
6 | 8%
8 | 14%
10 | 20%
Typical values, will change with different diameter. ~14% TE02 mode is an optimal choice.

## Slide 18: TE01/02 transmission line
At W-band 94 GHz with a 20m length, the transmission loss was -0.75 dB.
Lower loss can be achieved at Ka-band.
C. R. Donaldson, et. al, IEEE Trans. Electron Devices, vol. 68, no. 1, pp. 364-368, 2021.

## Slide 19: Output coupling – solution 2
150 cm
60 cm
Electron gun
Collector
Superconducting
magnet
Input window & coupler
Interaction circuit
Output window
Cooling
Quasi-optical launcher
Output in the transverse direction.
Output mode TEM00 (fundamental Gaussian mode, ~98% similarity with HE11 mode in low loss corrugated waveguide).
Better beam wave decoupling and more suitable design for depressed collector.

## Slide 20: QO launcher, transmission line
(1) L. Zhang, et. al, Journal of Synchrotron Radiation, vol. 26, pp. 11-17, 2019.
(2) P. McElhinney, et. al, IEEE Trans. Antennas Propag., vol. 61, no. 3, pp. 1453-1456, 2013.
A low loss corrugated waveguide can be used to transport the HE11 mode. The ohmic loss is similar to TE01 mode.
Vlasov step cut
window
quasi-parabolic mirror
elliptical mirror
The conversion efficiency can be 95% - 98%.

## Slide 21: Commercially available transmission lines
Straight corrugated waveguide
Low loss HE11 (as low as 1% per 100m, no mitre bends)
  Can be used with mitre bends
  High power, ~MWs in vacuum
    Higher power in vacuum, Helicoflex® vacuum seals
Non-vacuum miter bends are made with corrugated waveguides machined into a block.
Vacuum miter bends have corrugated waveguide arms machined in one piece with the miter block with microwave couplers for monitoring power.
  Cost ~1,000 euros per m for HE11 corrugated waveguide, mitre bends not included.

## Slide 22: 36 GHz gyro-klystron design
Voltage (kV) | 150 | Current (A) | 50
Velocity ratio | 1.3 | Drive power (W) | 400
Beam guide radius (mm) | 2.3 | Magnetic field (T) | 1.46
result |  |  | 
Power (MW) | 3.2 | Bandwidth (MHz) | 100
Efficiency | 44% | Saturated Gain (dB) | 39

## Slide 23: 48 GHz Gyroklystron
Start to oscillate
25% power drop with 10% velocity spread.
A 48 GHz gyroklystron was designed with a similar scheme by L. Nix.
The target power is 2 MW. 36.5dB gain @ 400 W input power.
The impact of velocity spread from MIG gun was considered.

## Slide 24: Summary of the design
A gyroklystron operating at 36 GHz was designed as the driving source for a 6th harmonic linearizer.
Three-cavity configuration.
Superconducting magnet of 1.5 T was used.
The major components including MIG, input coupler, input window, output window and collector have been designed.
Two output launching methods with low transmission loss were proposed to feed the power to SLED-II compressor.
A 48 GHz gyroklystron was also designed and simulated.
Full Specifications are listed in next page.

## Slide 25: Specifications
Beam voltage / Beam current | 150 kV / 50 A
Output power / 2nd harmonic component | 3.2 MW / 2.3%
Output power stability | 0.4% @0.5% variation of the modulator voltage
Output frequency / 3dB bandwidth | 36 GHz / 108 MHz (0.3%)
Magnetic field and frequency drift | 1.46 T and < 1 MHz frequency drift due to the drift of magnetic field
Frequency drift due to beam voltage | 24 MHz @0.5% / 4.8MHz @0.1% variation of the modulator voltage
Pulse repetition rate / Duration | 1000 Hz / 1.5 us
Drive power / Gain | 400 W / 39 dB
Input / output waveguide mode | Input TE10 (Rect.), output TE02 (Circular)
Efficiency | 42.7% (without energy recovery), 58.0% (with single stage depressed collector)
Dimensions | 60 cm (W) * 60 cm (L) * 1200 cm (H)
Phase stability | 17.0 degree@0.5%, 3.4 degree@0.1%, 0.34 degree@0.01 variation of the modulator voltage
Average spent beam power | 6.5 kW (mm-wave on), 11.25kW (mm-wave off)

## Slide 26: Acknowledgement
This work is supported by the European Commission Horizon 2020 Project “CompactLight” (777431-XLS), and the STFC, UK (Cockcroft Institute Core Grant)
Theory
&
New concepts
Modelling
&
Simulations
Design
Construction
&
Experiments
Testing
&
Applications
Technology
Transfer to Industry
&
Manufacturability
INTEGRATED CAPABILITY from IDEA to DEMONSTRATOR
Future work
Construct 3MW, 36GHz gyroklystron driven by a low pulse repetition frequency (1Hz) modulator
Longer term acquire a 150kV, 50A Scandinov modulator to operate at high pulse repetition frequency (1kHz)