## Slide 1
Phil DeMar, Ray Pasetes, Andrey Bobyshev
ICAC Review
10/15/2019
Fermilab WAN Capabilities

## Slide 2: Two Perimeter Security zones

## Slide 3: FNAL Campus LAN & Off-Site Network Paths
Internal
Network
Network
Perimeter
External

## Slide 4: FNAL Network Perimeter
Virtual Routing & Forwarding (VRF) technology on border routers
Perimeter has geographic diversity for both devices & fiber
Aggregate off-site bandwidth is currently 300Gb/s (3 x 100GE)

## Slide 5: ESnet – FNAL’s ISP
ESnet is FNAL’s only offsite internet service provider
ESnet backbone is extremely capacious & highly redundant:
  Including trans-Atlantic services to CERN & GEANT
Metropolitan area network (MAN) services for last mile(s)

## Slide 6: ChiExpress – FNAL’s Connectivity to ESnet’s PoPs
A local optical network operated by ESnet
Ethernet-based, not SONET-based:
  Wave reconfiguration within (O) 10 minutes
Site capacity upgrades involve only hardware

## Slide 7
General strategy – keep science data traffic logically separate, if feasible:
  Optimize performance over WAN science data network paths
  Internal LAN upgrades for high-impact science requirements easier to target
  More flexible perimeter security models
  Limit interaction with interactive traffic:
    Don’t want this to be your Zoom meeting data stream…
Examples – LHCOPN, LHCONE, NOvA Far Detector
Special-Purpose Science Data Networks
Phil DeMar | ICAC Review – 10/15/19

## Slide 8: LHC Optical Private Network (LHCOPN)
Star-shaped “private” network:
  - CERN (LHC Tier-0) at the center
  “Links” to the LHC T1s
  T0 <-> T1 and (some) T1 <-> T1 traffic
FNAL LHCOPN links are virtual circuits over ESnet:
B/W guarantees
Primary, secondary, & tertiary circuits

## Slide 9: LHC Open Network Environment (LHCONE)

## Slide 10: LHCONE Translated into Understandable Terms
LHCONE is an overlay network (in most places…):
  VRF technology typically used to separate routing
Logically separates LHC traffic from general R&E network traffic for traffic management purposes:
  Also can lower security risk profile at sites for LHC traffic
End sites are responsible for separating traffic:
  At FNAL, we use Policy Routing techniques to accomplish that
There (currently…) are no QoS capabilities within LHCONE
Several smaller HEP/Astro collaborations have been granted authorization to utilize LHCONE for their data movement:
  Belle-II, Pierre Auger, NOvA, XEON

## Slide 11: Point-to-Point Network Services
NOvA Far End Detector (FD):
  Redundant low-bandwidth pt-to-pt connection(s)
    vLANs with B/W guarantees plumbed through multiple service providers
  Logically, NOvA FD lies inside FNAL’s security perimeter
Pt-to-pt circuits to US-CMS Tier-2 facilities:
  UFL, MIT, Nebraska, Purdue, UCSD, Wisconsin
  Being phased out,; largely replaced by LHCONE

## Slide 12: DUNE Far Detector (in South Dakota)
Far Detector (FD) connectivity to FNAL:
  FD local network will lie within FNAL security perimeter
  WAN support model currently under discussion w/ ESnet
  B/W under study; targeting 100GE path
    Redundant path expected to be much, much less
Off-line DUNE network expected to look similar to LHC:
  LHCONE-like service (but probably not an LHCOPN-like service)

## Slide 13: Large Synoptic Survey Telescope (LSST)
Summit Site
Summit Facility
Telescope and Camera
Data Acquisition
Crosstalk Correction
Archive Site
Archive Center
  Alert Production
  Data Release Production
  Calibration Products Production
  EPO Infrastructure
  Long-term Storage (copy 2)
Data Access Center
  Data Access and User Services
Dedicated network infrastructure from telescope (Chile) to archive site (NCSA)
FNAL working with NCSA on operational support for the long-haul network:
  Experiences from LHC networking believed to be helpful
Base Site
Base Center Long-term storage (copy 1)
Data Access Center
  Data Access and User Services

## Slide 14: Metropolitan Research & Education Network (MREN)
Consortium of Chicago area research universities & National Labs (FNAL & ANL):
  Like a mini-regional network
  Universities directly connect
  The Labs indirectly via ESnet
Maintains network switch(es) at the StarLight International Exchange:
  Potential connectivity path to StarLight-connected networks

## Slide 15: ESnet6
The next generation of ESnet:
  2021-ish
ESnet will “own” fiber, optical infra., and routers
Topology similar to ESnet5
Trans-Atlantic & intra-European links still leased services

## Slide 16: ESnet6 – New Networking Model
“Smart” edge and “hollow” core
Network services pushed to sites
  Service & path decisions made at the edge
Core’s function is packet forwarding
  One routing hop across ESnet

## Slide 17: ESnet6 – Multiple Classes of Services
“No touch” services are essentially default IP routing
“Low touch” services are today’s LHCOPN & LHCONE-like services:
  More flexible, dynamic, & more automated
“High touch” services allow per packet tagging & manipulation
Service classes isolated from each other
Low Touch
Services
No Touch
Services
High Touch
Services

## Slide 18: Summary
FNAL WAN services have capacious bandwidth & high levels of resiliency
  Needs for more bandwidth can be satisfied relatively easily
  But trans-Atlantic bandwidth demands present challenges
“Special” handling for science data traffic is provided:
Network Service | Service Characteristics | Example(s)
Routed IP | General internet access | ESnet base service
“Private” network | Small # of tightly-restricted sites Bandwidth guarantees | LHCOPN
Science discipline network | Large # of loosely-connected sites No bandwidth guarantees | LHCONE
Pt-to-Pt circuits | Deterministic, secure path(s) Bandwidth guarantees | NOvA FD; DUNE FD StarLight (ie., Intl. networks…)

## Slide 19: Questions
?

## Slide 20: Extra Slides

## Slide 21: South Dakota Research Education & Economic Development (REED) network
SURF
(DUNE)
X
ESnet
(Kansas City)
ESnet
(Minneapolis)
100
100
10
100
100
100
100
100
100
10
10
10
100GE today
100GE planned
10GE-based