## Slide 1: Coil 206 shipment data
Shipment:
dedicated shipping fixtures
2 accelerometers on the LE and RE
5g and 10 g shock watches
Air ride dedicated truck
No shock watch was activated
 Crate did not experience shocks above 5g

## Slide 2: Accelerometers specs
GPL1 senseware
Range up to 6.7 g
Data recorded every sec
Event recorded if > 3g
Sample rate 50 Hz
LE
SLAMSTICK
Range up to 16 g DC (shocks)
Up to 25 g AC (vibration)
Data recorded every sec
Trigger for g> 3g then collect for 1 h
Sample rate 800 Hz for DC

## Slide 3: RE accelerometers
26 Sept
1 Oct
23 Sept
Max: 4.7g
Duration ~30 ms

## Slide 4
26 Sept: 4 to 5 pm
Max: 14g
Duration < 2 ms

## Slide 5: Analysis
Events reconstruction:
Coil was sometimes shaking within the shipping frame: i.e. very short displacements and stops against frame/clamps
Events analysis:
Local impacts
Bending

## Slide 6: Local Impact
The effect of local impacts can be evaluated by comparison with past events:
During MQXFS1 disassembly the two top coils fell. Coil 3 fell on the bottom coils, and coil 104 fell on the assembly table.

## Slide 7: Scene Reproduction
Normal setup
In the incident
  The center coil support spud was not in place;
  The technicians were removing the side collar pack, the steel angle block was released
Steel Angle block
Coil support spud
Assembly Table
Assembly Table
Return End
Return End
Disassemble the top collar stack
Disassemble the collar stack #2

## Slide 8
Scene Reproduction
Return end view
Coil 104 fell onto the assembly table, dented on the edge in the red circle. Strain gauge wires were damaged.
Coil 3 fell into coil 5; its edge cut off the strain gauge wires of coil 5.
03
104
103
05
03
104
103
05
03
104
103
05
Return end view
Ready to disassemble
Removed the collars
Coils fell off
03
104
103
05
103
104
104

## Slide 9: Coil 206 & 104 Impact Velocity
Coil 206 velocity before impact: < 0.03 m/s
  V=at; a=15g, t=0.002 s (square function)
  Most likely V ~ 0.015 m/s (triangular function)
Coil 104 velocity before impact: ~ 1.7 m/s
  V=SQRT(2gx); x=0.15 m

## Slide 10: Coil 104
Coil 104 showed several marks & indentations made by impact with rigid objects on the table

## Slide 11: Coil 206
  Example of marks under Clamping Rib 4

## Slide 12: MQXFS1
Exceeded Ultimate current; healthy training

## Slide 13: Local Impact Conclusion
Marks on coil 104 were significantly worse than the marks on coil 206
Impact velocity was higher for coil 104 than 206
Coil 104 performed well in MQXFS1
 coil 206 acceptable for use from this point of view (local impact analysis)

## Slide 14: Load Analysis on the MQXFA Coil Shipping Fixture
Heng Pan
LBNL

## Slide 15: FE Model Overview
The material of the coil shipping fixture components is Aluminum 6061.
All components are in contact using contact elements
  Contact174 --- 3D surface-surface contact element
  Target170 --- Associated 3D target element
  Friction coefficient is 0.2
  Inside coil winding --- bonded
  Between shipping fixture components --- bonded
  Between coil and fixture --- frictional, mu=0.2
Support Tube
Support Channel
Base Channel
End Stopper
Side Rail
Coil Clamp
Rubber Isolator
Fixed support on the bottom e surface
Vertical inertial load

## Slide 16: 5g Vertical Inertial Load
0.5GPa Isolator modulus
Vertical Deflection (mm)
0.39 mm
Coil Equivalent Strain,
Maximum strain is ~25.4 µε
Coil Vertical Deflection (mm)
Coil deformation is ~105 (µm)

## Slide 17: 10g Vertical Inertial Load
0.5GPa Isolator modulus
Vertical Deflection (mm)
0.71 mm
Coil Equivalent Strain,
Maximum strain is ~52 µε
Coil Vertical Deflection (mm)
Coil deformation is ~210(µm)

## Slide 18: To be added (10g):