## Slide 1: 2 GeV Linac + RCS Options for 2.4 MW upgrade of LBNF program
Jeffrey Eldred
Snowmass 2022
July 20, 2022

## Slide 2
2
H- Injection into
Accumulator Ring or Rapid-Cycling Synchrotron
2
2
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 3
3
H- Injection through Foil, Process
3
H- linac beam transported into injection chicane.
Carbon foil strips the two electrons from the proton.
Proton beam accumulates in the ring.
Unstripped H- ions are sent to an absorber.
Ring cheats Louiville’s theorem, concentrates beam current by x10-x1000!
Essential for long-baseline program and many experimental programs.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 3
3
3

## Slide 4
4
H- Injection through Foil, Challenges
4
Challenges:
- Chicane magnets must be sufficiently long (weak) to avoid stripping H- beam while also inflecting the beam towards the stripping foil.
- Losses from protons scattering off injection foil, high radioactivation.
- Thin stripping foil degrades from radiation and extreme heat.
- Losses of unstriped H- particles, requires absorber or extraction line.
- Injection optics interfere with symmetric ring lattice, causing resonances.
- Beam orbit must be maintained precisely over duration of injection.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 4
4
4

## Slide 5
5
H- Injection through Laser
5
Laser-stripping technology R&D underway to eliminate many of these challenges....
SNS demonstrated 95% stripping efficiency of a 1 GeV H- beam with 10 μs macropulse duration using a UV laser at 1 MW peak power.
However, millisecond duration with 99% efficiency is needed…
Present scenarios must proceed with a plan for H- foil injection (with laser-stripping as a subsequent retrofit).
Cousineau et al.
PRAB 2017
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 5
5
5

## Slide 6
6
Proton Complex
And PIP-II upgrade
6
6
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 7
7
7
7
Fermilab Upcoming Upgrades 700-900 kW
Record Main Injector power 893kW, Booster power 89 kW
H- Injection Location
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 7
7
7
7
7
7

## Slide 8
8
8
8
Fermilab Upcoming Upgrades PIP-II 1.2MW
PIP-II SRF
Linac
0.8 GeV
New SRF linac raises Booster injection energy, new LBNF beamline.
1.2 MW LBNF
Neutrinos
to DUNE
H- Injection Location
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 8
8
8
8
8
8

## Slide 9
9
9
PIP-II Linac & Upgrade
9
E. Pozdeyev, SpaceCharge19
Project started in 2016 (CD0)
First beam in Booster: 2028 (plan)
MI 1.2 MW beam on target: 2032 (projection)
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 9
9
9
9
9
9

## Slide 10
10
PIP-II Booster Power
10
PIP PIP-II
The primary purpose of the PIP-II is to inject into the Booster, and in turn power the high-energy proton complex including DUNE/LBNF program.
However, the PIP-II Linac is also designed to be CW-capable
and the Booster only uses ~1.2% of the CW beam power!
- What will form the GeV-scale experimental program?
- Do we need H- injection into an accumulator ring?
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 10
10
10

## Slide 11
11
Proposed “PIP-II Era” Accumulator Rings
11
PIP-II Accumulator Ring (PAR)
0.8-1.0 GeV proton storage ring.
474m folded figure eight, designed to match Booster circumference.
Dark Sector:
100kW hadron-absorber beam dump program that sets new exclusion limits.
Booster-MI Program:
Does not interfere with PIP-II Booster commissioning,
Enables later 1 GeV upgrade to Booster.
Compact PAR (C-PAR)
~0.8-1.2 GeV proton storage ring
~100m ring optimized for low duty factor, intense proton beam experiments.
Dark Sector:
Allows order of magnitude superior limits compared to PAR version.
Muon CLV program:
Allows 140 kW, 20ns pulses for subsequent muon CLFV AMF program
Related Snowmass White Papers
1) PAR accelerator design ArXiv 2203.07339
2) PIP2-BD Dark Sector program (PAR, C-PAR) ArXiv 2203.08079
3) AMF CLFV Muon program (related to C-PAR) ArXiv 2203.08278
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 11
11
11

## Slide 12
12
Proton Intensity Upgrade
after PIP-II
(construction complete ~2036)
12
12
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 13
13
Beam Power and Detector Size
13
DUNE long-baseline neutrino program calls for 2.4 MW
J. Eldred, JINST 2019
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 13
13
13

## Slide 14: DUNE physics program
Unambiguous, high precision measurements of Δm232, δCP, sin2θ23, sin22θ13 in a single experiment
Discovery sensitivity to CP violation, mass ordering, θ23 octant over a wide range of parameter values
Sensitivity to MeV-scale neutrinos, such as from a galactic supernova burst
Low backgrounds for sensitivity to BSM physics including baryon number violation
starts ~2032
2.4 MW
1.2 MW
δCP Discovery, sigmas over time
14
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 15
15
15
15
Fermilab Upcoming Upgrades Future 2.4MW
PIP-II SRF
Linac
1-3 GeV
Replace
Booster
Recycler?
Booster prevents x2 PIP-II power, injection energy and transition-crossing limits
2.4 MW LBNF
Neutrinos
to DUNE
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 15
15
15
15
15
15

## Slide 16
16
Upgrade Design History & Process
16
In 2008, Project X: 8 GeV SRF Linac, directly into Main Injector.
In 2010, Project X ICD-2: 2 GeV Linac, New 2-8 GeV RCS.
In 2018, S. Nagaitsev and V. Lebedev: updated version of ICD-2.
In 2019, J. Eldred, V. Lebedev, A. Valishev: parametric study of RCS design.
In 2021, Committee for Fermilab Booster Upgrade an integrated design effort:
Science Working Group chaired by R. Harnik
“Physics Opportunities for the Fermilab Booster Replacement”
Accelerator Working Group chaired by M. Syphers
“An Upgrade Path for the Fermilab Accelerator Complex” (RCS Scenario)
“An 8 GeV Linac as the Booster Replacement in the Fermilab Power Upgrade”
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 16
16
16

## Slide 17
17
Upgrade Design History & Process
17
In 2008, Project X: 8 GeV SRF Linac, directly into Main Injector.
In 2010, Project X ICD-2: 2 GeV Linac, New 2-8 GeV RCS.
In 2018, S. Nagaitsev and V. Lebedev: updated version of ICD-2.
In 2019, J. Eldred, V. Lebedev, A. Valishev: parametric study of RCS design.
In 2021, Committee for Fermilab Booster Upgrade an integrated design effort:
Science Working Group chaired by R. Harnik
“Physics Opportunities for the Fermilab Booster Replacement”
Accelerator Working Group chaired by M. Syphers
“An Upgrade Path for the Fermilab Accelerator Complex” (RCS Scenario)
“An 8 GeV Linac as the Booster Replacement in the Fermilab Power Upgrade”
Sam Posen presented on this scenario.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 17
17
17

## Slide 18
18
8 GeV Linac Option, direct to Recycler
18
Main Injector
(MI)
8 GeV Linac
PIP-II
Linac
Recycler
H- Injection Location
Optional
Accumulator
Ring
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 18
18
18

## Slide 19
19
8 GeV Linac Option, with Accumulator
19
8 GeV Linac
PIP-II
Linac
H- Injection Location
8 GeV
Accumulator
Ring
Optional
Accumulator
Ring
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 19
19
19

## Slide 20
20
Upgrade Design History & Process
20
In 2008, Project X: 8 GeV SRF Linac, directly into Main Injector.
In 2010, Project X ICD-2: 2 GeV Linac, New 2-8 GeV RCS.
In 2018, S. Nagaitsev and V. Lebedev: updated version of ICD-2.
In 2019, J. Eldred, V. Lebedev, A. Valishev: parametric study of RCS design.
In 2021, Committee for Fermilab Booster Upgrade an integrated design effort:
Science Working Group chaired by R. Harnik
“Physics Opportunities for the Fermilab Booster Replacement”
Accelerator Working Group chaired by M. Syphers
“An Upgrade Path for the Fermilab Accelerator Complex” (RCS Scenario)
“An 8 GeV Linac as the Booster Replacement in the Fermilab Power Upgrade”
There are actually two scenarios here, which I will discuss.
“Design Considerations for Fermilab Multi-MW Proton Facility” white paper
“ICD-2”
“BSR”
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 20
20
20

## Slide 21
21
RCS Option, “ICD-2” 10 Hz Ramp
21
Main Injector
(MI)
PIP-II
Linac
RCS
~2 GeV Linac Upgrade
H- Injection Location
Recycler
Optional
Accumulator
Ring
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 22
22
RCS Option, “BSR” 20 Hz Ramp
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
22
Main Injector
(MI)
PIP-II
Linac
Accumulator
Ring
RCS
H- Injection Location
Recycler?
~2 GeV Linac Upgrade

## Slide 23
23
RCS Scenarios
23
“Design Considerations for Fermilab Multi-MW Proton Facility” white paper
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 23
23
23

## Slide 24
24
RCS Scenarios (ramp rate and 8 GeV program)
24
“Design Considerations for Fermilab Multi-MW Proton Facility” white paper
ICD-2 RCS is more cost-effective, BSR RCS is more ambitious.
BSR delivers much more for 8 GeV program,
Also enables path to 4 MW at 120 GeV! But for whom?
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 24
24
24

## Slide 25
25
RCS Scenarios (required rings)
25
“Design Considerations for Fermilab Multi-MW Proton Facility” white paper
ICD-2 scenario require Recycler (or similar), maintains RR experimental program.
BSR scenario requires either a 2 GeV Accumator Ring or 5 mA linac upgrade.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 25
25
25

## Slide 26
26
Beam Accumulation and H- Stripping in a Storage Ring
26
BSR Injection Scenario 1: Retrofit PIP-II linac to 5mA pulsed.
BSR Injection Scenario 2: Use six 120 Hz painting cycles to collect full charge in a 2-GeV accumulator ring every 20 Hz.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 27
27
RCS Scenarios (required rings)
27
“Design Considerations for Fermilab Multi-MW Proton Facility” white paper
ICD-2 scenario require Recycler (or similar), maintains RR experimental program.
BSR scenario requires either a 2 GeV Accumator Ring or 5 mA linac upgrade.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 27
27
27

## Slide 28
28
Recycler Ring - Challenges
28
S. Antipov et al.
PRSTAB 2017
Electron cloud instability amplified Recycler in gradient dipoles
Smaller aperture
PIP-II Era Space-Charge
Shared tunnel space with Main Injector
R. Ainsworth et al.
PRAB 2019
Recycler Ring
Main Injector
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 28
28
28

## Slide 29
29
Recycler Ring - Advantages
29
Using the Recycler to collect batches (from RCS or from 8-GeV-Linac-AR) reduces the Main Injector cycle time – increasing beam power
- Improving cycle time vs intensity, better for neutrino target.
Recycler currently rebunches beam and sends it to Delivery Ring, currently a critical part of our muon campus research infrastructure.
- Will we miss that capability when its gone?
We will learn a lot more about Recycler limits in PIP-II era operation. Slip-stacking in PIP-II era may be more taxing than high-charge 2.4 MW era.
Recycler Ring was very cheap to build- it can be rebuilt with large aperture, better optics, low-SEY coating, large momentum acceptance as needed.
8-GeV Linac scenarios can use Recycler or avoid it.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 29
29
29

## Slide 30
30
RCS Scenarios (possible staging)
30
“Design Considerations for Fermilab Multi-MW Proton Facility” white paper
Possible Staging with 1.8 MW, smaller Linac upgrade, PIP-II era Main Injector RF.
If we are careful could be designed to be upgradeable to either 2.4 MW scenario.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 30
30
30

## Slide 31
31
Upgrade Design History & Process
31
In 2008, Project X: 8 GeV SRF Linac, directly into Main Injector.
In 2010, Project X ICD-2: 2 GeV Linac, New 2-8 GeV RCS.
In 2018, S. Nagaitsev and V. Lebedev: updated version of ICD-2.
In 2019, J. Eldred, V. Lebedev, A. Valishev: parametric study of RCS design.
In 2021, Committee for Fermilab Booster Upgrade an integrated design effort:
Science Working Group chaired by R. Harnik
“Physics Opportunities for the Fermilab Booster Replacement”
Accelerator Working Group chaired by M. Syphers
“An Upgrade Path for the Fermilab Accelerator Complex” (RCS Scenario)
“An 8 GeV Linac as the Booster Replacement in the Fermilab Power Upgrade”
Recent Ongoing Work:
- Realistic cost assessment and timetables for all scenarios
- Backup plans for DUNE/LBNF power if upgrades fall short of above scenarios
- PAR + Booster transition upgrades + Recycler replacement = 1.8 MW?
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 31
31
31

## Slide 32
32
Summary
32
PIP-II upgrade, massive potential for GeV-scale experimental program
Strategic planning for a subsequent Proton Intensity Upgrade.
- cost and timetable evaluations underway
ICD-2 RCS: Well-developed cost-effective proposal, focused on LBNF.
BSR RCS: More challenging injection, more 8-GeV power.
8-Gev Linac: Most challenging injection, highest 8-GeV potential.
What will be the future 0.8-2 GeV experimental program?
- power, beam structure, timeline.
What will be the future 8 GeV experimental program?
- power, beam structure, timeline.
- future role of Recycler Ring and Delivery Ring.
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS
Notes: 32
32
32

## Slide 33
33
Backup Slides
(Technical Details BSR)
33
33
Jeffrey Eldred | Snowmass 2.4 MW Upgrade with RCS

## Slide 34
34
Staging RCS with partial upgrade of Linac & MI
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
34
Linac can be commissioned concurrent with PIP-II operations, RCS can be commissioned at partial linac energy, etc.
At ~1.2 GeV, the PIP-II Booster 1.2 MW benchmark is crossed.
At ~1.6 GeV, we have 1.8 MW without Main Injector RF upgrade.
- If we can still use Recycler, RCS rep. rate only needs 10 Hz.

## Slide 35
35
Rapid Cycling Synchrotron (RCS)
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
35
The RCS would operate at 20 Hz and accelerate from 2 to 8 GeV
A second ring operating at 2 GeV is proposed to be located above the RCS and used to accumulate charge from the upgraded linac.

## Slide 36
36
Preliminary RCS Lattice Configurations
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
36
2 - 8 GeV RCS Ring,
one of eight periods
2 GeV Injection Ring,
one of four periods
2 GeV Ring Optimized for Injection
8 GeV Ring Optimized for Acceleration

## Slide 37
37
Beam Accumulation and H- Stripping in a Storage Ring
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
37
H- Foil Stripping Injection
17 m straight.
SR Circumference | 570 | m
SR Energy | 2 | GeV
Superperiodicity | 4 | 
Injection Insertion Length | 12 | m
Dipoles per Superperiod | 12 | 
Dipole Strength | <0.4 | T

## Slide 38
38
Anti-Correlated Painted Injection
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
38
Beam Distribution during Injection
Hit Distribution
Anti-correlated Painting Injection
Injection painting scheme chosen to:
Minimize foil hits from the circulating beam.
Optimize stability of the beam distribution.
Matthew Hoppesch beams-9123

## Slide 39
39
Main Injector Operations
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
39
Keep 8 GeV injection into MI, re-using portions of Recycler as injection line
Removing slip stacking operation (Recycler) creates lower momentum spread in MI; helps to alleviate issues at crossing of transition energy
“Transition”: energy where revolution frequency is independent of momentum
Special optics manipulation at the transition energy (left; part of PIP-II) and smaller momentum spread provide adequate phase space through transition:
transition energy in
Main Injector ( = 21.5)
R. Ainsworth, I. Kourbanis
Notes: 39
39
39

## Slide 40
40
Main Injector RF System
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
40
MI RF system would be upgraded with new modern RF cavity system
  increases RF power to meet final intensity requirements
  also enables increased ramp rate to achieve higher overall beam power above 2.4 MW
RF System Specifications |  | 
Frequency | 52.617 — 53.104 | MHz
Max. Acceleration Rate | 240 | GeV/s
Acceleration Voltage | 2.7 | MV
Peak Beam Power | 7.1 | MW
Average Beam Power | 3.6 | MW
Peak Voltage | 4.8 | MV
Average Beam Current | 2.7 | A
Fundamental RF Current | 4.6-5.2 | A
No. RF Stations required | 31 | 
I. Kourbanis
Notes: 40
40
40

## Slide 41
41
Possible MI Upgrade for Higher Power Beyond 2.4 MW
Jeffrey Eldred | An Upgrade Path toward Multi-MW Beam Power at Fermilab
41
Upgrade magnet power supply system to support higher ramp rate — reduce cycle time from ~1.5 s to about 0.9 s — factor of ~ 5/3
PIP-II
this
upgrade
MI PS
upgrade
240 GeV/s —> 600 GeV/s
I. Kourbanis
Notes: 41
41
41