## Slide 1
The Cool Copper Collider: An Advanced Concept for a Future Higgs Factory
Emilio Nanni for C3 Enthusiasts
AF 3/4 Discussion
7/17/22

## Slide 2
Baseline Design/Layout and Parameters
C3 – Cool Copper Collider – A cryogenic (80 K) high-gradient distributed coupling accelerator concept
8 km footprint for 250/550 GeV CoM ⟹ 70/120 MeV/m
7 km footprint at 155 MeV/m for 550 GeV CoM – present Fermilab site
Large portions of accelerator complex are compatible between LC technologies
Beam delivery and IP modified from ILC (1.5 km for 550 GeV CoM)
Damping rings and injectors to be optimized with CLIC as baseline
C3 - 8 km Footprint for 250/550 GeV

## Slide 3
Key Technologies
Modern Manufacturing
Prototype One Meter Structure
Maximize Structure Efficiency and Performance
Distributed Coupling
High Accelerating Gradients
Cryogenic Operation
Integrated Damping
Slot Damping with NiChrome Coating
Present Focus is the Main Linac
In Future Expand to Rest of Complex
C3 Cryo Test

## Slide 4
Accelerator Design
Engineering and design of prototype cryomodule underway
Focused on challenges identified with community through snowmass (all underway)
Gradient – Scaling up to meter scale cryogenic tests
Vibrations – Measurements with full thermal load
Alignment – Working towards raft prototype
Cryogenics – Two-phase flow simulations to full flow tests
Damping – Materials, design and simulation
Beam Loading and Stability - Thermionic beam test
Scalability – Cryomodules and integration
Laying the foundation for a demonstration program to address technical risks beyond RDR (CDR) level
Accelerator Design and Challenges
C3 Session at Snowmass Friday 22nd 340, HUB
https://indico.fnal.gov/event/22303/sessions/20646/#20220722
Cryomodule Concept
Vibration
Studies

## Slide 5
Compact footprint <8 km for 550 GeV allows for many siting options
Evaluating both underground and surface sites
  Underground – less constraints on energy upgrade
  Surface – lower cost and faster to first physics
Surface-Site Mockup (Tunnel in White Paper)
Rapid Excavation / Parallel Installation
No Vertical Shafts
National Lab and Green Field are Possibilities
Civil Engineering and Site
Fermilab Site Filler
Hanford Site

## Slide 6
250 GeV CoM - Luminosity - 1.3x1034
Parameter | Units | Value
Reliquification Plant Cost | M$/MW | 18
Single Beam Power (125 GeV linac) | MW | 2
Total Beam Power | MW | 4
Total RF Power | MW | 18
Heat Load at Cryogenic Temperature | MW | 9
Electrical Power for RF | MW | 40
Electrical Power For Cryo-Cooler | MW | 60
Accelerator Complex Power | MW | ~50
Site Power | MW | ~150
Temperature (K) | 77
Beam Loading (%) | 45
Gradient (MeV/m) | 70
Flat Top Pulse Length (𝜇s) | 0.7
Cryogenic Load (MW) | 9
Main Linac Electrical Load (MW) | 100
Site Power (MW) | ~150
Sustainability
Highview Power
Compatibility with Renewables
Cryogenic Fluid Energy Storage
Intermittent and variable power production from renewables mediated with commercial scale energy storage and power production

## Slide 7
Cryogenics Scale to multi-TeV
Beam power can be increased for additional luminosity
C3 has a relatively low current for 250 GeV CoM (0.19 A) - Could we push to match CLIC at 1.66 A? (8.5X increase?)
Pulse length and rep. rate are also options
Parameter | Units | Baseline | High-Lumi
Energy CoM | GeV | 250 | 250
Gradient | MeV/m | 70 | 70
Beam Current | A | 0.2 | 1.6
Beam Power | MW | 2 | 16
Luminosity | x1034 | 1.3 | 10.4
Beam Loading |  | 45% | 87%
RF Power | MW/m | 30 | 125
Site Power | MW | ~150 | ~180
Caution: Requires serious investigation of beam dynamics - great topic for C3 Demonstration R&D
Luminosity
Energy
Proposals for Upgrades and Extensions
Scalability studied to 3 TeV
Requires rf pulse compression for reasonable site power
Higher gradient option (155 MeV/m) in consideration
arXiv:1807.10195 (2018)
HTS Pulse Compressor
REBCO Coatings
Le Sage, CERN Collaborators
Qo ~ 400k

## Slide 8
Technically limited timeline
Community engagement through Snowmass to define the parameters of the C3 proposal
Stageability to Future Experiments

## Slide 9
State of Proposal and R&D needs (5 years)
Demonstrate fully engineered cryomodule
~50 m scale facility
3 GeV energy reach
Answer technical questions needed for CDR
Next Steps:
C3 Demonstration R&D Plan
https://arxiv.org/abs/2203.09076

## Slide 10
ITF Maturity Assessment

## Slide 11
Mitchell Schneider
Charlotte Whener
Gordon Bowden
Andy Haase
Julian Merrick
Bob Conley
Radiabeam
Cici Hanna
Zariq George
Valery Borzenets
More Details Here (Follow, Endorse, Collaborate):
https://indico.slac.stanford.edu/event/7155/
Acknowledgements
Additional Contributors