## Slide 1
Low-threshold Cryogenic Phonon Detectors for Reactor CENS
Rupak Mahapatra, Texas A&M

## Slide 2: Coherent Neutrino Scattering: Connection to WIMPs
Recoil energy in eV
Integrated rate/kg-year
Background
Requirements: Low Threshold and Low-background
CENS observed at SNS (~50 MeV ), thus accessible by many detector technologies: EmaxE 2
CENS process is yet to be discovered at a reactor! E~MeV hence need low threshold detectors

## Slide 3: CENS Detector Thresholds
DRU

## Slide 4: gm-kg scale MINER Detectors
Ge, Si, Al2O3
0V, LV (few V), HV (400V)
Smallest – 10 gm Si
Largest – 1.5 kg Ge
Athermal phonon sensor

## Slide 5: Detector Technology Developed for SuperCDMS
iZIP Detector with ionization and phonon sensors for ER/NR discrimination (>keV)
First SNOLAB Ge iZIP (fabricated at TAMU)
(More in Kurinsky talk on SuperCDMS)
High Voltage Detector with NTL gain. Give up discrimination in favor of low threshold (~100eV).
First SNOLAB Si HV (fabricated at TAMU)
Phonon
Ionization

## Slide 6: Anatomy of an event
h+
e-
-3V
0V
Hot charge carriers (3eV/pair)
Quasi-diffusive THz phonons
Ballistic low-frequency phonons
Ballistic Neganov-Luke phonons
Q inner
Q outer
Sensor A
Sensor B
Sensor C
Sensor D
Total Phonons = Direct Phonons + Luke Phonons
Electron Recoil
Nuclear Recoil
Ionization Energy
Phonon Energy (Recoil)

## Slide 7: Phonon Sensors
R0
R
T
T0
Athermal phonons are collected by superconducting Al fins (=~meV), creating quasi particles that are then trapped by the W Transition Edge Sensors (TES), held in equilibrium between Normal and Super Conducting temp using Electro-Thermal Feedback (ETF). SQUIDs measure change in current
Al
Superconducting Al Collector
W Transition Edge Sensor (TES)
Ge or Si
phonons
Cooper Pair
1 m TES
Quasi-particle assisted athermal phonon sensors provide much faster s timing than ms timing from thermal phonon sensors like used in EDELWEISS/CRESST

## Slide 8: Contact-Free High Voltage Detectors
100-gm single-e sensitive Contact Free Si HV Detector. Signal amplification observed without increase in leakage up to 300 V. Laser calibration done.
Initial demo with 250 gm Ge with =7 eV
https://doi.org/10.1016/j.nima.2017.02.032
Single-e/h pair 100 gm Si :
10.1016/j.nima.2021.165489

## Slide 9: Hybrid HV Detector
Phonon-mediated High-voltage Detector with Background Rejection for Low-mass Dark Matter and Reactor Coherent Neutrino Scattering Experiments: https://inspirehep.net/literature/1802528
Charge transport from LV region to HV almost 100%
55Fe
241Am
Main idea: Monolithic detector with a LV and a HV side – LV to measure primary phonons like iZIP and HV to measure NTL phonons. Do it without significant NTL pollution from HV to LV. ~100gm
Discrimination improves at low energies. Funded by DOE to push the DM and CENS discovery potential – background is key to discovery

## Slide 10: ~100gm 0-V sapphire detector with ~17 eVNR  baseline resolution
Calibrated based on 13.9KeV line. Exact value is within 15-18 eV, based on peak
~100 gm 3”x 4mm sapphire detector shown
~200 gm 3”x1cm sapphire detector also used
Calibration: Internal 55Fe, 241Am and external 57Co, 252Cf, AmBe.
Faster phonon pulses provide better position information, background rejection
https://arxiv.org/abs/2203.15903

## Slide 11: Low-Threshold Ge Detector inside Fully Hermetic Ge Shielding
Ge 3”x1” G15
Ge 3”x1” G22
Ge donut 3”x1”
12gm Ge coin. Next runs with~30-75 gm Ge coins
Inner active veto for highly effective (~100%) background rejection from Radon (and other) decays on detector sidewall and nearby copper in addition to reduction of Compton background by ~90%
MINER has several detector technologies in place, some focused towards establishing robust background models and some focused on signal detection

## Slide 12: $5M Dedicated Fab @ TAMU 1st SNOLAB Tower Completed!
Polish
Deposition
Photo Coat
Circuit Mask Exposure
Chemical Etch
Multi-step process repeatable for high quality detectors
XRD
Inspect and Package

## Slide 13
External muon scintillation veto in place recently

## Slide 14: Gm-Scale NUCLEUS calorimeter with thermal phonon sensors
based on CRESST technology
Thermometer
Transition-edge-sensor
20
0
20
40
60
80 100
time, ms
0.1
0.05
0
0.15
0.2
0.3
0.25
SQUID output, V
Δ𝑇 = Δ𝐸
𝐶
SQUID output [V]
Measured heat pulses (ms time constant compared to s for MINER)
CaWO4 and Al2O3 crystals
CaWO4
CaWO4 and Al2O3 crystals read-out with W-TES
Based on CRESST technology
Al2O3 prototype with threshold Eth = (19.7 0.8) eVnr
Arrays before cutting with
W-TES (20x20x5) mm3
CaWO4
Al2O3

## Slide 15: The NUCLEUS detector concept
Target crystals:
Two 3x3 arrays with a total mass of
6g (CaWO4) + 4g (Al2O3)
Inner veto: TES-instrumented holder to reject surface backgrounds and holder-related events
Germanium outer veto for active g/n background rejection
Si wafer
+ W-TES
Holding plates with electrical & thermal contacts
NUCLEUS slides from R. Strauss
Notes: - Reference to proof of concept?
- IV: detector support + 4pi veto
COV: 6 individual crystals with total mass of about 4 kg Ge, charge read-out

## Slide 16: O(100 counts/ (keV kg d)) seems to be in reach
Outer veto
Inner veto
Anti-coincidence
PRELIMINARY
Extensive GEANT4 Monte Carlo simulations of the full NUCLEUS setup have been performed
Estimated rate budget in CaWO4 (10-100 eV)
CEnNS
210Pb*
atmospheric m’s
atmospheric
neutrons
Muon veto
ambient g’s**
* 1 kBq/kg
** g-bck based on measurements @ VNS
Assembly has started at TUM
NUCLEUS slides from R. Strauss
Notes: Does the capture in the b4c produce any gammas or similar?
What does reduces impact of secondary neutrons mean?

## Slide 17: Nearly finished the experimental design and are preparing the NUCLEUS blank assembly.
Design phase
Blank assembly & Commissioning
@ TUM
On-site installation
@ Chooz
2023
Performance
Calibration
Background
2023
Towards a CEnNS precision measurement
stat+sys
stat
stat+sys
stat
Towards
NUCLEUS-1kg
Physics Run
NUCLEUS-10g
NUCLEUS slides from R. Strauss

## Slide 18: Ricochet
DETECTORS
Ge (semi-conductor) & Zn (super-conductor)
Ge: 22 eV RMS (heat). Target 10 eV heat, 20 eV charge
Gamma/recoil discrimination
1000 grams: 3x3x3 arrays of Ge & 3 x 3 Zn
(1) LOW ENERGY THRESHOLDS:
(2) BACKGROUND REJECTION:
(3) SIGNIFICANT TARGET MASS:
Target Crystal
Demonstrator Holder
Cryocube
RICOCHET slides from J. Formaggio

## Slide 19: Ricochet
REACTORS:
ILL Grenoble Reactor
(1)HIGH OUTPUT
58 MW power
(2)HIGH FLUX
~1.2 x 1012 ν/cm2/s
(3)BACKGROUND REDUCTION:
15 m.w.e overburden; heavy shielding
RICOCHET slides from J. Formaggio

## Slide 20: Ricochet
RICOCHET slides from J. Formaggio

## Slide 21: Q-Array TES Chip Testing
4
Recent R&D run at UMass Amherst in December 2021
Operated “Gen 2” TES chips coupled to a 1 gram silicon target
  Chips designed at Northwestern, fabricated at Argonne
Baseline resolution of 55 eV, calibrated with an 55Fe X-ray source
Future tests: resolution improvements, move to a superconducting target
TES
Absorber
Thermal Bath
“Meander” Impedance
RICOCHET slides from J. Formaggio

## Slide 22: Sharp Increase in Background: Non-Ionizaiton
Lowered sub-keV thresholds among DM/CENS experiments reveal a new signal of unknown origin. Typically starting at energies below 1 keV, the signal rises exponentially towards lower energies.
The signal is observed in various experiments with different detector materials, sensors and holding structures, below and above ground, at different temperatures and background levels.

## Slide 23: Sharp Increase in Background: Ionizaiton
An understanding of the observed background below 1 keV has a top priority for current low-threshold experiments, since this energy region is a crucial part of the DM/CENNS ROI
Uncovering the origin and whether it is a common effect among all the experiments, is a difficult task. Needs further collaborative work
Due to variations in the shape, rate and time dependence of the signal among experiments, detectors and measurements, a dark matter (DM) explanation seems unlikely.

## Slide 24: Summary
Reactor CENS is yet to be discovered – can open doors to new fundamental physics and applied nuclear non-proliferation programs
MIER, NUCLEUS and RICOCHET (and others) use many different low-threshold detectors developed for both DM and CENS experiments
Rich collection of targets (Ge, Si, Al2O3, CaWO4, Zn) and detection methods (0V, low-voltage, HV) with athermal/thermal phonon sensors
Required threshold (sub-keV and down to 100 eV) achieved in multiple detectors on MINER, NUCLEUS and RICOCHET
~100DRU backgrounds appear possible for multiple experiments using active inner veto (NUCLEUS, MINER). ~1000DRU already achieved with passive shielding only (MINER).
Sharply rising background observed in multiple detectors (MINER, NUCLEUS) at low (sub-250 eV) energies. Problematic for DM searches but can live with it for CENNS searches.