## Slide 1
Periodic Table of The Elements
Disclaimer: The views herein are solely those of the author and do not imply…
Me: (a) GeVTeV [… LEP, LHC] (b) keV  meV
Assignment (I think)
In 20 minutes, describe
Commonalities (where we speak the same language)
Potential common interests
Key investments
No way to be comprehensive
My personal slant (presenter-dependent biases)

## Slide 2: BES Grand Challenges
An elucidation of key questions
2007
1 How do we control material processes at the level of electrons?
2 How do we design and perfect atom-and energy-efficient synthesis of revolutionary new forms of matter with tailored properties?
3 How do remarkable properties of matter emerge from complex correlations of the atomic or electronic constituents and how can we control these properties?
4 How can we master energy and information on the nanoscale to create new technologies with capabilities rivaling those of living things?
5 How do we characterize and control matter away—especially very far away— from equilibrium?

## Slide 3: Basic Research On…
and many more…

## Slide 4: How to See Small Things
B Savitzky et al., Microscopy and Microanalysis (2021).
Static (structure)
Dynamic / Environment (function)
Atom ~Å
Speed of sound
~1 Atom/100 fs
meV (spectroscopy)
chemical sensitivity
Probe properties
(, , MFP)
Field of view
~10-6 .. 100 m


## Slide 5: Probes: electrons, photons, neutrons
Probe |  | x | t | Flavors
 | barn | nm | s | 
n | 101 | 106 | 10-3 | Reactor, Spallation sources
γ | 102 | 100-1 | 10-9 | Storage rings
 |  |  | 10-15 | FELs
e− | 105 | <0.05 | 10-5 | TEM, STEM, ...
Details!
: Carbon - 1Å n,  300 keV e

## Slide 6: User Facilities

## Slide 7: Seeing Small Things
d
λ
Flux
Brightness
Factor 2 in 2D resolution needs 24=16 x Brightness
in 1 dimension
Brilliance or Spectral Brightness
Some experiments need flux
Some need brightness
Some need spectral brightness

## Slide 8: Accelerator-based Characterization Tools
Annoying Synchrotron Radiation

## Slide 9: Synchrotron X-ray Light Sources (1st – 3rd Generation)
1st generation – parasitic use of synchrotron radiation [1960s – 1970s]
2nd generation – dedicated sources (bend magnet) [1980s]
3rd generation – insertion devices [1990s]
David Attwood, UCB 2007
104

## Slide 10: Synchrotron X-ray Light Sources  Diffraction Limit
Shin AAPPS Bulletin 2021
Double Bend Achromat
Triple Bend Achromat
Multi Bend Achromat
Hybrid MBA: SuperB design

## Slide 11: MBA Storage Rings
Existing (not MBA)
Upgrade/New
Construction
Bartolini 2017

## Slide 12: Free Electron Lasers
Uncorrelated electron motions
Correlated electron motions
Microbunching
Ways to create very short pulses

## Slide 13: FELs vs Storage Rings
1/10,000
1,000,000,000
what a laser buys you
SR
FEL
LCLS – 1st Hard X-ray FEL (2009)
Femtosecond Pump-Probe
Diffract Before Destroy

## Slide 14: Towards an Understanding of Photosynthesis
Kern et al. Nature 2018
Splitting water with 4 photons
Observing the Oxygen Evolving Complex with
Diffract Before Destroy + X-ray Emission Spectroscopy at LCLS
(Artificial photosynthesis)

## Slide 15: Peak and Average Brightness
LCLS-I
ns
ps
nJ
ms
fs
mJ
Storage Rings
1/104
106
Peak brightness (per pulse)
1
1
10huge
Average brightness
1

## Slide 16: High Repetition Rate FELs
Overcome the power limitations of warm linacs with superconducting RF
European XFEL
LCLS-II
SCRF: NP | HEP | BES

## Slide 17: Reactor and Spallation Neutron Sources
Anderson 2021

## Slide 18: Improving the Internal Combustion Engine
Wissink et al. PNAS 2020
Monitoring strain evolution of an alloy in a cylinder head in an operating engine using SNS

## Slide 19: Ultra-High Brightness Electron Linac
The Electron Microscope
“It would be very easy to make an analysis of any complicated chemical substance; all one would have to do would be to look at it and see where the atoms are. The only trouble is that the electron microscope is one hundred times too poor … I put this out as a challenge: Is there no way to make the electron microscope more powerful?”
– Richard P. Feynman, 1959,
“There’s Plenty of Room at the Bottom”
Y Yang, et al., Nature 2017
We can now see and identify every atom in a nanoparticle
Here: 6,569 iron and 16,627 platinum atoms in an iron-platinum nanoparticle

## Slide 20: Computer-Readable X-ray and Electron Detectors
Until ~10 years ago
Phosphor fiber-optically coupled to a CCD
Fiber-optic  radiation damage
QE (multiple conversions)
PSF (poor spatial resolution)
Speed (slow CCD readout)
Computer readable!
Phosphor
Fiber Optic
CCD
Phosphor
Fiber Optic
CCD
Canonical X-ray Detector
Canonical e Detector

## Slide 21: Hybrid Pixel X-ray Detectors
e.g. macromolecular crystallography
Connection: LHC (and before)

## Slide 22: CMOS Image Sensor-based Electron Detectors
Connection: ILC

## Slide 23: Data – Parochial Example
Per microscope rates today ~100 GB/s
x N microscopes
More generally (across facilities):
  Data volumes 
  Desire: data  information
  No (yet) obvious way to trigger
  History of serendipity
Opportunity?
Film
CCD
CIS
Data rates for cameras at the
National Center for Electron Microcopy

## Slide 24: BES Accelerator and Detector Research Program
Mission: Sustain research in accelerators and detectors to provide support for BES scientific user facilities
Support of existing facilities to guarantee their continued performance excellence and provide improved operating capabilities
Support of future electron, light, and neutron sources through innovative concepts, modeling, and design and testing of accelerator component prototypes.
Support of detectors capable of acquiring electrons, x-ray and neutron scattering data that will match the requirements of the fast advancement of electron, x-ray, and neutron sources
Support of next generation of x-ray optics instruments to advance photon-based science
How BES supports improving the state of the art
Slides thanks to Eliane Lessner / ADR program manager

## Slide 25: Some Supported Research Areas
High-repetition rate photo-injector: 1 MHz, CW injector
    Feasibility demonstration of a VHF SC RF Injector
SC undulator system that will increase hard X-rays brightness at APS –possible precursor to an FEL SCU system
High repetition-rate electron, neutron, and photon detectors covering a wide energy space
Development of seeding and pulse tailoring techniques for next-generation FELs
On-axis swap-out injection studies for optimizing the performance of diffraction-limited storage rings
Development of ultrafast x-ray optics with nanosecond temporal resolution for time-resolved x-ray science
Ultrafast structural dynamics at the nanoscale in MeV-UED
Machine Learning methods applied to beam-based optimization in circular machines and surrogate modeling for XFELs

## Slide 26: Funding Distribution: 8% University; 92 % Facilities
Chart: 
| Accelerating Structures | Advanced Dynamics | Detectors | Machine Learning | Photoinjectors | SC Undulators | TeraHertz | UED | XFEL Research | X-ray Optics
 | 0.035745 | 0.065069 | 0.18963 | 0.039007 | 0.16773 | 0.091328 | 0.017757 | 0.098327 | 0.098541 | 0.19687

## Slide 27: Current Research I
Feasibility Demonstration of Cavity-based X-ray FELs: CBXFELs will offer very high longitudinal coherence and the ability to trade off peak and average power, pulse duration and bandwidth
Superconducting Undulator R&D: FEL performance of multiple planar niobium titanium superconducting undulators
Development of Sub-fs Capabilities at FELs: Two-color attosecond soft X-rays based on a double chirp/taper scheme, as well as isolated TW pulses using superradiance in a modulated electron beam.
High-Power, High-Repetition-Rate THz Capabilities for High-repetition Rate FELs: Accelerator-based terahertz (THz) source driven by high-repetition rate superconducting linacs
Machine Learning for Improving Accelerator and Target Performance: Extend and integrate Machine ML techniques to enable timely and reliable condition monitoring, failure prediction, and parameter optimization of a high-current proton accelerator and target equipment

## Slide 28: Current Research -II
Very High-Speed EELS Detector: High-speed detector for electron energy loss spectroscopy, complement to a 100 K frame/second electron detector for use in “4D” Scanning Transmission Electron Microscopy
SparkPix-RT: An Edge Computing Engine for Ultra-Fast Photon Science Detectors: Address data transfer bottleneck in megapixel 100 kHz-1 MHz rate, high pixel occupancy X-ray detectors to the data acquisition system
Neutron detector development for high-rate neutron reflectometry: Scintillator-based, 2D positive-sensitive, large-area neutron detector with exceptional count rate capability
Evaluation of High-X Materials for Photon Sciences: Investigate different candidate materials of High -Z (high x-ray stopping power), for use in hybrid pixel array detectors (PAD) for imaging applications
X-ray Diffractive Optics for Accelerator Science: X-ray diffractive optics technology to measure the X-ray beam both spatially (beam size) and temporally (beam pulse duration) with high precision

## Slide 29: Current Construction Projects – X-ray SR Upgrades
APS Upgrade
ALS Upgrade
TPC: $815M
CD-4: 2QFY26
TPC: $590M
CD-4: 4QFY29

## Slide 30: Current Construction Projects – SNS Upgrades
Power Upgrade
TPC: $272M
CD-4: 4QFY28
Second Target Station
TPC: $1,800-3,000M
CD-2: 2QFY25

## Slide 31: Current Projects – LCLS Upgrades
LCLS-II
TPC: $1,136M
CD-4: 1QFY24
LCLS-II- HE
TPC: $660M
CD-4: 2QFY31
CRMF
TPC: $70-98M
CD-4: 2QFY23

## Slide 32: Overlaps

## Slide 33: Amuse Bouche
Accelerator-based probes
  (with concomitant detector advances)
  Blurry snapshots  movies
Broad common interests
  Technology, QIS, Microelectronics, …
Materials science towards HEP goals
BES facilities for HEP experiments?
…?

## Slide 34: Community Inputs

## Slide 35
Coupling precision
ILC vs XCC
0.5 x 106 Higgs events
XCC -- XFEL Compton Collider gg Higgs Factory
From: Tim Barklow (SLAC)

## Slide 36
C3 Demo:
LCLS-X:
100 nm Cryo Cu RF Injector
100 mJ LCLS-NC soft x-ray
100 mJ soft x-ray production and focusing Demo concurrent with C3 Demo:
Research on XCC high energy/pulse XFEL production and focusing can lead to new opportunities in photon science.
XCC -- XFEL Compton Collider gg Higgs Factory
From V. Shiltsev’s Accelerator Frontier Vision talk on Thursday:
From: Tim Barklow (SLAC)