## Slide 1: Questions about timing and synchronization
What is the requirement for timing synchronization across the different chips and components in the system?
For both CRYO and COLDATA, what is the method for synchronizing the system clocks?
How will synchronization be monitored?
How are phase issues associated with frequency multiplication or division handled, to ensure that the correct phase is always obtained?
What is the sensitivity of internal PLLs to voltage and temperature? How will differences in path length (cable lengths primarily) be accounted for?

## Slide 2: What is the requirement for timing synchronization across the different chips and components in the system?
The timing system distributes a 62.5 MHz clock and provides a method to synchronize this clock to better than 1 ns at each timing end point (the WIB is a timing end point).
We would like each ADC to sample at the same time to within a few ns.

## Slide 3: For COLDATA, what is the method for synchronizing the system clocks?
The timing system will initialize equal-time 64-bit time stamp registers in every WIB as well as for the Photo Detector readout system.
Each COLDATA will have a local (15-bit) time stamp that will count 62.5 MHz clock ticks.
The COLDATA time stamp register can be zeroed by a Fast Command from the WIB
  The WIB will need to delay this Fast Command (by the difference in cable delays, at least for 23 m & 7 m cables)
  All COLDATA timestamps should agree not only within 1 APA, but within a 10 kTon detector.

## Slide 4: How will synchronization be monitored?
Each WIB will keep a 64-bit time stamp that will also count 62.5 MHz clock ticks.
The WIB will check that all COLDATA data frames have the expected time stamp.

## Slide 5: How are phase issues associated with frequency multiplication or division handled, to ensure that the correct phase is always obtained?
COLDATA handles the divide by 32.

## Slide 6: What is the sensitivity of internal PLLs to voltage and temperature? How will differences in path length (cable lengths primarily) be accounted for?
The COLDATA PLL is insensitive to voltage (within its operating voltage range). The PLL is sensitive to temperature, but the change from room temperature to cold is much smaller than the design bandwidth of 1.5 MHz.
The change can be compensated by choosing a different PLL band (switching different capacitors in the VCO).

## Slide 7: Voltage mode pre-emphasis?
The noise/jitter caused by the spikes is much less than that caused by ISI which can be compensated significantly by our proposed techniques. (Current-mode equalization and voltage-mode pre-emphasis). The measurement results demonstrate wide open eye-diagrams and very good BER performance