## Slide 1: ICARUS Shifter Manual
Version N. 1
Created by: C. Montanari, Modified by …
Last updated: Nov 14, 2019

## Slide 2: Content
Revision Hystory – Slide 2
About this Manual – Slide 3
Instructions for the shifters during the cryogenic commissioning phase (V1)
E-log example page
E-log data entry page
West Module internal cryogenic display
East Module internal cryogenic display
Start the ifix application
Reference contacts

## Slide 3: Revision History
V1: First edition – Contains the instructions for the cryogenic commissioning phase – Claudio Montanari ; Donatella Torretta ; Angela Fava – November 14, 2019

## Slide 4: About this Manual
The present document describes the instructions and procedures for the people on shift during the ICARUS detector commissioning and operation.
The shifter is required to have read and understood the instructions contained in the present manual prior to take the shift.
On the last page of this manual, a list of useful numbers and contacts is provided. This list DOES NOT substitute the “List of Experts on call” that is provided by the Run Coordinator.
Amendments, major corrections and additions to the present manual have to be reported in chronological order in the “Revision History” slides, with names and dates.
This document is provided both as PDF (non editable) and PPTX (editable) formats as docdb # …
A printed version of the last revision of this document has to be available in the Control Room, together with the list of the Experts on call.

## Slide 5: Instructions for the shifter (1 of 6)
The shifts take place in Fermilab Wilson Hall 1st floor, ROC West room.
The shift schedule is: 8 AM – 5 PM ; 5 PM – 12 AM ; 12 AM – 8 AM.
Each shift is covered by one person that is required to remain in ROC West all the time, except from brief absences (max 20 minutes) or emergencies (e.g. fire or tornado alarms).
The shifter is required to arrive in ROC West at least 10 minutes before the beginning of the shift to receive the most updated information from the previous shifter.
In case of problems or delays in taking the shift, the person that is scheduled to take the shift is required to call ROC West in due time to inform the present shifter. Depending on the problem, the shifter is also required to call the Run Coordinator to find appropriate solutions for a substitute.
If a shifter, that has not previously notified the delay, is not showing up to within 10 minutes from the beginning of the shift, the current shifter is required to call the Run Coordinator, and, in case of no answer, the following persons in the call list provided at the end of this manual and ask for instructions. The call and the related instructions have to be notified in the e-log.

## Slide 6: Instructions for the shifter (2 of 6)
At the shifters’ location, in ROC West, three monitors are used to display the following windows:
  The e-log page;
  The internal temperature and level probes of the East and West modules;
  The status of the cryogenic plant.
  A fourth display is present, that is not used during the cryogenic commissioning.
  Examples of displays A, B and C together with the instructions on how to operate them are reported on slides 12 to 13, 14 to 15 and 16 to 17 respectively.

## Slide 7: Instructions for the shifter (3 of 6)
Upon arrival the shifter receives the most updated information from the previous shifter on the status of the experiment, on the activities to be performed during the shift and on additions or substitutions on the call lists.
  The shifter registers on the e-log:
    his or her name;
    the information received by the previous shifter ;
    the additions/modifications on the call lists;
    The status of the experiment: cooling/cooling stopped – filling (%)/filling stopped – pressure stabilizing - other…

## Slide 8: Instructions for the shifter (4 of 6)
During the shift the shifter is required to:
  During the cooling.
    The cooling is a slow process, so do not expect any rapid variation of the temperatures. If this event will occur, it has to be notified to the Technical Coordinator or his Deputy.
    Check the internal temperatures of the East and West modules at least once per hour (all temperatures are displayed in K);
    If the temperature difference between any two probes inside the same module reaches 47 K, the shifter has to call the cryogenic operator on shift and ask to stop the cooling.
        The call and the stop of the cooling procedure have to be recorded on the e-log.
      When the temperature difference of all probes inside both modules go below 35 K (this will take several hours) the shifter will call the cryogenic operator on shift to tell him that the cooling process can be re-started.

## Slide 9: Instructions for the shifter (5 of 6)
During the shift the shifter is required to:
  During the filling.
    The level of the liquid in the two modules are displayed on the cryogenic status page as the parameters circled in red on slide 11.
    The levels displayed on the internal probes display will turn on only at the very end of the filling process.
    During the filling, before the lowest one of the internal level probes turns on (in any of the two modules), the shifter is only required to review the internal level probes and the internal temperature probes every hour. Anomalies in the readings have be reported timely to the Technical Coordinator or its’ Deputy and registered in the e-log.
    As soon as the first internal level probe will turn on, the shifter will notify both the Technical Coordinator and the Cryogenic Operator on shift and register the event in the e-log.

## Slide 10: Instructions for the shifter (6 of 6)
During the shift the shifter is required to:
  During the filling (…continued from previous slide).
    From the moment when the first one of the internal level probes will turn on (point iv on the previous slide) the shifter will register on the e-log the status of the level meters every hour by taking a snapshot of the monitor. There are 4 sets of 5 internal level probes in each module. Each set is positioned in correspondence of one of the top corners of a module. The filling is complete when all second to last probes on all four corners of a module are lit.
    The shifter calls the Cryogenic Operator on shift as soon as the first second to last probe in a module turns on to notify that the filling in that module has to be stopped in a short time. The shifter calls the Cryogenic Operator on shift when the fourth second to last probes of a module has been reached to stop the filling in that module.
    The time of switching of all the internal level probes has to be recorded on the e-log.

## Slide 11: Level probes on the Cryogenic Plant Display
IMAGE TO BE INSERTED

## Slide 12: E-log sample page
IMAGE TO BE INSERTED

## Slide 13: E-log instructions
Text to be inserted

## Slide 14: Internal probes display
IMAGE TO BE INSERTED

## Slide 15: Instructions on how to display the Internal Probes page
Text to be inserted

## Slide 16: Cryogenic Plant display
IMAGE TO BE INSERTED

## Slide 17: Instructions on how to display Cryogenic Plant page
Text to be inserted

## Slide 18: Useful numbers
Role | Name | E-mail | Phone
Control Room |  |  | 
FD-Building |  |  | +1 (630) 840-6974
Technical/Run* Coordinator | Claudio Montanari | cmontana@fnal.gov | +1 (331) 701-8993
Deputy Technical/Run* Coordinator | Angela Fava | afava@fnal.gov | +1 (331) 701-8035
Cryogenic Manager | Michael Geynisman | hope@fnal.gov | +1 (630) 244-8703
* Ad interim