## Slide 1: APA3 in FELIX readout
Giovanna Lehmann Miotto
November 15th 2019

## Slide 2: APA 3 status
One FEMB running on a standalone clock and thus not completely synchronized with the others
WIB data formats (frames @2MHz):
RCE x 4 links | FELIX x 2 links
WIB header
Colddata 1
Colddata 2
WIB header
Colddata 1
Colddata 2
Colddata 3
Colddata 4
1 FEMB
1 FEMB
1 FEMB

## Slide 3: What happens with a bad FEMB
RCE case:
  Since each FEMB data is sent independently, it is relatively easy to realign data coming in the RCE (fix provided long time ago), though data compression must stay off
FELIX case:
  2 FEMBs come together and the colddata get corrupted
  No recovery

## Slide 4: Thinking towards DUNE
We foresee to have event building in the WIBs (2 FEMBs packed together) for DUNE
Is it possible to fix data in the WIB itself in case of a similar problem?
At present if one FEMB is turned off it seems that no data arrive for two FEMBs
  Can 0 padding be easily implemented in the WIB?

## Slide 5: Short term solution
APA3 put back on RCE readout
It would really be nice to learn from ProtoDUNE how to deal with such issues in interplay between FELIX/WIB
  Workplan over 3-4 months? Are there resources to work on the WIB FW?