## Slide 1: Magnets 302.2. Shipment Requirements and Execution
Maria Baldini - FNAL
HL-LHC AUP IPR DOE/SC Review – Jan. 14th–16th 2020

## Slide 2: Outline
Requirements
Travelers and shipping plans
Shock data
Lesson learned: coil 206, humidity test
Summary
Lab
Logo

## Slide 3: HL-LHC AUP shipments

## Slide 4: Coil shipping Requirements
Coils
<500 microstrain = shocks <10 g (FEM analysis on Docdb 2478)
dedicated shipping fixtures
Provision against moisture
A minimum of 2 accelerometers on the LE and RE
5g and 10 g shock watches
Air ride dedicated truck
Notes: FEM analysis confirmed that shocks up to 10 g are acceptable using the AUP MQXFA shipping fixture

## Slide 5: Magnet shipping Requirements
Magnets
conductor strain shall be <500 microstrain
the laminations shall always remain in contact during any MQXFA
4 point lifting and shocks < 5 g (FEM analysis in DocDb 838)
dedicated shipping fixtures
2 accelerometers on the LE and RE
5 g and 10 g shock watches
Air ride dedicated truck

## Slide 6: Coil QXFA Shipping travelers
Procedures are well defined by travelers in each lab.

## Slide 7: Planning
Coils shipped to LBNL from FNAL and BNL
fixture shipped back to BNL and FNAL from LBNL
At production peak: 6 shipping fixture (two spares)
Handling and shipping plan: US HiLumi Doc DB 1686
Magnets shipped to BNL from LBNL
Magnets shipped to FNAL from BNL
At production peak: 4 shipping fixture (one spare)
LABS | Trips | # fixture/crates | Accelerometers | # batteries
FNAL coils | 50 | 2+ 1 spare | 4 (2 for each fixture) +1 spare to be returned with the empty crate | 200
BNL coils | 50 | 2+ 1 spare | 4 (2 for each fixture) +1 spare to be returned with the empty crate | 200
LBNL magnets | 25 | 3 crates + 1 spare | 6 (2 each) | 100
BNL magnets | 25 |  | keeps the ones received and use them for the shipment | 100

## Slide 8: LARP Coil shipments summary (max shocks)
MQXFAP1
MQXFAP2

## Slide 9: LARP Magnet shipments summary (max shocks)
Accelerometer on the crate
loading/unloading
HL-LHC AUP IPR DOE/SC Review– Jan 14-16, 2020
Notes: Accelerometers on the crate for highest value after 2015
No info about accelerometers position before 2015

## Slide 10: Shock measurements: accelerometers
GP1L Senseware
g range up to 6.7 g
Sample rate 100 Hz
Frequency response 50 Hz
Event recorded if > 3g
SLAMSTICK X and C
g range up to 25 g and 16 g
Sample rate up 20 kHz or 3.2 kHz
Frequency response up to 2000 Hz or 500 Hz
Vibration spectral analysis
From FNAL coil 115
From BNL coil 206
From magnet MQXFA03

## Slide 11: Accelerometers data set examples
GP1L: entire trip in a snapshot
GP1L: event >3g, 100 s

## Slide 12
Accelerometers data set examples
Sept 21 2019
36 min of data

## Slide 13
AUP Coil shipments summary (max shocks)
MQXFA03
MQXFA04
Max shocks are during loading/unloading
No shock > 10 g

## Slide 14: AUP magnet shipments summary (max shocks)
Z-axis
After testing
No shock > 5 g

## Slide 15
Lesson learned: Coil 206 DR
  Example of marks under Clamping Rib 4

## Slide 16: Coil 206 DR: Axial Restraints Not Engaged
HL-LHC AUP IPR DOE/SC Review– Jan 14-16, 2020

## Slide 17: Accelerometer data for coil 206
GP1L: <5g
SLAMSTICK shocks > 10g along x and y axes
No shock > 10g along z-axes

## Slide 18: Accelerometer data for coil 206
GPL1 event time is 20 ms
SLAMSTICK event time is 2 ms
Very sharp shocks along x and y directions: coil is shaking because is not clamped well
Coil Vertical Deflection (mm)
Coil deformation is ~56 (µm)
Coil Equivalent Strain,
Maximum strain is ~1.4 µε
FEM: 1g Vertical Inertial Load---upward on Coil Only

## Slide 19: Coil 206: lesson learned
  Mitigations:
  Add rubber material under the fixture clamps
  Install locking nuts on axial restraints to prevent screws from backing out
  Wrap coil in Kapton/Mylar around fixture
  All those procedures have been specified in the coils shipping and handling requirements (Docdb 820)
  Travelers have been updated and modified accordingly
Based on results and FEM analysis Coil 206 was accepted

## Slide 20: Humidity and Temperature test
Trip from FNAL to LBNL (Nov 8-Nov 14 2019)
Coil 117
  80 units of desiccant in the crate
Empty crate
  10 units of desiccant in the empty crate
FINDINGS
Relative humidity in the empty crate is around 10%-20% higher than in the coil 117 crate
During the trip: relative humidity never raises above 33 % for both crates.
Relative humidity values are well below 60%
Humidity will be measured from now on for each trip
Data from Nov 11-14

## Slide 21: 302.2.: Summary
Requirements for QXFA coils and MQXFA magnets shipping and handling are established and well defined.
No shocks above 5g were observed for MQXFA magnet shipments
Shocks above 10g were observed only for 206 coil trip
Problems were identified and mitigated: Travelers and requirements were updated
Lab
Logo

## Slide 22: Backup Slides
You should keep the pie-charts and tables from the CAM e-Toolbox as backup slides in case someone asks questions

## Slide 23: Magnet MQXFA Shipping traveler @FNAL
FEM analysis confirmed that shocks up to 10 g are acceptable using the AUP MQXFA shipping fixture

## Slide 24: MQXFAP2 yoke and axial plate accelerometers

## Slide 25: FE Model Overview
25
The material of the coil shipping fixture components is Aluminum 6061.
All components are in contact using contact elements
  Contact174 --- 3D surface-surface contact element
  Target170 --- Associated 3D target element
  Friction coefficient is 0.2
  Inside coil winding --- bonded
  Between shipping fixture components --- bonded
  Between coil and fixture --- frictional, mu=0.2
Support Tube
Support Channel
Base Channel
End Stopper
Side Rail
Coil Clamp
Rubber Isolator
Fixed support on the bottom e surface
Vertical inertial load

## Slide 26: 5g Vertical Inertial Load
0.5GPa Isolator modulus
Vertical Deflection (mm)
0.39 mm
Coil Equivalent Strain,
Maximum strain is ~25.4 µε
Coil Vertical Deflection (mm)
Coil deformation is ~105 (µm)

## Slide 27: 10g Vertical Inertial Load
0.5GPa Isolator modulus
Vertical Deflection (mm)
0.71 mm
Coil Equivalent Strain,
Maximum strain is ~52 µε
Coil Vertical Deflection (mm)
Coil deformation is ~210(µm)

## Slide 28: Results with stiffer or softer isolators
Maximum vertical deflection (mm)
Coil deformation (mm)
Coil Strain (µε)
When the isolators are stiffer, the overall deflection and coil deformation become smaller.
  The stiffer the fixture is, the larger safety factor we have.
Coil strain is much below the limit of 500 µε with the current fixture design under 5g and 10g loads.

## Slide 29: 10g Vertical Inertial Load---upward (All parts)
29
0.5GPa Isolator modulus
Vertical Deflection (mm)
0.65 mm
Coil Equivalent Strain,
Maximum strain is ~16 µε
Coil Vertical Deflection (mm)
Coil deformation is ~653 (µm)

## Slide 30: 10g Inertial Load---Lateral (All parts)
30
0.5GPa Isolator modulus
Horizontal Deflection (mm)
Horizontal deformation: 1.42 mm
Coil Equivalent Strain,
Maximum strain is ~95 µε
Coil Vertical Deflection (mm)
Coil deformation (horizontal) is ~1.24 (mm)
Lateral inertial load