## Slide 1
RF Gun
S. Kazakov
11/25/2019

## Slide 2
F = 655.8 MHz
Coax_2_with_gun_no_potrt_eg_mode_2_materials
C:\CST_projects\ERDC\RF_gun\Coax_trans
File:
Design is based at standard 7/8’’ coaxial line.

## Slide 3
SS
Kovar
W
Alumina
Material | σ, S/m | %
Copper | 5.8 | 27.7
SS 316 | 1.45 | 23.9
Kovar | 2 | 46.9
W | 1.9 | 1.4
Alumina | Loos tg = 3E-4 | 0.14
Material | σ, S/m | %
Copper |  | 27.7
SS 316 |  | 23.9
Kovar |  | 46.9
W |  | 1.4
Alumina | Loos tg = 3E-4 | 0.14
Q = 629
Coax_2_with_gun_no_potrt_eg_mode_2_materials
C:\CST_projects\ERDC\RF_gun\Coax_trans
File:

## Slide 4
V = 2.9618E+5 V -> 1 J
V = 350 V -> 1.3964E-6 J
P_beam = 350 V x 12 mA = 4.2 W
Q_beam = 1338
Q_total = 430
P_wall = 9.067
P_total = 13.3 W
Curve 1
Curve 2
E-filed along curve 1
E-filed along curve 2

## Slide 5
C:\CST_projects\ERDC\RF_gun\Coax_trans\
Coax_2_with_gun_no_potrt_2_Q_cal_5
File:

## Slide 6
Qa = 36.6
Qb = 27.9
Qav = 32.3
Reflection G = (Qav – Q_total)/(Qav + Q_total) = 0.86
Power reflection = 0.74
Total power from source Ps = 13.3W / 0.26 = 51.2W

## Slide 7
C:\CST_projects\ERDC\RF_gun\Coax_trans\
Coax_2_with_gun_no_potrt_2_Q_cal_6
File:

## Slide 8
Qa = 103.
Qb = 105.
Qav = 104
Reflection G = (Qav – Q_total)/(Qav + Q_total) = 0.61
Power reflection = 0.37
Total power from source Ps = 13.3W / 0.26 = 21.2W

## Slide 9
C:\CST_projects\ERDC\RF_gun\Coax_trans\
Coax_2_with_gun_no_potrt_2_Q_cal_7
File:

## Slide 10
Qa = 46.9.
Qb = 47.8.
Qav = 47.4
Reflection G = (Qav – Q_total)/(Qav + Q_total) = 0.801
Power reflection = 0.642
Total power from source Ps = 13.3W / 0.26 = 37.2W

## Slide 11
C:\CST_projects\ERDC\RF_gun\Coax_trans\
Coax_2_with_gun_no_potrt_2_Q_cal_2
File:

## Slide 12
Qa = 160.4
Qav = 161
Reflection G = (Qav – Q_total)/(Qav + Q_total) = 0.455
Power reflection = 0.207
Total power from source Ps = 13.3W / 0.793 = 16.8W
Qb = 161.5

## Slide 13
C:\CST_projects\ERDC\RF_gun\Coax_trans\
Coax_2_with_gun_no_potrt_2_Q_cal_3
File:
Recommended geometry

## Slide 14
Qa = 46.2
Qb = 47.1
Qav = 46.7
Reflection G = (Qav – Q_total)/(Qav + Q_total) = 0.8
Power reflection = 0.64
Total power from source Ps = 13.3W / 0.36 = 37.0W
Recommended geometry

## Slide 15
Capacitive
Cap_1_kapton_gap_rnd_3d_acc_2
C:\CST_projects\ERDC\RF_gun\Capacitive\
File:

## Slide 16
Coax_2_with_gun_no_potrt_2_Q_cal_3_with_capacitive_2_ports
C:\CST_projects\ERDC\RF_gun\Coax_trans
File:
~128
~327
~ 20
~8.7

## Slide 17
Q=45.5
Radiation through port 2 is ~ -37 dB ( < 25 mW).