## Slide 1
Effect of Side and Foot Board Thickness Deviations
on
Wire Position
Lee Greenler
UW Physical Sciences Lab
2019 November 18

## Slide 2
a
δ
θ
What is the displacement, δ, of the wire for a given displacement, a, of the pin?
The wire displaces with the pin so the full displacement of the wire is equal to the pin displacement. But, only the part of the displacement perpendicular to the wire is important.
This part is:
δ = a cos θ
The perpendicular displacement of the wire varies linearly from this value near the pin to zero at the other end of the wire.

## Slide 3
For side boards θ is ~35.7 degrees so cos θ is approx. 0.81.
For foot boards θ is ~54.3 degrees so cos θ is approx. 0.58.

## Slide 4
For side board 10% too thick (= 0.32mm):
  If pin is displaced by full board overthickness,
  a = 0.32mm, δ = 0.32*0.81 = 0.26mm
  If pin stays centered on board, wire displacement would be less
If side board is 10% too thick and it’s sitting on another board 10% too thick:
  The pin can be displaced as much as:
  a = 0.64mm, δ = 0.64*0.81 = 0.52mm
So, depending on how the deviations stack up, the displacement of the wire near the pin on the U layer side board could be up to ~0.5mm (with 10% board overthickness).
Likewise, at the foot the U layer pin could be displaced by up to 3 board thicknesses, but the cosine factor is smaller:
a = 0.96mm, δ = 0.96*0.58 = ~0.5mm. (with 10% board overthickness)
This is with all errors the same direction and adding together.
Worst Case

## Slide 5
For side boards 10% too thick (= 0.32mm):
  Since tooth strip gluing fixture aligns inner surfaces of tooth strip and board the pin position of the first wouldn’t be significantly affected.
If side board is 10% too thick and it’s sitting on another board 10% too thick:
  The second board could be displaced as much as .32mm but, again, there would be little additional displacement from the outer board overthickness.
  a = 0.32mm, δ = 0.32*0.81 = 0.26mm
So, the displacement of the wire near the pin on the U layer side board could be up to ~0.26mm (with 10% board overthicknesses).
This is with all errors the same direction and adding together. Error magnitude would be the same for underthickness.
More Likely Case
Likewise, at the foot the U layer pin could be displaced by up to 2 board thicknesses, but the cosine factor is smaller:
a = 0.64mm, δ = 0.64*0.58 = ~0.37mm. (with 10% board overthickness)