## Slide 1: Primary Beamline Radio-Activated Water (RAW) Peliminary Design Review
Target Hall RAW - General Overview
Karlton E. Williams, II
February 19 & 20, 2020

## Slide 2
Nu Beam
to SURF, SD
Proton Beam
from MI-10
Absorber Complex
Target
Complex
Primary Beam Complex
Decay Pipe
Primary
Beamline
Fermilab
Main Injector
Tunnel
Proton Beam
Extraction
Target Hall RAW Room
Absorber Hall RAW Room
RAW System - Preliminary Design Review ISO Section View of Near Site – MI-10 to LBNF-30 Absorber Complex

## Slide 3: RAW System - Preliminary Design Review Target Hall RAW Systems
Systems located within the Target Hall RAW Room
Target RAW
Horn A RAW
Horn B RAW
Horn C RAW
Shielding Panel RAW
TH RAW Exchange
TH Intermediate
H+OH System
Other support equipment just outside the TH RAW Room
    RAW Capture Station
    Air Compressors
    Bottle Farm

## Slide 4: RAW System - Preliminary Design Review
Target Hall RAW Room
TARGET HALL COMPLEX
Target Chase

## Slide 5: RAW System - Preliminary Design Review
TARGET HALL COMPLEX
Target Hall RAW Room
Target Chase

## Slide 6: RAW System - Preliminary Design Review Target Hall RAW Room Arrangement
BEAM
Target Hall RAW Room
Target Chase
RAW Capture Station, Air Compressors, Bottle Farm

## Slide 7: RAW System - Preliminary Design Review Target Hall RAW Room Arrangement, cont.
RAW Exchange System
DI Casks
Target Shield Panel RAW
Intermediate Cooling Water
Horn A
Horn B
Horn C
Target
Piping Envelopes To Target Chase

## Slide 8: RAW System - Preliminary Design Review Target Hall RAW Room Arrangement, cont.
BEAM
Target Hall RAW Room
Piping Runs between RAW Room and Chase

## Slide 9: RAW System - Preliminary Design Review TH RAW Room - General Notes
NSCF reasonably certain about current layout, changes should be minimal
On main level of THC, same as high bay
Accessible only when beam is off
Large room, 36’ x 69’ x 22’ ceiling
  Room for a mezzanine if expansion upward is required
System outline boxes as shown are for area approximation only, not set in stone
Has containment for each system, containment at the door, and floor drains to contained & controlled sump
Fill for all systems is by 2” line from PB LCW

## Slide 10: RAW System - Preliminary Design Review Target Hall RAW Systems Block Diagram
Horn A
RAW System
Target
RAW System
Horn B
RAW System
Intermediate Cooling System
Other Target
Hall Loads
Target Hall
Cooling System
Surface Chillers
RAW ROOM
CF CIVIL SYSTEMS
Shielding Panel
RAW System
Arrow indicates direction of heat removal
Horn C
RAW System
Target Helium Systems
TARGET HELIUM ROOM
RAW ROOM
RAW Exchange System not shown
Targetry WBS
CF WBS
RAW Systems WBS

## Slide 11: RAW System - Preliminary Design Review

## Slide 12: RAW System - Preliminary Design Review

## Slide 13: RAW System - Preliminary Design Review Slide Title
Caption text for image.
Click to edit Master text styles
  Second level
    Third level
      Fourth level
        Fifth level