## Slide 1: Vacuum Design and Analysis
Beth Klein
Primary Vacuum Preliminary Design Review
March 10, 2020

## Slide 2: Agenda
Overview of Vacuum Layout
Vacuum Profile Plots
Magnet and Device Interfaces
Typical Weldment Drawings
Instrumentation and Controls
Compressed Air and Nitrogen
Turbocart Design
Main Injector Interface

## Slide 3: Primary Beamline Vacuum Sectors
Main Injector
Kickers
Lambertsons
BV221
BV210
BV203
BV200
BV214
Main Injector

## Slide 4: Vacuum Design
Mostly 3” tubing with some 4” tubing
Quadrupoles have 3” tube
Dipoles have MI elliptical tubing: 2.09”x4.84”
  Dipole beam tube marked for early procurement
6” tube through the wall
Typical dipole pump port
RF Slots
Typical pump port
3” tubing
Elliptical Tubing
BPM

## Slide 5: Primary Beamline Vacuum Profile
Vacuum system requirements:
Average total pressure of 1.0E-7 Torr or below
Maximum local total pressure of 1.0E-5 Torr or below
Assumptions:
Outgassing Rate = 1E-10
316L SS tubing
No bake, ultrasonically cleaned
Results:
Average Pressure = 7.44E-8 Torr 7.79E-8 Torr
Maximum Local Pressure = 1.83E-7 Torr 1.91E-7 Torr
7.79E-08
Chart: Length (meters)

## Slide 6: Primary Beamline Vacuum Profile for 20% failed pumps
Vacuum system Specification:
Average total pressure of 1.0E-7 Torr or below in case of failure of up to 20% of total number of pumps
Assumptions:
Outgassing Rate = 1E-10
316L SS tubing
No bake, ultrasonically cleaned
Results:
Average Pressure with 20% of pumps off = 1.34E-7 Torr
Local Maximum Pressure with 20% of pumps off = 2.98E-7 Torr
Chart: Length (meters)
1.34E-07
7.79E-08

## Slide 7: Primary Beam Enclosure Tunnel Cross Section
Cable Trays
Dipole Magnet

## Slide 8: Magnet and Device Interfaces
All flanges will use metal seals
Magnet/Device | Interface 1 | Interface 2 | Quantity of Device/Magnet
Dipole A | Transition Plate - Elliptical to 6" | Transition Plate - Elliptical to 3" | 13
Dipole D | EVAC Flange ISO 160 | Transition Plate - Elliptical to 3" | 12
Quadrupole - 3Q60 | 4" QD Flange |  | 4
Quadrupole - 3Q120 | 4" QD Flange |  | 17
Lambertson | 19" QD Flange |  | 3
Kicker | 6" Conflat flange |  | 6
C-magnet | 4" QD Flange |  | 1
Corrector magnet | Beam tube captured by aperture |  | 23
Multiwire | 4" QD Flange |  | 12
BPM | 4" QD Flange | Welded 3" OD Beam Tube | 24
Toroid | 4" QD Flange |  | 2
Wall Current Monitor | 4" QD Flange |  | 1
Gate Valve | 6" Conflat flange |  | 5
Beam Window | 4" QD Flange |  | 1

## Slide 9: Dipole Beam Tube
Dipole A - Transition plate and then bellows and EVAC flange will be welded prior to bringing in tunnel
Dipole D - EVAC flange will be welded on dipole beam tube prior to bringing in tunnel
Elliptical to transition plate – inside weld
Dipole A
Dipole D

## Slide 10: Dipole – Dipole Connection
Only flange will have to be made up in tunnel
Transition Plate
EVAC Chain Clamp
EVAC Flanges
6” Edge-Welded Bellows
Dipole A
Dipole D
Profile of knife edge seal

## Slide 11: Corrector Magnet Interface
Magnet aperture equals beam tube OD and captures beam tube
Split magnet during installation

## Slide 12: Primary Beam Window
Target Hall US Wall
Typical 4” QD Flange
LBNF Primary Beam Window
Beam

## Slide 13: Wall Penetration Weldment

## Slide 14: Typical Weldment Drawing

## Slide 15: Instrumentation and Controls
Name | Device
IP101D1 | Lambertson Ion Pump
IP101D2 | 
IP101D3 | 
IP101D4 | 
IP102A1 | Lambertson Ion Pump
IP102A2 | 
IP102A3 | 
IP102A4 | 
IP102B1 | Lambertson Ion Pump
IP102B2 | 
IP102B3 | 
IP102B4 | 
BV200 | Gate Valve
IP200 | 45 L/s Ion Pump
PG200 | Pirani Gauge
 | Turbo Cart Valve
IP201A | 45 L/s Ion Pump
IP201B | Ion Pump
IP201C | Ion Pump
IP202A | Ion Pump
IP202B | Ion Pump
 | Turbo Cart Valve
PG202 | Pirani Gauge
IP203A | 200 L/s Ion Pump
IP203B | 200 L/s Ion Pump
BV203 | Gate Valve
PG203 | Pirani Gauge
IP2040 | 45 L/s Ion Pump
IP2041 | 45 L/s Ion Pump
IP2042 | 45 L/s Ion Pump
 | Turbo Cart Valve
IP2051 | 45 L/s Ion Pump
IP2052 | 45 L/s Ion Pump
IP2060 | 45 L/s Ion Pump
IP2061 | 45 L/s Ion Pump
IP2062 | 45 L/s Ion Pump
IP2071 | 45 L/s Ion Pump
IP2072 | 45 L/s Ion Pump
IP2080 | 45 L/s Ion Pump
IP2081 | 45 L/s Ion Pump
IP2082 | 45 L/s Ion Pump
 | Turbo Cart Valve
Name (cont) | Device (cont)
IP2091 | 45 L/s Ion Pump
PG209 | Pirani Gauge
IP2092 | 45 L/s Ion Pump
BV210 | Gate Valve
IP210A | 45 L/s Ion Pump
PG210 | Pirani Gauge
IP210B | 45 L/s Ion Pump
IP211A | 45 L/s Ion Pump
 | Turbo Cart Valve
IP211B | 45 L/s Ion Pump
IP211C | 45 L/s Ion Pump
IP2120 | 45 L/s Ion Pump
IP2121 | 45 L/s Ion Pump
IP2122 | 45 L/s Ion Pump
 | Turbo Cart Valve
IP2131 | 45 L/s Ion Pump
PG213 | Pirani Gauge
IP2132 | 45 L/s Ion Pump
IP2140 | 45 L/s Ion Pump
IP2141 | 45 L/s Ion Pump
IP2142 | 45 L/s Ion Pump
BV214 | Gate Valve
IP2151 | 45 L/s Ion Pump
PG215 | Pirani Gauge
IP2152 | 45 L/s Ion Pump
IP2160 | 45 L/s Ion Pump
IP2161 | 45 L/s Ion Pump
 | Turbo Cart Valve
IP217A | 45 L/s Ion Pump
IP217B | 45 L/s Ion Pump
IP217C | 45 L/s Ion Pump
IP219A | 45 L/s Ion Pump
IP220A | 45 L/s Ion Pump
IP221A | 45 L/s Ion Pump
IP221B | 45 L/s Ion Pump
 | Turbo Cart Valve
IP222A | 45 L/s Ion Pump
IP222B | 45 L/s Ion Pump
PG222 | Pirani Gauge
BV221 | Manual Gate Valve
PG223 | Pirani Gauge
 | Turbo Cart Valve
IP223A | 45 L/s Ion Pump
Pneumatic Gate Valves
  LBNF line is broken into 4 vacuum sectors by gate valves
  Sector lengths: 56m, 100m, 70m, 85m
  All metal gate valve DS of Lambertsons
  Last gate valve is manual
Right angle Valves
  2 per sector plus 1 after last gate valve
  All metal valve DS of Lambertsons

## Slide 16: Instrumentation and Controls
PLC controlled, ethernet where possible
Cables
  Cable trays will be used to run cables to LBNF-5 Controls Room
    This includes MI extraction items (Lambertson pumps, BV200, Pirani’s, etc)
  Cable lengths range from 300 to 1100 feet
Ion pumps
  Ion pumps will read pressures - no ion gauges
  All 45 l/s except (2) 200 l/s on each side of wall mainly place 20’ apart
Pirani Gauges
  2 per sector plus 1 after last valve
Manual Gate Valve
Pirani Gauge
Turbo Cart Valve
Ion Pump

## Slide 17: Instrumentation and Controls
Interlocks
  Main Injector/NuMI scheme will be used
  The vacuum system will interlock section valves with pressure differential
    2 sets of ion pumps in each sector for permitting
    Alarms generated for average pressure
  The vacuum system will interlock beam extraction with total pressure

## Slide 18: Compressed Air and Nitrogen Systems
Compressed Air System
  Design is similar to NuMI/NOvA and the Main Injector systems
    Operates beamline vacuum gate valves
    Incorporates small receiver tanks in the enclosure due to the length of the piping system (~ 1,000 ft)
    Compressors and dryers located in LBNF-5
Nitrogen System
  Used for letting up beamline vacuum
  Nitrogen cylinders and manifold located in LBNF-5

## Slide 19: Compressed Air System P&ID Drawing

## Slide 20: Nitrogen System P&ID Drawing

## Slide 21: Turbocart
Turbocart with 80/20 frame

## Slide 22: Turbocart Components
Turbocart with frame hidden and beamline section shown
500 L/min scroll pump
70-90 L/s turbo pump
Leak checking valve
Turbo bypass valve
+/- 2” stroke bellows
Cold cathode gauge
Anti-suckback valve
Pirani gauge
Beamline pump out port
Beamline

## Slide 23: Main Injector Interface
Changes to MI vacuum for LBNF extraction include:
  Installing the Kicker magnets and Lambertson magnets
  Switching location of wide aperture Q101 and 102
  Removal of injection Lambertson upstream of Q101 – will no longer be injecting into MI from 8 GeV
Q102
Q100
For LBNF extraction
Q101
Current MI
LBNF Kicker Magnets
LBNF Lambertson Magnets
MI Lambertson

## Slide 24: Lambertson Magnet Bakeout
August 2018 – Lambertson Magnet Bakeout in MI
Reusing NuMI ILA Lambertsons for LBNF
Ranges between 2E-8 Torr and 4E-9 Torr
Steady state vacuum after bake, no beam

## Slide 25: Kicker Magnets Vacuum Profile
ITO coating: Outgassing Rate = 2.35E-11
Areodag: Estimated Outgassing Rate = 1.9E-11
Stainless Steel: Outgassing Rate = 1E-10
45 L/s pumps
Chart: Kicker Magnet Vacuum Profile
| 0 | 0.32003999999999999 | 0.64007999999999998 | 1.9575779999999998 | 3.2750759999999994 | 3.4147759999999994 | 3.5163759999999993 | 3.6001705999999993 | 3.7045391999999993 | 4.5655991999999994 | 5.4266591999999996 | 6.2877191999999997 | 7.1487791999999999 | 8.0098392 | 8.8708992000000002 | 8.9467817000000007 | 9.0226642000000012 | 9.0985467000000018 | 9.1744292000000023 | 10.035489200000002 | 10.896549200000003 | 11.757609200000003 | 12.618669200000003 | 13.479729200000003 | 14.340789200000003 | 14.607489200000003 | 15.312339200000004 | 16.017189200000004 | 18.303189200000006 | 19.418249200000005 | 20.533309200000005 | 21.470569200000003 | 23.566069200000005 | 25.661569200000006 | 27.820569200000005 | 29.979569200000004
1E-10 outgassing for Kicker magnets | 4e-08 | 4.2822e-08 | 4.5168e-08 | 4.9821e-08 | 4.6418e-08 | 4.5585e-08 | 4.5167e-08 | 4.4798e-08 | 4.58e-08 | 5.2721e-08 | 5.7231e-08 | 5.9329e-08 | 5.9016e-08 | 5.6292e-08 | 5.1156e-08 | 5.0587e-08 | 5.0001e-08 | 5.0608e-08 | 5.1197e-08 | 5.6567e-08 | 5.9525e-08 | 6.0073e-08 | 5.8209e-08 | 5.3933e-08 | 4.7247e-08 | 4.4687e-08 | 4.6879e-08 | 4.7455e-08 | 5.3648e-08 | 5.7231e-08 | 5.5043e-08 | 5.3627e-08 | 5.643e-08 | 5.2921e-08 | 5.3416e-08 | 4.7211e-08
2.35E-11 outgassing for Kicker magnets | 4e-08 | 4.1347e-08 | 4.2218e-08 | 4.0799e-08 | 3.1323e-08 | 2.9846e-08 | 2.9135e-08 | 2.8523e-08 | 2.8646e-08 | 2.9225e-08 | 2.9239e-08 | 2.8685e-08 | 2.7566e-08 | 2.5879e-08 | 2.3626e-08 | 2.34e-08 | 2.3162e-08 | 2.3447e-08 | 2.3713e-08 | 2.6345e-08 | 2.8411e-08 | 2.991e-08 | 3.0841e-08 | 3.1206e-08 | 3.1005e-08 | 3.0828e-08 | 3.6168e-08 | 3.9893e-08 | 4.714e-08 | 5.3519e-08 | 5.4126e-08 | 5.3144e-08 | 5.6427e-08 | 5.34e-08 | 5.4084e-08 | 4.8069e-08