## Slide 1: Introduction
Kevin L. Duel
Primary Vacuum Preliminary Design Review
March 10, 2020

## Slide 2: Links to More Information
Indico event page (presentations):
  https://indico.fnal.gov/event/23424/
DUNE DocDB 18159 preliminary design files:
  https://docs.dunescience.org/cgi-bin/private/ShowDocument?docid=18159

## Slide 3: Agenda
Introduction - Kevin
Technical Presentations – Beth, Kevin
Break
Cost & Schedule - Kevin
Summary, Questions & Discussion

## Slide 4: Introductions
Many thanks to the Review Committee
  Lucy Nobrega – Chair
    Senior Engineer AD/MSD
  Alex Chen
    Principal Engineer AD/MSD
  Denton Morris
    Engineering Physicist III AD/MID
Thanks to the engineers, drafters, technicians, engineering physicists etc. who contributed to the material being presented today!

## Slide 5: ISO Section View of Near Site – MI-10 to LBNF-30 Absorber Complex
Nu Beam
to SURF, SD
Proton Beam
from MI-10
Absorber Complex
Target
Complex
LBNF-5 Service Building
Decay Pipe
Primary
Beamline
Fermilab
Main Injector
Tunnel
Proton Beam
Extraction
Area of vacuum system

## Slide 6: Installation Area of Vacuum System Overview – Primary Beamline Enclosure and LBNF-5
LBNF-5 Service Building Controls Room & Pump Room (for compressed air, N2)
US Start: MI Kickers at Q100
Vehicle Access Corridor (MVA)
Beamline Components
DS End: Primary Beam Window
MI10 Alcove

## Slide 7: Primary Beamline Magnets and Vacuum
US Start: MI Kickers at Q100
Vehicle Access Corridor Junction (MVA)
DS End: Primary Beam Window
Lambertsons
MI Wall Penetration
25 dipoles
21 quads
23 correctors

## Slide 8: General Design Points
Primary Vacuum system approximately 1,000 ft long from extraction at MI-10 to the primary beam window in the Target Hall
Design is similar to existing systems for Main Injector, Main Injector transfer lines, and NuMI
  MI dipole and NuMI quad magnet designs
  Reusing ILA Lambertsons currently being used for NuMI
  New kickers with ANU beam tube design
1x10-7 Torr or better average pressure requirement
60 ion pumps, 5 sector valves, 2 Pirani gauges and 2 pump out ports per sector, turbo carts
Standard UHV practice regarding materials, cleaning and handling

## Slide 9: Review Charge
Review Emphasis:
  The focus of this review is primarily technical in nature and a brief review of cost and schedule will be given.
  Does the design meet the technical requirements?
  Are all interfaces adequately identified and defined?
  Are Fermilab standard vacuum practices adequately applied to the design together with any applicable codes/standards?
  Have ES&H issues been identified and analyzed appropriately?
  Have long lead procurement items been identified?
  Have all major risks been identified and does a mitigation strategy exist?

## Slide 10: Review Charge
  Is the design maturity at a satisfactory level giving confidence for the Primary Vacuum sub-system to be recommended to proceed to CD-2/CD-3a and Director’s readiness review?
    Based on acceptable progress for preliminary design as a minimum of 50 to 60% at the time of this review, with 100% equal to “ready for procurement”.
  Is there an adequate confidence level on cost and schedule estimates?
    Is the final design schedule start date appropriate when taking considerations such as the design maturity of interfacing systems?
In addition to the charge questions, please comment and offer recommendations on other aspects of the vacuum design.

## Slide 11: Agenda
Introduction - Kevin
Technical Presentations – Beth, Kevin
Break
Cost & Schedule - Kevin
Summary, Questions & Discussion