## Slide 1: Vacuum simulation of the Korea 4th Generation Storage Ring
Pohang Accelerator Laboratory, Postech
4GSR Project Headquarters
Hosun Choi
OLAV-VI
Apr. 17, 2024

## Slide 2
Contents
The Korea 4th Generation Storage ring
The Korea 4GSR vacuum system
Estimation of outgassing rate for the storage ring
Vacuum simulation using the Synrad and Molflow+
Summary

## Slide 3
The Korea 4th generation storage ring
Layout of the 4GSR
The Korea 4th generation storage ring
The storage ring circumference : 800 m (with 28 cells)
Beam energy : 4 GeV
Beam current : 400 mA
1 cell length (normal cell) : ~28 m
  Acr-section : 21 m
  Straight section : 7 m
1 cell 3D model
Arc-section
Straight section
800 m

## Slide 4
The Korea 4GSR vacuum system
Cross-section of the SR vacuum chamber
Beam chamber
24(H) x 18(V)
Cooling water
SR
Pill-type getter
Sheath-type heater
Storage ring vacuum system of the arc-section for storage ring
Beam channel internal cross-section size: 24 mm (H) x 18 mm(V) , Octagon
11 EA of SIP and 8 EA of NEG pumps are installed
Total pumping speed : 4300 L/s (H2)
Comprised of 13 vacuum chambers
  6 EA aluminum extrude type chambers
  2 EA aluminum machine type chambers
  5 EA stainless steel chambers
e-
CH01
CH02
CH03
CH04
CH06
CH07
CH10
CH11
CH12
CH13
CH05
CH09
Stainless steel (5 ea)
Aluminum (6 ea, extruded)
Aluminum (2 ea, machined)
Sputter Ion Pump (11 ea, 60 L/s)
NEG Pump (8 ea, 400 L/s)
NEG Pump(1.33”) (3 ea, 30 L/s)
Photon beam (ID)
Photon beam (BM)
4 mm
CH08
Vacuum device of the arc-section

## Slide 5
The Korea 4GSR vacuum system
Cross-section of the SR vacuum chamber
Beam chamber
24(H) x 18(V)
Cooling water
SR
Pill-type getter
Sheath-type heater
Storage ring vacuum system of the straight section for storage ring
Beam channel internal cross-section size: 24 mm (H) x 18 mm(V) , Octagon
2 EA of SIP and pill type NEG pumps are installed
Comprised of a total of 3 vacuum chambers
  1 EA aluminum extrude type chamber
  2 EA stainless steel chambers
Total pumping speed : 300 L/s (H2)
One Rf-shielded GV per cell are installed
e-
CH16
CH14
Stainless steel (2 ea)
Aluminum (1 ea, extruded)
Sputter Ion Pump (11 ea, 60 L/s)
Gate Valve (1 ea, All metal Rf-shielded)
4 mm
Vacuum device of the straight section
Pill-type getter
CH15

## Slide 6
After sufficient commissioning, estimation of effective pumping speed per cell
Parameters | Value
Energy (GeV) | 4
Circumference (m) | 800
Beam current (mA) | 400
Photon linear density of the 4GSR
N(ph·s-1·m-1) = 8.08 x 1020 · 4[GeV]· 0.4[A]/ 800[m]
=1.62 x 1018 ph·s-1·m-1
If PSD yield η = 1 x 10-6 mol/ph (After sufficient commissioning)
ή (mol · s-1 · m-1) = 1.62 x 1018 x 1 x 10-6
=1.62 x 1012 mol·s-1·m-1
The average line gas desorption rate along the storage ring
Qlin (mbar·l ·s-1 ·m-1) = ή x K = 1.62 x 1012 x 4.04 x 10-20
= 6.53 x 10-8 mbar·L · s-1· m-1
K- converts number of mol to pressure units 4.04x10-20 [mbar·L/mol], (PV=NmolkBT)
The required effective pumping speed (1 cell) to meet the average pressure level <1 x 10-9 mbar (when η = 1 x 10-6 mol/ph)
Qcell (mbar·L/s) = 6.53 x 10-8 x 28 m (1 cell length) = 1.82 x 10-6 mbar·L/s S(eff·1cell) = 1.82 x 10-6 / (1 x 10-9)= 1800 L/s
After sufficient commissioning(η = 1 x 10-6), achieving 1 x 10-9 mbar requires an effective pumping speed of 1800 L/s per cell

## Slide 7
Building a 3D model for simulation (Molflow+ and Synrad)
Modeling of the vacuum chamber(Inventor)
Import the vacuum chamber modeling from the Ansys program into SpaceClaim (STP)
Use the “volume extractor” feature within SpaceClaim to generate the internal space of the vacuum chamber
Convert the generated modeling into an STL
Internal modeling of the vacuum chamber(Ansys)
Simulation modeling (Synrad & Molflow+)
Bulind a 3D simulation model
Utilized the volume extractor feature of the Ansys program to create the internal modeling
Loading the .STL file
The ansys program into “Spaceclaim”
Modeling vacuum chamber using the Inventor

## Slide 8
Vacuum simulation using Synrad and Molflow+
NEG pump (5 ea, 30 L/s, H2)
NEG Pump (10 ea, 400 L/s, H2)
Pill type NEG
NEG pump coverage
Sputter Ion Pump (12 ea, 60 L/s, H2)
SIP coverage
Pumping speed setup for Molflow+
The module type NEG pump and SIP apply pumping speed
The pill type NEG pump apply measured data (PAL)
  Activation condition : 180 ℃, 24 hr
Activation condition : 180 ℃, 24 hr
Pumping speed vs adsorption capacity of the Pill type NEG pump
the pressure along the beam path

## Slide 9
Vacuum simulation using Synrad and Molflow+
Calculating the dynamic pressure of the storage ring
Calculating the vacuum profile during operation for the major residual gases, H2 and CO
  After the storage ring vacuum system has undergone sufficient commissioning
PSD values (mol/ph)
  H2 : 1 x 10-6
  CO : 2 x 10-7
10%
2%
Average pressure (1.38 x 10-9 mbar)
88%
Dynamic pressure profile of the storage ring according to the gas type
Partial pressures of gases in ultra-high vacuum

## Slide 10
Re-fitting of the Photon stimulated desorption value
PSD yield vs beam dose for Aluminum
C K Chan et al 2008 J. Phys.: Conf. Ser. 100 092025
treatment A : Oil machining and chemical cleaning
We re-fitted using the “A” data selected from the graph
Photon stimulated desorption gas loads
To perform beam dose-dependent simulations, the PSD measurements are required
We have fitted the data based on literature references as we don’t have experience in the PSD measurements
Photon flux distribution in Synrad
e-
Ref.
Molflow+

## Slide 11
Evolution pressure in Molflow+ (H2)
Evolution pressure calculations per beam dose during the early stage (400 mA)
Pressure profile per beam dose of 0.01, 0.1, and 10 Ah at the storage ring
The 4GSR directly absorbs some of the photon beam in the chamber. If handled carefully in the early stages, it is expected to achieve better pressure levels after a sufficient beam dose
A
B
e-
Section A
Section B
In the initial stages, the area directly exposed the photon beam experiences a faster decrease in gas desorption rate compared to the area not directly exposed to the photon beam.
The time-dependent outgassing rate of section A and B
Pressure profile by beam dose
@ 400 mA
Incident area
@ 400 mA

## Slide 12
Estimation of the re-activation timing for the Pill type NEG
Calculated the adsorption capacity of the Pill type getter pump during the early stage
Apply the CO adsorption capacity measured by PAL
Activation condition : 180 ℃, 24 hr
Average pressure and sorbed quantity as a function of commissioning time for CO
The re-activation timing of the pill type getter pump is required 100 hours, about 4 days, later
Apply the Saturation point
10 mA
50 mA
100 mA
Pill-type getter
In-situ baking condition for 4GSR
Pumping speed VS Sorbed quantity (CO)
per pill

## Slide 13
Summary
We conducted the vacuum simulation of the 4GSR using Molflow+ and Synrad
When the beam operation has run for a while, the average total pressure is about 10-9 mbar (H2+CO)
Initially, the areas directly impacted by the photon beam have higher pressure, but over time, the pressure decreases relatively due to the beam cleaning effect
When the early stages of commissioning, we predicted the re-activation timing of the NEG pump by calculating the pressure and CO adsorption during operation
Thank you for listening

## Slide 14
@400 mA: 1.62 x 1018 ph/sec/m