## Slide 1
Design Status of Vacuum System for the Korea-4GSR
Taekyun Ha (on behalf of PAL vacuum group)
Vacuum & RF Team Leader
Pohang Accelerator Laboratory (PAL)
POSTECH, Korea
April 17, 2024
OLAV-VI Workshop (April 15 – 19, 2024)

## Slide 2
Contents
Overview of the Korea-4GSR Project
Brief Introduction of Linac & Booster Vacuum System
Storage Ring Vacuum System
  Design Philosophy
  Overview
  Change Log of Chamber Design
  Impedance Budget
  Photon Fan and Beam Branch Chamber
  ID Beam Opening
  Thermal Analysis of the Main Photon Absorbers
  Vacuum Simulation
  Vacuum Chamber Prototyping
  Pressure Measurement after NEG Activation
  Fabrication schedule
Summary
OLAV-VI Workshop (April 15 – 19, 2024)
 See Hosun Choi’s Talk
 See Sehyun Kim’s Talk

## Slide 3
OLAV-VI Workshop (April 15 – 19, 2024)
(10 at the initial stage)
Chung-ju, Chungcheongbuk-do

## Slide 4
OLAV-VI Workshop (April 15 – 19, 2024)
Construction Site

## Slide 5
LINAC
Booster
Storage Ring
OLAV-VI Workshop (April 15 – 19, 2024)
Accelerator Vacuum System
Linac vacuum
  Electron beam energy 0  200 MeV
  Photo-cathode E-gun (~10-11 mbar), AC and wave guide (~10-8 mbar)
  Successfully being operated in PLS-II & PAL-XFEL
Booster vacuum
  Electron beam energy 200 MeV  4 GeV
  Circumference ~770 m with 30 cells
  Beam duct OD ∅24~32 mm, thickness 0.7 mm (low eddy current)
  Vacuum requirement ~10-8 mbar
Beam transfer system vacuum
  Transfer line length ~ 40 m
  Special chambers for the injection system
  (Ceramic kicker chamber, In-vacuum septum chamber, …)
Storage ring vacuum
  Electron beam energy 4 GeV & beam current 400 mA
  Circumference ~800 m with 28 cells
  Beam duct Inner diameter ∅18(V) x 24(H) mm
  Vacuum requirement during operation ~10-9 mbar
4 | GeV
400 | mA
800 | m Ring

## Slide 6
OLAV-VI Workshop (April 15 – 19, 2024)
Linac Vacuum System
Photo-cathode E-gun:
  Vacuum requirement during operation ~ 10-11 mbar
  Low outgassing vacuum chamber with SIP(1 ea, 60 L/s), NEG cartridges(2 ea, 400 L/s)
Accelerating columns and wave guides
  Four S-band accelerating columns with two modulator-klystron stations
  Vacuum requirement during operation ~ 10-8 mbar
  Five SIPs per module (60 L/s), vacuum interlock with CCG signal
Linac to Booster (LTB): Vacuum requirement during operation ~ 10-8 mbar

## Slide 7
OLAV-VI Workshop (April 15 – 19, 2024)
Booster Vacuum System
Circumference ~770 m with 30 cells
Circular beam duct with OD ∅24 mm (dipole magnet), ∅32 mm (multipole magnet)
Chamber materials: SS316L (0.7 mm-thick)  Max. stress < 2.5 MPa
Eddy current heating effect < 1 mW/cm2  Negligible temperature rise
Outgassing rate < 1.5x10-10 mbar l/s cm2  Avg. pressure < 5x10-8 mbar
※ Pressure distribution w.r.t. pump distance

## Slide 8
Design Philosophy of the Storage Ring Vacuum System
Distributed pumping system using “Pill-type Getters”
Bake-out & NEG activation in the tunnel (“In-situ bake-out”)
Maximize the exposure of the chamber wall to synchrotron radiation for rapid beam cleaning
Two step installation:
  Pre-assemble magnets and vacuum chambers on a girder outside the tunnel
  Connect the chamber between the two girders using bellows in the tunnel
Low impedance design:
  24x18 octagon-shaped e-beam channel with 4 mm high winglet for synchrotron radiation handling
  Try to make the transition angle less than 1:10
  Bellows and gate valve having RF-shielded finger which is made of thin copper plate with slots
  No components penetrate into the beam channel (cross section change only in the winglet)
OLAV-VI Workshop (April 15 – 19, 2024)
SR
e-
Cooling water
Sheath heater
Pill-NEG

## Slide 9
OLAV-VI Workshop (April 15 – 19, 2024)
Overview of the Storage Ring Vacuum System
Photon beam (ID)
Photon beam (BM)
e-
※ Arc-section length: 22.3 m
※ Bending angle (1 Cell): 12.857°
※ 28 cells (800 m)
<Hybrid 7BA Lattice>
SR one cell diagram
Bending magnet
CH01
CH02
CH03
CH04
CH06
CH07
CH08
CH10
CH11
CH12
CH13
SR one cell vacuum system
Pill-NEG
Cooling water
Beam chamber
24(H)×18(V)
SR
e-
Photon beam (ID)
Photon beam (BM)
e-
Vacuum chamber cross-section
CH05
CH09
※ 13 vacuum chambers per arc-section

## Slide 10
OLAV-VI Workshop (April 15 – 19, 2024)
Design Change of the Vacuum Chamber
Pill-NEG
Cooling water
Beam chamber
24(H)×18(V)
SR
e-
ID beam port
Bending magnet beam port
ID beam port
Bending magnet beam port
Conceptual Design
SR
e-
SR
e-
Cooling water
Sheath heater
Sheath heater
Pill-NEG
Current Design

## Slide 11
OLAV-VI Workshop (April 15 – 19, 2024)
Main Components of the SR Vacuum System
CH01
CH02
CH03
CH04
CH06
CH07
CH08
CH10
CH11
CH12
CH13
Arc section vacuum system
BPM (10 ea, STS316)
RF-shielded Bellow (10 ea)
Photon absorber (4 ea, OFHC)
Photon mask (3 ea, OFHC)
CH05
CH09
Stainless steel (5 ea)
Aluminum (5 ea, extruded)
Aluminum (3 ea, machined)
Sputter Ion Pump (11 ea, 60 L/s)
NEG Pump (10 ea, 400 L/s)
Ion Gauge (5 ea)
RGA (2ea)
All-metal Angle Valve (2 ea)
RF-shielded Gate Valve (1 ea)

## Slide 12
OLAV-VI Workshop (April 15 – 19, 2024)
Straight section vacuum system
Pill-NEG
OVU Chamber
Photon mask
IVU Chamber (3 m)
Main Components of the SR Vacuum System

## Slide 13
OLAV-VI Workshop (April 15 – 19, 2024)
Impedance Budget
 |  | Single Component |  | Sum |  | 
Components | Number | kz [V/pC] | Znz [mOhm] | kzT [V/pC] | ZnzT [mOhm] | ZnzT [mOhm]
Resistive Wall | 1 | 14.78 | 158.20 | 14.78 | 158.2 | 158.2
Main RF cavity | 10 | 1.17 | 5.98 | 11.65 | 59.80 | 59.80
LGBM1U chamber | 28 | 2.34E-02 | 0.16 | 0.65 | 4.37 | 4.37
LGBM2D chamber | 28 | 3.42E-02 | 0.34 | 0.96 | 9.39 | 9.39
BPM | 176 | 2.30E-02 | 0.17 | 4.05 | 30.62 | 30.62
Gate valve | 112 | 3.38E-02 | 0.30 | 3.79 | 33.82 | 33.82
ID taper | 26 | 2.56E-03 | 0.89 | 0.07 | 23.17 | 23.17
Bellows | 224 | 7.09E-03 | 0.07 | 1.59 | 15.19 | 15.19
BPM-Bellows 1 | 56 | 2.72E-02 | 0.23 | 1.52 | 12.94 | 12.94
BPM-Bellows 2 | 56 | 2.50E-02 | 0.23 | 1.40 | 12.94 | 12.94
Flange | 840 | 3.00E-05 | 0.02 | 0.03 | 15.96 | 15.96
RF taper | 6 | 7.70E-02 | 1.89 | 0.46 | 11.32 | 11.32
LFS | 1 | 1.58E+00 | 6.30 | 1.58 | 6.30 | 6.30
RF transition chamber | 5 | 8.50E-02 | 0.75 | 0.43 | 3.76 | 3.76
Pump tee | 56 | 5.16E-03 | 0.13 | 0.29 | 7.45 | 7.45
TFS (vert-) | 1 | 1.82E-01 | 0.67 | 0.18 | 0.67 | 0.67
TFS (hori-) | 1 | 1.82E-01 | 0.67 | 0.18 | 0.67 | 0.67
Center bend chamber | 28 | 3.52E-03 | 0.21 | 0.10 | 5.88 | 5.88
CH08 entrance | 56 | 7.90E-04 | 0.03 | 0.04 | 1.68 | 1.68
CH08 exit | 56 | 1.82E-04 | 0.01 | 0.01 | 0.73 | 0.73
Collimator | 4 | TBD |  | TBD |  | 
Total |  |  |  | 44 | 415 | 
Chart: Loss factor
| RW | Main RF | BPM | GateValve | Others | Diagnostics | Bellows | Transitions | Flange
 | 14.78 | 11.65 | 6.9724 | 3.7901 | 2.3259 | 1.946 | 1.587 | 0.68168 | 0.0252
Loss factor Effective
impedance

## Slide 14
OLAV-VI Workshop (April 15 – 19, 2024)
Photon Fan and Beam Branch Chambers
Photon absorber (mask)
Crotch absorber for the bending beamline
Crotch absorber for the ID beamline
※ SR power density along the ring
(for Φ24 mm uniform beam pipe)

## Slide 15
OLAV-VI Workshop (April 15 – 19, 2024)
ID Beam Parameters & Orbit Interlock Tolerance
ID | Gap (mm) | λu (mm) | L (m) | B [x/y] (T) | K [x/y/⊥] | Max. Power density (kW/mrad2) | Max. Divergence (mrad)
IVU20 | 5 | 20 | 3 | 0.8867 | 1.6558 | 142 | ± 0.2 (H)
EPU98 | 15 | 98 | 3.6 | H: 0/1.2020 | 0/11/11 | 45 | ± 1.5 (H)
 |  |  |  | V: 0.8015/0 | 7.335/0/7.335 | 30 | ± 1.0 (V)
 |  |  |  | C: 0.6667/0.6675 | 6.1/6.108/8.633 | 12 | ± 0.8 (H,V)
※ Power density profile @ 10 m from the ID center
※ Parameters for typical IDs
IVU20
EPU98 (H mode)
EPU98 (V mode)
EPU98 (C mode)
± 1.5 mrad
± 1.0 mrad
± 0.8 mrad
± 0.2 mrad
± 0.8 mrad
※ Orbit interlock condition of e-BPMs for the ID
  ±0.1 mrad ± 400 μm offset
  (Rms orbit error ~ 150 μm)

## Slide 16
ID Photon Beam Opening & Clearance
Crotch absorber
EPU98 (H mode), Top view
※ Scale X : Y = 1 : 100
Beam clearance
3.0 mm
3.3 mm
2.6 mm
Beam opening
: 3 mrad
Beam clearance
3.3 mm
EPU98 (V mode), Side view
Beam opening
: 2 mrad
ID center
Crotch absorber
ID center
Beam
pipe #1
Beam
pipe #2
Beam pipe #3
Beam
pipe #1
Beam
pipe #2
Beam pipe #3
Beam clearance
2.8 mm
±0.1 mrad±600 μm
mis-steered beam
(green lines)
Beam clearance
2.9 mm
Beam clearance
3.4 mm
Beam clearance
2.7 mm
※ Scale X : Y = 1 : 100
3.4 mm
2.7 mm
12.67 m
12.67 m
44.5 mm
32 mm
Pivot
Pivot
Green line:
mis-steered beam
±0.1 mrad±600 μm
mis-steered beam
(green lines)
Mis-steered case
: 3.2 mrad
Mis-steered case
: 2.2 mrad
Green line:
mis-steered beam
OLAV-VI Workshop (April 15 – 19, 2024)

## Slide 17
Thermo-mechanical Analysis
Crotch absorber 2 (for the bending beamline)
EPU98 beam
Crotch absorber 1 (for the ID beamline)
[Beam opening]
±1.5 × ±1.0 mrad (H×V)
[PA LGBM1U]
[Photon fan from upstream bending magnets]
[Max. Temperature for EPU98 (Hor. mode)]
[Max. Temperature for EPU98 (Ver. mode)]
[Max. Temperature]
[Photon fan from upstream bending magnets]
SD = 6 m
118℃
OLAV-VI Workshop (April 15 – 19, 2024)
[Beam opening]
±1.0 mrad (H)
※ Max stress ~ 70 MPa

## Slide 18
Vacuum Profile Simulation
Synrad & Molflow simulation
  We assumed the PSD yield of 1E-6 (H2) and 2E-7 (CO)
  Average pressure after fully cleaned ~1×10-9 mbar
Average pressure (1.38 x 10-9 mbar)
OLAV-VI Workshop (April 15 – 19, 2024)
Commisioning stage
Fully cleaned stage
※ See Hosun Choi’s Talk

## Slide 19
Vacuum Chamber Prototyping (1)
Dipole magnet chamber (extruded type, CH12)
1. Extrusion
2. Bending
3. Curvature test
4. Machining
5. Chemical cleaning
8. Assemble & alignment
7. Welding
※ Error < ±0.5 mm
※ He leak rate < 10-10 mbar l/s
6. NEG insertion
19
OLAV-VI Workshop (April 15 – 19, 2024)
※ See Sehyun Kim’s Talk

## Slide 20
Beamline branch chamber (machined type, CH02)
2. Chemical cleaning
3. Welding
4. Assemble & vacuum test
1. Machining
※ He leak rate < 10-10 mbar l/s
20
Vacuum Chamber Prototyping (2)
OLAV-VI Workshop (April 15 – 19, 2024)

## Slide 21
Vacuum Test of the Prototype Chamber
Al extruded chamber with Pill-NEGs (2 lines)
Baking at 180℃ for 48 h
Base pressure measured at 3 points
Base pressure at the center of the chamber
P2 < 5×10-11 mbar
Measurement of the ultimate pressure
Measurement set-up
P1
P2
P3
21
Sheath heaters
OLAV-VI Workshop (April 15 – 19, 2024)

## Slide 22
Fabrication Schedule (Aluminum Chambers)
22
OLAV-VI Workshop (April 15 – 19, 2024)

## Slide 23
Summary
OLAV-VI Workshop (April 15 – 19, 2024)
Design Status
- Deign optimization of vacuum system is done
- Vacuum profile estimation completed (average pressure = 1E-9 mbar)
- Thermal analysis of photon absorbers completed
- Vacuum chamber prototyping and performance test are done
Future schedule
- Completion of manufacturing drawing: ~ 1/2 of 2024
- Vacuum chambers prototyping: ~ 1/2 of 2024
- Purchase order of vacuum chambers: 2/2 of 2024
- Purchase order of commercial components : 2025
- Assembly and vacuum test: 3/4 of 2024 ~

## Slide 24
Thank you for your attention
OLAV-VI Workshop (April 15 – 19, 2024)

## Slide 25
SD = 6.086 m
※ Beam opening
±1.5 × ±1.0 mrad (H×V)
Crotch absorber for ID beams
Photon beam pipe #1
Photon beam pipe #2
Photon beam pipe #3
Photon Beam Opening & Clearance Issue

## Slide 26
EPU98 Power Density @ the Crotch Absorber
※ Source distance = 6.1 m
± 1.0 mrad
± 1.5 mrad
Photon absorber
Photon absorber
Photon absorber
Photon absorber

## Slide 27
Location | CH02 |  | CH03 | CH05 | CH07 | CH10 | CH11 | CH13
Type | absorber |  | absorber | absorber | mask | absorber | absorber | mask
power [W] | ID horizontal mode | ID vertical mode | 168 | 593 | 1,090 | 9,213 | 229 | 311
 | 1,312 | 1,834 |  |  |  |  |  | 
Synchrotron Radiation Power on 1 cell

## Slide 28
The yield strength of the cold forged OFHC is enhanced up to 240 MPa.
Cold forged oxygen free copper

## Slide 29
29
RF-shielded bellows and BPM module