## Slide 1: Vacuum System of RAON Installation & operating experience
Hyungjoo Son
2024. 04. 17
Institute for Rare Isotope Science
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
1
Notes: Hello Everyone
I’m Hyungjoo Son from Institute for Rate Isotope Science Laboratory of Korea
At the previous OLAV-5 Workshop. I presented on the ‘Design of RAON vacuum system’
RAON is the name of the heavy ion accelerator constructed in Daejeon South Korea. We have installed and operated the RAON vacuum system based on that design.
I’d like to talk about current status of RAON vacuum system

## Slide 2
Outlines
Introduction of IRIS
Configuration of RAON
RAON Vacuum System
Status and Plan
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
2
Notes: This is outlines of the presentation. Firstly, I’d like to talk about IRIS simply.
And I will present about configuration of RAON and the RAON Vacuum System.
Lastly. I will conclude my presentation with current status and plan

## Slide 3
Introduction
Institute for Rare Isotope Science is a new name of Rare Isotope Science Project (2012-2022).
RISP complete the 1st step project for low energy experiments of RAON.
- IRIS was launched as a heavy ion accelerator research institute in Aug 2022 at Daejeon.
IRIS
PAL
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
3
Notes: RIS is a new name of Rare Isotope Science Project.
RISP complete the first step project for low energy experiments of RAON
IRIS was launched a heavy ion accelerator research institute in Aug 2022 at Daejeo.

## Slide 4
Configuration of RAON
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
IF system
Low Energy Experiments
Nuclear Astrophysics
Driver LINAC
SCL (200 MeV/u, 8.3 pμA for U+79)
(600MeV, 660 μA for p)
Post Accelerator
CB : Charge Breeder
HRMS : High Resolution Mass Separator
MEBT
ECR-IS
Cyclotron
(p, 70 MeV, 1mA)
ISOL system
High-precision
Mass Measurement
High Energy Experiments
Nuclear Structure/
Symmetry Energy
RF Cooler
RFQ
CB
HRMS
ISOL
Target
IF Target
IF Separator
μSR,
Bio-medical
1st step project
SCL3(Super Conducting LINAC 3)
SCL2(Super Conducting LINAC 2)
4
Notes: Our original plan was construct the entire heavy ion accelerator facility during the project period. But some reason like budget and manpower and technical capabilities, project has been delayed twice.
We have ultimately finalized the first step goal to transfer the beam to the low-energy experimental facility. And the high energy accelerator and high experimental facility construction has become second step goal has bee.
The construction of the low energy section has been completed at 2022.

## Slide 5
Super Conducting LINAC
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
In R&D to 2027
Not yet finalized
5
Notes: Next, I will talk about the SCL3 of RAON. SCL3 consist of 54 cryo-modules and 53 warm section vacuum chambers. End of the SCL3, the beam energy is reached 18.5MeV / nucleus.
At the first beam commissioning, the beam energy was reached 16.5MeV / nucleus.
The type of SCL2 cavity has not yet been finalized. We are considering 2 types cavity for SCL2 section. There are SSR and HWR types.

## Slide 6
RAON Vacuum System
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
SCL3 vacuum system
250L/S
250L/S
500L/min
500L/min
CCG
PG
P
V
d
V
b
MFC
micro
filter
V
f
TMP
He Leak
Detector
V
c
V
e
V
a
G
A
S
Portable
Pumping System
Dry
CCG
CCG
CCG
CCG
CCG
CCG
CCG
CCG
Warm section vacuum pump
NEG 400 L/s (Z400, SAES) + SIP 5L/s , NEXTORR 300-5
Using portable cart to pump down to 10-7 mbar
(Slow pump down to 10-1 mbar with MFC)
Insulation vacuum system of Cryo module
TMP (250L/s, OSAKA), DRY pump (500L/min, OSAKA)
Redundancy & String structure for cost and maintenance
6
Notes: This picture is the configuration of SCL3 vacuum system. Main pump of warm section chamber is the NEG. And small Ion pump installed auxiliary pump.
The Cavity and warm section vacuum chamber are pumped to 10-1 mbar by slow pumping separately using portable pumping system.
The cryo-module’s insulation vacuum consist of string line for cost and maintenance and redundancy.
The insulation vacuum is pumped down to the 10-4 mbar before the cooldown. The insulation vacuum is maintained at 10-8mbar after the cooldown.
During 1 year operation, many dry pumps were malfunctioned. There are no pictures in this presentation. We confirmed that the dry pump mulfunctioned by water.
So, now we are considering replacing them with a water resistant pump.

## Slide 7
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
Warm section chambers are composed of vacuum chamber(38ea) and Beam Diagnostic Chamber(15ea)
Assembly and Conditioning of chambers performed in Clean Room (class 10)
JUN 2019
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
7
Notes: Next I will talk about the clean assembly procedure and conditioning of the vacuum chamber.
The warm section vacuum chambers are composed of two types. 38 Vacuum chambers and 15 beam diagnostic chambers.y
All vacuum chambers assemblies and conditioning were performed in a class 10 cleanroom.

## Slide 8
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
A
cold cathode gauge
G1
AV 1
KF40
Bellows
B
AV 2
G2
Full range gauge
RGA
SIP 5L/s
Effective pumping speed
pumping system
Cross-section excluding BPM : about 4,000 cm2
Chamber Volume : 8 liter
JUN 2019
- No additional cleaning after manufacturing (Just cleaning by manufacturer)
- To verify the vacuum performance of the chamber, a vacuum exhaust test performed without a NEG.
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
- Chamber A, B, Bellows, SIP are baked-out with 150°C, 2 weeks
After bake-out Pressure of A : 3.3E-7 mbar
q = 3.3 x 10-10 mbar l s-1 cm-2
8
Notes: And the vacuum test was performed without NEG pump to verify the vacuum performance of the chamber. The vacuum chamber was delivered from the manufacturer with cleaning processes already completed.
So, The vacuum test was proceeded without additional cleaning procedures. I briefly calculate the outgassing rates of the chamber. After 2 weeks bake-out. The outgassing rates measured too high,
Since I thought the chamber’s condition was abnormal and my test method was not collect. So, I asked for assistance to the Pohang accelerator laboratory vacuum group to more accurately measure the chamber’s condition.

## Slide 9
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
chamber
Orifice
RGA
TMP
- Performing RGA measurements during bake-out
contamination peak
SEP 2019
PAL
- To remove contaminants and reduce H2 outgassing
Cleaning & Vacuum Firing at 600°C for 36 h
9
Notes: The vacuum chamber was installed with an orifice and RGA to conduct measurements for precise experiments. In this experiment, We were able to observe contamination peaks and hydrogen level.
To remove contaminants and reduce the release of hydrogen, We decided to perform cleaning and vacuum firing.

## Slide 10
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
Ultra Sonic Cleaning
- Cleaning performed for 1 hour with Liquinox 1% solution
- Rinsing performed for 1 hour with DI water
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Vacuum firing (600°C for 36 h)
- 4 TCs were in contact with the chamber components.
- Base pressure of VF chamber was ~10-8 mbar at RT.
- Firing performed 36hours at 600°C
10
Notes: The vacuum chamber cleaning was performed for 1 hour with 1% Liquinox solution. And rinsing was performed 1 hour with DI water.
Vacuum firing was performed for 36 hours at 600 degree C considering chamber thickness.

## Slide 11
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
09 SEP , 2019
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Vacuum chamber Assembly & conditioning process
3. Cleaning & Rinsing
2. Vacuum firing
5. Chamber assembly (class 10)
8. NEG degassing & chamber bake-out
6. Slow pumping to 1mbar with MFC
7. Pumping to ~10-7 mbar
9. N2 slow venting up to 1.2 bar
1. Chamber entry
4. Chamber Dry(48h, class 10)
11
Notes: After that procedure, We confirmed that the contaminants were removed and the outgassing rates of hydrogen were reduced. Based on these results, we established assembly and conditioning procedures for the vacuum chamber.
After the conditioning, the vacuum chambers are moved to tunnel with 1.2bar nitrogen charging.

## Slide 12
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Warm section chamber carried in tunnel
Magnet + vacuum(beam diagnostic) chamber assembly/alignment
CM carried in ISOL building
upper magnet separation
Alignment between warm sections and Cryo module
Moving CM into the SCL3 tunnel
12
Notes: These pictures shows the process of the transporting the cryo-modules with warm secion. The vacuum chambers are installed onto the cryo-module after assembling with the quadrupole magnet.
After the chamber installing process, Cryo-module is moved to SCL3 tunnel.

## Slide 13
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
Dec 07, 2022
Installation of CMs were completed on Dec 07, 2022
Signal & Power cable inspection
Clean assembly
Slow pumping Line connecting
CM is seated on the foot base
Portable clean booth
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
13

## Slide 14
RAON Vacuum System
SCL3 vacuum system (Cleaning / Assembly / conditioning / Installation)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Very narrow gap
Length adjuster
10mm between parts
10cm working area
socket cutting
expanding
shrinking
Helcoflex seal
Seal guide
14

## Slide 15
RAON Vacuum System
SCL3 vacuum system (Research for particle movement)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
1. Slow pumping /venting test
2. Gate valve operation test
Particle monitor : SHIMAZ (ISPM-P-NW)
BG : Baratron Gauge
MFC : Mass Flow Controller
FG : Full range Gauge
TMP : Turbo Molecular Pump
15

## Slide 16
RAON Vacuum System
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Class 100 ~ 1000
Class > 100,000
6 mbar / min
12 mbar / min
Particle contamination by Assembly condition (pumping)
SCL3 vacuum system (Research for particle movement)
Background
16

## Slide 17
RAON Vacuum System
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Particle contamination by flow speed
SCL3 vacuum system (Research for particle movement)
Class 100 ~ 1000
3L/min
16L/min
17

## Slide 18
RAON Vacuum System
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
SCL3 vacuum system (Research for particle movement)
Pressure: < 1x10-2 mbar
Pressure: 1013 mbar
Particle movement by Gate valve operation
18

## Slide 19
RAON Vacuum System
SCL3 vacuum system (Degassing & NEG Activation)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Vacuum requirement of warm section : 5E-9mbar (After cavity cool-down)
19

## Slide 20
RAON Vacuum System
SCL3 to KOBRA vacuum system (Configuration)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
End of SCL3
KOBRA experimental facility
P2DT(Post Accelerator to Distribution Transfer Line)
SCL2 connection point
Vacuum device | Spctification | Q'ty | Manufacture / Model
Ion Pump | 125L/s(N2) | 7 | Agilent/ VacIon Plus 150
Turbo Pump | 355L/s, | 3 | Agilent / Twistorr 404FS
Dry pump | 600L/min | 3 | Laybold / Eco Dry
CCG | 1E-3~5E-10 | 10 | MKS / 422
Gate valve | UHV | 10 | VAT / UHV gate valve
wall
KOBRA : KOrea Broad acceptance Recoil spectrometer and Apparatus
NDPS : Nuclear Data Production System
NDPS beam Line
20

## Slide 21
RAON Vacuum System
SCL3 to KoBRA vacuum system (Operation)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Ar+9 beam existing in SCL3 to KOBRA section
(The faraday cup at the end of the KOBRA beam line is in the down position)
CCG1
CCG3
21

## Slide 22
RAON Vacuum System
SCL3 to KoBRA vacuum system (Malfunction & Maintenance)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
CSK
1
CG
2
GV
3
AV1
DRY1
CSK
2
BM
GV1
CG1
GV2
BM
TMP1
CSK
4
CG
10
GV
11
AV3
DRY3
TMP3
CG
3
MAV
SIP2
SIP1
MAV
CG
4
MAV
SIP3
GV5
GV
Rebuncher
GV
MAV
SIP4
CG5
GV6
GV7
MAV
SIP5
CG6
MAV
SIP6
CG7
GV8
CSK
3
CG8
GV
9
NEG
MAV
CG
MAV
SIP7
CG9
GV10
To be replaced with NEG
Replaced with NEG
★ For 1 year, 3 TMP malfunctioned
Because of the long storage time ???
22

## Slide 23
Status & Plan
IRIS successfully transmitted the Ar+9 beam to the KOBRA (Nov. 2022)
IRIS is Preparing for the second beam commissioning (Apr ~ Jun. 2024)
High energy accelerator (SCL2) is under R&D to 2027
The vacuum system for NDPS & P2DT are under vacuum pumping procedure.
Ar+8 beam will be provided to the KOBRA experimental facility. (July. 2024)
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
NDPS beam Line
P2DT(Post Accelerator to Distribution Transfer Line)
SCL2(R&D)
KOBRA experimental facility
23

## Slide 24
OLAV VI / April 2024 / Fermi National Accelerator Laboratory
Thank You
24