## Slide 1
Status of the Vacuum Systems of the FAIR Accelerator Complex
Andreas Kraemer
GSI Helmholtzzentrum für Schwerionenforschung GmbH
15th of April 2024

## Slide 2: FAIR – Facility for Antiproton and Ion Research Beam Parameters and Intensities
Primary Beams
5x1011/spill; 2 GeV/u; 238U28+
Factor 10-100 over present in intensity
2x1013/cycle 29 GeV protons
Secondary Beams
Broad range of radioactive beams up to 1.5 - 2 GeV/u
up to factor 10 000 in intensity over present
Antiprotons 3 GeV
Storage and Cooler Rings
Radioactive beams
1011 stored and cooled 0.8 - 14 GeV antiprotons
The system of storage and cooler rings allows to drastically improving the quality – e. g. energy spread and emittance - of the secondary beams in order to use them for high precision experiments. Moreover, in connection with the SIS100 synchrotron an efficient parallel operation of all four scientific programs can be realised.

## Slide 3: What do we do at GSI/FAIR?
We explore the universe…
…in the lab.
Photo: J. Hosan/GSI/FAIR, “NASA, ESA, the Hubble Heritage Team (STScl/AURA), A. Nota (ESA/STScl), and the Westerlund 2 Science Team”
A world-wide unique particle accelerator
Exotic forms of matter occurring in the universe can be produced and investigated in the laboratory
Basic research and the development of applications for materials research, radiobiology, space travel, etc.
Collaboration between several teams of internationally leading researchers (more than 3,000 scientists)
Milestone in the European research roadmap (ESFRI)
Top priority in the European nuclear physics community

## Slide 4: The four scientific pillars at FAIR
CBM Compressed Baryonic Matter: Inside a neutron star (500 scientists)
PANDA Antiproton-Annihilation at Darmstadt: Antimatter research (500 scientists)
APPA Atomic, Plasma Physics and Applications: From atoms to planets to cancer research (720 scientists)
NUSTAR Nuclear Structure, Astrophysics and Reactions: Stars and nuclei (850 scientists)

## Slide 5: FAIR Shareholders worldwide
Shareholders
Germany (70,2%)
Finland (0,5%)
France (2,7%)
India (3,5%)
Poland (2,3%)
Romania (1,2%)
Russia* (17,4%)
Sweden (1,0%)
Slovenia (1,2%)
Associated
United Kingdom
Aspirant
Czech Republic
Graph: GSI/FAIR
*Russian contracts/collaboration
on hold
Realization and operation with international cooperation's
Cooperation with around 400 institutes in more than 50 countries
1,580 employees on the FAIR/GSI campus in Darmstadt

## Slide 6: FAIR stepwise approach towards MSV
till 2028
after 2028

## Slide 7: Areal View of Construction Site - October 2023
© D. Fehrenz (GSI/FAIR)
Photos and videos of the FAIR construction site
https://www.gsi.de/en/researchaccelerators/fair/fair_civil_construction/photos_and_videos
Latest video: https://www.youtube.com/watch?v=AfeGI4JkQlE
7

## Slide 8: Status Civil Construction
SIS100 Tunnel
© GSI/FAIR, L. Möller/Zeitrausch
8

## Slide 9: Impression of the Warehouse
SIS100 SC Dipole Modules
Super-FRS SC Multiplets
HEBT
NC Magnets
SIS100 Cryogenic Lines
9

## Slide 10: Installation of Cryogenic Infrastructure
SIS100 Valve Box
(supplied by Demaco)
Warm Compressor Station
(supplied by Linde Kryotechnik)
Main Cold Box CRYO2
(supplied by Linde Kryotechnik)

## Slide 11: FAIR Vacuum Requirements
Ring Accelerator
SIS100
Production
of new nuclei
Production
of antiprotons
Experimental and
storage ring CR
Ring Accelerator SIS18
Existing facility
Planned facility
Experimental setups
Graph: GSI/FAIR
Linear Accelerator UNILAC
Beam Vacuum System:
Total length: ~ 3.9 km
Volume: ~ 65 m3
Vacuum: 10-6 – 10-12 mbar
Cryogenic sections with operating temperatures of 5-20 K
Bakeable sections (up to 300°C) operated at room temperature
Insulation Vacuum System
for superconducting magnets in SIS100 & SuperFRS and
cryogenic transfer & bypass lines
Total length: 2.8 km
Volume: ~ 300 m3
Vacuum: <10-6 mbar
CBM
Panda
Low & High-Energy Cave
p ≈ 5·10-12 mbar
Super-FRS,
p ≈ 10-6 – 10-8 mbar
p = 10-7 mbar
p < 10-11mbar
Linear Accelerator
p-Linac
p = 10-8 mbar
p < 10-10 mbar
HEBT
10-11mbar < p < 10-8 mbar
p ≈ 10-9 mbar
Antiproton Ring
HESR

## Slide 12: Principles and Status of System Design
Use of standard components (catalogue items) for pumps, gauges and valves, no further development from manufacturer needed (only adaption of interface for vacuum controls)
In UHV systems with very low gas load, only capture pumps for keeping up the vacuum.
The concept for the design of the vacuum system is based on the operation experience with existing GSI accelerators.
Keep all electronics out of the accelerator tunnel and install racks for controllers and controls racks (PLC) in dedicated electronic/supply rooms.
  use of passive gauges with dedicated controllers
  controllers for pumps located in supply rooms
  valves will be controlled and monitored from supply rooms
  In case of a failure of the electronics the controller can be changed without access to the tunnel
  long cables (power and signal) for all devices
Status:
The system design 95% finalized, procurement for vacuum chambers and standard components ongoing, large parts already contracted and delivered.

## Slide 13
Ultimate pressure p < 3·10-11 mbar (if required per Detailed Specification)
Integral leak rate Q < 1·10-10 mbar l/s
Outgassing rate q < 1·10-12 mbar l/s/cm² after bake-out to max. 300 °C
Outgassing rate q < 5·10-10 mbar l/s/cm² without bake-out
clean RGA spectrum without any CxHy and other residues
46 Ion getter pumps
48 NEG catridge pumps
94 NEG/IGP pumps
NEG coating
Cryogenic wall pumping
53 gauges extractor type
48 cold cathode gauges
52 all-metal gate valves
Circumference: 1083.6 m
~1000 vacuum chambers, ~600 vacuum components (pumps, gauges, valves, …)
~82% at cryogenic temperatures: ~890 m; pcold < 1·10-12 mbar
~18% at room temperature: ~194 m; pwarm < 3·10-11 mbar
average H2 particle density: Nmax < 8·1011 m-3 (with 2% beam loss @ 2.7 GeV U28+)
Basic Requirements for FAT / SAT for each UHV chamber and component:
The UHV System of SIS100 – Basic Requirements

## Slide 14
The dipole and quadrupole chambers represent 81% of the total surface in the cryogenic sectors.
Chamber design was optimized in terms of:
Low wall temperatures during magnet ramping to assure effective H2 cryopumping
field quality (additional harmonics)
beam dynamic aspects (e.g. impedances)
Solution:
Thin-walled chamber (d = 0.3 mm) with ribs for stiffening
Special stainless steel Böhler P506 (X 2 Cr Mn Ni Mo N 19 12 11 1) with mr = 1.002 at 4.2 K [also used for LHC beam screen]
Cooling of chamber with supplementary cooling tubes
Problem:
Fast ramping of the magnets induces eddy currents
The chamber walls are heated up.
Generation of additional harmonics in field.
SIS100: Dipole & Quadrupole Chamber Design
14

## Slide 15
Status Dipole Chambers
Series production by Pink Vakuumtechnik.
All 115 chambers delivered and integrated into dipole magnets
Dipole Chamber
Length ~3,4m
Aperture: 120x60mm2
Bending angle 3.33°
cooling tubes
stiffening ribs
Status Quadrupole Chambers
Series production finished by Research Instruments
Integration into quadrupole module by Babcock Noell (BNG) finished
Quadrupole chambers:
11 different types (short and long)
Length: between ~1.3m and ~2.7m
Aperture: 133x65mm2
SIS100: Thin-walled Dipole & Quadrupole Chambers

## Slide 16: SIS100: Further Vacuum Components
Series production of 50 pcs at Pfeiffer Vacuum
Roughing Cold-Warm Transitions (RCWT)
Cryosorption Pumps
R-CWT polyimide foil
heater (design: St. Zeller)
Manufacturer:
Standard Pumping Chamber
Series production of 31pcs by VA-TEC
Assembly with pumps and gauges started
In-house development of a pump prototype with charcoal
Contract with ILK Dresden
All 87 pumps delivered and tested

## Slide 17
High radiation at target area and first separator stage
Large aperture vacuum chambers, normal conducting and superferric magnets (insulation vacuum)
Total length: ~350 mof DN400 beamline, 35 SC multiplets, 27 SC dipoles, 5 NC radiation hard dipoles, 20 focal-plane chambers, target chamber and 3 beam stopper chambers.
Required vacuum: ~ 1x10-6 - 1x10-7 mbar
Complex vacuum system due to remote handling in target area (pillow seals and inflatable bellows) and large number of focal plane chambers (20 pcs) with a lot of insertions for the experiments
Schematic Layout of the
Super-FRagment Separator (Super-FRS)

## Slide 18: Super-FRS: 3D Model
SC Multiplet
rad. res. Dipole
SC Multiplet
SC Dipole
Target Chamber
SC Multiplet
SC Dipole
SC Dipole
SC Multiplet
SC Dipole

## Slide 19
57 Ion Getter Pumps (150 – 800l/s)
29 Turbo molecular pumps (850 – 1350l/s)
39 beam vacuum sectors separated by 38 DN400CF gate valves (Viton and EPDM).
64 Penning gauges, 46 Pirani gauges
81 TMP stations for generating the insulation vacuum.
Super-FRS: Vacuum Schemes
19

## Slide 20
Standard Dipole Stage
Branching Dipole Stage
Bending angle type 1: 11° & 9.75°
Length= 3 - 3.2m
Aperture: 38x14cm2
Wall thickness: 6 – 11mm
Flanges DN400CF
Call for tender open
length 2.8m
aperture: 38x14 (resp 68x14)cm2
wall thickness max 11mm
flanges DN400CF or racetrack/rectangular for metallic sealing ( e.g. HELICOFLEX)
Contract to be awarded soon
outgassing rate 1x10-9mbar l/s cm2
leak rate 1x10-9mbar l/s
special RGA acceptance criteria
Required relative magnetic permeability: ≤1.01
Material: DIN EN10088: 1.4306, 14307 or higher quality
Super-FRS: SC Dipole Chambers

## Slide 21
Dipole chamber will absorb P = 3 W/cm2, Energy 4.5 J per pulse
Chamber to be produced out of Titanium Ti6Al4V (3.7165)
Length: ~365cm
aperture entrance: 50x14cm2
aperture exit: 120x14cm2
Quadrupoles & Sextupole
Dipoles
Magnet:
weight ≈ 95 tons
aperture of yoke: 1200x180mm
overall length of magnet: 3.2m
Contract signed with: CNIM Systèmes Industriels
Under construction
Super-FRS: Chambers for Radiation Resistant Dipole Magnets in Target Area
21

## Slide 22
Dimensions of the chambers: max 460 x 100 x100 cm3
Thick top plate required: approximately 40 mm
High requirements on overall flatness of the top plate (0.1 mm)
stainless steel grade according to DIN EN 10088: 1.4301, 1.4306, 1.4307, 1.4404, 1.4435 or 1.4429
outgassing rate 1x10-9 mbar l/s cm2
leak rate 1x10-9 mbar l/s
special RGA acceptance criteria
Protoype by Pfeiffer Vacuum
S-FRS: Diagnostic Chambers
22

## Slide 23
Beam line length: about 1500 m
p ≈ 1x10-8 mbar, non bakeable
only sections directly connected to SIS100, will be baked up to 300°C to achieve a vacuum of 1x10-10 to 1x10-11 mbar
46 vacuum sectors, length between 10 and 50 m
55 gate valves (Viton and all-metal)
Beam Pipe Aperture DN100CF – DN400CF
Pumped by ion getter pumps
Passive Penning and Pirani gauges
Vacuum chamber stainless steel grades EN 10088: 1.4301, 1.4306, 1.4429 or 1.4435
Integral leak rate ≤ 1x10-10 mbar l/s
Outgassing rate ≤ 5x10-10 mbar l/(s cm2)
Residual gas composition as acceptance criteria
Most vacuum chambers were supposed to be produced by Budker Institute of Nuclear Physics BINP, Russia. Due to Russian war in Ukraine collaboration is stopped. Procurements of chambers for FS+ via calls for tender.
HEBT: Schematic Layout
23

## Slide 24
from SIS18
from SIS100
to SIS100
to pbar/APPA/
Super-FRS
to CBM
HEBT: 3D Model of part of HEBT
24

## Slide 25
51 Dipole Chambers produced by Budker Institute of Nuclear Physics (BINP) Russia and installed in magnets
In-house production and cleaning of 73pcs round chambers at GSI
©Gaby Otto (GSI)
HEBT: Vacuum Chambers

## Slide 26
38 pcs
length ~400-800mm
diameter ~160mm
height ~650mm
Flanges: 5x DN160CF, 1x DN40CF
Contract signed with SAES Rial Vacuum
under construction
Pumping Cambers
Dipole Chambers
Quadrupole Chambers & Steerer Chambers
Bellows
Quadrupole Chambers: 93pcs
Steerer Chambers: 45pcs
length 0.5 – 2m
aperture: 100mm, 120mm, 150mm
Contract signed with SAES Rial Vacuum
Partially delivered and under construction
309 pcs
length: ~186mm, aperture: 154mm
Contract signed with SAES Rial Vacuum
Partially delivered and under construction
15 pcs
length: 2.5 – 3.8m
aperture: 110x67mm2, 120x60mm2, 120-200x60mm2
wall thickness: ~4-6mm
Contract signed with Fantini S.p.A.
under construction
HEBT: Vacuum Chambers

## Slide 27
3+1x HEBT (incl. bake-out in one)
2+1x Super-FRS
10x SIS100 (incl. bake-out)
Vacuum controls and controllers for beam vacuum and bake-out are
distributed over 22 different electronic rooms at FAIR to keep cables „short“.
1x p-Linac
1x CR
1x pbar
2x HESR (incl. bake-out)
Vacuum Supply Areas (Electronic rooms) Beam Vacuum

## Slide 28
Procurement via frame work contracts
NEG Pumps SAES Getters: CapaciTorr Z3500, NexTorr D500, …
Controllers for NEG pumps SAES Getters: NEG Power C4
Ion Getter Pumps: Agilent Technologies: StarCell (from 75 – 1000l/s)
Controllers for Ion Getter Pumps Agilent Technologies 4UHV (neg polarity)
Extractor type gauges: Leybold IE514
Controllers gauges extractor type PREVAC MG15
Passive Penning & Pirani gauges & controllers: INFICON PSG018, MAG070, VGC094
Passive cold cathode gauges MKS Instruments 422
Turbo pumps and controller Leybold TurboVAC iR (300 – 1200l/s) & TurboDrive 500e
Gate and Angle valves VAT Viton/EPDM/all-metal gate & angle valves DN100 – DN400
Primary pumps: call for tender in progress
Status Vacuum Standard Components
28

## Slide 29
4x HV
per channel
1x AI
ProfiBus DP
per Channel
1x AI
1x DO
4x
ProfiNet
2x DI
1x DO
Tunnel
Controller Cabinet
PLC Cabinet
(Slovenian In-Kind)
ET200M
ET200M
ET200M
PLC & Communication Module
Long cables up to 200m
Supply Area
Ion Getter Pump
Gauges
Turbo molecular pump
ProfiNet
Roughing pump
Schütz-steuerung
Gate- & Angle Valves
Schematic Setup of Vacuum Controls

## Slide 30
Design/software development by COSYLAB Slovenia as In-Kind
Manufacturing by INEA d.o.o
@Björn Mai (GSI)
All delivered by NATUS Industrial Solution Systems
SIS100, HEBT & SFRS (40 pcs)
Controller Cabinets
PLC Controls Cabinets
Controller and PLC Cabinets for Vacuum Control System

## Slide 31
Terminal Box
Connection of power for bake-out jackets, thermocouple, thermal cut-out device (thermos switch)
Temperature Compensation (transition from thermocouple to Cu wire)
8 Channels, max 7 heating jackets per channel
Solid State Rack
Cabinet with Solid State Relais & Fuses
deliver Power to bake-out jackets
24 channels (supplies three Terminal Boxes)
PLC Cabinet
contains PLC & PID controllers, I/O modules
controls six Power Controls Racks
with max 144 control circuits each
Thermo switch
Thermocouple
Power
Thermocouple
Power
Power & Thermal
Cut-Out
2 cables
Digital I/Os:
Status on thermal cut-out devices, fuses, on/off switch, fast stop,...
5 cables
Tunnel
Supply Area
Schematics of Bake-Out Control System

## Slide 32
16 PLC cabinets
91 Solid State Racks
273 Terminal Boxes
contract signed with NATUS Industrial Solution Systems
under construction and partially delivered.
PLC Cabinet
Solid State Rack
Terminal Box
Hardware Bake-out System (HEBT & SIS100)

## Slide 33: Installation of First Components at FAIR in March 2024
© FAIR
SIS100 Standard Pumping Chambers before transport
to tunnel © GSI/FAIR I. Pongrac
Quadrupole Magnets with Chambers HEBT
Beam Diagnostic Chambers HEBT
RF Components in SIS100 tunnel
33

## Slide 34
  Thank you for
  your attention!
Graph: ion42/FAIR
  Acknowledgements: Thanks to I. Pongrac, S. Purushothaman, P.M. Suherman, L. Urban, S. Wilfert, S. Zeller