## Slide 1
Status of PIP-II Vacuum Systems
Raul Campos, PIP-II Vacuum Systems Project Manager, on behalf of the PIP-II Vacuum Team
OLAV VI
April 16, 2024

## Slide 2: Outline
PIP-II Overview and PIP-II Vacuum Sections
PIP-II Vacuum Systems Requirements
Vacuum Systems Design
Analysis and validation
Fast acting valves and interlocks
Integration with other systems
Current Status

## Slide 3: PIP-II Mission
PIP-II Capabilities
Beam Power
1.2 MW proton beam
Upgradeable to multi-MW
Flexibility, multi-user capability
CW-compatible
Customized beams
Multi-user delivery
Reliability
Modernizes Fermilab accel complex
PIP-II is an essential upgrade to Fermilab accelerator complex to enable the world’s most intense beam of neutrinos to LBNF/DUNE, and a broad physics research program for decades to come.
PIP-II Scope
800 MeV H− SRF linac
  CW RF Operations
Linac-to-Booster transfer line
Accelerator Complex Upgrades
  Booster
  Recycler
  Main Injector
Conventional Facilities
  Space reserved for two CMs for 1 GeV Upgrade
The PIP-II scope enables the accelerator complex to reach 1.2 MW proton beam on LBNF target

## Slide 5: PIP-II Vacuum Systems Sections
PIP-II Vacuum Sections:
Warm Front End (WFE)
Superconducting Linac (SCL)
Beam transfer line and Beam absorber line (BTL/BAL)

## Slide 6: Performance Requirements
 | Ion Source | LEBT | RFQ | MEBT | MEBT-DS | CMs* | Warm Units** | Trans. Section | BTL
Pressure (torr) | <10-2*** | <5x10-7 | <5x10-7 | <5x10-7 | <1x10-9 | <10-10 | <1x10-9 | <5x10-8 | <5x10-8
Leak check sensitivity (mbar-l/s) | 2x10-9 | 2x10-9 | 2x10-9 | 2x10-9 | 2x10-10 | 2x10-10 | 2x10-10 | 2x10-10 | 2x10-10
Vacuum seals joints | Metal gasket or elastomer, CF or KF |  |  |  | CF only: metal gasket only | CF only: metal gasket only |  | Weld or Metal gasket | Weld or Metal gasket
Parts cleaning | UHV procedure |  |  |  |  |  |  |  | 
Gauging | CC gauge + Pirani |  |  |  |  | CC gauge + Pirani |  | CC gauge + Pirani | 
Low Particulate practice | No | No | No | No | Yes | Yes | Yes | Yes | No
Controllers | Equipped with RS485 to communicate with control system via a PLC |  |  |  |  |  |  |  | 
Particle Free Regions

## Slide 7: Warm Front End

## Slide 8: Warm Front End
Addition of a second ion source for PIP2 design
Protection for superconducting linac tested here
IS&LEBT
RFQ
MEBT
PIP2IT – built and tested
PIP-II

## Slide 9: Warm Front End Ion Sources and LEBT
Turbo Sets
End plate of RFQ
Ion Source (H2)

## Slide 10: Warm Front End : MEBT
Ion Pumps
Gate Valves
Fast Gate Valves
NEG: to improve vacuum for the entry to CM
Low Particulate Region
Gauges on the top of same devices as Ion Pumps at
Differential Pumping Insert, with gate valve upstream
Turbo Pumps @ Beam Absorber, high gas load due to beam lose
Kicker
Absorber

## Slide 11: Transition to Low-Particulate Zone
Low-particulate vacuum field connections
Pre-assembled section inserted through wall
Conventional UHV
HWR
Fast Acting Valve
Beam absorber
Differential pumping insert
Pneumatic valve
Refer to Curtis Baffes’ presentation for details of field installation

## Slide 12: Differential Pumping Insert (DPI)
Reduction of conductance between UHV and particle free UHV
Construction of DPI
Copper – 200mm long, 10mm ID (from 1.25in ID)
Ceramic isolation – for electrical isolation for lost beam current – monitored by Machine Protection Systems (MPS)
Fins/disks (aluminum) shrink fit on stainless for thermal cooling

## Slide 13
Superconducting Linac

## Slide 14: SCL (HWR-SSR1-SSR2-LB650-HB650)+ Warm Units
325MHz Warm Units
Vacuum
Instrumentation
325MHz SSR cryomodule
(SSR2 shown)
650MHz cryomodule
(LB650 shown)
650MHz Warm Units
Vacuum
Instrumentation
Magnets
Warm units: Room-temperature beamline between each PIP-II Cryomodule
  Qty 10 325MHz Warm Units (including HWR-SSR WU)
  Qty 13 650MHz Warm Unit (including units downstream of HB650)

## Slide 15: Warm Units and Integration
Warm units vacuum systems are integrated with warm magnets and beam instrumentation devices
Selected a combined ion pump/NEG as the pumping technology for warm units. Benefits include:
  Less particle generation
  Lighter than other options (2.3kg vs. 43 kg); does not require a structural support
  Smaller, which benefits integration with beam instrumentation

## Slide 16: Warm Units Hand-Offs and Integration
BI Hand-off to VAC
VAC Hand-off to LI
VAC integrates and Vacuum- certifies assembly
Vacuum certified laser wire vacuum chamber
Vacuum-cleaned BPM
Vacuum-certified warm unit vacuum assembly
Vacuum-cleaned vacuum equipment, spools, fittings, bellows
Integrated Warm Unit

## Slide 17: Transition from Low-Particulate Zones
Low-particulate vacuum
field connections
Conventional UHV
FAV
First Dipole
Gauges (special sensors for FAV set) for valve are downstream
Straight ahead dump
Refer to Alex Chen’s presentation for details of FAV operation

## Slide 18: Insulating Vacuum of Cryomodules
Insulating Vacuum Pumpout Port
HB650
SSR
Insulating Vacuum Pumpout Port

## Slide 19: Insulating Vacuum
After cooldown, insulating vacuum does not require active pumping

## Slide 20: PIP2IT Beam Valve Control Schematic for Interlocks
IS
LEBT
RFQ
MEBT
HWR
SSR1
HEBT
P:M03WRP
P:R40VGP
P:R10VGP
P:M52WRP
P:M92WRP
P:R50VSO
P:M61VSO
P:L10VSO
P:L01GIP
P:L20GIP
P:HWRBVACPCC1
P:SSRBVACCC2
P:HBTVACPCC1
P:HBTVACPCV2
P:HBTVACFSTVFS
P:M81VSO
P:HBTVACBV
P:SSRVACBVD
P:SSRVACBVU
P:HWRBVACBVU
P:HWRBVACBVD
P:HBTVACPCV3
Controlling
Gauge
Fast Valve Kit
Beam Valve
Permit Criteria:
<5E-9 torr for HWR, SSR1
<1E-5 torr for others
<1E-4 torr for Fast Valve
P:SSRVACBVD Stays open due to burst disc at downstream
ACNET NAMES
All gate valves are interlocked with vacuum status
PIP-II CM&WU
Regular valves closure

## Slide 21
Vacuum Analysis

## Slide 22: IS, LEBT, RFQ Vacuum Pressures
Chart: PXIE_IS_LEBT_RFQ Pressure Profile, ISUP588
Devices | 10 | 10 | 200 | 200 | 14 | 14 | 220 | 220 | 72.9 | 72.9 | 150 | 150 | 72.9 | 72.9 | 50 | 50 | 72.9 | 72.9 | 200 | 200 | 34.8 | 34.798 | 72.9 | 72.9 | 20 | 20 | 319 | 319

## Slide 23: Differential Pumping Insert

## Slide 24: SSR1 MolFlow Simulation
pump3
Transition:
300K-50K-5K-2K

## Slide 25
2nd Half SSR1 Cavity String (COLD)
HEBT
Dump
2.77E-6 mbar.L/s
@Dump
2mA, 1.1%
Hydrogen outgassing rate on all inner surfaces All 2.E-10 mbar.L/s.cm2
Ion Pumps 200 L/s
CM: 2K, 0.99 Stick factor
Transition:
2-5K (0.7)
5-50K(0.1)
50-300K, (0.0)
LPM
(2.4E-7 mbar.l/s)
SLIT1
(4.6E-7 mbar.l/s)
F.C
(3.5E-7 mbar.l/s)
SLIT2
(4.6E-7 mbar.l/s)
F.C.
(3.5E-7 mbar.l/s)
Lg Tube
(2.2E-6 mbar.l/s)
SSR1-HEBT VACUUM Simulation

## Slide 26: SSR1-HEBT VACUUM Simulation
The sticking factors of hydrogen for the three transitions region 2-5K, 5-50K, 50-300K are 0, 0.1, 0.7
Entire cavity was under 2K, sticking factor 0.99 was assigned
Most significant hydrogen flux arrived on the face of downstream wall
It takes 1.5 week to buildup one monolayer on the face, however, on 1st cavity, H2 will diffuse on the other surfaces due to beam induced desorption
2-5K
(0.7)
5-50K
(0.1)
50-300K
(0.0)
Entire Cavity under 2K, 0.99 sticking factor, surface 8900cm2
Gas Flux

## Slide 27
Chart: HEBT H2 Presure Profile Along Beam Line
End of cavity
SSR1-HEBT VACUUM Simulation (Hydrogen pressure profile)

## Slide 28: Testing and Validation at PIP2IT and Test Stand
Critical technologies tested at PIP2IT

## Slide 29: PIP-II Injector Test (PIP2IT)

## Slide 30: Differential Pumping Insert

## Slide 31: 1st Test on MEBT DPI-FV
M72WRP
M61VSO
M71S2P
M63WRP
M63DIP
M11PIP
M81VFC
LD
PG
Leaker Volume=0.29 liter
M72PIO
M92WRP
V1=36.5 liters(M61VSO-FV)
V2=95.1 liters(POST FV)
Permeation rate from Scanner O-Ring is about 6E-7 torr.l/s
M52WRP
Refer to Alex Chen’s presentation for details of test

## Slide 32: PIP-II Test Stand
Beamline and Insulating vacuum stations assembled and tested
Pressures meet PIP-II vacuum requirements
  Beamline vacuum
    2e-10 mbar (requirement <1e-9 mbar)
  Insulating vacuum
    2e-5 mbar before cooldown (requirement <5e-5 mbar)
    <1e-8 mbar cold

## Slide 33: PIP2IT (650 Test Stand)
EPICS vacuum interface is developed and realized
mbar
HB650 Insulating Vacuum Pumpdown
Vent for leak repair
Begin cooldown
initial pumpdown
1 day to reach 5E-5 mbar, qualification of cooldown

## Slide 34: Beam Transfer Line and Beam Absorber Line

## Slide 35: PIP-II BTL/BAL Layout
BTL-BOOST
BTL-ARC2
BTL-STRAIGHT, BAL2(25kW)
BTL-ARC1
BTL-STRAIGHT, BAL1(2kW)

## Slide 36: BAL(25kW), BTL STRAIGHT2 & ARC2
BAL2 (25kW)
Gate valves: 2
Roughing/Gauge Ports:2
Ion Pumps:14
Quads:14
Dipole:7
Bellows: xx
Stands: xx
2” beamtube length: xx
BTL Straight2
BTL ARC2
Gate Valve: segmentation of SCL- BTL
Gate Valve: divided long arc2
Gate Valve: divided BTL
BEAM
Typical vacuum cell

## Slide 37: BTL/BAL Vacuum Sections and Components
 | SCL-BTL ARC1 | BAL1 | BAL2 | BTL STAIGHT | BTL ARC2 | BTL-BOOST | Total
Section Length (m) | 116m | 41m | 32m | 82m | 110m | 16m | 397m
Ion Pumps | 17 | 3 | 7 | 14 | 18 | 4 | 63
Gauge/Ports | 2 | 1(2) | 1(2) | 2 | 2 | 1 | 9(11)
Bellows | 61 | 13 | 4 | 36 | 52 | 9 | 175
Quads | 17 | 2 | 4 | 14 | 19 | 4 | 57
Dipoles | 8 | 0 | 5 | 14 | 17 | 2 | 46
Special tube | 2 Collimators 2 Large Quad 1 Separator 8 Dipoles | 1 Window | 1 Window 5 Dipoles | 14 Dipoles | 17 Dipoles | 2 Dipoles | 
2” Beamtube Length | 51m | 41m | 10m | 68m | 57m | 13m | 240m
Stand/Girders | 25 | 8? | 9 | 14 | 18 | 3 | 78

## Slide 38
SCL-BTL ARC1
BAL-S
BTL Strt2
BAL-L
BTL ARC2
BTL-BOOST
Controlling
Gauge
Fast Valve Kit
Beam Valve
Permit Criteria:
<1E-5 torr for gate valve
<1E-4 torr for Fast Valve
Gate valve stays closed at power off
Gate Valves are controlled by vacuum level( average readings of gauges in the section) at both sides
All gate valves are interlocked with vacuum status via PLC
PIP2 BTL/BAL Valve Control Scheme

## Slide 39: Summary
Final design reviews are complete
PIP-II Vacuum will have its final Integration review soon
Procurement is starting now, followed by fabrication and hand-offs to installation teams
PIP-II completion scheduled for 2029

## Slide 40: Thank you for your attention!
This work has been authored by Fermi Research Alliance, LLC under Contract No. DE-AC02-07CH11359 with the U.S. Department of Energy, Office of Science, Office of High Energy Physics