## Slide 1: The vacuum systems of LIGO Janos Csizmazia Lead vacuum engineer, Hanford
General overview, current enhancements
Document G2400921

## Slide 2
“Matter tells space how to curve, space tells matter how to move.”
~ John A.Wheeler
Document G2400921

## Slide 3
Image courtesy of The Manhattan Rare Book Company
Albert Einstein
1915
The General
Theory
Of
Relativity
Document G2400921
Notes: REMEMBER: 1915!!!!!!
MATRIX!

## Slide 4
Document G2400921

## Slide 5
Document G2400921

## Slide 6
The Most Sensitive “Ruler”!
Document G2400921
Notes: 1000x smaller than diameter of a proton!!!

## Slide 7: Precision of measurement
E-19 – E-20 m in 4 km (2.5 mi)
Analogy: human hair thickness distance change between Earth and Alpha Centauri (~4 LYs)
Why?
“Stiffness” of spacetime: freq. dependent, at 100 Hz: 10^20 times of steel stiffness
Document G2400921

## Slide 8
Document G2400921

## Slide 9: Vacuum system overview
2nd and 3rd biggest vacuum systems in the world
Pressure: high E-8 – high E-10 Torr. Why?
  Thermal / sound insulation – rough vacuum
  Minimizing light scattering – E-4 Torr
  Contamination tracing (RGA useability) – E-7 Torr
  “Silent” pumps shall be used: Ion pump, cryogenic getter pumps: E-8 Torr and beyond
  Contamination control: as high vacuum as it can be
Document G2400921

## Slide 10: Vacuum processes 1 – maintaining vacuum
Biggest sections have not been vented since 2000! – during vents, separated by 40-44” GVs
“Silent” pumps:
Ion pumps
Cryotraps
Getters
Enhancements: more NEGs, Ion – getter pump tandems
Document G2400921

## Slide 11: Vacuum processes 2 – pumping down to UHV vacuum
Tools: oil-free scrolls + Turbos (later Ion-pumps)
Enhancements: boost speed (reduce pumpdown time), clean system. 2 major projects:
1. Gas-cleaning
2. Getting rid of pump downtime  ADAM
Document G2400921

## Slide 12: Gas cleaning – a brief overview
Problem: opening up system during a vent  water adsorption (no bakeout)
Our problem is not the particle contamination, it is the molecular contamination
Document G2400921

## Slide 13: Gas cleaning – a thorough analysis
💥
💥
Main goal: get rid of the vast majority of contamination before HV pumping
Cleaning of: main volume; circulation lines; beamtube regeneration
Very delicate technological window, and a very complicated set of variables:
Type of gas: N2, Ar, O3, etc…
Flow rate increases: pressure (number of molecules) increases, desorption rate decreases
Huge sizes  Re number big – linear speed of molecules decreases
Finite time – ideally ~8 hrs
Document G2400921

## Slide 14: Evacuation of Large Volumes Adam K Branch Vacuum engineer, Livingston
Improving system pump down times
Document G2400921

## Slide 15
Start
Resume
Resume
Resume
EOD
EOD
WEEKEND
EOD
Document G2400921

## Slide 16: System Configuration
Pumps
  Pfeiffer ATH2303M – Turbo – 2150 l/s
  Pfeiffer HEPTA 100P – Screw – 36 l/s
  Anest Iwata ISP 250 – Scroll – 5 l/s
Controls
  TPG-362 Dual Gauge Controller
  PKR-361 Full Range Gauge
  TPR-270 Pirani Gauge
Document G2400921

## Slide 17: Current Operational Experience
Setpoint requires personnel present to update
Slow reaction time to various failures
Possibility to not detect a gauge failure
Mitigation Goals
Automate setpoint in relation to changing pressures
Reduce reaction time
Monitor for erroneous gauge activity
Document G2400921

## Slide 18
Document G2400921

## Slide 19
Estimated Benefit
Reduced time to achieve desired pressure
  760 torr to 5 torr in 24 hours
    Time spent valved out 93 hours
    Total time elapsed 116 hours
Consistent safety valve reaction times
  Reduce loss of progress
  Reduce chance of contamination
Possible Risks
Introduction of new failure modes
Unexpected erroneous outcomes
I automate myself out of a job.
Document G2400921

## Slide 20: Present of Gravitational Wave Astronomy
VIRGO, Italy
LIGO, LIV
LIGO, HAN
Document G2400921
KAGRA, Japan

## Slide 21: Future of Gravitational Wave Astronomy
LIGO India – 3rd leg of LIGO
CE – Cosmic explorer
ET – Einstein Telescope
LISA – Laser Interferometer Space Antenna
Document G2400921