## Slide 1: Possible Baffle Features for Beam Based Alignment
Keith Gollwitzer
March 11, 2020

## Slide 2: Assumptions
Baffle can be driven up/out of the ideal beam path by twice the distance that the beam can be directed
  If beam can be moved upward 25 mm, then baffle can be moved
    Y = R_outer + 50 mm
The vertical motion/readback of the baffle is “well understood”
Baffle is located in the up/out of the way position for the Beam Based Alignment of the downstream components (horns & target)

## Slide 3: Cross-hair like features
Nothing to scale or exact place
Cross piece hangs 10mm below outer edge of baffle
Side features are +- 10mm from beam line
Cross piece hangs 5mm below outer edge of baffle
Side features are +- 5mm from beam line
R_outer
Baffle

## Slide 4: Alignment of Baffle using Cross-Hair
Low power beam is put on ideal trajectory
Lower baffle noting when ionization indicates (R_outer+10mm) and (R_outer+5mm); now can adjust vertical angle of baffle
  If baffle tilt was adjusted, recheck by driving baffle through cross-hair features
Drive baffle so that ideal beam is at (y=R_outer+2.5mm)
Scan beam horizontally to find four horizontal features; now can adjust baffle to set horizontal angle
Drive baffle down so centered upon ideal beam (y=0).
  Verify by moving beam to find inner edge of baffle

## Slide 5: Bafflette like features
Nothing to scale or exact place
Features are 20cm long parallel to beam path
Similar alignment procedure as cross-hair except using
Hadron Detector instead of ionization chmabers
Baffle
5mm
5mm
5mm
5mm
5mm
5mm
5mm
5mm

## Slide 6: Next Steps
Determine if there is enough baffle travel
What is “good enough” for linear motion of the baffle vertical movement?
Beam Based Alignment simulations need to be done to optimize feature dimensions
  Here, multiples of 5mm were picked based upon low power beam sigma is expected to be 1mm.
Need to determine pros/cons of each method
  Cross-hair like
    Where to put (new) ionization monitors?
      Able to see interactions with upstream feature?
  Bafflette like
    Will Hadron Detector “see” feature intercepting beam since full target will also intercept ideal trajectory beam?
    Lever arm is smaller since signal is associated with center of mass of feature