## Slide 1: DUNE Requirements
Technical Integration Meeting
April 2, 2020
Steve Kettell

## Slide 2: Outline
Requested changes to EB held requirements
Proposed changes to “TDR” (TB) requirements
Proposed format for consortia requirements

## Slide 3: EB-owned requirements (EDMS-0000195183)
Process: Consortium brings proposed changes to TB for discussion. TB will send proposals with recommendation to EB.
Initial list of possible proposals:
Clarification requested from HV for #2249 (SP-FD-11)
  Current “<1\% throughout volume “
  Proposed “<+/-1% in >99.9% of the active volume”
Other proposed changes
  ???

## Slide 4: TDR (TB owned) requirements (EDMS-0000195183)
Process: Consortium brings proposed changes to TB for discussion and decision.
Current list of proposed changes:
HV (2281-2282): Transfer one (#2329: SP-CISC-27) from CISC to HV
  Cold camera coverage, 80% of HV surfaces “Difficult to achieve with availability of signal feedthrough ports”
TPC electronics (2283-90)
  Add some
APA (2275-80)
  Add 3
CALCI (Cal: 2307-2313, CISC: 2323-2332)
  Change names from Cal and CI to “SP CALCI”
  drop 2 (2312-3) and add 1 in Calibration
  Move 3 SC requirements to DAQ/SC (2330-2)
  Move 1 CI requirement to HV (2329)
  edit text in 1 CI (2328)
DAQ/SC (DAQ:2314-22, SC:2330-32)
  Drop a couple of SC (2330, 2332)
Other proposed changes
  ???

## Slide 5: Consortia requirements
Proposal from Alberto
Fabrication Requirements (e.g. APA-FAB-1)
Transport Requirements (e.g. APA-TRN-1)
“Installation” Requirements (e.g. APA-INS-1)
Interface Requirements (e.g. APA-INT-1)
All of these to be managed in spreadsheets by Consortium
  Propose 1 spreadsheet per consortia with 4 tabs
  Should be in good shape for the Preliminary Design Review
  Need to be signed off as part of the Final Design Review
(QA/QC Requirements)
(Derived from interface docs)

## Slide 6
APA Interface Requirements
APA-INT-1 APA frames shall allow the mounting of CE Cold Boxes over the head frames
APA-INT-2 APA frames shall allow routing of CE cables for bottom APA along the side
tubes of bottom and top APA
APA-INT-3 APAs shall allow insertion of 10 PD modules between the wire planes on
each side of the frame
APA-INT-4 APA frame shall allow the mounting of at least 4 temperature sensors, of
which 2 will be in thermal contact with the APA frame
APA-INT-5 APAs should accommodate cablings for the readout of the PD modules and
the temperature sensor
APA-INT-6 APAs will provide support points to connect to the HV Field Cage and to the
HV End Wall
APA-INT-7 Mechanical suspension of the APA shall be accomplished using insulated
supports.
APA-INT-8 APAs shall be insulated from each other
APA-INT-9 The APA frame shall be connected to the COMMON of all FE ASICs.

## Slide 7
APA Fabrication (QA/QC) Requirements
APA-FAB-1 APAs should be fabricated at different production sites using exactly the same
winding machines and QA/QC procedures
APA-FAB-2 Wire tensions should be measured for each wire, possibly utilizing an electronic
wire tension method
APA-FAB-3 Board size tolerance (SP-FD-10-S1)
APA-FAB-4 Board hole positioning tolerance (SP-FD-10-S2)
APA-FAB-5 Board thickness tolerance (SP-FD-10-S3)
APA-FAB-6 Board tongue position tolerance (SP-FD-10-S4)
APA-FAB-7 Both glue and solder anchoring (SP-APA-6-S1)
APA-FAB-6 Mill-Max pins…. (SP-APA-6-S2)
APA-FAB-7 APA frame max bow (SP-APA-5-S1)
APA-FAB-8 APA frame max fold (SP-APA-5-S2)
APA-FAB-9 APA frame max twist (SP-APA-5-S3)

## Slide 8
APA Transportation Requirements
APA-TRN-1 An APA transport frame, containing a top and a bottom APA, shall be built to allow
safe transportation of APAs by ship and by road
APA-TRN-2 Individual APAs during transportation shall be protected by protection panels.
APA-TRN-3 The APA transport frame shall be designed to be lowered safely down the
shaft at SURF and transported to the clean room in front of the cryostat.
APA-TRN-4 The APA transport frame shall be designed to allow easy access the head boards of
each APA for possible testing while in storage

## Slide 9
APA Installation Requirements
APA-INST-1 APAs shall be delivered to the installation site in clean condition for operation in LAr
APA-INST-2 APAs shall be built to connect them in pairs (APA-doublet)
APA-INST-3 APA-doublets shall be hanging from the Detector Support system from a single
point
APA-INST-4 APA-doublets shall be connected to adjacent APA-doublets by a simple mechanical
system to constrain them in a plane
APA-INST-5 APAs shall be delivered to the installation site with all possible provisions to
facilitate and accelerate the installation process (e.g.: protection panels should be
easily removable in order to minimize the possibility of damaging the APA during;
conduits for CE cable routing already installed at the APA production factories)
APA-INST-6 APAs shall be built to allow the positioning of survey points

## Slide 10: requirements summary
Proposal is that each consortia develops, maintains and owns its requirements in a 4-tab spreadsheet in edms
Each consortia prepares any proposed changes to EB or TDR requirements for a TB meeting discussion.

## Slide 11: Backup

## Slide 12: edms organization
Should store your consortia requirements someplace. Maybe here?
You should define what is needed, but since your interface documents only discuss interfaces to other consortia, requirements are a good way to specify interfaces internal to your consortia