## Slide 1: Neutrino Beamline Horn A Preliminary Design Review
Nnamdi Agbo
22 – 24 April 2020
Horn A Hanger FEA

## Slide 2: Outline
Introduction
Structural Analysis for Horn A Hanger Utility Beam Support
  Problem Statement
  Analysis setup
  Analysis Result
Thermal Analysis for Horn A Hanger Utility Beam Support
  Problem Statement
  Analysis Setup
  Analysis Result
Summary

## Slide 3: Problem Statement
Utility support beams for LBNF are significantly longer and more heavily loaded than in prior horn designs. This loading and length could effectively create, due to asymmetrical line loading, a large moment at the connection to the horn & module. The rotation at this point could effectively impact both the ability to thread on utility lines remotely, as well as the overall horn position when in the beamline.
The objective is to perform a structural analysis to determine if;
    The Utility Support beam are sufficiently sized
    A negligible transverse horn position offset (< 0.01”) results from maximum differential loading scenario

## Slide 4: Horn A Model
Single Drawbar connection

## Slide 5
Simplified Analysis Model: Initial Design
Horn replaced with a point mass to reduce mesh count and increase computational speed.
Remote mass located at the CG as due from the model.
Remote point A and B to track horn A transverse displacement due to asymmetric loading
A
B

## Slide 6
Deformation Results: Initial Design
Max Utility beam deformation : 2.02mm
Image on the R-T Corner showing the effect of the moment created around the Drawbar Connection

## Slide 7
Equivalent Stress: Initial Design
Equivalent stress: 79.18 MPa
Material: Stainless Steel 304L
Yield Strength: 215MPa
FOS: 2.72

## Slide 8: Remote Points Deformation
Pt A & B represent the centers of the horn on either ends so we could track the displacement of these centers
0.026”
A
B
0.025”
With an infinitely stiff utility beam assumed. Displacement of Pt A & B along the principle x axis was relatively the same

## Slide 9: Proposed Design
 | Horn Displacement – Pt A (mm) | Equivalent Stress (MPa) | Max Deformation for Utility Beam Support (mm)
Initial Design | 0.026” (0.67) | 79.18 | 2.02
Updated Design | 0.0028” (0.64) | 50.31 | 0.9
A new design with two drawbar support was proposed to reduce horn A transverse displacement due to asymmetric loading. The utility beam support mounting bolt holes was equally increased to 10 in the center to better spread the load. Both changes resulted to an improved design as seen on the table below

## Slide 10: Problem Statement: Thermal Analysis for Horn A Hanger Utility Beam Support
The length of the utility beams is a concern when accounting for thermally induced growth during steady state operation. It is the intention of LBNF that this assembly be used for all high-power operation, and therefore, may experience a significant amount of beam induced internal heat generation (EDEP). Excessive thermal expansion will subtract from the nominal 0.125” radial clearance allowed for all utility lines running through the support module.
The objective is to perform a structural analysis to determine;
  Document what & where maximum temperature occurs.
  Document what & where maximum deformation occurs
  expected steady state thermal clearance between the utility / instrumentation lines and module feedthrough holes

## Slide 11: MARS DATA & Boundary Conditions
Boundary Conditions: Provided by Cory
Module end wall snout for horn A gets the most energy (282,678 W/m^3). This was used for all stainless stain parts
Aluminum parts scaled by its mass ratio (set at 40%)
External surface cooled @10W/m^2*C
Hidden Pockets at 3W/m^2*C
Draw bar contact points held at 25C.
Internal cooling passages should have 6576 W/m^2*C convection cooling @ 25C
Ejector line utility cup have 8898 W/m^2*C convection cooling @ 25C

## Slide 12: Thermal Results: Max Temperature
Max temperature of 151.8C @ the stainless steel utility beam
98.4C for the Aluminum block shown below

## Slide 13: Thermal Structural Results: Deformation
Max deformation of 1.6mm
Radial clearance of 3.175mm between horn module and utility line

## Slide 14: Thermal Results: Max Temperature
Utility beam support changed to 7075-T6 Aluminum
Max temperature of 111.6C @ the stainless steel utility beam

## Slide 15: Analysis Inputs: MARS DATA
Max deformation of 1.25mm
Radial clearance of 3.175mm between horn module and utility line
 | Horn Max Deformation | Max Temperature(Deg C)
Initial Design | 1.6 | 151.8
Updated Design | 1.2 | 111.6

## Slide 16: Ongoing Analysis: Problem Statement
The segment of horn stripline between the bottom of the stripline block and the mounting points on the face of the horn is designed to provide flexibility while fine-tuning horn position in the beamline during both final survey and beam operation. This segment was historically required to accommodate vertical and horizontal translation on order of +/- 3mm for the NuMI / NOvA design, and successfully did so. Drive system revisions for LBNF have reduced the design requirements on this structure however, as all horizontal translation occurs on the module / horn assembly structure, not independently at the horn.
Vertical translation is now the only motion the stripline must accommodate and the expectation is that it will similarly need to have the ability to shift horn position on order of +/- 3mm.

## Slide 17: Ongoing Analysis:
+3
-3
Notes:
Striplines are 6013-T651.
All stripline ceramics are magnesia partially stabilized zirconia (MGO-PSZ is common material identifier).
All bolts / studs are 6Al-4V Grade 5 titanium.
All flat washers are 304SS.
All Bellville washers are 718 Inconel.
Model is fixed at Spike base
A +/- 3mm displacement is applied as shown in the image on the left

## Slide 18: Summary
Structural Analysis for Horn A Hanger Utility Beam Support
  Horn A design updated to accommodate two drawbars
  The design change resulted to a 0.0028’’ transverse horn displacement which the less than requirement (less than 0.026”)
  Equivalent stress below material yield strength showing that design is properly sized
Thermal Analysis for Horn A Hanger Utility Beam Support
  Utility beam support material changed to Al7075-T6
  Max temperature reported is 111.6 Deg C
  Clearance between module feedthrough hole and utility line reduced to 2mm due to thermal expansion