## Slide 1: Low Energy Calibration
Robert Svoboda
2020 CALCI Review
May 28, 2020

## Slide 2: Content
The calibration systems
Why do low energy calibrations?
  Systematic uncertainties in LBL Physics
  Supernova physics
  Other physics
What do we get from low energy calibrations?
  Absolute energy scale
  Detector variations over the active volume
  Time-dependent variations
Previous Experience

## Slide 3: Pulsed Neutron Source
Deuterium-Deuterium (DD) generators are sources that produce a short (5-200 ms) pulse of neutrons via the reaction:
Typical DD generator source
Typically 100-1000 n/pulse
No neutrons when turned off
Commercially available ~$175k
Portable
DT used in many physics experiments
Super-Kamiokande, SNO, SNO+,…
Control setup for CERN test

## Slide 4: Pulsed Neutron Source
Deployed outside the cryostat so no issues with contamination or operation in a cold environment
Neutrons can travel many meters into the detector and reach all parts of the active volume
The basic calibration is via neutron capture on 40-Ar which yields a 6.0988 MeV gamma cascade.
38-Ar and 36-Ar give 6.6 and 8.8 MeV but are only 0.4% abundance
gamma cascade
from natural argon
well-understood to,
with the SUM
of gamma enegies
understood to
4 significant figures

## Slide 5: Radioactive Source Deployment
A Cf-Ni gamma source can be deployed to specific locations in the detector to give precision 9 MeV gamma measurements
Completely passive device
Gamma spectrum well-understood
Very inexpensive
source is sized
to fit into a standard
25 cm port.

## Slide 6: Why do we need these devices?

## Slide 7: Supernova
The requirements for energy resolution for SN events are fairly loose since the complexity of the final states (including neutrons) systematically smears the reconstructed energy
The requirements on the energy threshold for individual events to be recorded and the trigger efficiency are more relevant
Smearing of MARLEY generated events by physics and reconstruction is equivalent to roughly a 20% energy resolution
Report by E.Conley DocDB-14068 details the effects of detector performance on SN spectral parameter measurements
Simulation of 30 MeV SN neutrino interaction in DUNE
(E.Conley, DocDB-14068 v7, 2019)

## Slide 8: Supernova
(E.Conley, DocDB-14068 v7, 2019)
(Left) Effects on SN spectral parameter measurements for making wrong assumptions on a “true” 30% energy resolution
(Right) Fractional difference from the
“true” value of spectral parameters from incorrect energy resolution assumptions
Recommended Uncertainty
Requirements:
Energy Scale: <5%
Energy Resolution: <10%
Energy Threshold
Uncertainty: <1.5 MeV
note: this study assumes a 5 MeV step threshold – current expectation is higher with more gradual turn on.

## Slide 9: Trigger efficiency (TDR)

## Slide 10: Supernova Burst Trigger
current trigger algorithm efficiency as a function of number of events in a 10 kton module of the SP FD
(from TDR)
Testing of the SN trigger algorithm is critical, as it is not a simple system and depends on being able to correlate small over the whole detector. The PNS is essentially a “fake” SN with the 6.1 MeV energy and few second time scale similar to what is expected.
(Note: this may change depending
on the neutron background)
LMC
100% inside
our home galaxy

## Slide 11: Other Physics: Solar
8-B neutrino
day/night effect
measurement
using both
ES and ArCC
100 kton-yrs
Achieving an energy resolution of 7% at 5 MeV could allow DUNE
to make an important measurement in solar neutrinos. Exact energy
uncertainties yet to be determined, but low energy calibrations are certainly key.

## Slide 12: Systematic uncertainty in dCP due to the absolute energy scale
Includes full FD simulation and automated
reconstruction; parametrized ND samples;
detailed treatment of systematics
(E.Worcester, ND Review June 2019)
..of course, this assumes
the energy scale shift is
constant over 7 years
This is the major detector uncertainty
remaining after ND inputs
assumes 2% systematic
shift in energy scale

## Slide 13: Systematic uncertainty in dCP due to the absolute energy scale
How will we reach 2% energy scale uncertainty?
  Through-going CR muons
    dE/dx issues underground
    coverage and rate
  Stopping CR muons
    coverage and rate
  Low energy sources
    extrapolation issues
What role can calibration sources at ~10 MeV play in physics at ~1 GeV?
Could the uncertainty be reached with CR muons?

## Slide 14: CR Muon Energy Spectrum
Adam, W. & Bergauer, Thomas & Dragicevic, Marko & Friedl, M. & Frühwirth, Rudolf & Haensel, S. & Hrubec, J & Krammer, M & Oberegger, M. & Pernicka, M. & Schmid, Stefan & Stark, R. & Steininger, H. & Uhl, D. & Waltenberger, Wolfgang & Widl, Edmund & Mechelen, P. & Cardaci, M. & Beaumont, W. & Tsang, K.. (2009). Performance studies of the CMS Strip Tracker before installation. 10.1088/1748-0221/4/06/P06009.
V.Pec Cosmic WG update 20200326
muon energy distribution at sea level
3% stopped m
Mean Em ~ 4 GeV
30.6 days of throughgoing CR muons

## Slide 15: CR Muon Energy Loss
(Ingles, Junk, and Marchionni)
V.Pec Cosmic WG update 20200326
At 280 GeV simulations show a wide
spread in dE/dx due to the fact that
Bremsstrahlung and direct pair production
become increasingly important.
mean energy
variation in
muon dE/dx
for fixed
energy muons
Michels from stopped muons are useful,
but only about one every 8 minutes/module

## Slide 16: Super-Kamiokande Experience
At low energy Super-Kamiokande was able to achieve and maintain <1% systematic shift in the energy scale
  DT generator every few months
  Electron LINAC with a moveable beam pipe into the fiducial volume
  Automated optical and electronics calibration nearly continuously
(MC-Data)/Data
Electron energy
+/- 1%
Repeated at
many locations
direct injection
LINAC data

## Slide 17: Super-Kamiokande Experience
Absolute energy scale to 0.7% accuracy
Need to know the systematic
uncertainties in the standard
candle physics to <1%
(R.Svoboda, et al)

## Slide 18: Super-Kamiokande Experience
At low energy Super-Kamiokande was able to achieve and maintain <1% systematic shift in the energy scale
  DT generator every few months
  Electron LINAC with a moveable beam pipe into the fiducial volume
  Automated optical and electronics calibration nearly continuously
Moveable
LINAC
Portable
DT Generator

## Slide 19: Time Variation in SK
In SK it was not enough just to do a calibration once in a single spot
  Moveable LINAC that could be placed at many different radii and depths, and a deflecting magnet to change electron direction
  Portable DT generator that could do a complete calibration at a single port in about a day.
Experienced changes in backgrounds due to circulation ”cells” that formed in the large tank due to miniscule temperature variations of few tenths of a degree. These patterns were affected by forced circulation configuration from pumps.
Need to make sure that 1996 neutrino energy scale and resolutuon are the same as 2016 energy scale and resolution. In all DUNE studies I am aware of this is automatically assumed.
Will not automatically be true…

## Slide 20: Time Variation in DUNE
We should not expect the DUNE cryostat to be a benign isothermal mass of liquid argon with no currents or variation in drift parameters over a decade
We should not expect that the energy scale measured in 2026 for neutrinos will be the same in 2036. Need to prove it to be credible
Need a “standard candle” that is invariant over decade time scale and can be deployed in many different locations
BTW – It would be interesting to look at a systematic energy scale shift between neutrino running and anti-neutrino running, as they occur years apart.

## Slide 21: Time Variation in DUNE
Will neutrinos measured
in 202x have the same
Energy scale systematic as
anti-neutrinos in 202x+7?
Need to prove that it is so.
Our competition will.

## Slide 22: Conclusions
Energy scale systematic shifts and energy resolution uncertainties affect all our physics measurements
Number of options for calibrations is very limited, but low energy sources represent one way to address problems in spatial and time variation across the detector
Experience with previous precision neutrino measurements calls for a relentless program of calibration checks by as many techniques as possible.

## Slide 23: Supernova Trigger: background effects
current trigger algorithm efficiency as a function of neutron background rate

## Slide 24: Cosmic Ray Rates

## Slide 25: Trigger Efficiency with Electron/g Sample
David Rivera, David Last & Josh Klein
(with default DAQ trigger
and continuous data taking)
(majority of RSDS data planned to be recorded with just one APA at a time recording ALL hits free-running
and rest of detector uses default DAQ trigger and continuous data taking w/ partitioned DAQ
-> can offline compare to the definition of efficiency for SN bursts and single solar neutrino events)
DUNE threshold in TDR