## Slide 1
J. Holzbauer on behalf of the Technical Integration Group
SRF/Cryo Integration Workshop
Thursday, May 14, 2020
PIP-II Integrated FMEA

## Slide 2: Existing Failure Mode Analysis Process
PIP-II must be made robust against a myriad of failure scenarios
Each L3 system must assess the impact of and recovery from:
  Potential system-internal failures
  External Conditions (e.g. power outages, other L3 system failures)
These two categories are traditionally captured in:
  Failure Mode and Effect Analysis (mostly internal failures)
  What-If Analysis (mostly external conditions)
FESHM 5032 describes a clear definition of these two documents as a requirement for successful Cryogenic System Reviews at FNAL
  FESHM FMEA is relatively prescriptive and component list driven, and traditionally done for (and focused on) piping/cryogenic systems
  Grading of the risks identified in a FESHM FMEA is also quite prescriptive
The FNAL Quality Assurance Manual calls out FMEAs as a standard tool for assessing and managing technical risk
  Many examples are available from industry and other authorities

## Slide 3: Look Through Examples in Teamcenter
FESHM What-If (LCLS-II CDS and Cryomodule What-If)
  ED0001804
FESHM FMEA (CMTF Kinney Valve and Inst List & FMEA)
  ED0003665
PIP-II FMEA (650 MHz Prototype RF Coupler FMEA)
  ED0011536

## Slide 4: FMEA Goals and Requirements for PIP-II
FESHM requires a specific set of assessments be done as part of approval for operation of cryogenic systems at FNAL
  It is unlikely (and arguably undesirable) that this process will change
Duplication of documentation effort is undesirable
  Any additional documentation burden should be clear and add value to the overall design and project
Assessment of potential failures and associated risks during production and operation is essential for PIP-II
The goal of an integrated FMEA is to ensure that all failure modes are documented, appropriately mitigated, and that their potential cross-system impacts are captured
This is especially true for systems as intimately connected as Cryoplant, CDS, and CMs

## Slide 5: Proposal for an Integrated PIP-II FMEA
Identify/refine clear guidance for a PIP-II FMEA
  Several examples of good FMEAs exist, but clearer guidance must be given to ensure all relevant failure modes and scenarios are captured
Document existing FMEAs and ensure they are updated
  Additional information must be captured for each failure including specific interface reference from the Master ICD across which the failure may propagate (and thus affected stakeholders)
  Some allowance must be made for designs that are not well advanced (FESHM FMEA requires almost complete design)
  Each L3 owns the FMEA(s) of their systems
Failures that cross system boundaries should be traceable from source to mitigation via auditing
  Propagation of failures across interfaces must be explicitly labeled
  If a failure is mitigated outside of your system, responsibility of external mitigations or propagation of information (MPS, RFPI, etc.) should be noted including where these requirements are managed

## Slide 6: Worked Example
A Cold Compressor Trip in the Cryoplant is a likely failure scenario during PIP-II operation
CP Cold Compressor Trip causes internal disruption
CDS 2K return pressure rises
SSR1 2K circuits pressure rises and cavities start to warm
SSR2 2k circuits...
Cryoplant Trip 'Failure'
Propagation to other system
Further Effects
Etc.
Pressure rise in 2K circuit trips RFPI
Interlocks Trip
RFPI permit is pulled, tripping MPS, LLRF, HPRF, etc.
Interlocks Propagate Shutdown
CP FMEA
CDS FMEA
CM FMEAs
SRF Interlock Plan/RFPI FRS/TRS
MPS/LLRF/HPRF FRS/TRS

## Slide 7: Additional Example
Beamline vacuum failure in a CM (small, medium, or catastrophic)
  Impacts to CDS via increased heat load, relief event
  Impacts to Vacuum systems via beamline (pumping stations, gate valves, etc.)
  Impacts on neighboring modules, potentially
Discussion question:
  Based on experience, does a What-If of a certain system generally capture all the relevant failure modes of systems around them?
  Can a What-If style analysis be done early in the design?

## Slide 8: External Failures List
Power outage
  Long term/short term
  Local, machine-wide
Fire in the local area
Installation damage caused by other installation/tunnel activities?

## Slide 9: Worked Example (External)
A PIP-II Cryoplant Building loses power (short term) is a possible failure scenario during PIP-II operation
Power Outage disrupts CP operation
CDS Circuits pressures change and flow rates drop
SSR1 2K circuits pressure rises and cavities start to warm
SSR2 2k circuits...
Cryoplant Trip 'Failure'
Propagation to other system
Further Effects
Etc.
Pressure rise in 2K circuit trips RFPI
Interlocks Trip
RFPI permit is pulled, tripping MPS, LLRF, HPRF, etc.
Interlocks Propagate Shutdown
CP What-If
CDS FMEA
CM FMEAs
SRF Interlock Plan/RFPI FRS/TRS
MPS/LLRF/HPRF FRS/TRS
Remains the same as previous example

## Slide 10: Discussion Questions
A PIP-II FMEA must be more clearly defined because there are significant scenarios that the existing PIP-II FMEAs don’t address. True?
The value of the What-If is clearly high and should not be lost. Should the basic structure of FESHM be kept, i.e., an FMEA that is more component focused and a What-If that is more scenario focused?
Do all realistic failure scenarios propagate across existing interfaces that are captured in the MICD? Will this labeling scheme work? (if yes, then the number of stakeholders to be notified and cross-checked is greatly reduced)