## Slide 1
Donato Passarelli
SRF/Cryo Integrated Workshop
May 14, 2020
SSR Scope and Status

## Slide 2
SCOPE

## Slide 3: Scope and Deliverables
WBS 121.02.03
SFRs – Single Spoke Resonator CryoModules
Management, design, procurement, fabrication, and testing of the Single Spoke Resonator cavities and cryomodules.
 | SSR1 | SSR2
# CMs | 1+2 | 1+7
Cavities per CM | 8 | 5
Solenoids per CM | 4 | 3
CM configuration c: cavities; s: solenoids | 4x (csc) | sccsccsc
CM length (m) | 5.2 | 6.5
Proto SSR1 cryomodule
Final scope will be delivery of qualified CMs ready for installation into PIP-II tunnel
10

## Slide 4: Scope and Deliverables
Item | Quantity | DOE | BARC (India) | CNRS/IN2P3 (France)
SSR1 proto CM (not installed in the LINAC) |  |  |  | 
Cryomodule | 1 | 1 |  | 
Jacketed Cavities | 8 | 10 | 2 | 
Couplers | 8 | 11 |  | 
Tuners | 8 | 10 | 2 | 
SC Solenoids | 4 | 5 |  | 
Cold BPMs | 4 | 5 |  | 
SSR1 CM 1-2 |  |  |  | 
Cryomodule | 2 | 2 |  | 
Jacketed Cavities | 16 | 9 sets of Nb | 18 | 
Couplers | 16 | 18 |  | 
Tuners | 16 |  | 16 | 
SC Solenoids | 8 |  | 10 | 
Cold BPMs | 8 | 10 |  | 
CM assembly and final qualification testing at Fermilab
SC5/6/7 L. Lari

## Slide 5: Scope and Deliverables
Item | Quantity | DOE | BARC (India) | CNRS/IN2P3 (France)
SSR2 ppCM (not installed in the LINAC) |  |  |  | 
Cryomodule | 1 | 1 |  | 
Jacketed Cavities | 5 | 3 | 2* | 3
Couplers | 5 | 4 | 3* | 4
Tuners | 5 | 1 | 2* | 4
SC Solenoids | 3 |  | 4* | 
Cold BPMs | 3 | 4 |  | 
SSR2 CM 1-7 |  |  |  | 
Cryomodule | 7 | 6 | 1 | 
Jacketed Cavities | 35 |  | 5 | 40
Couplers | 35 |  | 5 | 40
Tuners | 35 |  | 5 | 37
SC Solenoids | 21 |  | 23 | 
Cold BPMs | 21 | 23 |  | 
CM assembly and final qualification testing at Fermilab
*IIFC Addendum 1
SC5/6/7 L. Lari

## Slide 6: Partners
India
France
CNRS/IN2P3
BARC
DAE/BARC
Sub-Project Coordinators
Fermilab
Sub-Project Managers
CNRS/IN2P3
Sub-Project Coordinators

## Slide 7
REQUIREMENTS and SPECIFICATIONS

## Slide 8: EPDM for PIP-II SSR scope
Engineering Process Documentation Management (EPDM) | Teamcenter No.
Prototype SSR1 | ED0001256
Production SSR1 | ED0011856
Pre-production SSR2 | ED0001257
Production SSR2 | ED0011912
The EPDMs listed contain all the references for the Design, Procurement, Fabrication, Assembly and Testing for all components and subassemblies for the cryomodule.

## Slide 9: SSR1 Requirements and Specifications
 | Prototype CM | Production CM
FRS | ED0001316 | ED0011838
TRS | ED0009534 | ED0011907
ISD | ED0004129 | ED0011908
Internal ISD | N/A | ED0011405
P&ID | F10082628 | F10137214
EPDM | ED0001256 | ED0011856

## Slide 10: SSR1 Requirements and Specifications (cont’d)
 | Prototype CM | Production CM
Fabrication Specification | ED0001256 (CM/Tuner) ED0371029 (Cav) ED0001772 (Coupler) ED0004855 (Sol) | ED0011856 (CM/C/C/T) ED0011935 (Sol)
Acceptance Plan | N/A | N/A (CM) ED0012002 (Cav) ED0011961 (Coup/Tune/Sol)
Acceptance Criteria | N/A | N/A (CM) ED0012003 (Cav) ED0011962 (Coup/Tune/Sol)
Due to the Potential for Multiple Fabrication Specifications, the EPDM is Referenced

## Slide 11: SSR2 Requirements and Specifications
 | Prototype CM | Production CM
FRS | ED0001829 | ED0011909
TRS | ED0009651 (CM) ED0009784 (C/C/T) ED0011214 (Sol) | ED0011910 ED0009784 (C/C/T) ED0011214 (Sol)
ISD | ED0010943 | ED0011911
Internal ISD | ED0011023 | ED0011023
P&ID | F10117244 | F10137882
EPDM | ED0001257 | ED0011912

## Slide 12: SSR2 Requirements and Specifications (cont’d)
 | Prototype CM | Production CM
Fabrication Specification | ED0001257 (CM/C/C/T) ED0011935 (Sol) | ED0011912 (CM/C/C/T) ED0011935 (Sol)
Acceptance Plan | ED0011897 (In2P3) ED0011957 (DAE) | ED0011963 (In2P3) ED0011961 (DAE)
Acceptance Criteria | ED0011898 (In2P3) ED0011958 (DAE) | ED0011964 (In2P3) ED0011962 (DAE)

## Slide 13: Requirements
Main Cryomodule Parameters | Units | SSR1 | SSR2
Energy for section | MeV | 10 to 32 | 32 to 177
Cavities (solenoids) per cryomodule | # | 8 (4) | 5 (3)
Cryomodule flange-to-flange length | m | 5.3 | 6.5
2 K heat load | W | < 33 | < 71
5 K heat load | W | < 55 | < 48
50 K heat load | W | < 206 | < 185
Environmental magnetic field | mG | ≤ 15 | ≤ 15
Transverse cavity (solenoids) alignment error, RMS | mm | ≤ 1 (0.5) | ≤ 0.5 (0.5)
Angular cavity (solenoids) alignment error, RMS | mrad | ≤ 5 (0.5) | ≤ 5 (0.5)

## Slide 14: Requirements
Main Cavities Parameters | Units | SSR1 | SSR2
Frequency | MHz | 325 | 325
Cavity operating temperature | K | 2.0 | 2.0
βg (βopt) |  | 0.186 (0.222) | 0.398 (0.472)
Aperture diameter (Effective length) | mm | 30 (205) | 40 (438)
Operating energy gain per cavity | MV | 2.05 | 5
Unloaded cavity quality factor (Q0) at 2K |  | 8.2×109 | 8.2×109
MAWP at room temperature (at 2K) | bar | > 2.05 (4.1) | > 2.05 (4.1)
Sensitivity to LHe pressure fluctuations | Hz/mbar | < 25 | < 25
Coupler power | kW | 10 | 20

## Slide 15: Interfaces
PIP-II Master Interface Control Document: TC# ED0010433
121.02.03
SSR
121.03.03
High Power RF
121.03.06
Vacuum
121.03.04
Low Level RF
121.03.07
Controls
121.03.02
Accelerator Physics
121.02.05
Cryo Plant
121.06.05
Linac Complex
121.04.03
Test Infrastructure
121.02.06
Cryo Distribution Systems
121.03.09 Beam Instr.
121.03.05 Magnet PS

## Slide 16: Standardization of Interfaces
650 Configuration
SSR Configuration
770 mm
Guidance and requirements for the instrumentation are available in Teamcenter through several documents (TRS, FRS, ISD and the PIP-II cryomodule design handbook).
The heat exchanger will be common to SSR1, SSR2, LB650 and HB650 cryomodules.
The gate valve on the pumping line (Ref MDC 302004) and bayonets will be common to all cryomodules.
The cryogenic valves will be similar but the diameter may change, based on pressure drop calculations
The cryogenic size port will have similar layout for SSR1, SSR2, LB650 and HB650 cryomodules. Just the distance from the vacuum vessel will change between SSR and 650 cryomodules.

## Slide 17
TECHNICAL PROGRESS

## Slide 18: Proto SSR1 CM: assembly completed

## Slide 19: CM testing at PIP2IT
The testing of the proto SSR1 CM will validate:
Installation, alignment and external interfaces
Warm strongback layout
Scheme to monitor and maintain the alignment of key-elements during and after cooldown
Cryogenics and heat loads performance
Solenoids and current leads performance
RF performance of cavity, coupler and
tuner
Instrumentation layout
Procedures and travelers:
Transportation traveler Vector 464489
Installation traveler: Vector 464539
Testing procedure: In progress

## Slide 20: SSR2 cavities
Procurement of cavities was initiated
3 from FNAL; 3 from CNRS/IN2P3; 2 from BARC
Ring end view
Cross section

## Slide 21: SSR2 tuner
Chart: Delta Weight [kg]
| 1.889284278985019 | 1.4169635255279891 | 0.94464207874001005 | 0.47232066231226 | 0
S Contour_Th | 5849.7607 | 4337.4107 | 2520.0463 | 747.1511 | 0
S Max_H | 2837.435 | 1064.5323 | 0
S Top_Th | 2496.8213 | 730.9642 | 0
S Central_Th | 5507.8775 | 2258.3938 | 0
P3
P1
P2
P4
Topology optimization
Parametric optimization
FEM Optimization
SSR1 tuner design
SSR1 tuner tests
SSR2 tuner design
Procurement of tuner is ongoing

## Slide 22: SSR2 coupler
Design completed

## Slide 23: SSR2 string assembly and cryomodule
TC# F10127014
Design is ongoing

## Slide 24
Thank you for your attention!