## Slide 1: protoDUNE – II issues Use of Jack Screws to lower inverted APA in cryostat. Note: all illustrations are very conceptual
Space needed =7043.4-6769.3=274.1+clearance
Space gained = 615-366=249mm
Space still needed = 25.1+clearance.
~Cable tray
2 x ½ ton jack screws mAPA=632kg

## Slide 2: Step 1 – The yoke is initially mounted close to the foot tube
Yoke
Cross arms on link to be used for lowering
Foot tube

## Slide 3: Steps 2 and 3 (After APA is delivered)
Jack screws and lowering hardware are installed
Inverted APA is lowered ~125mm and short link is installed
Short link.
Connection of lifting beam to cross arms of link to be determined.
Lowering beam
APA link

## Slide 4: Steps 4 and 5
Jack screw is raised and jack screw link is installed
APA is lowered another ~125mm to final height. Long link is installed
Long Link
Jack screw link

## Slide 5: Step – Final configuration
Long Link
Jack screw link
Jack screw and lifting beam is removed