## Slide 1: Lessons learned from HERA - the 1st ep Collider
José Repond
Argonne National Laboratory
EIC User’s Meeting
Argonne National Laboratory
July 7 – 9, 2016

## Slide 2
Over the hill…

## Slide 3
A quick reminder: What was HERA?
The one and only ep Collider (so far)
Electron/positron beam of 27.5 GeV
Proton beam of 820 → 920 GeV
Center of mass energy √s = 300 → 318 GeV
Location
Deutsches Elektronen Synchrotron DESY,
Hamburg, Germany
Operation
Started in 1992 (exactly on time!), ended in 2007
Experiments
Collisions: H1 and ZEUS
Electrons/positrons and gas jet target (polarized): HERMES
Protons and wire target: HERA-B

## Slide 4
The Colliding Beam Experiments:
Multi-purpose 4π detector with
Charged particle tracking
Si - μVTX
Central drift chamber
Liquid Argon calorimeter
Rear Pb-scintillator plug
Muon chambers and more…

## Slide 5
The Colliding Beam Experiments:
Multi-purpose 4π detector with
Charged particle tracking
Si - μVTX
Central drift chamber
Uranium-Scintillator calorimeter
Muon chambers and more…
Note: both detectors are asymmetric around the interaction point

## Slide 6
Acronyms
HERA
Hadron-Elektron Ring Anlage
H1
First experiment at HERA
H2 → ZEUS
Zero Experience with Uranium - Scintillator

## Slide 7
Lessons learned from HERA…
Caveats
This is my personal view
I am/was more familiar with ZEUS, H1 was just as good
It’s been a long time – some details might not be accurate

## Slide 8
HERA was a complex/difficult collider
HERA contained 2 machines
An electron machine
A proton machine
→ Need to collide the 2 beams
Backgrounds
Electrons radiate synchrotron radiation
Radiation deteriorates the vacuum
Protons interact with gas → beam-gas events
Useful variable
For DIS events …
(losses down the forward beam pine give a negligible loss)
Without
With timing cuts
ZEUS
Phys Lett B 303(1993)183
Precise timing is important

## Slide 9
Slow Start-up of HERA
H1, ZEUS detectors
Designed for High-Q2 physics
The hope was to discover Lepto-quarks
DIS cross-section
High Q2 requires high luminosity
Photoproduction
Real photons: Q2 ~ 0
Study came as an afterthought, while waiting for the luminosity to improve
Design your detector to measure/do everything…

## Slide 10
Luminosity upgrade
HERA I
CY 1992 – 2000
Integrated luminosity 193 pb-1
Machine upgrade
CY 2000 – 2002
Decreasing proton beam size
Decrease electron beam size
(move quadrupoles closer and increase their strength)
HERA II
CY 2002 – 2007
Serious problems with synchrotron radiation/shields
Integrated luminosity 586 pb-1
Not all upgrades are worthwhile

## Slide 11
ZEUS Trigger System
Bunch crossings
Every 96 ns
The 3-level trigger system of ZEUS
- First level
Data stored in 5 microsecond pipeline,
clocked at 96 ns
Reduction from 100 kHz to 1 kHz
- Second level
Microprocessors analyze digitized data
Reduction from 1 kHz to 100 Hz
- Third level
Full event building
Analyzed by computer farm
Reduction from 100 Hz to 10 Hz
Invented by ZEUS and now being used at the LHC

## Slide 12
Expect the unexpected: Diffraction
Normal low-Q2 DIS event
Low-Q2 DIS event w/out p-remnant
Events without proton remnant
About 10% of all DIS events: totally unexpected!
Several methods to identify/measure
Rapidity gap, MX, leading proton detection
Precision measurements
Diffractive structure functions

## Slide 13
Expect the unexpected: Gluons at low-x
Pre-HERA knowledge of F2
Limited to x > 5 × 10-2
Low x behavior totally unknown
Precise measurements at HERA
Pinned down low-x behavior
Spectacular increase of gluon density at low-x
Perhaps the most important result from HERA

## Slide 14
Jet Physics: Infrared safe jet algorithms
Hadronic jets
At collider energies, hadrons tend to cluster in ‘jets’
Jets reflect physics of underlying hard (parton) scattering
Various algorithms to define jets
Pre-HERA
Jet-physics at the colliders of the day (Tevatron,SppS, LEP, PEP, PETRA…)
Use of so-called ‘Cone Algorithm’
Group all particles together within a certain cone in η-φ space
Major disadvantage
Algorithm not infrared safe, i.e. soft and collinear divergencies do not cancel
Problem for theoretical calculations
Introduction of unphysical Rsep parameter
Precise comparison with theory → impossible

## Slide 15
Jet Physics: Infrared safe jet algorithms
kt Algorithms
Infrared safe (divergencies cancel)
Distance measures
Systematic studies by H1 and ZEUS
Comparison with fixed order NLO calculations
Precision jet physics is possible
→

## Slide 16
Forward detectors are challenging
Initial design
3 disk-like chambers
Drift cells with fixed wire orientations
→ Problems with occupancy!
Straw Tube Tracker
Implemented in 2001
Straws running tangentially to beam pipe
→ solved occupancy problem
Possibly first fully functional forward tracker
in a colliding beam experiment

## Slide 17
H1 versus ZEUS
Optimized for hadronic measurement: 35%/√E
Optimized for electron measurement: 12%/√E
Physics reach?
Despite different detector philosophy, comparable physics reach

## Slide 18
Combined H1 and ZEUS Results
7 combined papers since 2009
- Multi-Leptons with High Transverse Momentum
- Events with an Isolated Lepton and Missing Transverse Momentum…
- Combined Measurement and QCD Analysis of the Inclusive e+p …
- Combined Inclusive Diffractive Cross Sections…
- Combination and QCD Analysis of Charm Production Cross Section…
- Combination of Differential D*+ Cross-Section Measurements in…
- Combination of Measurements of Inclusive Deep Inelastic Scattering…
Useful to have 2 detectors with different systematic uncertainties: 1 + 1 > 2

## Slide 19
Commensurate Theory Effort Needed
Cost
HERA accelerator ~ $1B
HERA experiments ~ $0.5B
1 theorist <$0.0005B/year
Precision measurements
Diffraction
Jet production
….
Theoretical calculations
Lower precision
Often limiting factor

## Slide 20
Conclusion