## Slide 1: Update of R&D Optical Cvities at KEK-ATF
Introduction
Status of the cavity R&D
Recent activities
Out Look
KEK, Hiroshima University
LAL (Orsay) in Collaboration withCELIA (Laser lab., Bordeaux) and LMA ( coatings Lab., Lyon)
Tohru Takahashi
Hiroshima University
for
September 6 2013
PosiPol 2013 ANL

## Slide 2: Compton at KEK ATF
Polarized e+ by laser Compton Scheme
Ee~1GeV for 10MeV gammas
controllability of polarization
Toward the positron sources
ー> increase intensity of g rays
Omori
Proof of principle
M.Fukuda et al., Phys. Rev. Letts. 91, 16480(2003)
T.Omori et al., Phys. Rev. Letts. 96, 114801(2006)

## Slide 3
29th Mar 2013
detector
γ
Laser cavity
ATF parameter
1.3GeV
1×1010 electron/bunch
Up to 10 bunch/train
2.16×106 turn/s
Setup at the KEK-ATF

## Slide 4
The Optical Cavity
IP
Plane Mirror
Concave Mirror
Plane Mirror
Concave Mirror
Main Parameters
Circumference:1.68m
Finesse:4040(Measured)
Power Enhansement:1230

## Slide 5: 3D 4 Mirror Cavity
2D 4 M cavity has astigmatism
sx sy at the focal point of the cavity
2 D cavity
3 D cavity
See next speaker

## Slide 6: Polariaztion in the 3D4M cavity
Resonates only for circular polarization
  geometric phase due to twisted pass
  cavity only resonates with circular polarization
  usable for pol. switching
circumference of the cavity
left handed
right handed
transmitted light

## Slide 7: 4 mirror cavities are at the ATF
KEK-Hiroshima
installed 2011
LAL-Orsay
installed summer 2010
relatively simple control system
employs new feed back scheme
sophisticated control
digital PDH feedback

## Slide 8: Laser spot size 13mm achieved
vertical position[μm]
g ray yield [A.U]
s=18mm
electrons
vertical deirection
se=10mm
sL=13mm
30mm w/ 2 M cavity

## Slide 9: Cavity feedback with 3D feature
New feedback scheme utilizing the polarization property of the cavity
cavity length must be kept L = nl with very high precision
(for enhancement of 2000 dL<< 80pm while L = 1.64m)
L
L
R
+
=

## Slide 10: Stored Laser Power in the cavity
Stored Power [w]
Right pol
Left pol
Sotred power
Laser Power: 2.6kW
w/ 38W fractuation
14th Sep 2012
must control
ΔL<<110pm
achieved
ΔL<<8pm

## Slide 11: gray Generation
ATF 2.16MHz
~2.6×108/sec
5bunches/train
2970±20 MeV
⇒ ~120gs / trainのガンマ線に相当
e-
laser
g
5.6ns
Eγ[MeV]

## Slide 12
Quantitative Understanding of the Cavity
Finesse
  ・Airy function
  ・Life time of the laser light in the cavity
Stored Power in the cavity
  ・From injection power
  ・From transmitted power
Profile at the interaction point
  ・Using Compton gamma (laser-wire)
  ・Estimate from a measured laser light profile

## Slide 13
Finesse: FWHM / FSR
=4040±420
Life time of the laser light
Airy Function
Finesse
2πcτ / L
=4040±110
PD

## Slide 14
Two Estimates are consistent
  Injection(1.3W) × Enhancement(1230) =1.6kW
  Transmitted(130mW) / Transmittance(0.008%) =1.6kW
Stored Power
(Measured)

## Slide 15
Profile of the laser light at the IP
x
27um
10um
y
Calculated 16um
Measured 13um
レーザー光
電子ビーム

## Slide 16
Issues
x
27um
10um
y
must revisit optical property in the cavity
Transmitted power
Reflected power
20s
・Possibly a thermal effect
・Profile at the IP
due to (unexpected) power loss on mirrors

## Slide 17: What next ?
For positron sources, we need;
  more than 100 times more power in the cavity
  a few tens of more
    power enhancement
    injection laser power
Mirrors with
  higher reflectivity
  low loss

## Slide 18: Future prospect
Try high reflectivity mirror
  w/ careful handling
  Trying 3000~5000 power enhancement this year -> more than 10,000 in next a few years
Low loss mirrors
  collaboration with NAO (gravitational wave guys)
  careful investigation of commercial mirrors
  develop mirrors (substrates) by ourselves?

## Slide 19: Summary
Current 3D4M cavity works well
  we have basic technologies in our hand
but
  optical properties yet to be understood
  mirrors should be studied for high power storage
Issues are clear
  step back once to basic study(PHYSICS) to go forward

## Slide 20: Digital Feecdback system
Digital
PID

## Slide 21: Automatic Restoration
cavity cont. signal
Stored Power

## Slide 22: Summary and Prospect
So far
  2.6kW stored w/ enhancement of 1230
  Highly stable ΔL～4pm
  vertical laser size at the IP 13μm
  120g/5bunches -> ~2.6×108/sec
  Digital Feedback
Quantitative understanding
  Finesse
  Powers
  Profile

## Slide 23: Summary and Prospect
Issues
  Laser profile at the IP
  possible thermal effect
Near term plan
  test Laser profile issue
  low loss mirrors
  Higher finesse

## Slide 24: Resonance Finding
cavity cont. signal
Stored Power