## Slide 1: Status of the CLIC study
CLIC status, general
Injector, positron production update
Drive Beam Injector Project
Conclusions and outlook

## Slide 2: Context for the CLIC studies
LHC and LHC luminosity upgrades (until ~2030)
  Higgs and BSM physics
ILC in Japan, a possibility for exploring the Higgs in detail, starting at 250 GeV
  Requires significant integrated luminosities, and increased energies in steps (at least to 500 GeV), also long program
BSM – does it show up at LHC at 13-14 TeV (2015 onwards) ?
  What are the best machines to access such physics directly post LHC …. we don’t know but we can prepare main options
  Two alternatives considered, higher energy hadrons (HE LHC or VHE LHC), or highest possible energy e+e- (CLIC).

## Slide 3
ENERGY FRONTIER PROJECTS AT CERN AFTER LHC – THE CONTEXT OF THE CLIC ACTIVITIES
Open Session during the CLIC workshop end January:
Common session with main other alternatives for energy frontier projects at CERN after LHC (LHC energy upgrades), including presentations of what we can expect from LHC and a potential Higgs-factory
Status and very first focus on potential common or co-ordinated activities in the coming years (2013-2017)
European strategy for high energy physics

## Slide 4: The LCC Organization and CLIC
Issues for CLIC:
Improve common work with ILC (optimize resources) – see below
Keep strong CLIC physics and detector activities as identifiable part of overall P&D box (we have common CLIC steering group and very direct weekly contacts)
Understand machine committee organization
Sources (common working group on positron generation)
Machine Detector Interfaces
Damping rings
Beam dynamics (covers along entire machine)
Beam delivery systems
Physics and detectors
How do we integrate POSIPOL activities ?, How to we organise ourselves in the common Sources working group ?

## Slide 5
Goal for next strategy update (2018):
Present a CLIC project that is a “credible” option for CERN beyond 2030:
Physics studies updated taking into account LHC-14 TeV (assume the physics case will be there for an energy frontier machine – i.e. not only the Higgs)
Physics no later than 2035
Initial costs at around LHC+50% for project construction
Upgradable in 2-3 stages over a 20-30y period, without major (max 3-4 years) operational breaks, and with upgrade costs contained to 3-5 B/10 years as “determined” by CERN budget when personnel and operation are accounted for
Promote ‘CLIC technology’ in other projects and field (XFEL, medical)
CLIC guidelines and overall goals

## Slide 6
Design and Implementation studies:
Baseline design and staging strategy
Solid cost basis and more optimized power/energy (aim for 20% energy reduction)
Proof of industry basis for key components/units, in particular those specific for CLIC
Comprehensive reliability/robustness/uptime analysis
Pursue increased use of X-band for other machines/applications (hard to set concrete goal)
CDR status: not optimized except at 3 TeV and not adjusted for Higgs discovery, not optimized cost, first power/energy estimates without time for reductions, limited industrial costing, very limited reliability studies
System-tests:
Complete system-tests foreseen for next phase, and comprehensive documentation of the results at CERN (CTF3) and elsewhere
Strategy for further system verification before construction (XFEL, connected to light-sources, further drive-beam verifications) or as part of initial machine strategy.
CDR status: CTF3 results initial phase (as of early 2012), ATF and FACET very little, no convincing strategy for further system verification
Demonstrator of drive beam FE and RF power unit based on industrial capacity – will open for larger facilities beyond 2018 if necessary
CDR status: Nothing done beyond CTF3
X-band developments:
Statistics for gradient and structure choice (energy reach) and other X-band elements
CDR status: Single elements demonstrated – limited by test-capacity
Technology developments:
Demonstration of critical elements and methods for the machine performance:
  DR, main linac, BDS with associated instrumentation and correction methods (combination of design, simulation, system-tests and technologies)
  Stability/alignment (locally and over distances)
  Module including all parts
CDR status: alignment/stability partly covered, BBA assumed, wakefield mon. perf. assumed, no complete module
Main activities and goal for 2018

## Slide 7: CLIC Test Facilities
High current, full
beam-loading operation
Operation of isochronous lines and rings
Bunch phase coding
Beam recombination and current multiplication by RF deflectors
12 GHz power generation by drive beam deceleration
High-gradient two-beam acceleration
4 A, 1.4us
120 MeV
30 A, 140 ns
120 MeV
30 A, 140 ns
60 MeV
Several other test-facilities are important:
ATF at KEK
FACET at SLAC
X-band test facilities at KEK and SLAC (more in progress)
CesrTA for electron cloud studies
…. and several more for specific technical developments
Do we need a positron production test facility ?

## Slide 8: CLIC Main Beam Injectors Layout
Primary 5 GeV e- Linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e+ Linac
Pre-injector
e- Linac
e- DR
gun
PDR
e+ DR
DL’s
BC1
DC gun
target
9 GeV
2.86 GeV
0.2 GeV
PDR
Spin rotatator
Two hybrid positron sources (only one needed for 3 TeV)
Common injector linac
All linac’s at 2 GHz , bunch spacing 1 GHz before the damping rings

## Slide 9: Positron source conventional ?
Primary beam
Linac for e-
2 GHz
AMD
Gun
5 GeV
Primary beam
Linac for e-
200 MeV
Hybrid target
AMD
Primary beam
Linac for e-
200 MeV
Hybrid target
RF-deflector
Bunch compressor
AMD: 200 mm long, 20 mm radius, 6T field
Target Parameters Crystal |  | 
Material | Tungsten | W
Thickness (radiation length) | 0.4 | 0
Thickness (length) | 1.40 | mm
Energy deposited | ~1 | kW
Target Parameters Amorphous |  | 
Material | Tungsten | W
Thickness (Radiation length) | 3 | 0
Thickness (length) | 10 | mm
PEDD | 30 | J/g
Distance to the crystal | 2 | m

## Slide 10: Hybrid target
Target Parameters Crystal |  | 
Material | Tungsten | W
Thickness (radiation length) | 0.4 | 0
Thickness (length) | 1.40 | mm
Energy deposited | ~1 | kW
Target Parameters Amorphous |  | 
Material | Tungsten | W
Thickness (Radiation length) | 3 | 0
Thickness (length) | 10 | mm
PEDD | 30 | J/g
Distance to the crystal | 2 | m

## Slide 11: Yield simulations capture and pre-injector linac
Accelerating mode
decelerating mode
Energy density at 200 MeV
O. Dadoun
Positron yield: after target: ~8 e+/e- at 200 MeV: 0.9 e+/e- into PDR: 0.39 e+/e-

## Slide 12: CLIC hybrid source-vs- ILC 300Hz scheme
Parameter | ILC 300 Hz scheme | CLIC hybrid
No. of bunches | 2640, 20 *132 | 312
Rep. rate | 300 Hz / 5 Hz; 63 / 200 ms | 50 Hz, 20 ms
Bunch spacing | 6.15 ns | 0.5 ns / 1 ns
Bunch charge (driver) | 2 x 1010 e- | 1.1 x 1010 e-
Drive beam energy | 6 GeV | 5 GeV
Charge per train Average charge | 264 x 1010 e- in 992 ns 26320 x 1010 total | 343 x 1010 e- in 156 ns 17150 x 1010 total
Beam radius | 4.0 mm | 2.5 mm
Capture frequency/ aperture | 1.3 GHz 45 mm | 1-2 GHz 20 mm
Yield at DR | 1.6; Ax+Ay < 0.09 mm | 0.39; e = 7 mm, 17 MeV, 5.4 mm
Average power target, thickness | 35 kW 14 mm | 11 kW 10 mm
PEDD | 23 J/g | 30 J/g

## Slide 13: CLIC hybrid source-vs- ILC 300Hz scheme
Parameters not to different, can we find a ‘global’ optimum Do we understand well the yield optimisation, what is the limiting factor, PEDD and capture efficiency ? For CLIC: increase aperture, magnetic field, beam size to optimise ?
Heat load on target less serious for CLIC but shock-wave sensitivity likely more important for CLIC  anyway ILC target should work as well for CLIC (slowly rotating or fixed)
What about the hybrid scheme, benefits for CLIC or ILC ?
CLIC can’t stretch the train on the target due to 50 Hz rep. rate

## Slide 14
Cost reduction for the main injectors
CDR design was focused on low risk, conventional, state of the art facility to guarantee excellent beam quality and not worry about cost or feasibility
It turned out that the injectors have a significant cost impact even on CLIC
 In the frame work of the new base-line for CLIC, in particular optimizing a low energy first stage we decided to focus as well on cost and efficiency
Main proposals:
PDR for electrons not needed
Use 2 GHz bunch spacing through out the complex, shorter rf pulses in linac’s and no need for delay loop
Optimise timing of the beams to gain efficiency (PC optimisation)
Investigate to use booster linac as positron driver (saves positron driver)
Provide cost model for optimization
350 MCHF savings potential identified !

## Slide 15
Alternative layout
Without positron driver linac and e- PDR, 2 GHz bunch spacing everywhere
Pre-injector
e- Linac
e-
e-
3300 ns
156ns
156ns
e+
Positron production pulse
Save two rings, positron driver linac, and tunnel length (saving potential 200 MCHF)
Injector Linac
Booster Linac
2 GHz
e- DR
gun
PDR
e+ DR
BC1
DC gun
target
6 GeV
2.86 GeV
0.2 GeV

## Slide 16
Undulator based positron source for CLIC
Wanming Liu
Together with the Argonne gang we decided to study in more detail this option which has a path to positron polarization and might have cost benefits as well

## Slide 17
Layout with undulator based positron source
IP
target
BDS
Main Linac
Main Linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e- Linac
e- DR
gun
e+ DR
BC1
DC gun
target
6 GeV
2.86 GeV
0.2 GeV
Spin rotator
to main linacs
Undulator
positron source
Undulator 350 m
2.86 GeV linac ? 300m
BDS
Photons 300 m
~1000 m
to transfer line, DR
Main beam bypass line
from injectors
PDR
Minimum scenario for upgrade to positron polarization and fully compatible with conventional layout
from transfer line

## Slide 18
Undulator based positron source
Consequences:
400 -1000 m more tunnel length (both sides ?)
Separate injector linac for positrons 2.86 GeV
transfer line from the tunnel to the injector complex
Spin rotator before and after damping ring (needed anyway for any polarized scheme)
Gap in damping ring due the delayed beams
Main beam bypass around positron production
Coupling of the two beams

## Slide 19
How about a dedicated scheme ?
IP
BDS
Main Linac
Main Linac
Booster Linac
6 GeV
e- DR
DC gun
2.86 GeV
BDS
PDR
e+ DR
BC1
Central Injectors and DR in deep tunnel

## Slide 20
How about a dedicated scheme ?
IP
BDS
Main Linac
Main Linac
Booster Linac
6 GeV
e- DR
DC gun
2.86 GeV
BDS
PDR
e+ DR
DR and injector at the end of each side

## Slide 21
Undulator based positron source
To be studied
Impact in cost, length and performance
Emittance preservation in undulator and bypass
Beam loading in PDR due to a likely gap of ~ 43 ms (500 GeV)
General timing consideration
Upgrade scenarios, energy scans
Undulator parameters, can we get 60% polarization
Wei Gai, Wanming Liu and CLIC team

## Slide 22
CLIC DB front end,
Post CDR Project
For time being only major component development:
GUN, SHB, high bandwidth 500 MHz source, 1 GHZ MBK, modulator and fully loaded accelerating structure
Gun
SHB 1-2-3
PB
Buncher
Acc. Structures
IOTs ?, 500 MHz
Modulator-klystrons, 1 GHz, 15 MW
~ 140 keV
~ 12 MeV
Diagnostics
~ 3 MeV

## Slide 23
CLIC DB injector specifications
Parameter | Nominal value | Unit
Beam Energy | 50 | MeV
Pulse Length | 140.3 / 243.7 | ms / ns
Beam current | 4.2 | A
Bunch charge | 8.4 | nC
Number of bunches | 70128 | 
Total charge per pulse | 590 | mC
Bunch spacing | 1.992 | ns
Emittance at 50 MeV | 100 | mm mrad
Repetition rate | 100 | Hz
Energy spread at 50 MeV | 1 | % FWHM
Bunch length at 50 MeV | 3 | mm rms
Charge variation shot to shot | 0.1 | %
Charge flatness on flat top | 0.1 | %
Allowed satellite charge | < 7 | %
Allowed switching time | 5 | ns

## Slide 24: Sub Harmonic Bunchers (SHBs)
Phase coding
180 phase switch
Acceleration n0
Deflection n0 / 2
Sub-harmonic bunching
n0 / 2
odd buckets
even
buckets
  RF deflector n0 / 2
Gap creation and combination
Gun
SHB 1-2-3
PB
Buncher
Acc. Structures
IOTs, 500 MHz
Modulator-klystrons, 1 GHz, 15 MW
~ 140 keV
~ 12 MeV
Diagnostics
Main challenge of SHBs:
Fast 180° phase flipping capability, simulation indicate < 18 ns switching time needed

## Slide 25
Tentative klystron
parameters
PARAMETER | VALUE | UNITS
RF Frequency Bandwidth at -1dB RF Power: Peak Power Average Power RF Pulse width (at -3dB) HV pulse width (at full width half height) Repetition Rate High Voltage applied to the cathode Tolerable peak reverse voltage Efficiency at peak power RF gain at peak power Perveance Stability of RF output signal at nominal working point RF phase ripple [*] RF amplitude ripple Pulse failures (arcs etc.) during 14 hour continuous test period Matching load, fundamental and 2nd harmonic Average radiation at 0.1m distance from klystron Output waveguide type, | 999.516 ≥ 1 ≥ 20 150 150 165 50 tbd, ≤ 180 tbd 67 ≤ 70 tbd, > 48 tbd ±1 (max) ±1 (max) < 1-2 tbd < 1 WR975 pressurised | MHz MHz MW kW μs μs Hz kV kV % dB μA/V1.5 RF deg % VSWR μSv/h 2-3 bar
Status: Call for tender

## Slide 26
Sub-harmonic bunching system
Status:
RF design existing, mechanical design advanced,
Next: launch prototype (in aluminum ?)
Power source:
500 MHz, 34-82 kW, wide band (60 MHz) sources needed for fast phase switching. Started to discuss with industry.
Hamed Shaker, see IPAC paper

## Slide 27
DB injector review and optimization
Total losses reduced from 30% to 11%
Shahin Sanaye Hajari, see as well IPAC paper

## Slide 28
Typical MAGIC snapshot: particle positions in r-z
Typical MAGIC snapshot: kinetic energy of particles along z
Contour plots of field components at t=35ns
Jacques Gardelle, CEA-CESTA

## Slide 29
Gun design concept

## Slide 30: Conclusion
Optimizing CLIC for lower energies, cost and power consumption
Seems there is still room for optimization of the conventional positron source for CLIC
Saving potential of 350 MCHF identified
Start to look into undulator based positron production
Challenging drive beam injector project
CLIC collaboration workshop, February 2014
POSIPOL 2013, ANL, September 4th, 2013

## Slide 31: End

## Slide 32
DB injector review and optimization
Shahin Sanaye Hajari, see as well IPAC paper
Final phase space at 50 MeV after re-optimization of the injector with realistic rf parameters, 4% satellites, good longitudinal phase space

## Slide 33
Gun simulations
Emittance vs voltage

## Slide 34
Cost per linac
Cost estimate per linac (1.5 TeV parameters)
LINAC | Energy Gain (MeV) | Bunch charge (10^9) | rf pulse length (ns) | Power per structure (MW) | Loaded gradient (MV/m) | Configuration (structure/2 klystrons) | No of rf modules | pulse compressor gain | No of structures | Length (m) | Energy gain per module (MeV) | Cost
e- pre-injector | 200 | 4.3 | 1300-1700 | 54 | 18 | 4 | 2 | 2.3-2.5 | 8.0 | 30 | 108 | 5830
e+ pre-injector | 200 | 11 | 1300-1700 | 56 | 15 | 4 | 3 | 2.3-2.5 | 9.0 | 40 | 90 | 8745
injector linac | 2660 | 6 | 3600-4000 | 44 | 15 | 2 | 60 | 1 | 119.0 | 300 | 45 | 127950
positron drive linac | 5000 | 11 | 1300-1700 | 56 | 15 | 4 | 56 | 2.3-2.5 | 223.0 | 400 | 90 | 163240
booster linac | 6140 | 4 | 1700-2000 | 53 | 16 | 4 | 64 | 2-2.3 | 256.0 | 473 | 96 | 186560
Bunch charge and gradient determine power/structure, optimized for a 2x 50 MW klystron + pulse compressor configuration to feed a maximum of structures
Cost of structure 13%
Cost of high power system 75%, ~ factor 2 of this could hopefully be gained (150M)
Efficiency (%) | Structure efficiency for 312 bunches (%)
2.68 | 
4.58 | 
6.64 | 31
6.13 | 32
4.79 | 27

## Slide 35
Gun Test Facility
Gun test area:
former GTF available, Bldg. 162-R-004/008, needs some refurbishment

## Slide 36
Gun simulations
Using EGUN
e ~ 12 mm mrad

## Slide 37: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex

## Slide 38: Electron linac requirements
For non-Gaussian beams the minimum required acceptance:
To avoid an e- PDR:
  In horizontal Rmin < 1 mm-rad
  In vertical Rymin < 1.2 mm-rad
Required emittances from the electron injection linac in order to remove electron PDR
  εxrms= 25 μm-rad
  εyrms= 50 μm-rad
DA of the main DR
F. Antoniou

## Slide 39: Linac Parameters
Primary 5 GeV e- Linac
Injector Linac
Booster Linac
2 GHz
Pre-injector
e+ Linac
Pre-injector
e- Linac
e- DR
gun
PDR
e+ DR
DL’s
BC1
DC gun
target
9 GeV
2.86 GeV
0.2 GeV
PDR
Spin rotatator

## Slide 40: CLIC Layout at 500 GeV
Drive Beam Generation Complex
Main Beam Generation Complex

## Slide 41: Injector linac rf system
Structure Parameter | Value
Frequency | 1998 MHz
Structure length (30 cells) | 1.5 m
Filling time | 389 ns
Cell length and iris thickness | 50 mm, 8 mm
Shunt impedance | 54.3 – 43.3 MW/m
Aperture a | 20 – 14 mm
Cell size b | 64.3 – 62.9
Group velocity vg/c | 2.54 -0.7 %
Phase advance per cell | 2p/3
Acc 1
Acc 2
Acc 3
Acc 4
Quad
BPM
Mod
Pulse compressor
Kly 1
Kly 2
50 MW, 8 ms
250 MW, 1.5 ms

## Slide 42: Links to other applications

## Slide 43: CLIC project time-line (input to European Strategy)
The CLIC concept have been developed over many years. During the last 4-5 years there has been a concerted effort to prepare a Conceptual Design Report, to be ready when LHC data-taking was expected to be well underway (part of the European Strategy as formulated in 2006)
Focus has been on addressing all key critical issues for the concept, as well developing a coherent implementation model, and associated detector and physics studies to illustrate the physics performance