## Slide 1: Capture and Booster Linac Issues for 300Hz Scheme
K. Yokoya
2013.9.5 POSIPOL2013
@ANL

## Slide 2: R&D Issues of the Conventional Source
“conventional” but still needs some more R&D
High current, high rep rate driver linac
Moving target
Flux concentrator
Booster linac
Overall simulation

## Slide 3: Loading Compensation in Booster Linac
Accurate loading compensation needed because of the limited DR energy aperture
Much easier if continuous 132 bunches instead of triplet (DR e-cloud issue: Is triplet absolutely needed?)
Junji gave a linac design using phase shifter at S-band
a triplet: 132 bunches 992ns
a train: 20 triplet
= 2640 bunches 63ms
3.3ms
2×1010/bunch

## Slide 4
precise control of
the phase shifters needed
200MW, 3ms
300Hz Power
Supply
Low Level RF
Phase Shifter
and Amp.
3dB High Power
RF Combiner
50W High Power
Terminator
80MW Klystron
3m long constant gradient travelling wave structure
3x1010 positron/bunch
300Hz triplet beam
Less than +/- 0.7%
Loading Compensation Scheme
Urakawa
+/- 0.7% corresponds to +/- 35MeV at end of 5GeV booster
Big fraction of the DR energy aperture +/- 37.5MeV
Factor ~2 energy compression at linac end helps but not enough

## Slide 5
Yield as a function of DR energy aperture
35MeV
Ushakov

## Slide 6: Bunch Length
DR aperture
  DE < +-37.5MeV
  Dz < +-34mm
  Ax+Ay < 70mm.rad
Is S-band linac acceptable?
Clearly No according to this figure
Need bunch compression
But not at this energy because the (relative) energy spread is too large
Some more acceleration with L-band is needed
But L-band is too expensive (NC linac!!)
Time (ns)
Pz(MeV)
Longitudinal Phase Space
S-band 90deg
An example of t-E phase space at end of first L-band section by T.Takahashi

## Slide 7: A Possible Solution
Use L-band up to ~1GeV (relative energy spread around ~5%?)
Bunch compressor with L-band plus chicane by factor ~2
The S-band to up 5GeV
Followed by energy compression by factor ~4
  Larger factor than in ILC standard (undulator) design
  This will make the effect of miss-loading-compensation +/- 35MeV to +/- 9MeV
Optimization of the red numbers needed