## Slide 1
Sandeep Miryala
ASIC Group, Fermilab
Rad-Hard Methodology and CAD Tools

## Slide 2: Outline
Introduction
  Radiation Effects on Semi-Conductor Devices
TID effects
  Device models
  Library characterization
SEE mitigation using TMR
  TMR insertion by RTL engineers
  TMR Macro
  SEE tolerant Digital Logic Synthesis Flow (Genus & Innovus)
Summary

## Slide 3: Radiation Effects on Semi-Conductor Devices
Radiation Effects
Cumulative Effects
Single Event Effects
Ionization (TID)
Displacement (Fluence)
Permanent
Single Event Burnout
Single Event Gate Rupture
Single Event Latchup
Transient
Single Event Transient
Static
Single Event Upset

## Slide 4: Total Ionizing Dose (TID)

## Slide 5: Total Ionizing Dose (TID)
Ionizing radiation builds up interface trap states
TID-induced charge in the oxide decreases with the thickness
Thick oxide used for device isolation introduces leakage
Parameters:
  Temperature
  Bias
  Annealing
  Dose Rate

## Slide 6: Device Irradiation (65nm)
Narrow Transistors
  NMOS less affected by TID
Short Transistors
  PMOS and NMOS devices are degraded
Narrow and Short devices
  PMOS completely off for 1 Grad
F.Faccio et al., TWEPP 2015, TID effects in 65nm transistors: summary of long irradiation study at the CERN X-rays facility

## Slide 7: Irradiation Effects Modeling
Spectre model corners were developed based on irradiation tests
  200Mrad and 500Mrad and the dependence on W and L is included
  Threshold voltage increase is included for PMOS and NMOS
  Leakage current variations are included for NMOS
Assumptions
  Room temperature irradiations and worst case biasing (VDS = VGS = 1.2)
  Does not include annealing
HVT and LVT models were extrapolated from NVT device measurements
Mohsine Menouni et.al, Main results of radiation of CMOS 65nm technology and the impact on the design of RD53A, a large scale pixel chip prototype for HL-LHC

## Slide 8: TID effects on Circuits
Analog Designs
  Avoid excessively narrow and short transistors
  NMOS: L >= 120nm, any W, PMOS: L >= 120nm, W >= 300nm
Digital Designs (Semi-Custom Design Flow)
  Small size transistors in standard cells  Speed degradation
  Generate timing Libraries at 200Mrad and 500Mrad
    Liberate tool (Cadence)
    Used by several cad tools
Timing, Power, Signal Integrity
Synthesis
Floorplanning
Place & Route
Timing, Power and Signoffs
.libs (P, V, T)

## Slide 9: Library Contents (.lib)
Timing
  Combinational
    Delay & Transition Time
  Sequential
    Delay & Transition Time
    Hold and Setup
    Recovery and Removal
Power
  Leakage
  Internal Power
Noise
  Signal Integrity analysis
Data is arranged in Look Up Table (LUT) format
  Sample 4 x 4 LUT
Index | cl1 | cl2 | cl3 | cl4
Trin1 | D11 | D12 | D13 | D14
Trin2 | D21 | D22 | D23 | D24
Trin3 | D31 | D32 | D33 | D34
Trin4 | D41 | D42 | D43 | D44

## Slide 10: Liberate Tool Flow
Extracting arcs & indexes
1
2
3

## Slide 11: Define_Cell and Define_Arc
Generate arcs from existing .lib

## Slide 12: Library Comparison (LC Plot)
Cells (INV and DFD)
200MRad radiation models
Timing includes (Delay, Slew, setup, hold)
X axis: pre-rad Library
Y axis: 200Mrad Library

## Slide 13: Liberate Applications for HEP
Re-characterize cells
  New PVT corners
  New Models (Radiation & Cold models)
  Modify input slew and output load templates
Characterize new cells
  Multi-bit latches
  Dynamic Flip-Flops, SEU DFF
Characterize new standard cell libraries

## Slide 14: Single Event Effects

## Slide 15: Radiation Effects on Semiconductor Devices
Image taken from Introduction to SEU, Altera, white paper, Sep 2013

## Slide 16: SEUs on SRAM
Initial state : A = VDD, B= GND
Current spike/charge at drain of M1
Transient current changes the state of node A
  VDD -> GND
The second inverter (M3-M4) switches node B
  GND -> VDD
A
B
VDD
GND

## Slide 17: Single Event Effects (SEE) Classification
Soft Errors
  Transient
    Single Event Transient (SET)
  Static
    Single Event Upset (SEU)
Soft Error mitigation
  Technology level
    Bulk CMOS Vs SOI
  Cell level
    Dice latch
  System level redundancy : Triple Modular Redundancy (TMR)
Mitigate Soft Errors using TMR
SEE tolerance is needed in:
Global configuration registers
Pixel configuration registers
Data path registers

## Slide 18: Triple Modular Redundancy (TMR)
Q1 | Q2 | Q3 | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Data is replicated on multiple nodes
Additional area and power consumption
DFF
DFF
DFF
Clk
Clk
Clk
Din
Q1
Q2
Q3
Voter
reset
reset
Q = (Q1&Q2)| (Q2&Q3)| (Q3&Q1)
reset
Din
DFF
Q
set
set
set
reset
set

## Slide 19: TMR insertion by RTL designers
module TMR (Din, Q, clk);
Input Din;
output Q;
reg Q1, Q2, Q3;
always @(posedge clk)
begin
Q <= Din;
Q1 <= Din;
Q2 <= Din;
Q3 <= Din;
end
assign Q = (Q1 & Q2) | (Q2 & Q3) | (Q3 & Q1)
endmodule
Synthesis
Disadvantages:
1. Redundant logic is removed by synthesis tools
2. Additional don’t touch commands
3. Complex for chips with huge # of registers
DFF
DFF
DFF
Clk
Clk
Clk
Din
Q1
Q2
Voter
Q
Q3
Q
Din
DFF
Clk

## Slide 20: TMR Macro
Clk
DFF
DFF
DFF
Voter
Din
Q
Q1
Q2
Q3
Realize TMR as a macro
  Single row implementation
  like a standard cell
After synthesis, replace the registers with TMR Macro
Disadvantages:
Non-optimal placement
Routing issues

## Slide 21: SEE Tolerant Semi-Custom Flow
Specification
RTL (Verilog)
Synthesis (Genus/RC)
Placement
Clock Tree Distribution
Routing
Physical Verification
TMR Insertion
Memory Elements Spatial Separation
Clock Delay/Skew Insertion
Physical Design (Encounter/Innovus)
TMR Insertion methodology with timing /placement aware in semi-custom design flow

## Slide 22: Logic Synthesis Flow
Load Libs and RTL
Apply SDC
Set Avoid on undesirable Flipflops
Synthesize Design
Write Final Netlist
1
2
3
4
FF1
FF2
FF3
FF4
Combinational Data Path

## Slide 23: TMR Synthesis
Load Libs and RTL
Apply SDC
Set Avoid on undesirable Flipflops
Synthesize Design
read TMR Netlist
Use Change Link to convert desired flops to TMR
Remove TMR flop design
Uniquify
Write Final Netlist
Read_netlist TMR.v
foreach I [filter –regexp libcell DFQD* [find /designs/$DESIGN –instance instances_seq/*tmr*]] {
Change_link –inst $i –design_name /designs/tmr_flop
}
rm /designs/LTMR
Uniquify $DESIGN
Set_attr preserve size_ok [find / -subdesign TMR*]
Synth –to_map incr
1
2
3
4
5
6

## Slide 24: TMR Insertion Automation
FF1 C
FF2 A
FF3 C
FF4 A
DATA PATH
FF1 B
FF1A
voter
FF2 B
FF2 C
voter
FF3 B
FF3 A
voter
FF4 B
FF4 C
voter
TMR_Hinst
Additional steps in synthesis flow does TMR insertion

## Slide 25
TMR_DFQD.v
module TMR_DFQD (CP, D, Q);
input CP, D;
output Q;
wire CP, D1, D2, D3, Q, Q1, Q2, Q3, n_0;
DFQD1 DFFQ2_reg(.CP (CP), .D (D), .Q (Q2));
DFQD1 DFFQ1_reg(.CP (CP), .D (D), .Q (Q1));
DFQD1 DFFQ3_reg(.CP (CP), .D (D), .Q (Q3));
MAOI222D0 p4324D(.A (Q1), .B (Q2), .C (Q3), .ZN (n_0));
CKND0 Fp4461A(.I (n_0), .ZN (Q));
endmodule
read_netlist TMR_DFQD.v
foreach I [filter –regexp libcell DFQD* [find /designs/$DESIGN –instance instances_seq/*reg*]] {
Change_link –inst $i –design_name /designs/TMR_DFQD
}
Each flipflop type must have its corresponding TMR netlist
4

## Slide 26
read_netlist TMR_DFQD.v
foreach i [filter –regexp libcell DFQD* [find /designs/$DESIGN/* –instance instances_seq/*reg*]] {
change_link –inst $i –design_name /designs/TMR_DFQD
}
Search for all the sequential instances with instance name consisting of *reg*
Filter all the *reg* instances mapped to DFQD cell in the technology library
Change_link, built-in command in RC compilers which
Replaces the cell with LTMR cell
rm /designs/TMR_DFQD
Uniquify $DESIGN
Set_attr preserve size_ok [find / -subdesign TMR*]
Synth –to_map incr
4
5
Delete independent designs
Incremental Synthesis

## Slide 27: TMR Insertion Scenarios
Triplicating only the registers having *tmr* in RTL
Triplicating all the registers in the RTL
Triplicating in one of the hierarchical module in RTL
module TOPModule ();
…
reg in_tmr;
…
endmodule
read_netlist TMR_DFQD.v
foreach I [filter –regexp libcell DFQD* [find /designs/$DESIGN/* –instance instances_seq/*tmr*]] {
Change_link –inst $i –design_name /designs/TMR_DFQD
}
module TOPModule ();
…
reg in;
…
endmodule
read_netlist TMR_DFQD.v
foreach I [filter –regexp libcell DFQD* [find /designs/$DESIGN/* –instance instances_seq/*reg*]] {
Change_link –inst $i –design_name /designs/TMR_DFQD
}
module submodule();
reg test;
….
endmodule
module TOPModule ();
…
submodule hierInst ();
endmodule
read_netlist TMR_DFQD.v
foreach I [filter –regexp libcell DFQD* [find /designs/$DESIGN/instances_hier/hierInst –instance instances_seq/*reg*]] {
Change_link –inst $i –design_name /designs/TMR_DFQD
}

## Slide 28: Physical Design
Requirement
  Flops within the same TMR module must be at least X um apart
  Voter logic can be placed anywhere without any spacing restrictions
FF1 C
FF2 A
FF3 C
FF4 A
Data Path
FF1 B
FF1A
voter
FF2 B
FF2 C
voter
FF3 B
FF3 A
voter
FF4 B
FF4 C
voter
>=X um
>=X um
>=X um
>=X um
>=X um
>=X um

## Slide 29: Encounter Implementation
Innovus 16.X has native space group constraints
  Create space group constraint
  Enable space group constraint during placement
  Place design
Default placement
Separated by 1 row (1.8 um)

## Slide 30: INNOVUS 16.2
Takes horizontal and vertical spacing during place & route
create_inst_space_group tmrSpaceGrp${n} -inst [ dbget [dbget$thPtr.allInsts.cell.isSequential 1 -p2].name ] –spacing_x $reg_spacing –spacing_y $reg_spacing
9 rows = 16.2uM
15.3 um
Triangular placement

## Slide 31: SET Mitigation
DFFQ1
DFFQ2
DFFQ3
Voter
delay1
delay2
delay3
Clk
Din
Simplest solution, Different delay values
Din
DFF
DFF
Clk
Data
SET Latching
D
D
Q
Q

## Slide 32: SET Mitigation : Clock Delay Insertion
set CkDel1 0.50 set CkDel2 1 # Clock Insertion Delays on the TMR flops for SET Mitigation set_ccopt_property insertion_delay -delay_corner {av_typ_dc} $CkDel1 -pin DFFQ2/CP set_ccopt_property insertion_delay -delay_corner {av_typ_dc} $CkDel2 -pin DFFQ3/CP
insertion delay of 0.5ns
insertion delay of 1ns
1st
2nd
3rd
DFFQ1
DFFQ2
DFFQ3
Voter
Din
Clk

## Slide 33: Summary
TID Effects
  Device modeling
  Library Characterization using Liberate
Single Event Effects
  TMR insertion during synthesis
  Specific distance between memory elements during physical design
  SET mitigation with clock delay insertion
  Timing/Placement aware TMR insertion methodology

## Slide 34: Acknowledgements
RD53 Collaboration
ASIC group, Fermilab
Cadence Support
!!! THANK YOU FOR YOUR ATTENTION !!!

## Slide 35: DRAD Test Chip
Objective
  To study the radiation
  effects on digital standard cells
7 Track (7T)
  High Vt (HVT)
9 Track (9T)
  Nominal Vt, High Vt
  Nominal Vt with increased width
12 Track (12T) (Modified)
  Nominal Vt, Low Vt, High Vt
  Nominal Vt with L=130n
18 Track (18T) (Custom)
  Enclosed layout transistors, for LPGBT grp.
9T
12T
18T
7T
FOUNDRY

## Slide 36: DRAD Test Structures
Standard Cells
  INV, NAND, NOR, XOR, Clock buffers, DFF and latches
Modes of Operation
  Delayed Mode
  Ring Oscillation Mode

## Slide 37: DRAD Measurements
Simulation results goes in the same direction as irradiation tests
  Model overestimates the TID damage level
  Models were done for worst case of biasing
Chart: Ring Oscillator frequencies 9T_NVT
| INVD1 | INVD4 | ND2D1 | ND4D1 | NOR2D1 | NOR4D1 | XOR2D1 | LH_DEL
Experimental Pre-rad | 60252500 | 72530000 | 47206100 | 29691100 | 44510600 | 30761200 | 27670400 | 23612000
Simulation Pre-rad | 63961111.6441 | 71282950.5439 | 49805509.4855 | 31212934.6401 | 48153320.1714 | 32953272.2599 | 27062647.3223 | 24524891.5387
Experimental 200MRads | 52168300 | 62984400 | 41888700 | 27152500 | 38280500 | 27372900 | 24052500 | 19938300
Simulation 200MRads | 38389042.2318 | 43404661.6607 | 29429942.023 | 17789257.7788 | 28310967.6689 | 19155877.1189 | 15501088.1764 | 14085102.1874
Experimental 500MRads | 25926800 | 34845200 | 23990100 | 16463500 | 20395800 | 14826300 | 11840400 | 8920400
Simulation 500MRads | 15964494.9632 | 18338192.9545 | 12884937.5081 | 8175277.9595 | 11208249.2715 | 7861326.2057 | 4381161.0077 | 4141935.858

## Slide 38: Library Comparison
Luis Miguel Jara Cases et.al, Characterization of Radiation Effects in 65nm Digital Circuits with DRAD Digital Radiation Test Chip, Twepp, 2016

## Slide 39
### Spacing distance
set LEN 15
### TMR Module Name Prefix
selectInstByCellName TMR*
### Foreach TMR Module Create Spacing Group & Assign the Corresponding Flops To The Spacing Group
foreach thPtr [dbGet selected] {
create_inst_space_group tmrSpaceGrp${n} -inst [ dbget [dbget $thPtr.allInsts.cell.name DFQD* -p2].name ] -spacing_x $LEN -spacing_y $LEN }
### Enable Spacing Constraint During Placement
setPlaceMode –place_detail_check_inst_space_group true
### Place Design
place_opt_design
built-in command in Innovus

## Slide 40: Back Up: TMR with Correction
DFF
DFF
DFF
Clk
Clk
Clk
Din
Q1
Q2
Q3
Voter
Voter = Q1&Q2 + Q2.Q3 + Q3.Q1
resetMux
Din
DFF
Q
setMux
reset
set
SEU
Error
E
reset, set
Error = Q1Q2Q3+ Q1Q2Q3
E
Q
resetMux, setMux

## Slide 41: Back Up: TMR with Correction
Din
DFF
DFF
DFF
Voter
Load
Q1
Q2
Q3
Q
CLK
CLK
CLK
DFF
Din
Load
Q
TMR Cell