## Slide 1: HEP IP development and sharing
F.Brewer, M. Miller
Supported by UCSB Academic Senate,DOE, CERN Exploratory Funding

## Slide 2: UCSB HEP IP
Pulse-gate standard-cell library
  Very high performance, variance tolerant, timing BB
Rad-Hard* Clocks, Small Footprint Hardened Clocks
  polyphase clock
Rad-Hard (TD and SEU) SERDES
Parallel PRBS sources/checker
Pads
  HSTL/SSTL 2.5+GHz single ended
  Differential edge (7+Gb/s)
  Trinary pulse (>4Gb/s)
Vast majority of IP is specific to 8rf (130nm CMOS), also pad and some cell designs in TSMC 65nm.

## Slide 3: Sharing IP Experience
Majority of designs are high speed – require tuning for correct operation:
  Pulse gates are standard cells so can use P&R tools with very tight interconnect constraints for medium scale IP.
  Pads are very technology specific, but likely needed for any high speed design (>300MHz IO/pin).
Link IP is tough in practice, needs tuning for environment.
  Cable Mass and attenuation/distortion
    Pre-emphasis essential
  Fiber is potentially much easier if willing to go slower than cots
    Vcel and APD TID is likely serious problem.
Rad-Hard EDA Tools
  Hierarchical Mitigation Analysis
  TID compensation flow
  Cell optimization

## Slide 4: Interoperability Models
Given a Technology Choice— Hard or Soft IP Re-use
Design documentation and assumptions
  Nobody pays for decent documentation of university IP
  Verilog-A or equivalent drop-in model: verified co-simulation in realistic test environment
  Pin state timing, Impedance, load, power noise model, level assumptions, defaults
Need simulation (or verification) based use validation
  Atrenta SpyGlass: Started as Verilog “Lint” tool, but added cell interface and timing, analog sense and impeadance/load etc. Currently owned by Synopsys, so available to universities – potential for inexpensive or free access
Need to specify and share Experiment Environment Model!
  Physical/Voltage/Radiation Suite
  Mitigation strategy and allowable failure modes and rates

## Slide 5: Discussion Spares

## Slide 6: Rad-Hardness Issues
Radiation effect modeling/testing is expensive
Need baseline test strategy and target environment
Need requirement level of hardness
  No point in huge expense if can be dithered out of measurements, but if IP fails permanently…
Design Centering Tools?

## Slide 7: HEP IC?
Whenever possible, use COTS parts! But:
  Total Dose Hardness
    Geosync Satelite/Reactor Electronics may see similar total dose but small market segment, very high prices and often limited distribution (ITAR and other restrictions)
  SEU/MEU Event Hardness
    Highly variable fault model, most COTS parts assume Elder or LEO Dose rates
  Triggered Latchup/Catastrophic Failure
    COTS parts often operated close to stress limits to make specs at lowest cost
Adopt standards when possible
  (eg) JES204b signaling supported by many parts
  Exploit inexpensive surround/communication/filter parts and cables
Still need custom ICs
  High resolution ADC w. time-scale pulse filtering
  pS scale Time of arrival, data marking
  Avoid BJT/Varactor/Diode radiation pitfalls (ADC is CMOS but voltage/bias source?)

## Slide 8: Digital Parts of HEP IC
Memory – likely biggest design issue
  COTS Memory IP Radiation issues
    TD problems with soft fuses/redundant selectors
    SEU hits multiple cells at once (strike lambda is 1-2x cell pitch)
  Memories usually escape foundry rules
    RAD-Hard mitigation must be weighed against area/performance/power overhead
    Need realistic expectation of error rates
Logic (Soft IP)
  Total Dose Degradation added to variance model (Relax timing, stiff clock)
  Hierarchical error mitigation strategy (High Dose Rates vs. Error Persistence)
  Strategy for error sensitivity analysis/Fault simulation
Triggering/Timing Sensitive (Hard IP)
  Modular Construction
  Variance Mitigation

## Slide 9: More Digital Parts
Triggering/Timing Sensitive (Hard IP)
  Modular Construction
  Variance Mitigation
  Clock Hardness
    PLL losing sync for 10uS
  Clock Distribution hardness
Interface (Pads)
  Unavoidable high voltage regions
    Latchup Quenching/Dissipation
  Redundant Driver Segments
    Converts SEU to level noise
  ESD protection TD tolerance?
    Low impedance analog
  RC clamp stability vs. Heavy Ion?