## Slide 1: Improvements in performance of the Muon Campus beamline
Diktys Stratakis
Fermi National Accelerator Laboratory
Mu2e II Workshop
December 08, 2017

## Slide 2: Outline
The Fermilab Muon g-2 Experiment
The Fermilab Muon Campus
  Description of its main components
Expected performance of the Muon Campus
  End-to-end simulation model
  Muon, pion and proton rates
Possibilities for improvements
  Describe a novel idea that could increase the # of stored muons
Future work and summary

## Slide 3: A hint of new physics?
Standard model: gtheory= 2.00 233 183 630 (99)
Last measured : gmeas = 2.00 233 184 178 (126)
What other physics must be added to make gtheory=gmeas?
Current discrepancy between theory/experiment
Theory
Experiment
Blum et al., arXiv:1311.2198v1
Goal of the new g-2 experiment (fourfold improvement: 140 ppb)

## Slide 4: Principle for measuring g-2
Precession frequency:
Inject polarized μ+ into a
storage ring (SR)
Detectors: Detect the decay e+.
Exploit the property that direction
of e+ is strongly correlated with the direction of μ+ spin
Electrostatic quadrupoles: For vertical focusing
Uniform field: B=1.45 T
Zero: by using “magic” 3.1
Gev/c μ+

## Slide 5: Muon Campus overview
8.89 GeV/c p beam impacts the target
3.1 GeV/c secondaries (π+, μ+, p) travel along M2 & M3
μ+ are extracted from the ring and transferred into the storage ring via M4, M5
After a few turns all π+ convert to μ+
μ+ enter the g-2 storage ring
Protons separate and are removed
A precision of 140 ppb will require the delivery of 1.1x1014 muons at the end of M5

## Slide 6: Estimating the rates of secondaries
Significant effort has been placed, over the last two years, so that to estimate accurately the pion, muon and proton rates along the Muon Campus
Goal: Have at least two codes for each beamline section
Fortunately, good agreement between individual codes has been found
G4beamline
MARS
TARGET
G4beamline
BMAD
COSY
BEAMLINES
STORAGE RING
G4beamline
BMAD
COSY
gm2ringsim

## Slide 7: Target station
Pulsed magnet
Collimator
Target
Li-lens
Parameter | Value
Protons on target (POT) per pulse | 1012
Pulse width | 120 ns
Number of pulses | 16
Cycle length | 1.4 s
Incoming beam momentum | 8.89 GeV/c
Selection momentum | 3.1 GeV/c
π+ before
selection
π+ after
selection

## Slide 8: Performance within M2 & M3 lines
1.37x10-4 POT (p)
DR entrance
2.62x10-6 POT (μ+)
1.87x10-5 POT (π+)

## Slide 9: Performance in the Delivery Ring (DR)
Extraction point

## Slide 10: Separation of protons in the DR
Entrance to DR
Turn 1
Turn 3
Turn 4
210 ns

## Slide 11: Performance within M4 & M5 lines
SR entrance
Beam at SR Entrance
Simulation predicts ~7x105 muons per fill make it to the SR

## Slide 12: New Phys. Rev paper
Simulated rates have been published!

## Slide 13: The g-2 storage ring
Beam physics is very complex and can lead to losses
  Beam is injected through a narrow aperture (inflector)
  Beta function mismatch
  Dispersion mismatch
  Momentum mismatch

## Slide 14: Momentum acceptance
Storage ring accepts particles only within

## Slide 15: Delivered beam at the end of M5
At the end of M5, near 85-90% of the muon beam is outside the desired momentum acceptance
Unfortunately, there is no good way to control this
Particles | Value
Total number of muons | 7.8x10-7 POT
Muons in | 6.8x10-7 POT
Muons in | 2.1x10-7 POT
Muons in | 0.8x10-7 POT
Particles | Value
Total number of muons | 7.8x10-7 POT
 | 6.8x10-7 POT
 | 2.1x10-7 POT
 | 0.8x10-7 POT

## Slide 16: Solution: Cooling
Place a wedge material in a dispersive area in such a way that the high-energy particles traverse more material that the low energy ones.
The wedge creates a correlation between the amounts of energy loss within the wedge material with the energy of the individual particles when placed in a region of dispersion
As a result the net energy spread is reduced

## Slide 17: Cooling requirements
There are competing processes involved in ionization cooling
  Cooling from ionization of the material
  Heating from Coulomb scattering
We require a material with:
  Low atomic number Z to reduce scattering
We require a location with:
  High dispersion
  Low beta function...

## Slide 18: Wedge geometry is important
Optimized for different materials: polyethylene, beryllium, diamond, vanadium, lithium hydride, nickel,…

## Slide 19: Location in the Muon Campus
Maximum allowed length = 150 mm

## Slide 20: Effect in momentum

## Slide 21: Stored muons
Preliminary simulations inside the Muon g-2 storage ring have been performed

## Slide 22: Summary of main findings
Suitable location
  Last bend of the M5 which is 70 m upstream the SR
Material of choice
  Many attractive materials. Taking into account cost, availability and performance polyethylene is very promising
Performance
  Near ~30% gain on stored muons by installing two 150 mm long wedges
Polarization
  Polarization remains 96% as desired by g-2

## Slide 23: LDRD proposal status
September 2017: Submitted LDRD preproposal
October 2017: Encouraged for submission of a full proposal
December 2017: Submitted the proposal…
The team:
  Diktys Stratakis (PI) & Mike Syphers (co-PI)
  Jim Morgan (Project manager)
  Jesse Batko (Mechanical Engineering)
  Dirk Hurd (Designer/Drafter)
  Dave Peterson (Electrical Engineering)
  Dan Vrbos (Lead Installation Tech.)
  Jim Budlong (Cable installation)
  Carol Johnstone + Grad. Student/ Postdoc (Beam optics)

## Slide 24: Conclusions
Developed a end-to-end simulation model for the Muon Campus – first results published in Phys. Rev. AB
Muon campus can deliver ~700,000 μ+ per bunch at the entrance of the SR. 3% are stored eventually.
A LDRD proposal with the goal to design, install and commission an innovative wedge absorber system before injection into the Storage Ring has been submitted
It will provide improvements in the number of stored muons that are required to minimize the statistical uncertainty in the Muon g-2 measurement.
Devices are relatively inexpensive and straightforward to implement and thus the benefits to the Experiment potentially can be high for a fairly modest investment.

## Slide 25: Acknowledgment
Joe Bradley from Univ. Edinburgh (Helen Edwards 2017 Intern)

## Slide 26: Parameter sensitivity (polyethylene)

## Slide 27: Beam polarization
Turn 1
Entrance to SR
Turn 4
Entrance to DR
<P>=96%

## Slide 28: Design
Wedge vacuum assembly, with the vacuum pipe and wedge at left and insertion actuator at right.