## Slide 1
Peter Müller
Physics Division, Argonne National Laboratory
Weak Interaction Studies with
Laser Trapped 6He
… and what MCPs have to do with it
P. Mueller, A. Leredde, T.P. O’Connor, K. Bailey
Physics Division, Argonne National Laboratory
A. Garcia, M. Sternberg, D. Zumwalt, R. Hong, Y. Bagdasarova, H.E. Svanson, Z. Alexander, T. Cope, Y. Kim, G. Harper, F. Wauters
CENPA, University of Washington
X. Flechard, E. Liennard
LPC Caen
O. Naviliat-Cuncic NSCL, Michigan State University
$ PM DOE Early Career Research Grant, DOE CENPA, LPC $

## Slide 2: Weak Interaction Studies
da/a = 1% from 6He decay
Johnson, Pleasonton, Carlson, PhysRev 1963
da/a = 0.1%
Left-handed
Right-handed
F. Wauters et al., arXiv:1306.2608
Standard Model
Only V-A terms
aSM = -1/3 for GT
aSM = +1 for Fermi
Beyond Standard Model
Exotic couplings have not been excluded beyond the 5-10% level
a = +1/3 for pure tensor GT
GT transition sensitive to CT & CT’
ß-Decay Rate
J.D. Jackson, S.B. Treiman, H.W. Wyld, Nucl. Phys. 4 (1957) 206

## Slide 3: Beta Decay and LHC
Effective field theory approach
effective nucleon couplings CX vs. effective quark couplings e X
correlate via lattice calculations
Beta-Decay Weak Interaction Studies in the Era of the LHC,
Solvay Institutes Workshop, Brussels, Sept. 3-5 2014
Future Projections
Future experiments
need to aim for 10-3 for b
and 10-4 for a
Bhattacharya et al. PRD 85, 054512 (2012)

## Slide 4: Weak Interaction Studies: b-n Angular Correlations
6He
6Li
t1/2=0.808 sec
100%
b
0+
1+
Qb=3.510 MeV
21Na
Atom Trap
Ion Trap

## Slide 5: Experimental setup
10-5
x 80-100
Capture velocity:
900 m/s → 70%
Capture efficiency
1.10-7
+LN2 cooling
18 MeV
15 μA
2H(7Li, 3He) 6He
2.1010 pps

## Slide 6: Helium MOT Setup @ CENPA

## Slide 7: Beta-Decay Study with Laser Trapped 6He
Recoil time-of-flight spectrum
(MC simulation)
~5x109 6He/s production yield
trapping rate ~1x103 6He/s
~0.1% statistics in ~8 weeks beam time
Atom trap properties
Highly selective capture
No RF fields or space charge
Low temperature sample (<mK)
Tight spatial confinement (< 100mm)
250
300
350
400
450
a
= -1/3
Counts
Time of Flight, ns
a
= +1/3
b-Detector
Trapped 6He
6Li recoil ion detector

## Slide 8: MCP - Recoil Ion Detector
Xavier Flechard, Etienne Liennard
MCPs (micro channel plates)
Delay line anodes
On test flange with calibration mask
RoentDek DLD80 with custom
digital readout, FPGA processing
(LPC FASTER DAQ system)

## Slide 9: Recoil Ion Detector
Position calibration with mask, Na+ beam
DAQ system for beta and recoil detectors works
MCP efficiency 52 % (70%)
MCP uniformity 95.5 – 99.8%
Timing resolution ~100 ps
Position resolution ~100 mm
Position reconstruction ~ 1 mm
Need to do
In situ calibration with 6He BG
Timing calibration with 4He Photo-ions (337 nm pulsed N2 laser)

## Slide 10: 4He trap diagnostics with MCP
He* + X -> He + X+ + e-
He* + He* -> He + He+ + e-
t (ms)
ms
dtx (ns)
dty (ns)

## Slide 11: MCP Image of Trapped 6He
dtx (ns)
dty (ns)
8 cm MCP diameter

## Slide 12: Results: First coincidences
  150 6He/s in 2nd MOT
  Up to 0.5 coincidences/s (trapped 6He)
  ~ 0.15 coincidences/s background (untrapped 6He)

## Slide 13: Systematic effect budget

## Slide 14: What we could do with a larger MCP
Need to improve systematics toward a 0.1 % (or below) measurement
Recoil ion detection with 15 - 20 cm diameter MCP
Collect 100 % solid angle, even at lower electric field
-> eliminate acceptance uncertainties
-> reduce electric field systematics
Shake-off electron detection with ~ 6 cm diameter MCP
Coincidence with low-energy shake-off electrons instead of beta
  -> reduce systematic effects from tracking beta scattering
  -> increase coincidence detection efficiency
Questions:
Combine large area MCP with delay line readout
Gain uniformity, timing and position resolution for recoil ions and electrons
Energy and impact angle dependence
In-situ position calibration
…

## Slide 15
P. Mueller, A. Leredde, T.P. O’Connor, K. Bailey
Physics Division, Argonne National Laboratory
A. Garcia, M. Sternberg, D. Zumwalt, R. Hong, Y. Bagdasarova, H.E. Svanson, Z. Alexander, T. Cope, Y. Kim, G. Harper, F. Wauters
CENPA, University of Washington
X. Flechard, E. Liennard
LPC Caen
O. Naviliat-Cuncic NSCL, Michigan State University
$ PM DOE Early Career Research Grant, DOE CENPA, LPC $
Thank you!

## Slide 16: 6He Production @ CENPA, U Washington
6He decay curve
6He half-life
ft-value
Compare with ab-initio calculations of |MGT| to obtain gA in nuclear medium
-> less than 2% quenching
A. Knecht et al., PRL 108, 122502 (2012)
A. Knecht et al., PRC 86, 035506 (2012)
Li target
A. Knecht et al., NIM A 660, 43 (2011)
~1×1010 atoms of 6He/s
via 7Li(d,3He)6He
15 mA d beam
18 MeV

## Slide 17: Experimental setup: Transfer/Detection
  Push beam MOT 1 → MOT 2 : 30%
  2nd MOT : Science chamber
      Beta-ion coincidence
      Penning ions
      Photo-ions
Zeeman Slower
MOT 1
MOT 2
Transverse cooling
Push beam
Slowing beam

## Slide 18: Example of systematic studies
  Ion detection
    X/Y position stability
    Width
  Trap lifetime > 2s (T1/2(6He)=807 ms)
  With pusled Nitrogen laser
    Z position stability or
    Electric field
80 mm
UV photons
4He

## Slide 19: Expanding Cloud of ~1 mK 4He Atoms