## Slide 1
Fast Timing Detector R&D
Use time difference between protons in pp->pXp events to measure z-vertex compared with primary tracking vertex
Purpose: Pileup background rejection/signal confirmation
Andrew Brandt, University of Texas at Arlington
+Jim Pinfold (Alberta),M Rijssenbeek
(Stony Brook)+FP420 +Giessen+others
Ex: Two protons from one interaction and two jets from another
Intro to fast timing
The key issues for detector design
The key issues for MCP-PMT (newish lifetime results)
Switching from Hamburg Pipe to Roman pot
Upgrading from low lum to high lum running

## Slide 2: Timing System Design Goals
2
Requirement | Low Lum | High Lum
High efficiency (90%) | X | X
Large Acceptance (~1) | X | X
Robust operation in radiation environment | X | X
L1 Trigger | Essential | Useful
Resolution | 30 ps or better | 10 ps or better
Reconfigurable/ Upgradeable | X | X
High rate capability | N/A | ~5 MHZ/pixel
Detector lifetime | N/A | > 100 fb-1

## Slide 3
Initial design: 4x8 array of 6x6 mm2 ~10 cm long quartz (fused silica) bars, not coincidentally well-matched to 2-inch micro-channel plate photmultipler (Photonis Planacon)
QUARTIC Concept (an oldie but a goodie)
Idea of Mike Albrow for FP420 (joint ATLAS/ CMS effort) 2005 based on “Nagoya detector “
Proton is deflected into one of the rows and measured by up to eight consecutive bars with a MCP-PMT
More rows limit rate/pixel
and multi-proton effects
proton
photons
MCP-PMT
1 2 3 4
1.4.1.1
Quartz bars at Cherenkov angle read out by MCP-PMT
Isochronous—by mounting detector at Cherenkov angle, light emitted at different z reaches the PMT in coincidence
If t= 40 ps/bar need 16 measurements/row for 10 ps
If t= 28 ps/bar need 8 measurements/row for 10 ps

## Slide 4
Components of an LHC Fast Timing System
We have developed all the necessary components of the readout electronics chain to preserve the detector/PMT resolution and validated them in pulser, laser, and beam tests
4

## Slide 5
Detector composed of radiator (default: fused silica bars) and
photosensor (default: MCP-PMT). Optimization of radiator/sensor
is strongly coupled and depends on running conditions and physics
goals .
Detector optimization issues:
Layout of quartz bars; this should
provide as much light as possible in a short a time window
maximize acceptance (avoid cracks)
have pixelation for multi-proton timing
MCP-PMT issues:
a) timing
b) rate
c) lifetime
d) cross talk
Detector R&D : UTA, Alberta, Giessen
Optimization done through
simulation, laser tests, and
test beam.
5

## Slide 6
An R&D Success Story
Led by UTA/Brandt raised ~400k$ in Generic R&D funds from Texas ARP (2006) , DOE ADR (2007 w/ Burle/Photonis), NSF SBIR (2011 w/ Arradiance Inc.) , DOE ADR (2011 w/Stony Brook), and in-kind from Universities, +~100k$ from U.S. ATLAS
From 2006 to 2012 averaged nearly one TB/year. Improved the resolution: - by a factor 5 from 100 ps/bar to 19 ps/bar (for DET/AMP/MCP-PMT/CFD) or by a factor 4 (24 ps/bar) if you include the HPTDC
The improvement was due to a combination of many factors:
- starting with a lack of knowledge of the subject
- improved amplifier and CFD (based on Louvain design refined by
Alberta + Stony Brook) . Note: a low noise, well-shielded amplifier is
a crucial, rarely discussed aspect of fast timing
- interface of quartz bars to PMT, improvements in MCP-PMT: pore size
25 µm to 10 µm, optimized gain/HV
6

## Slide 7
MCP-PMT is Heart of Timing System
Only one multi-anode reasonably-sized tube when we started: Burle/Photonis Planacon (now also Hamamatsu SL101/4 Planacon)
Time resolution aka TTS=transit time spread
(single pe response) ~35ps [~20 ps for 10 pe’s]
Multi anode: 8x8 has pixel size of ~6.5 mm x 6.5 mm
(defined initial detector concept), or 32x32 (1/4 pixels)
Pore Size: 10 m or 25 m
Tube Size: 2 inch square (53 mm active area)
In addition to timing performance, need to have capability of simultaneous measurements of multiple pixels, and be ready for next event, which could be 25 ns later, and also sufficient rate capability and lifetime, acceptable cross talk
(8x8)
Independent control of Cathode, MCP, and anode voltages
(32x32)

## Slide 8: MCP-PMT: TTS and Cross Talk
Cross talk could correlate adjacent channels within a row and reduce expected N improvement
Cross talk can give a false signal in channel in adjacent row which distorts/biases time measurement if there is a second proton in that row
Anode 2
Photons
Anode 1
Electrical
Crosstalk
(charge
sharing)
Pe Rebound
Optical Crosstalk
TTS=transit time spread
Photoelectron Recoil
t=38 ps
(σ of main peak)
Recoil
Rebound
Will get back to these points anon

## Slide 9
Rate Lifetime Issues
Historically MCP-PMT’s have not been extremely robust, and were typically capable of operating only for a few hundred mC/cm2 before their performance (QE) degrades, presumably due to positive ions damaging the photocathode.
If operated at high gain without sensible pixelation, the current demands would be too large for normal operations and the accumulated charge would render the tubes inoperable in a few weeks (rule of thumb at LHC for every 10 fb-1 or so 1 C/cm2 is accumulated). Considered by some as “an unsolvable problem”
We said “Challenge accepted!”
Helped form a collaboration between UTA, Arradiance Inc. , and Photonis in 2009 to address PMT lifetime (2011 SBIR funds important for Arradiance/Photonis ALD development including refining process leading to Lehman Super tube)

## Slide 10
Photocathode
Dual MCP
Anode
Photoelectron
DV ~ 400V
DV ~ 400V
DV <2500V
photon
+
+
MCP-PMT
+
2) Ion Barrier keeps positive ions from reaching photocathode
(Nagoya/Hamamatsu) also NEW! Photonis active ion supressor
3) Use more robust “Solar Blind” photocathode
4) Also considered 3rd MCP (Zstack) and improved vacuum
Increase anode voltage to reduce crosstalk (UTA)
Gain <105
Run at low gain to reduce integrated charge (UTA)
Brandt’s Ideal MCP-PMT
e-
1) Suppressed positive ion creation (Arradiance)
Increase cathode voltage to improve collection efficiency (UTA)
Improved lifetime (3 main options)
Reduce anode gap to reduce cross talk
10 m pore EDR MCP for max rate
ALD by Arradiance
+

## Slide 11
LeCroy Wavemaster
6 GHz Oscilloscope
Laser Box
Hamamatsu
PLP-10 Laser Power Supply
laser
lenses
filter
MCP-PMT
beam splitter
mirror
Established in 2009 at UTA with DOE Advanced Detector Research,+Texas ARP funds, primarily to evaluate MCP-PMT’s for use in fast timing.
Relies heavily on undergraduate manpower
The PTL serves as a permanent configurable test bed to study a myriad of subtle effects associated with picosecond timing
Early setup
1)Evaluate MCP-PMT and electronics with laser tests 2) Evaluate detector/full chain with test beam
beam mode
fiber mode

## Slide 12: MCP-PMT Rate and Current
Anode Current = proton Rate  Number of photo-electrons generated by each proton  Gain  charge
4 MHz proton rate with 10 pe’s at 106 gain gives 6.4 µA in a 0.4 cm2 pixel or about 16 µA/ cm2, several times what is possible!
Conventional wisdom: need high gain for fast timing
(but it was based on single pe experience). From UTA
laser tests timing is ~ independent of gain as long as
For 10 pe’s reduces current requirement by x10 to 20

## Slide 13
Extended MCP-PMT Lifetime!
UTA accelerated tests of 1st Generation 25 uArradiance ALD modified tube shows initial 15% gain loss but no QE loss over 2-3 C/cm2
In house Photonis tests showed same beaviour
(Needed laser for other tests at this point).
Linear corrects for saturation (gain reduction due to
pores not fully recharged before next event).
Saturation would be reduced/eliminated by using a
10 m pore tube (smaller pore size, means more pores)
and/or EDR (extended dynamic range), a special low
resistance MCP glass that allows higher current
Note Nagoya/Hamamatsu
have achieved 2 C/cm2 lifetime with orthogonal ion barrier approach
No QE loss
at 3 C/cm2
Notes: lehman

## Slide 14
Improved Lifetime with ALD
Photonis Planacon with Arradiance (Gen 1) ALD-coated 10 m pores
Lehman et al. (Panda conditions) No loss in QE with Q>6 C/cm2 >10x improvement over non-ALD tube For LHC 1C~10 fb-1
Hamamatsu ion barrier SL10

## Slide 15: Timing vs. Rate
Chart: Laser Rate (Hz)
| 1000 | 10000 | 100000 | 500000 | 1000000 | 2000000 | 5000000 | 5000000
5E4 Gain | 18.5 | 18.079 | 18.009 | 18.202 | 18.503 | 19.502 | 20.217 | 20.217
1E5 Gain | 16.558 | 16.273 | 16.95 | 17.044 | 17.402 | 18.512 | 19.865
1575V 12att | 1
1575V 9att | 19.865
1575V 6att | 1
Time resolution ~constant 17 to 18 ps out to about 1 MHz, where saturation starts and timing begins to degrade; 10% to 20% worse at 5 MHz
a 10 µm pore (EDR) tube would have 3 to 5 times the current capability and should maintain timing beyond 5 MHz
Arradiance Gen 2, 25 µm pore Planacon with EDR MCP (high current capability).
Expected to have 2-3 times longer life than Gen 1, would in principal be > 100 fb-1 tube, but needed for rate tests + test beam, so not life tested yet (no funding for dedicated lifetime setup
Timing resolution (t) measured using CFD as read out by scope and fitting distributions
12 pe’s @ low gain: 5x104 and 1x105
5MHz
(~2 µA/cm2)

## Slide 16: Timing vs. Rate for mini-planacon

## Slide 17
Photonis Parallel Development Effort (patent pending)
Could be used instead of, or as a complement to, ALD coating of MCP’s
-Features an electrostatic ion suppression
grid (basically an energized ion barrier)
Grid between MCP and photocathode
to reduce/prevent + ions from reaching
and damaging photocathode.
Complete suppression requires grid bias
to be energetically higher than the highest bias source of + ions (MCP-out)
Time delay (ion TOF aka afterpulsing) increases as the ions are decelerated
and eventually suppressed from reaching the photocathode
NOTE 1) Could still get some level of afterpulsing from ions on surface of MCP or from energetic neutrals 2) barrier reduces collection efficiency (effective QE) by about 40%
Lifetime Solutions (NEW!)

## Slide 18
Grid off
Grid 20%
Grid 60%
Grid 40%
Afterpulsing as a f(GridVoltage)
Large suppression ~x20 in “heavy metals” as grid is activated;
generic positive ion suppression factor (#AP grid on/grid off) is about 4x
Tests
Done
In
Secret
At
UTA
PTF
Preliminary

## Slide 19
Active Ion Barrier Improves TTS
Secondary electron peak is focused a couple ns later, results in improved TTS by 10-20% (we obtained 34 ps for 25 um tube)
Scattered electrons are organized and delayed (separated from main peak)
Tail of TTS distribution is suppressed

## Slide 20
MCP-PMT Lifetime Summary
Over past several years the difficult problem of PMT lifetime has been attacked on several fronts leading to significant improvements in the prospects of using MCP-PMTs in a high rate environment
Operational
a) Reduce pixel size near beam (x3)
b) Operate tube at lower gain x10-20
2) Technological
a) ALD suppresses creation of +ions x10-100
b) Electrostatic x4- x20
3) Further suppression possible with more ALD tuning O(2-3)
*The net effect of these gains is O(1000) improvement over initial calculations
that led some to abandon the technology.
HOWEVER, too early to declare victory! Development effort is
not complete! More R&D funds required to finish optimization
and make “long-life” a standard product option

## Slide 21: Cross Talk and other MCP-Issues
Have studied many features of MCP’s @PTF
(in close contact with Jeff Defazio, primary Photonis MCP-PMT engineer )
Cross talk: Using a series of fibers with different path lengths to simulate proton arrival time, found that ~10% of pulse is collected in adjacent pixel due to charge sharing
-improves resolution for pixels in same row and correlates pixels since light is in time
-degrades resolution and biases time for pixels in adjacent row (on either side) for later arriving proton
Two protons in same pixel mixes time in complicated manner
After pulsing and correlation to lifetime
Forming a data-based simulation of MCP response to augment GEANT capabilities
Raising cathode voltage to increase collection efficiency and sharpens timing
(up to 20% resolution improvement)
Pedro Duarte, Masters Thesis on early test beam studies 2007
Ryan Hall UTA, Honors Thesis on cross talk 2010
Paul Pryor UG Thesis on Lifetime 2011
James Bourbeau, Honors Thesis on Phase 0 2013
-Currently have team of 5 undergraduates (10/hr/week/person)

## Slide 22: T958 DAQ (FNAL 1/2012)
2 3 4 5 6 7 Avg
Just your garden variety 20 channel, 20 GHz/ch, 40 Gs/s/ch (point every 25ps) 500k$ LeCroy 9Zi scope! Thanks for the loaner LeCroy
Time difference between 10-12 ps reference detector (FNAL SiPM in Nagoya mode courtesy of Albrow +Ronzhin) and 6 –bar Quartic average gives online FWHM=47 ps (=20 ps), removing SiPM resolution gives Qavg=14-15 ps
“mini-Nagoya” SiPM

## Slide 23
SiPM- Quartic 6-Bar Average
Extract QUARTIC resolution (6 bar) 14 to 15 ps including Q-HPTDC
(Note: edge channels had different gain, not useful for this run)
t =19.5 ps
26.2 ps
QUARTIC and SiPM signals amplified, sent to CFD, then to scope, calculate
t(SiPM-Qi) and average over 6 bars. Repeat for HPTDC readout. Difference between the measurements is dominated by 16 to 18 ps resolution of SiPM HPTDC
CFD read out by HPTDC
CFD read out by SCOPE
t 26.2 ps

## Slide 24: Validate Thin Bar
With 10 um tube and 2x6x140mm quartz bar we get same results as 5x6x140 mm bar, and both are improved from 1/2012 single bar timing. Resolution: Bar+PMT+CFD=22ps - SiPM = 19 ps +HPTDC~24 ps/bar!
We have some 1x6 bars, but
they look very fragile

## Slide 25
We Developed a 10 ps TOF System for use with a Hamburg Pipe
Design considerations:
1) full acceptance, excellent timing expected <10 ps
8 rows with x =1.5 to 3 mm (x=distance of proton from beam) to
minimize multi-proton effects (>90% efficient ) and keep rate/pixel
under 5 MHz to help control current/lifetime issues
gaps between rows to reduce cross talk
capable of operating beyond 50 interactions/crossing (where <N>=1/det/BC)
beam
Deflection from beam)
Validated the components of this design in test beam and at UTA Picosecond Test Facility with laser and “undergrad army”
Large x proton
2 cm x2 cm

## Slide 26: New Challenge: Adapt Timing Detector to be compatible with Roman Pot instead of HBP…
Q-Bar straight bar at Cherenkov angle
LQBar still at Cherenkov angle but take light out at 90 degrees
(Albrow Lbar parallel to beam takes light out at 90)
1) Arggh! 2) Challenge Accepted!
Notes: LHC logistics required us to move away from our original Hamburg Pipe design to a Roman pot design
Need to conserve detector performance
Simulation of single elements, now require a 90 degree bend

## Slide 27
New GEANT4 Simulation Effort
Led by Tom Sykora’s group at Palacký University, Olomouc Czech Republic (Libor Nozka, Leszek Adamczyk et al with with input from moi and help from UTA UG Tim Hoffman)
Start with straight Qbar (c ~48) (2mm x 6mm x 150 mm), since we have test beam data for this we can normalize simulation of LQbars and other geometries to Qbar
We also are undergoing detailed studies of how MCP-PMT treats different photon arrival time distributions , as correlations between photon arrival times exist are a f(TTS, gain, rise time, etc.) and are generally not well modeled.

## Slide 28: LQbar* (radiator bar at c +light guide bar) 2x6x(30+120)mm
45 degree bend to route light from radiator to perpendicular light guide bar, lose some light at elbow
Aluminizing helps but light ~ to mirror lost opposite to elbow.still lost at elbow
Without Mirror
With Mirror
*Not to be confused with Albrow’s Lbar
which is oriented parallel to beam and has no elbow
Notes: Talk about bouncing up and down vs. side to side (mapping a cone onto a rectangle)

## Slide 29
LQbar vs. Qbar Initial Performance
As expected LQbar is worse: significantly less early light
What can we do to improve the amount of light ?
QBAR (15 cm)
LQBAR (3+12 cm)
Notes: long tail out to large times due to light reflecting mutliple times
Our studies show it is the light within the first 100-200 ps that is the most important, after 400 ps
Very little impact

## Slide 30
The parallel cut captures the lower hemisphere of the Cherenkov
cone for small (x,y), however benefits only extend to about y=5 mm
LQbar Modification: Parallel Cut
Parallel cut
Square cut
LQbar y=0.1 mm
Qbar
What about this
2nd peak?
Notes: Show height of proton on plot
Perhaps draw one photon on parallel cut

## Slide 31: Phi vs Time for Parallel Cut on Qbar
Much of bottom hemisphere of the Cherenkov cone (negative phi) is reflected up the bar as shown earlier (depending on proton height with respect to parallel cut)
 = /2 straight down bar   /2 longer path
length  longer time
Color dispersion

## Slide 32: The 2nd Peak aka“Wings”
Taking the Cherenkov cone around the 90 degree bend leads to “wings” that are relatively faster (shorter path length) compared to the prompt light then for the straight bar case.

## Slide 33
Speed up the “Wings”
As taper angle increases,
bulk of 2nd peak
merges with first peak
5º
30º
15º
Add a “taper”
and optimize angle
to “straighten” wings speeding up 2nd peak
33

## Slide 34: All Together Now!
QBAR (15 cm)
LQBAR (3+12 cm)
LQBAR with parallel cut y=0.1
and 30 taper
Simulation says this is a superior detector with up to 2x more light in the same time window as the Qbar case! TB says (Censored)
Notes: After optimizing we can incorpoarte these bars in a detector

## Slide 35: New Nuclear Interaction Study
At 14 TeV find about 2% chance per bar (8 mm of quartz) of an interaction
These interactions have a high multiplicity
O(tens) particles, which would typically saturate amps and cause that bar timing to be mismeasured (but the event could be salvaged with somewhat degraded resolution almost all of the time).
Significant Implications on timing detector optimization: Ex. Filling a pot or pipe w/quartz is a good fixed target experiment, may not be so great as timing detector

## Slide 36
Two Arm UPTOP Detector
16 ch/side, 4 layers (depths in x)
2 rows (depths in z)
2 y measures (+/-) [the 2arms]
Main features:
Takes advantage of
parallel cut (lots of light)
Very compact 5x9 cm
Segmentation of 8, so this detector can not only serve as lowlum detector but also could be used for highlum tests
Only two very accurate
measurements per proton
Easily upgradeable to 32 channels (see next slide)
Could have 6mm x4 mm light guide bars
Ultra Precise Timing of Protons
New ¼ planacon
makes this design
viable

## Slide 37
Two Arm UPTOP Detector
Silicon lives
here (don’t cross the
red line!)
6.5 cm allows for all 16 pixels/tube to be instrumented (adds in yellow and pink bars)

## Slide 38
Component | t(ps) Current (HBP) | t(ps) Projected (RP 1arm 16 ch) | t(ps) Projected (RP 2arm 16 ch) | t(ps) Projected (RP 2arm 32 ch) | t(ps) Ultimate (RP 2arm 64 ch)
Radiator/MCP-PMT/CFD | 19 | 19* | 14* | 14** | 12***
HPTDC | 15 | 15 | 15 | 15 | 5
Total/bar | 24 | 24 | 21 | 21 | 13
Total (ideal) | 11 | 14 | 14 | 10 | <5
Timing System Resolution
Ideal=Assume clock, cables, unknown unknowns don’t contribute
*1 arm with 4 channels has ~½ the light of two arms 2 channels,
So should be comparable resolution; **2x32 adds 2nd detector or
uses 4 rows/side;*** 2x64 adds both also 6 µm pores +new HPTDC

## Slide 39: Highlights of Timing R&D
At CERN test beam (10/2012) a single quartz bar/PMT/CFD resolution of 19 ps was obtained, independent of bar cross section (2x6 mm vs 5x6 mm).
This corresponds to a 6 bar resolution of 11 ps including prototype readout electronics for a Hamburg-pipe-based QUARTIC detector
Developed with background group new simulation and visualization techniques
Used these to demonstrate that multiple interactions in quartz, while measurable, result in a modest efficiency loss or resolution degradation; after a design optimization only a few % of events are affected
Using new simulation, a modified design suitable for installation in a Roman pot has been obtained. Compared to design used in test beam, the new design gives more accepted light in the same time window, implying that we can achieve <10 ps in a dedicated Roman pot, and <20 ps in a shared Roman pot
Arradiance+Photonis with assist from UTA/Erlangen have developed a special phototube capable of sustained proton rates in the 5-10 MHz /pixel range. It has been demonstrated to have lifetime >50 fb-1, with an additional factor of 2 -3 expected from new processing techniques, this implies one tube could be expected to be operable for >200 fb-1
We have also tested for Photonis a new orthogonal life time approach, involving an active ion barrier, which shows 4-20x reduction in after-pulsing, believed to be the cause of PMT lifetime
Have successfully modified low-jitter SLAC Phased Lock Loop Clock circuit for AFP’s circumstances and obtained <5ps jitter
Developed a 20 ps detector suitable for sharing a Roman pot in 2015
no known technical obstacles to a 10 ps high lum ToF system in 2016

## Slide 40: Proton Distribution and Rates
40
To design detector need to take account of rates and their distribution
PYTHIA: about 2% of all interactions have a proton in AFP acceptance
For µ=25 (50) the integrated detector rate @25 ns
is thus 0.02*25*(40MHz*0.8) = 16 (32) MHz
Distribution is peaked at low x (displacement from
the beam), such that the closest 2 mm receives
20 to 25% of the rate and the closest 6mm receives
50 to 60% of the rate. So to equalize the rate
per bin, it is necessary to have smaller bins clsoe to
the beam: four bins in x as shown (bars integrate
over y), each would have a rate near 4 (8) MHz
Can an MCP-PMT deal with these rates? What about multi-proton effects?
Num of int. | n=0 | n=1 | n=2 | n=3 | n=4 | n>1
µ=25 | 61% | 30% | 8% | 1% | 0% | 9%
µ=50 | 37% | 37% | 18% | 6% | 2% | 26%
2 4 6 8 mm

## Slide 41
Is 50 Interactions a Problem for QUARTIC?
As the number of interactions increase, the rate/pixel increases (rate and lifetime concerns for MCP-PMT), combinatorics reduce your rejection, multi-proton events ( 2 protons in a bar) reduce efficiency, cross talk between rows becomes an issue
1 proton/detector/event average background (big, but not so bad) 32 MHz so 8-10 bins okay for rate and average multiplicity/bar only 0.1 to 0.2 so efficiency okay
Increasing the number of pixels helps with rate and efficiency, but the only way to keep the rejection from degrading with increased µ, would be to improve the timing resolution, or raise the mass threshold
*START THE HIGH LUM
PROGRAM AS EARLY AS POSSIBLE OR EARLIER*

## Slide 42
Pixelation and Efficiency for Different Scenarios
Scenario 1:
7 rows
2, 6x3.25 mm
Scenario 2:
10 rows @ 2 mm
Scenario 3:
10 rows @ 1 mm
Royon and Sampert study confirms pixellation of 8-10 is adequate