## Slide 1: Upgraded AWA Drive Beamline CONFIGURATION SIMULATIONS DIAGNOSTICS
John Power
AARD DOE Review
March 07, 2013
Direction of beam propagation
75 MeV
drive gun

## Slide 2: The AWA Upgrade drive beamline
drive gun
Direction of beam propagation
75 MeV
Upgrade Goals
Upgraded Drive Beam (Targets)
Single bunch operation
  75 MeV
  Q = 0.1-100 nC
  @ 100 nC
    sz = 2 mm
    High Current: ~16 kA
  emittance < 200 um
Bunch train operation
  10 bunches x 100 nC
  32 bunches x 30 nC
  Train Length = 10 - 50 ns
Original Drive Beam (Achievements)
Single bunch operation
  15 MeV
  Q = 0.1-100 nC (world record!)
  @ 100 nC
    sz = 3 mm
    High Current: ~11 kA
  emittance < 200 um
Bunch train operation
  4 bunches x 20 nC
  16 bunches x 5 nC
  Train Length = 10 - 25 ns

## Slide 3: Outline
Beamline configuration and installation of the beamline components
Beam Dynamics Simulations
Beam Commissioning Plan

## Slide 4: 1. beamline configuration AND INSTALLATION
Building up the beamline …

## Slide 5: Installation of beamline components (PROGRESS)
DIAGNOSTIC
BEAMLINE
COMPLETED
ONGOING
Solenoids
*arrived Summer 2012
*installed Winter 2013
RF Gun
*Conditioned to Full power
(Spring ‘11)
6 New RF cavities
*tuned & balanced Fall ‘12
*installed Winter ’13
Waveguides
*installed Winter 2013
+Spectrometer
+Quads
+Def Cavity
+etc.

## Slide 6: 1300 MHz rf cavity
Parameter (unit) | Value
unloaded voltage gain, V (MV) | 11.8
e = Ub/U0 @ 1 mC (%) | 43.15
energy droop along beam1 (%) | 27
s = rms energy spread due to wakes1 (keV) | 159
m = mean energy loss due to wakes1 (keV) | 394
Esurf (MV/m) | 33.5
Hsurf (kA/m) | 58.8
pulsed heat temp. rise (oC) | 1.5
Q0 | 25147
U0 (J) | 27.49
coupling parameter, b | 1.28
mode separation (MHz) | 14.7
power flow phase shift (o) | 0.17
…to installed in beamline
1for Pin = 10 MW and Qb = 100 nC, sz = 2 mm.
from design …
waveguide
RF window
Installed RF cavity
RF conditioning next

## Slide 7: 2. beamline simulation
Expected beam performance

## Slide 8: RF power distribution
DG
DL6
DL5
DL4
DL3
DL2
DL1
28 MW
25MW
25MW
30MW
f
f
WG
WL1
f
f
Total Power Budget = 96 MW
75 MeV
10 MeV
K1 (Orig.) 28 MW 25 MW
K2 (Litton) 30 MW 27 MW
K3 (Thales) 25 MW 22 MW
K4 (Thales) 25 MW 22 MW
Total 110 MW 96 MW
+
Klystron Maximum Operated
Power Power (90%)
K4
11 MW
K3
K2
K1
11 MW
11 MW
11 MW
13 MW
14 MW
PWR
14 MW
6 MW
5 MW
f

## Slide 9: Start-to-end simulations (Parmela/Impact-T)
Single bunch
Bunch train (beam loading and its mitigation)
Combined effects
z= 1093 cm
Full Width (3s) Beam Envelope (mm)
DL1
DL2
DL3
DL4
DL5
DL6
GUN
Example: 100 nC beam through the linac
Simulations performed

## Slide 10: 1. Single bunch start-to-end simulations
Beam parameters: Q = 100 nC, R (at cathode) = 8.0 mm, z = 3.40 ps
Single Bunch Wakefields*:
negligible effect on transverse phase-space
increased correlated energy spread.
decreased longitudinal emittance.
*Impact-T implementation of the wakefields based on, K. L. F. Bane, SLAC-PUB-9663, 2003 and benchmarked to ABCI.

## Slide 11: 2. Bunch Train start-to-end simulations
initial stored energy
U0
U0- DU
U0-N*DU
Goal: minimize droop  Ub/U0 @ Qb=1mC
Solution:
  large stored energy (U0)  rf cavity design
  vary launch phase  during operation
Ub=N*DU
BUNCH TRAIN

## Slide 12: 2. Bunch Train start-to-end simulations
10 bunches on crest
Bunches at different phases
T
T+Dt
Multibunch wakefield effects and its mitigation

## Slide 13: 3. Bunch Train start-to-end simulations
On crest (DE/E = 26%)
Vary phase (DE/E = 2.3%)
5 bunches x 100 nC
Vary phase (DE/E = 1.3%)
Notes: Equal time separation vs unequal time sep

## Slide 14: Example: 40 nC x 10 bunch train
quad
triplet
DLA
L=0.5 m
radius = 2.5 mm
Solenoid
Solenoid
DL1
DL2
DL3
DL4
DL5
DL6
GUN
Notes: High Gradient, hundred of MV/m

## Slide 15: 3. beamline commissioning
Diagnostics

## Slide 16: Drive Beam Commissioning
wide dynamic range
  charge: (100 pC < Q < 100 nC)
  emittance: (1 mm < eN < 200 mm)
fast pulse trains
  pulse train: single microbunch to bunch trains of up to 32 bunches spaced by 769 ps.
Main Diagnostic Beamline
Transverse: sigX/Y, emittanceY
Longitudinal: E, DE/E, sigZ
75 MeV Drive Beamline
sx,y
sx,y
Q
sx,y
sx,y
<x>, <y>
<x>, <y>
Front-end diagnostics
Drive beamline front-end (19 MeV )
sx,y
Q
sx,y
Q
Challenges for Diagnostics

## Slide 17: Front-end diagnostics Installed Winter 2012-13
Trim
Gun
RF cavity
Solenoid
In-flange FCT-ICT from Bergoz
  FCT: rise time ~175ps  resolve bunches inside the bunch train
  ICT: calibrated measurement of total charge in train
45o incidence YAG screen
50mm x 100 mm
Diagnostic Cross #1
Faraday cup
YAG
mirror
Diagnostic Cross #2
Normal incidence YAG screen
50mm x 100 mm
Laser Input
66mm
<x>, <y>
Drive beamline front-end (19 MeV )

## Slide 18: Imaging Station:(inside vacuum)
YAG:Ce Screen
  reduced depth of focus (normal incidence )
  High resolution (100 mm thickness)
Resolution
target
camera
45o Si-wafer, double-side mirror
  300 mm: very little energy deposited,
  very flat: good for laser alignment
  can be used for OTR at other locations (if YAG screen is removed)
Dual YAG-alignment screen
Normal incidence YAG screen
50mm x 100 mm
installed Winter 2013 (ongoing)

## Slide 19: Imaging Station (outside vacuum) To be Installed Spring ‘13
Motorized Lens Controller
Zoom, Focus, and Iris
10X Motorized Zoom Focal Length =
12.0 - 120.0 (mm)
8-to-1 DB25 Switch
Remote: Zoom, Focus, and Iris
The cameras are mounted:
below table
inside of the legs
To be installed Spring 2013

## Slide 20: Main Diagnostic Beamline
dump
A
A
A
2m
15 deg
1m
1m
dump
Def Cav
0.762m
1.0 m
1.0 m
DIAGX4
DIAGX1
DIAGX2
1.5 m
DIAGX3
DIAGX5
DIAGX6
DIAGX7
0.4 m
End of linac
Cav 6
A
1m
DIAGX8
0.762m
OTR
YAG+
mirror
Trim
BPM
Slit
ICT
Quad
DIAGNOSTIC
CROSS
A
USAF
target
Transverse: ey,rms,normalized [mm]
Longitudinal: sz [mm]
Transverse: sx,y[mm]
Q[nC]
75 MeV
Longitudinal: Dp, p [MeV]
TEST
AREA
To be installed Spring 2013

## Slide 21: Transverse: ey,normalized [mm]
dump
A
A
A
2m
15 deg
1m
1m
1m
A
Transverse: Emittance measurement
Multiple slits: 50um, 100um, 300um
Centered slit: quick estimate
Motorized slit: accurate measurement
Multiple drifts: ~70cm, ~1.7m, ~2.7m
0.5mm tungsten  q=64 mrad
dump
A
USAF
TARGET
NORMAL
INCIDENT
YAG:Ce
TUNGSTEN
SLIT
OTR
SCREEN
TRIM
COIL

## Slide 22: Longitudinal: sz [mm]
dump
A
A
A
2m
15 deg
1m
1m
0.762m
1m
dump
A
Longitudinal: Bunch length
RF Deflecting Cavity
OTR mirror + Streak camera
Longitudinal: sz [mm]

## Slide 23: Longitudinal: sz [mm]
Deflecting cavity first results
  3.4 MV @ 4.2 MW (1300 MHz)
  bunch length measurements
  longitudinal phase space
Resolution study
OFF
ON
La
Lb
200 cm
Q=0.1 nC & E=14 MeV
Resolution ~ 35 fs @ 0.1 nC  1 ps @ 100 nC @14 MeV
1/Vperp
Vperp
Lb
Lb

## Slide 24: Longitudinal: {E, DE/E}
Spectrometer based on existing 15o dipole
BEND
DRIFT
QUAD
LSOL
BEND
SCREEN
QUAD
LSOL
BEND
SCREEN
dump
DIAGX3
DIAGX4
DIAGT2
dump
DIAGQ1
BEND
DIAGT3
DIAGT4
A
A
DIAGX2
(50 mm)
(100 mm)
24

## Slide 25: Transverse: centroid {BPM system}
Stripline BPM (recently commissioned front end)
  lock beam phase to LLRF (new effort at AWA)
  slow orbit feedback system (new effort at AWA)
~400ps
1.3 GHz Stripline BPM (in house)
1.3 GHz BP filter
(commercial)
BPPM circuit board
(Euclid-ANL; in house)

## Slide 26: Summary
  Beam dynamics simulations for the 75 MeV beamline - Complete
  Front-end (<19 MeV) beamline – Spring 2013
    Install beamline (1st cavity and diagnostics) - Complete
    Condition 1st RF cavity to full power
    Generate and characterize single bunches and trains
  75 MeV beamline – Spring/Summer 2013
    Install remainder of beamline (cavities and diagnostics) - Complete
    Layout of 75 MeV diagnostic beamline - Complete
    Condition RF cavities 2-6
    Install diagnostic beamline
    Begin full beam commissioning at 75 MeV
First wakefield experiments – Fall 2013