## Slide 1: AM based approach for future Tracking Trigger applications
Ted Liu (Fermilab)
CPAD meeting at Arlington
Oct 6th, 2015

## Slide 2: Guideline of the talks
“Please remind speakers, should there be any doubt, that we are not looking for them to deliver review talks but instead to focus on the key technological limitations to address the P5 science drivers. Speakers should indicate areas where there is a potential for high return on investment. This emphasis will be repeated in our introduction to the workshop”.
Will try to follow this guideline, not easy.
Will not cover extensive simulation work already done (>50% work has been simulation)
Will not cover any tracking trigger demonstration details (on going work)
Still have many slides, will skip some.

## Slide 3
The workshop focused on the problems posed by high luminosity at hadron colliders, … from 1029 to 1034 cm-2 s-1 …1 TeV and 20 TeV energy….
~ 30+ years ago …
Some of the old worries became a reality
at Tevatron Run II 20+ years later ! …

## Slide 4
Trigger Working Group Report (1983, DPF workshop)
Some of the old worries became a reality
at Tevatron Run II 20+ years later ! …

## Slide 5: And the old worries continue in the coming decade & beyond …
HZZ  ee, MH= 300 GeV for different luminosities in CMS
1032 cm-2s-1
1033 cm-2s-1
1034 cm-2s-1
1035 cm-2s-1
Raw information from silicon detector/tracker reaches ~ Pb/s at Phase II luminosity

## Slide 6
Silicon based tracking trigger at L1 will be crucial for trigger objects reconstruction at
higher luminosity:
Electron
Photon
Muon
Tau
Jets
b-jets
missing ET
….
Essential for establishing
nature of EWSB,
new physics …
See Ulrich Heintz’s CMS Higgs talk yesterday and Darin’s talk earlier on CMS
Phase 2 upgrade.
Pileup at HL-HC: > ~ 140 (only 20 shown here)
Actual event
With tracking information

## Slide 7
CMS L1 Tracking Trigger:
Will need to reconstruct charged particle trajectories “on-the-fly” for every beam crossing (25 ns, or 40 Million beam crossings per second), from an ocean of input data (bandwidth required to transfer data ~ 100Tb/s)
This requires extremely
fast high bandwidth data communication as well as massive pattern recognition and track fitting power,
with near zero latency (~ few μs total)
This is challenging!
Pileup at HL-HC: ~ 140 (only 20 shown here)
With tracking information
Simulation with 140 PU

## Slide 8: High Performance Computing  from US “Report to the President and Congress” by President’s Council of Advisors on Science and Technology, Dec. 2010 (page 65)
Compute-intensive
  massively parallel computation involving very large number of processing elements;
Communication-intensive
  high-speed transfer of data among processing elements;
Data-intensive
  high-speed manipulation of very large quantities of data
HL-LHC L1 Tracking Trigger is High Performance Computing
(Non-von Neumann approach)
but with very Low Latency and in Real Time
HL-LHC requires the most advanced Real Time processing technology

## Slide 9: Use HL-LHC as an example
Frontier physics at LHC in the future:
Go to Higher Energy: needs more aggressive R&D in Magnet
OR
Go to Higher Luminosity: needs aggressive Tracking Trigger R&D
It has become clear that track based trigger capability will be crucial to the frontier physics reach at LHC in the future, as luminosity increases.
The current technology using fiber data transfer, FPGAs, custom chips and modern PCs cannot be scaled in a simple manner to accommodate all the tracking trigger demands.
Significant improvements, or breakthroughs, will be needed. In other words, aggressive R&D efforts will be required.
 How to take advantages of modern (new/emerging) technologies

## Slide 10
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Detector design for triggering
L1 Tracking Trigger challenges at HL-LHC
Partition detector into
trigger towers/sectors
Pick your favorite method
Finer pattern recognition

## Slide 11
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Detector design for triggering
L1 Tracking Trigger challenges at HL-LHC
Partition detector into
trigger towers/sectors
Pick your favorite method
Finer pattern recognition
CMS new Tracker Design:
Pt stub finding reduce the
data volume by ~ 10-20.

## Slide 12
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Detector design for triggering
L1 Tracking Trigger challenges at HL-LHC
Partition detector into
trigger towers/sectors
Pick your favorite method:
Finer pattern recognition
Very challenging

## Slide 13
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Detector design for triggering
L1 Tracking Trigger challenges at HL-LHC
Partition detector into
trigger towers/sectors
Pick your favorite method
Finer pattern recognition
Need massive parallelism: divide and conquer (100Tb/s)
regional multiplexing as well as time multiplexing.
Requires high bandwidth, low latency, and flexible real time communication.

## Slide 14
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Detector design for triggering
L1 Tracking Trigger challenges at HL-LHC
Partition detector into
trigger towers/sectors
Pick your favorite method:
Associative Memory Approach
Hough Transformation
Tracklet-based
Adaptive Pattern Recognition
Biology Inspired …
your choice here… (any new ideas?)
Finer pattern recognition
Here we should be able to take advantage of
commercial technology development, but will need to develop
new ways to implement known HEP techniques or develop new techniques.

## Slide 15
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition (using AM as a filter)
(5) Track Fitting … (track fitting is done in FPGA)
Detector design for triggering
L1 Tracking Trigger challenges at HL-LHC
Partition detector into
trigger towers/sectors
Pick your favorite method:
Associative Memory Approach
Hough Transformation
Tracklet-based
Adaptive Pattern Recognition
Biology Inspired …
your choice here… (any new ideas?)
Finer pattern recognition
Associative Memory approach is a known HEP technique for silicon based tracking trigger for hadron collider.
The challenge in the future is pattern density and performance …

## Slide 16
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Core R&D for AM + FPGA approach:
High performance Data Formatting/Delivery
High performance Associative Memory (ASIC)
Will use CMS L1 Tracking Trigger as an example next
Detector design for triggering
AM + FPGA based Tracking Trigger
Partition detector into
trigger towers/sectors
Associative Memory Approach
Finer pattern recognition
Tracking Trigger

## Slide 17: Overview of the R&D
System architectural design (2012-2013) for CMS L1
  System Architecture fully studied/established in 2013
  Concept of demonstrator developed in 2013
System level performance simulation (2013-
  Preliminary results on system requirements:
  AM patterns ~ 2M patterns/Tower, or ~200K/chip
  Linearized Track Fitting details worked out for all regions
High performance ATCA board R&D (2011 - )
  The Pulsar2 project goal: ~ 1Tbps ATCA board with large mezzanines for AM chips
  This goal has been achieved in 2014 with Pulsar 2b design
  High performance pattern recognition mezzanine card design in 2015 (done)
High performance Associative Memory (2010 – )
  The VIPRAM project (Vertically Integrated Pattern Recognition Associative Memory)
  Goal: few x 100K patterns/cm^2 @ few x100MHz speed
  First 2D protoVIPRAM00 chip successfully tested in 2014 and works as designed
  The first 3D protoVIPRAM01 chip design in 2015 (to be submitted)
  The first 2-tier protoVIPRAM02 dedicated for L1CMS in 2015 (to be submitted)
  The first FPGA implementation of L1CMS ASIC working
Bottom up
Top down
Technical board to system level demonstration work started …

## Slide 18: Comparison: ATLAS L2 FTK and CMS L1 Track Trigger
New
Tracker/Cabling
to be designed for
Tracking Trigger
for HL-LHC
Existing
Tracker/cabling
not designed for
Tracking Trigger
4 η x 16 φ = 64 trigger towers
6 η x 8 φ = 48 trigger towers
This leads to new Architecture….

## Slide 19
ATCA
CMS
Tracking Trigger Towers
AM or other track finding approaches implemented on mezzanine (PR engine)

## Slide 20
Pulsar II Web page: http://www-ppd.fnal.gov/EEDOffice-w/Projects/ATCA/
User information: https://twiki.cern.ch/twiki/bin/view/Main/PulsariibTesting
Data IO capability ~ 1 Tbps

## Slide 21
Pulsar II Web page: http://www-ppd.fnal.gov/EEDOffice-w/Projects/ATCA/
User information: https://twiki.cern.ch/twiki/bin/view/Main/PulsariibTesting
Demonstrated Interconnection Bandwidth:
Pulsar IIb FPGA to full mesh backplane channels 10Gbps/lane
Pulsar IIb FPGA to FMC Mezzanine (GTH) 10Gbps/lane
Pulsar IIb FPGA to FMC Mezzanine (parallel LVDS) 800 Mbps/pair
Pulsar IIb FPGA to Rear Transition Module QSFP+ over fiber 10 Gbps/lane
ProtoPRM FPGA to QSFP+ over fiber 10 Gbps/lane
ProtoPRM Master-Slave UltraScale FPGA interconnections 15.6 Gbps/lane

## Slide 22: Pulsar IIb FPGA to Full Mesh ATCA Backplane
The latest COMTEL “AirPlane” 100G full mesh ATCA backplane. This new backplane has to date yielded the most consistent link performance with all eight Pulsar IIb boards running all GTH transceivers simultaneously (56 lanes) at 10 Gbps.
COMTEL new full mesh

## Slide 23
15.6Gbps between UltraScale FPGAs
10Gbps

## Slide 24: Pulsar 2b achieved performance  data delivery capability demonstrates 24 crates system is feasible
Data sink capacity:
10 x 400Gbps/RTM = 4Tbps/crate
24 crates x 4Tbps ~ 100 Tbps
One crate with 10 Pulsar 2b

## Slide 25
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Challenging issues
(1) Data Reduction at detector/sensor stage
(2) Data Transfer (rad hard, high bandwidth, low power link)
(3) Data Formatting
(4) Pattern Recognition
(5) Track Fitting …
Core R&D for AM + FPGA approach:
High performance Data Formatting/Delivery
High performance Associative Memory (ASIC)
Detector design for triggering
AM + FPGA based Tracking Trigger
Partition detector into
trigger towers/sectors
Associative Memory Approach
Finer pattern recognition
Tracking Trigger

## Slide 26: The AM approach
Pattern Recognition Associative Memory (for HEP)
  Based on CAM cells to match and majority logic to associate hits in different detector layers to a set of pre-determined hit patterns (simple working unit, yet massively parallel)
  Pattern Recognition finishes right after all hits arrive
  A PR engine naturally handles a given detector region: divide & conquer
Layer 1
Address 4
Match
Layer 1
Address 4
Match
Match
Layer 3
Address 7
Match
Match
Layer 3
Address 7
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Layer 3
Address 9
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Layer 2
Address 1
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Layer 4
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Layer 2
Address 4
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Match
Road!
CAMs
Linearized track fitting can follow each road found (FPGA implementation)
Animation by Jim Hoff (FNAL engineer)
…….
Millions of
Patterns
compared
at the same
time

## Slide 27: Pattern Recognition Associative Memory approach
Pattern Recognition using Associative Memory (AM):
  Massive parallel processing to tackle the intrinsically complex
  combinatorics of track finding algorithms, avoiding the typical power
  law dependance of execution time on occupancy
  solving the pattern recognition in times roughly proportional to the number of hits, making the downstream task much easier
  Usually requires custom ASIC
The Track Fitting stage (in FPGA) after AM:
  Examples: linearized track fitting … etc
  The more powerful the AM stage, the less demand on TF/FPGA
  The more powerful the TF/FPGA, the less demand on AM
Roads

## Slide 28
A slide from Luciano Ristori
at TIPP 2011 conference
Back then:
Crucial emerging technology for
CDF silicon detector and silicon vertex trigger….
(top quark discovery, rich b/c physics program …)
The first Amchip for CDF/SVT was implemented in the 90s, 128 patterns/chip

## Slide 29
The AM approach was successfully used at CDF for secondary vertex trigger (SVT) in Run 2
Found roads
  Massive parallel processing to tackle the intrinsically complex
  combinatorics of track finding algorithms, avoiding the typical power law dependance of execution time on occupancy

## Slide 30
  avoiding the typical power law dependance of execution time on occupancy (large combinatorics …)

## Slide 31
HZZ  ee, MH= 300 GeV for different luminosities in CMS
1032 cm-2s-1
1033 cm-2s-1
1034 cm-2s-1
1035 cm-2s-1
Occupancy or combinatorics will be much worse at HL-LHC

## Slide 32: Before and after AM stage: Associative Memory for CMS case at HL-LHC ~100M patterns, or ~2M pattern per trigger tower, or few x 100K per chip
Roads found
A factor of > 10 reduction of occupancy, and more importantly,
stubs/hits are organized in roads (“hits of interest”),
making the track fitting task inside FPGA much easier.
PU200+4Top event simulation
(endcap)

## Slide 33
2 meters
0,1
2,3
4,5
6,7
8,9
10,11
fan-out
fan-in
CDF original SVT system had ~400K patterns total …
128 patterns per AMchip -- commissioned around ~2001
(initial concept started in 1980s)
Question: can one integrate all these into one chip for HL-LHC?

## Slide 35: “A New Concept of Vertically Integrated Pattern Recognition Associative Memory” TIPP 2011 Proceedings http://www.sciencedirect.com/science/article/pii/S1875389212019165
Pattern recognition for tracking
is naturally a task in 3D
track
fired road

## Slide 36
The 3D stack is very thin ( < ~ 10 um per tier)
Directly shortens the longest of the driving lines in the
pattern recognition cell (address match lines).
 reduced power density or increased speed

## Slide 37
Connecting the Dots “in slow motion”

## Slide 38: Design involved
CAM cell design
Majority Logic
Cell design
Control/interface
Initial R&D goal:
Proof-of-principle demonstration
25μm
In 130nm

## Slide 39
Fig. 4 - A 3D PRAM
VIPRAM concept
In 3D, with 130 nm, VIRPAM ~160K AM patterns/cm^2
CDF AMchip03: 180 nm, standard cell, 5K AM patterns/chip
3D Architecture intrinsically open/flexible:
“CAM cell” doesn’t have to be CAM
e.g. simple algorithm or even NN …
platform to implement more advanced/fast
pattern recognition algorithm…
possible area for breakthrough

## Slide 40
VIPRAM Project Status Summary
The past: with steady progress
Initial Idea: ~2010
VIPRAM concept paper: 2011
CDRD award: 2012
First 2D Design submission: 2013
First ProtoVIPRAM00 chip successfully tested: 2014
 Design building blocks are ready for 3D stacking
2D design fully compatible with 3D stacking
CAM cell size: 25 um x 25 um, @ 130nm GF CMOS
On going work (2015)
The 3D multi-tier design (protoVIPRAM01) ready
A 2-tier design for CMS L1 tracking trigger (protoVIPRAM02) at final stage
both designs ready for submission later this year (2015)

## Slide 41: Extensive simulation and optimization work done at different levels  much of the work done by engineering students
Full-chip
Pattern core
Single Pattern
CAM cell
Majority Logic cell
Power delivery
Signal timing …

## Slide 42
The project has attracted
engineering school students.
Few engineering school thesis,
work done at Fermilab as intern
or URA fellowship.
Second URA fellowship for
VIPRAM project:
Northwestern EE school
Ph.D student:
Dawei Li (June 2014 – June 2015)

## Slide 43
Chip delivered Jan 2014:
Found patterns the day after
the chips were wire bonded.
Successfully/extensively tested in 2014, no problem found.
People involved from Fermilab (highly coherent team)
Engineers: G. Deptuch, J. Hoff, S. Joshi, J. Olsen, M. Trimpl,
Physicists: S. Jindariani, T. Liu, N. Tran
Power/thermal analysis by
W. Xia, P. Gui ( SMU EE)
D. Li, S. Memik (NWU EE)
First ProtoVIPRAM00 Chip
Collaboration with Tezzaron company

## Slide 44: Test Mezzanine Card
Voltage regulators
DDR3
FMC (LPC)
Connector
protoVIPRAM
CMC/PMC size
74 mm x 149mm
4 SFP+ Transceivers
Up to 6.6 Gbps
protoVIPRAM Voltage and Current Readback
Kintex 7 FPGA (XC7K160T-1)
protoVIPRAM voltage regulators (programmable)
Config Flash

## Slide 45: Chip Testing and Performance Study
Use data and patterns from 140 Pile Up CMS AM simulation for HL-LHC to study the chip performance in close to “battle field” conditions
protoVIPRAM00 shows 100% performance around ~111 MHz,
design target was 100 MHz
Power consumption ~ 300mW,
as expected
Extensive stress test performed to study chip performance in extreme conditions.
layer | <Nstubs>
1 | ~90
2 | ~60
3 | ~50
4 | ~40
5 | ~40
6 | ~40
stub
inputs
Fired
patterns

## Slide 46: Moving forward: 3D stacking (protoVIPRAM01)
There are minimal modifications to that existing 2D protoVIPRAM00 design. In fact, only those changes that are consequences of 3D are being permitted
This would allow an apples-to-apples comparison of our design in 2D and its 3D cousin, using the exact same test setup.
We will learn the effect of 3D on speed, power consumption, thermal dissipation etc this way.
The design is finished and ready for submission …
TWEPP 2014 Aix-en-Provence
1st step
More stacking
Using the same test setup
for apple-to-apple comparison

## Slide 47: Moving Forward: VIPRAM for L1CMS
This will be a Two Tier design: protoVIPRAM02
IOtier: handles the System Interface of the chip with the goal to bring it to maturity.
CAMtier: Complete PRAM pattern structure on one tier with 8 CAM Cells/1 Control Cell
70 x70 um
at 130 nm
One pattern for 8 detector layers
Focus on speed

## Slide 48: Moving Forward: protoVIPRAM02 for L1 CMS Focus on the System Interface
2 Tiers
  ioTier – handles all data input and output. Hits received on the ioTier are passed immediately to the PRAMtier. Road flags are read out through the ioTier
  PRAM or CAMtier – handles all pattern recognition
Pipelined
  On command, all road flags raised by the CAMtier are captured into the ioTier, and then the PRAMtier is free to start digesting the next event.
TWEPP 2014 Aix-en-Provence
Strategic Planning
3D is an emerging technology. What if it is not ready in coming year(s)?
  This design can be realized with existing bump bond technology.
70 x70 um
per pattern

## Slide 49: Pattern Recognition Mezzanine
IO Tier
PRAM Tier(s)
Roads
Track Stubs
VIPRAM multi-tier pipelined operation
VIPRAM

## Slide 50: The L1CMS “CAM Tier and I/O Tier ” Schematic and Layout
Layout is done,
At final design verification stage

## Slide 51: The technology of B-TSVs
B-TSV test 8” wafer on probe station during measurements
This year, success from
B-TSV test wafers from
Tezzaron (done at FNAL)
With 111,360 TSVs chains
working
Single TSV vs double TSVs
B-TSV measurements:
resistance ~ 0.3 Ohm
capacitance ~ 8 fF
as expected
Results rather promising …

## Slide 52: 3D MPW Run
Internal FNAL 3D-IC run - GF130 nm CMOS process and Tezzaron/Novati (Naperville, IL) 3D IC technology with B-TSV (Via-Last) – for VIPIC-L and VIPRAM
the most significant 3D efforts in int’l scientific community, to provide science ready camera for XCS experiments and proof of principle of AM-based track-triggering
reticle map, single mask for 3D assemblies
> for 1 Megapixel Detector for X-ray Correlation Spectroscopy
Generic detector R&D and US-CMS
VIPIC-L
VIPRAM
A slide from Gregory Deputch

## Slide 53
Event N
Event N-1
Implementing VIPRAM functionality in FPGA
FPGA
AM
4K patterns (64x64) in KU40

## Slide 54
Track fitting
in main FPGA
4K patterns in UltraScale FPGA KU40 @250MHz
Will be used for initial demo and
performance optimization
Very cost effective way to guide the ASIC design …
FPGA-AM
VIPRAM
Main
FPGA

## Slide 55: Pattern Recognition Engine flow
AM
with N patterns
stored
Stubs library
Stubs from
Pulsar for a given BX and Trigger Tower
Super Strip ID
of each stub
~ few x100
unique Roads fired
Roads
with all
associated
stubs
stubs
Pt
Check
for each
comb
Track
fitting
stage
Stubs library
Stubs library or
Data Organizer
Main FPGA
tracks
Clean
up
Δt2
Δt3
No time to show
Track fitting details
here

## Slide 56: Before and after AM stage: Associative Memory for CMS case at HL-LHC ~100M patterns, or ~2M pattern per trigger tower, or few x 100K per chip
Roads found
A factor of >~10 reduction of occupancy, and more importantly,
stubs/hits are organized in roads (“hits of interest”),
making the track fitting task inside FPGA much easier.
(PU200 + 4Top) simulation (endcap)

## Slide 57
Fired
road
Linearized Track Fitting (PCA) (default for AM)
Tracklet-like (being explored)
Hough Transform (being explored)
Retina (being explored)
AM
Relationship among different algorithms (one way to look at it)
AM’s role is to make things much easier for the FPGA, whatever algorithm runs inside

## Slide 58: High Performance AM chip development
Three
approaches
being
explored
Future AM chip from INFN:
from 65nm down to 28nm, pure 2D
Future chip from FNAL for CMS L1:
Simple 2-tier design, scale from current 130nm to 40 nm
to reach ~200K patterns/chip
More cost effective and feasible
FNAL generic R&D exploring multi-tier VIPRAM @ 130nm.
Jointed effort
in the future

## Slide 59
Potentially possible to directly
identify/confirm lepton objects at L1,
many advantages this way…
potential for lepton isolation on chip…
animation
After all, the main
purpose of
L1 tracker info
is to confirm
L1 muon
and electron
candidates
Associative memory
||
Confirmation memory
(Food for thoughts for future colliders)

## Slide 60: Experiment on chip Lepton isolation in a chip?
High Pt lepton
High Pt lepton takes much less patterns
Isolation veto doesn’t require high eff for low Pt tracks much less patterns
Number of fired roads MUCH less (track fitting stage MUCH simpler/faster)

## Slide 61
What if one could implement
much more patterns with 3D?
Triggering Taus at L1?
Need detailed studies
tau

## Slide 62: Initial Board Level demo (2015- early 2016)
Data Source Board(s)
Pattern Recognition Board
Pattern Recognition
Mezzanine
10 x QSFP+ (40 x 10Gbps)
One board emulating
~40 modules worth of data

## Slide 63: One Trigger Tower can be fully demonstrated with two ATCA shelves (2016 - 2017)
Sourcing ~ 400 modules/fibers worth of data
from one full Trigger Tower
Data Source
with 10 Pulsar2b
10 Pulsar2b
and Pattern
Recognition
Mezzanine
All 10 Pulsars take turn to process events
1 2 3
with 3 unique towers, 1,2,3

## Slide 64
Data formatting /delivery
Pattern Recognition (PR)
Track
Fitting
Data transfer
AM based Tracking Trigger Demonstration 2015 - 2017
Partition detector into trigger towers
Finer pattern recognition
Data Sourcing
Emulate tracker output using
HL-LHC simulation data
Tracks out
Processing
Latency Δ t
Δt1
Δt2
Δt3
system level demonstration:
Study processing latency vs performance vs cost
Demonstrate the feasibility of tracking trigger
Identify bottlenecks and guide future R&D
Goal: ~4 μs
  People currently involved within CMS:
  USCMS: Florida/FNAL/Northwestern/TAMU
  Non-US: Brazil/Lyon/INFN/KIT/PKU/CERN/ …
AM approach as example

## Slide 65: AM-based Tracking Trigger R&D for HL-LHC
Data formatting
Pattern Recognition
Track
Fitting
Data transfer
Detector design for triggering
VIPRAM in 3D (DOE CDRD)
Custom
ASIC
L1 Track Trigger
architecture
ATCA
Pattern Recognition Mezzanine (PRM)
Pulsar II
VIPRAM:
Vertically Integrated Pattern
Recognition Associative Memory
Extensive
simulation
work

## Slide 66: HL-LHC tracking trigger challenges & new/emerging technologies & R&D
CDF SVXII
Data formatting
Pattern Recognition
Track
Fitting
Data transfer:
3D technology may allow
major breakthrough here
tracks
Detector design for triggering
Beam spot
Telecommunication technology natural fit
Frontier Physics reach at
high luminosity LHC require the most advanced
Real Time processing technology.
LHC developments in this respect are also a “playground”
for developing and experiencing novel Real Time field.
Module design:
modern packaging
technologies
FPGA technology

## Slide 67: backup

## Slide 71: Outlook: Tracking Trigger & Future Hadron Colliders
Generally speaking, the ultimate physics reach of any higher energy hadron collider (given a center-of-mass energy) will be governed by its luminosity.
Given the huge cost associated with any future higher energy hadron collider, it is crucial to push for higher luminosity (similar to HL-LHC or beyond). This is to maximize the new physics reach of the huge investment already made, before a new higher energy collider can be proposed or built.
Because tracking information is the most effective means for high pile-up mitigation, a high performance, real time tracking trigger will be mandatory.
On going Tracking Trigger R&D projects: not only will they be important for the success of physics program in the HL-LHC era, they also lay some of the technological foundations for the future of the field…

## Slide 72
Data formatting /delivery
Pattern Recognition (PR)
Track
Fitting
General comment on demonstration
Data Sourcing
Emulate tracker output using
HL-LHC simulation data
Tracks out
Δt1
Δt2
Δt3
Processing
Latency Δ t
Goal: ~4 μs
latency
performance
cost
(system/board/chip)
design optimization