## Slide 1: CMS Phase-2 Trigger Upgrade Plans and R&D
Darin Acosta
University of Florida

## Slide 2: First: Phase-1 Level-1 Trigger Upgrade
To address the rate and pile-up challenges of LHC Runs 2 and 3, upgrade to improve:
  e/γ and τ cluster footprints and isolation
  Muon pT resolution and muon isolation
  Jets and Energy sums with pile-up subtraction
  Menu sophistication (#lines, complexity)
A complete replacement of the Run 1 system
  Increase system flexibility with high bandwidth optical links and large FPGAs
  Further standardization across systems using μTCA telecomm platform
  Build and commission upgrade in parallel with current trigger in 2015, deploy in 2016
Designed to achieve ultimate performance without:
  Silicon tracking at Level-1
  Crystal granularity for electromagnetic calorimetry
  Raising the read-out rate ceiling for FE electronics
  Increasing the trigger latency
CERN-LHCC-2013-011
Endcap muon

## Slide 3: Phase-1 Trigger Architecture
~6 Tbps
Global Decision
~3 Tbps

## Slide 4: Challenges of High Luminosity LHC
Integrated luminosity of 3000 fb-1 beyond LHC Run 3
  Fully explore the electroweak sector (Higgs couplings) and reach ultimate sensitivity for TeV scale physics
Luminosity leveled to 5×1034 Hz/cm2 (pile-up ~140), possibly as high as 7.5×1034 Hz/cm2 (pile-up ~200)
  Compare to Runs 2+3: L<2×1034 Hz/cm2 (pile-up ~50)
Increased rate and pile-up effects:
  Muon thresholds pushed into the flat region of rate curve because of limited PT resolution
  Very high e/gamma trigger rates
  Degradation of the utility of calorimeter-based isolation due to high pile-up
  Blow-up in rate of energy sum and multi-jet triggers due to high pile-up
Nevertheless need thresholds efficient for precision electroweak scale measurements (Higgs) and TeV scale

## Slide 5: CMS Phase-2 Upgrade for the HL-LHC
CMS Technical proposal:
  CERN-LHCC-2015-010
  https://cds.cern.ch/record/2020886
Detector upgrades:
  Silicon strip Outer Tracker
  Pixel Tracker
  Forward calorimetry
  Forward muons
  Bream radiation protection and luminosity
  Trigger /DAQ

## Slide 6: Phase-2 Level-1 Trigger & Readout Design Specifications
Incorporation of tracking at Level-1 from the silicon tracker
  Major missing ingredient!
Correlation of tracks with other Level-1 objects
  Better charged lepton ID, refine (muon) momentum, assign jet vertex, determine primary vertex, provide track-based isolation …
Introduction of crystal granularity at Level-1 for ECAL barrel
  ΔϕΔη = 0.0175 × 0.0175 vs. 0.0875 × 0.0875
  Better spike rejection and EM shower identification
Incorporation of Phase-2 forward muon detectors into muon Track-Finder trigger (GEM, iRPC)
  Increased redundancy, more bending angles
Trigger rates up to 750 kHz @ Level-1, 7.5 kHz @ HLT
  Compare to today: 100 kHz and ~1 kHz
  Alleviate a Level-1 bottleneck and allow HLT to do more
Level-1 trigger latency of 12.5 μs (500 BX * 25ns/BX)
  Compare to today: 4.0 μs
  Allow time for additional processing (Track Trigger, Correlation)

## Slide 7: A Possible Level-1 Trigger Architecture
New
New
New
New
New
New
But need to develop details of a design to understand layer structure and segmentation
Modeled after Phase 1 design
~50 Tbps
~25 Tbps
~4 Tbps
~50 Tbps

## Slide 8: Phase-2 Outer Tracker Design
Baseline design has 6 barrel layers and 5 endcap disks
  10 and 11 layers, respectively, in current Tracker
  220 m2 area
Two sensor modules in all layers for triggering (stubs)
  2S: 2.5cm strips, 90μm pitch
  PS: Long Pixel (1.5mm) in 3 inner layers for z-coordinate, and 5cm strips, 100μm pitch
  50M strips
  220M macropixels
  Sensor spacing optimized to obtain 2 GeV pT threshold
Inner pixels not shown 

## Slide 9: Track Stub Finding
Stub efficiency vs. PT for various layers and disks 
Barrel
Endcap
Double layers help reduce data bandwidth.
Require a coincidence within a road, limits PT > 2 GeV
  < 3% of tracks
“Push” design: all stubs forwarded
  3-4 stubs/module/BX for Barrel layer 1
  ~10K stubs/BX
  O(50) Tbps
1 BX = 25ns

## Slide 10: Track-Finding
Again a “push” design, not region of interest
  Input: Expect ~10K stubs/BX @ PU~140, of which 5-10% belong to tracks with PT>2 GeV
  Output: ~100 bits/track  several Tbps to track correlators
  Latency: ~5 μs allocated
Multiple approaches under consideration to find tracks:
  Pattern-based: Track patterns stored in Associative Memory chips
    Target implementation in custom ASICs to store large number of patterns (~100M overall)
  Hough transform: transformation of track patterns to clusters in transformed space
    Target implementation in FPGAs
  “Tracklet” approach: Track building from stubs with pair-wise layer extrapolations
    Target implementation in FPGAs
Generally implemented with time-multiplexing of the input data (round-robin of event data to processors)
All followed by a track-fitting stage to extract track parameters
More in T.Liu’s and A.Ryd’s reports

## Slide 11: Pattern Recognition with AM Approach
Identify track patterns from hits across different detector layers
  Content addressable memory cells with provision for majority logic in pattern
  Generally does well for high occupancy environments
  Massively parallel approach
CMS AM Track-Trigger Concept
  Partition geometry into 48 towers (6 in η × 8 in φ)
  Target:
    1 ATCA crate per tower, with 40 Gbps full mesh backplane (Time MUX)
    ~2M patterns per tower
    ~200K patterns/AM chip
      Ultrascale FPGA for current prototype
      Develop ASIC prototypes in 2D (~2018) and 3D (~2021)

## Slide 12: Track-Finding Performance
Efficiency curves vs. eta and PT for PU=140:
Z0 resolution:
1mm
Tracklet approach

## Slide 13: Standalone Muon Trigger
New detectors in forward region to add redundancy and enhance trigger
  GEM in first 2 layers
  Improved RPC in outer layers
Additional inputs and improved angular information (bend angle) for track-finding for better efficiency and rate rejection
Rate just in GE1/1 region

## Slide 14: Example from Phase 1 Upgrade
Muon rate reduction comes from improved PT resolution
Large look-up table has been very successful for the muon PT assignment at Level-1 in CMS forward region
  Non-uniform B-Field
  Ability to use multiple deflection angles in φ and η within and between measurement layers
  Phase-1 making use of Boosted Decision Trees for calculation
4MB (legacy)  1 GB for Phase 1 upgrade LUT
  Memory type: Micron RLDRAM3
    Total size: 1G x 9 bits, 30 address bits
      Upgradeable in future
    Clock frequency: 200 MHz
    Random address read operations: 5/25ns
    Latency: 2 LHC clocks
    Memory array is split into 32M banks, 32 words each
Notes:       Firmware logic ensures restriction that that random address reading not done from same bank on 2 consecutive clocks

## Slide 15: Muon-Track Correlation
Match standalone muons to tracker tracks, take measurements from track
  PT resolution improves from O(20%) to 1-2%
Sharpens turn-on efficiency
Drops rate ~10X from current 2015 muon trigger
  However, closer to ~5X rate reduction after 2016 Phase 1 muon upgrade
L=5E34

## Slide 16: High Granularity Calorimeter (HGC)
New endcap calorimeter with high granularity to survive radiation does and high pile-up environment of HL LHC (inspired by ILC detector design)
  Electromagnetic (EE): 28 layers of silicon/tungsten
  Front Hadronic (FH): 12 layers of silicon/brass
  Back Hadronic (BH): 12 layers of scintillator/brass
Trigger primitives:
  850K sums for EE+FH @ 40 MHz transferred off detector
    2x2 sensor pads, alternate active planes, each 2 x 10 Gbps links  O(50) Tbps transferred
      Comparable to tracker output
  Form longitudinal clusters and projective towers in off-detector electronics
589 m2
6.1M ch.

## Slide 17: ECAL Barrel Trigger Primitives
In order to meet the requirements for an L1 rate of 750 kHz and a latency of 12.5 μs requires a redesign of the ECAL barrel front-end electronics
Take opportunity also to deliver trigger information at crystal granularity (vs. 5x5 currently)
  Utilize newer rad tolerant link technology for O(10) Gbps/ch.
  Improves spike rejection in single APD channel from hadron interaction in APD (energy comparison to 4 neighbors)
  ΔϕΔη = 0.0175 × 0.0175 (vs. 0.0875 × 0.0875) better granularity to match to tracks
  O(25) Tbps transferred off detector!
    Comparable to Tracker output

## Slide 18: Calorimeter Trigger
Cluster energies into electron/photons, taus, jets, and form energy sums (HT, ETmiss, total ET)
 Processing workflow
Barrel e/γ rate vs. ET for single xtal resolution vs. 5x5 
2 – 3X rate reduction

## Slide 19: Electron-Track Correlation
Match EG objects to tracker tracks
  Reduced track efficiency compared to muons from material interaction
Drops rate ~5X for ET >20
  ~2X after single xtal improvement
Track isolation
  Tracks in cone about lepton with consistent z0
  Cut on relative isol: ΣPTtrk / Pte
  Rate reduction ~2X

## Slide 20: Tau Track Triggers
Two approaches studied:
  Matching calo tau objects with track
    High quality track in narrow cone with PT>15 and no other tracks in isolation cone
  Matching tracks to e/γ clusters
    Combine high quality tracks with consistent z0 and e/γ clusters with ET>5 with inv. mass < mt
Rate vs. VBF Hττ effic. for single (left) and double (right) tau triggers
Rate reduction ~2X with tracking (~50 kHz @ 50%)

## Slide 21: Energy Flow with Tracks
Event vertex
  Resolution ~5mm for tracks with PT>2
Jet-vertex matching
  Energy sums such as HT and HTmiss purely based on calorimeter quantities are very sensitive to pile-up
  Requiring consistency with a vertex greatly improves multijet and jet sum triggers
Track-based MET
  Reconstruct missing transverse momentum from tracks associated to primary vertex
    Less affected by pile-up
Impact of several triggers with and without tracking for a SUSY scenario
Tracking

## Slide 22: Particle Flow at Level-1?
Full exploitation of tracking at Level-1
  Requires matching all calorimeter clusters to all tracks, removing clusters not attached to the primary vertex, and replacing cluster energy with track parameters for rest
  Significantly improves the jet and hadronic energy flow measurements at CMS. Also reduces pile-up dependence.
  Very successful in offline reconstruction and at HLT
Likely very ambitious for Level-1…

## Slide 23: Simplified Example Level-1 Trigger Menu
Target L = 5.6E34, PU=140
  Main track-based triggers
  Thresholds are comparable to Phase 1 as intended
  Estimate 30% of rate missing to all other cross triggers
  260 kHz @ PU=140
Scales to 500 kHz @ PU=200
  Then add safety factor of 1.5  design for 750 kHz ultimate rate from Level-1

## Slide 24: Dependence of Trigger Threshold vs. Total L1 Bandwidth
Bandwidth assumed for previous menu
Illustrates benefit of tracking
Thresholds obviously can be reduced with more L1 bandwidth
  Note current bandwidth limit is 100 kHz
Diminishing returns beyond 750 kHz

## Slide 25: HLT
If we have full tracking at Level-1, what is left for HLT to achieve another factor 100 reduction in rate?
Tracking
  Has access to pixel hits in addition to strips  b-tagging
  HLT so far has not had the resources to perform global tracking for the entire Level-1 bandwidth
  But with the Track-Trigger, the full collection of tracks can be accessed by HLT for every event and used even if Level-1 did not need to for all triggers to achieve rate reduction
    Like FTK for ATLAS trigger
Particle Flow
  As mentioned, maximally combining tracking with calorimetry greatly improves performance of jet and energy sum triggers
  Likely that HLT would be much closer to offline performance than what could be possibly achieved at Level-1
More on DAQ in R.Mommsen report

## Slide 26: Milestones for Phase-2 Trigger
Demonstrators in 4 years

## Slide 27: Trigger Electronics R&D Directions, 1
I/O bandwidth and system/PCB design
  Electronic systems designed to handle O(50) Tbps input
  High bandwidth optical data links at O(25) Gbps
  High bandwidth backplane communication
Logic implementation
  Ultrascale FPGAs
    And associated high-level synthesis tools to improve productivity
  Associative Memory ASIC, 3D technology for high density
Large, fast memory access
  Access to >GB memory near logic resources for quick, complex calculations via large lookup table (PT assignment in tracking triggers)

## Slide 28: Trigger Electronics R&D Directions, 2
Electronic controls
  Clock and trigger control signal distribution to systems
  On-board processors (e.g. Xilinx ZYNC) for board control and monitoring
Platform technologies
  Evaluate platforms for backplane bandwidth, card real estate, power density …
  xTCA? (Telecommunications Architecture)
    CMS Phase-1 upgrade electronics are based on μTCA standard
    Advanced TCA for some Phase 2 implementations?
Note: important to maintain ties with industry as well as ECE colleagues at universities on technology and tool developments

## Slide 29: Summary
CMS has an ambitious but achievable program to upgrade its detectors and the Level-1 Trigger electronics for HL-LHC
  For the Level-1 (HLT) Trigger, the goal is to maintain sensitivity for electroweak and TeV scale physics with rate < 750 (7.5) kHz and 12.5 μs latency
  Bring more of what was done at HLT to the Level-1 Trigger
Initial algorithms demonstrate meeting goal, but much more R&D required for implemented algorithms and system design
  Likely performance can improve further (e.g. particle flow at Leve-1)
Many Level-1 trigger subsystems will absorb many tens of Tbps data input
  Order of magnitude higher than current Phase-1 upgrade
Trigger logic similarly expands by a large factor
  e.g. tracking logic for the silicon detector trigger
Need to achieve this during the next decade within roughly the same budget and overall system size as for the current Level-1 trigger system