## Slide 1: VDT-DCache
Neha Sharma
OSG Storage Forum
June 30 – July 1’2009
Fermi National Accelerator Laboratory
Work supported by the U.S. Department of Energy under contract No. DE-AC02-07CH11359

## Slide 2: Focus
Changes in dCache Configuration/installation procedure in the VDT-dCache package
* New Tools available
dCache Info Service
OSG Community Toolkit
Core dCache Operations RPM
dCache Chronicle RPM

## Slide 3: Installation Process Old New
Download the tarball
Untar it
Read README/UPGRADE
file
Configure your dCache SE
Run site configuration script
./config-node.pl
This creates site-info.def file
Run the install script
./install.sh
Download the tarball
Untar it
Read README/UPGRADE
file
Configure your dCache SE
Populate various key/value pairs in siteinfo.conf
Run the install script
./install.sh
http://vdt.cs.wisc.edu/software/dcache/server/

## Slide 4: Configuration
siteinfo.conf (VDT_INSTALL_DIR/install)
Example:
# +++++++++++++++++++++++++++++++++++++++++++
# SECTION 1 - Some General Stuff
# You must fill in all values in this section
# +++++++++++++++++++++++++++++++++++++++++++
# File System Domain
# Example: fnal.gov
MY_DOMAIN=“fnal.gov”
# Would you like java to be installed by the dcache install script?
# Options: yes or no
INSTALL_JDK=“yes”
# Would you like to install/use Gratia dCache storage and transfer probes?
# Options: yes or no
INSTALL_DCACHE_GRATIA_PROBES=“yes”

## Slide 5
# ++++++++++++++++++++++++++++++++++++++++++++++++++++++++
# Section 2 -dCache Nodes Configuration
# You need to specify Fully Qualified Host Names. example - gwdca04.fnal.gov
# ++++++++++++++++++++++++++++++++++++++++++++++++++++++++
#Recommended distribution of services based on number of non-pool nodes
… (for 2,3,4 and >=5 number of nodes)
# It's mandatory that you specify these
# dCache Admin node
DCACHE_ADMIN=“fgt5x5.fnal.gov”
# dCache SRM node
DCACHE_DOOR_SRM=“fgt5x5.fnal.gov”
# dCache node running gPlazma
DCACHE_GPLAZMA=“fgt5x5.fnal.gov”

## Slide 6
# +++++++++++++++++++++++++++++++++++++++++++++++++++++++++
# SECTION 3 - Gratia dCache storage and transfer probes
# Skip this section, if you do not want to use these probes
# +++++++++++++++++++++++++++++++++++++++++++++++++++++++++
# Name of the storage element
# Example: FNAL_Gridworks
GRATIA_SITE_NAME=“TEST”
# Name of the grid to which this Storage Element belongs
# Options: OSG-ITB or OSG or LOCAL
GRATIA_GRID_NAME=“”
# Port used to connect to dCache Admin Interface
# Most Probably: 22223
GRATIA_ADMINSRV_PORT=“”
# Login name to connect to dCache Admin Interface
# Most Probably: admin
GRATIA_ADMINSRV_LOGIN=“”

## Slide 7
# Password to connect to dCache Admin Interface
# Default: dickerelch
GRATIA_ADMINSRV_PASSWORD=“dickerelch”
# Would you like to send notification emails about Gratia probes
# Options: yes or no
GRATIA_SEND_EMAIL=“yes”
# SKIP, if you chose 'no' to question above
# Mail server that should be used to send emails
# Example: smtp.fnal.gov
GRATIA_EMAIL_SRVHOST=“smtp.fnal.gov”
# SKIP, if you chose 'no' to question above
# Sender's name under which you would like the emails to be sent
GRATIA_EMAIL_FROM=“GratiaProbe”

## Slide 8
# SKIP, if you chose 'no' to question above
# Single email address or a comma separated list of email addresses
# to which you would like to send email. Skip, if you chose 'no' above
GRATIA_EMAIL_TO=“neha@fnal.gov,tlevshin@fnal.gov”

## Slide 9
#+++++++++++++++++++++++++++++++++++++++++++++++++++++++
# Section 4 - "Core dCache Operations" and "dCache Chronicle" Utilities
# Skip, if you do not care what these are or what they do
#+++++++++++++++++++++++++++++++++++++++++++++++++++++++
# Detailed Description of RPMS
…
# Core dCache Operations RPM
# Would you like to install/use this rpm?
# Options: yes or no
INSTALL_CORE_DCACHE_OPERATIONS_RPM=“no”
# dCache Chronicle RPM JYTHON, PNFS mounted
INSTALL_DCACHE_CHRONICLE_RPM=“no”
Needs
Needs

## Slide 10: Installation
[root@fgt5x5 install]# ./install.py -h
++++++++++++++++++++++++++++++++++++++++++++++++++++++++
+ This is the vdt-dcache installation script.It takes as +
+ input the siteinfo.conf file and installs software such +
+ as Postgres, PNFS, dCache, Gratia Probes etc. This +
+ script must be run as root, on each dCache node. +
Usage:
install.sh [-h] [-d]
where:
-d, --dryrun
Print what will be done, but don't run any commands
-h, --help
Print the help message
++++++++++++++++++++++++++++++++++++++++++++++++++++++++

## Slide 11: Upgrade….is simple 
Edit the existing “siteinfo.conf” file, if any new site customizations are required (If not, then no need to do anything)
Run installation script

## Slide 12: Why the change?
the interactive site configuration script was getting very unorganized as new software was added
common configuration approach in OSG
no extra overload on users – for fresh install or upgrade process (we are working on porting of old configuration file to new one)

## Slide 13: dCache Info Service
“A robust, best-effort, one-stop shop overview of the current status of a dCache instance for external consumption.
–Robust: the info service will continue to work independently of the rest of dCache.
–Best-effort: there may be delays in information being updated (1 minute order-of-magnitude).
–One-stop shop: you should be able to get all the information you require.” Paul Millar @ DESY
Relevant Parameter in siteinfo.conf file:
# dCache node running the Info Provider Service
DCACHE_INFO_PROVIDER="fgt5x5.fnal.gov” (an example)

## Slide 14
Information about entities such as pools, poolgroups, doors, domains, reservations etc.
Information may be obtained
  in raw xml format using wget http://{ADMINNODE}:2288/info
  through the admin interface etc.
More Information
http://www.dcache.org/manuals/dCache info-20080813.pdf

## Slide 15: OSG Community Toolkit
Core dCache Operation RPM
dCache Chronicle RPM
…Details in Abhishek’s Talk to follow

## Slide 16: New Release
Will contain dCache server 1.9.3 rpm
In testing phase at the moment