## Slide 1: CLIC Machine Detector Interface
D. Schulte

## Slide 2: Introduction
Machine detector interface issues have been studied for the 2003 CLIC Physics Report
  parameters have changed since but are relatively close today
  Conclusion are basically still valid
  But need refinement of studies
A new linear collider detector working group has been formed
  In collaboration with the beam physics has made and will verify a number of design choices
    Luminosity spectrum
    Crossing angle
    Solenoid field and configuration
    Beam pipe size
    Forward region design
Also a machine detector working group has been created to deal with technical issues
  QD0 magnet design, stabilisation and integration
  Push-pull scheme, detector infrastructure and many other items

## Slide 3: Background
A number of background sources exist
  From the machine
    Synchrotron radiation
    Muons
  From the beam collision
    Beamstrahlung
    Coherent pair production
    Incoherent pair production
    Hadronic events
  From the spent beams
    Backscattered pairs
    Neutrons
    …

## Slide 4: Luminosity Spectrum
Can be reduced for some luminosity loss

## Slide 5: Z’ and Luminosity Spectrum
For cross section rise use of peak luminosity is reasonable approximation
O. Cakir

## Slide 6: Spent Beam Content

## Slide 7: Spent Beam Angles
Conclude that crossing angle should be more than 20mradian

## Slide 8: Solenoid Effects
Weak focusing: in the two transverse planes
Orbit deviation: the beam is bent as it traverses the magnetic field
Coupling between x-y plane: the particle position in one plane depends on the position in the other plane
Dispersion: particles at lower energies experience a larger deflection than those at higher energies
The beam emits Incoherent Synchrotron Radiation (ISR) as it is deflected
Schematic view of the two beam colliding with a crossing angle in the detector solenoid.
θc/2
B. Dalena

## Slide 9
Compensating Solenoid
“Anti-solenoids” (bucking coils covering QD0), cancelling the main solenoid magnetic field component in QD0, and reduces offset at IP (z=s=0).
QD0
QD0
solenoid
reference system
beamline reference system
B. Dalena et al.

## Slide 10
Vertical Dispersion and <x’,y> Coupling
< x’,y > coupling and
vertical dispersion at IP
Tracking trough FFs and IP Solenoid
Tracking trough FFs and IP Solenoid + anti-solenoids covering QD0
Tracking trough FFs only
Residual <x’,y> coupling and dispersion can be compensated using the other FFs magnets
a
b
c

## Slide 11
Incoherent Synchrotron Radiation
Full beam tracking from linac entrance to IP (PLACET)
Beam-beam simulations (GUINEA-PIG)
Map | Bz [T] | L[m] | Lumi loss [%]
Old SiD | 5 | 2.8 | ~4.0
New SiD | 5 | 2.8 | ~3.0
ILD | 4 | 3.7 | ~4.0
ILD + AntiDiD | 4 | 3.7 | ~25.0
Conclude that crossing angle should be no more than 20mradian
No antiDiD
B. Dalena et al.

## Slide 12: Incoherent Pair Creation

## Slide 13: Deflection by the Beams

## Slide 14: Aperture Requirements

## Slide 15
Impact on Vertex Detector
Simplified study using simple cylinder without mass
  Coverage is down to 200 mrad
Simulating number of particles that hit at least once
  Experience indicates that number of hits is three per particle
At r1  30 mm expect 1 hit per train and mm2
z=r

## Slide 16: Hit Distribution and Vertex Detector Radius
GEANT 3 based simulation
Angular coverage z/r = 3, 5 and Bz = 5 T
 hit density does not depend on coverage angle if the radius is large enough to avoid deflected particles
Angular coverage z/r = 5 and Bz = 3, 5 T
 vertex radius for constant hit density scale as:


## Slide 17
CLIC_ILD Detector Concept: Forward Region
Version 3 Nov. 2009
ECal end-cap
HCal end-cap
Yoke end-cap (partial)
LumiCal
BeamCal
QD0 (partial)
Andre Sailer

## Slide 18
Courtesy M.Battaglia and A.Sailer
Direct
pairs
Backscattered + direct pairs
Backscattered
pairs (not read)

## Slide 19: Hadronic Background

## Slide 20: Hadronic Background (cont.)
Jean-Jacques Blaising
Data base with hadronic events available
Hadronic background is very much peaked in the forward and backward direction
collision of one soft and one hard photon
Adds to background
adds 25% of hits in vertex detector
tracks overlayed with events
D. S. et al.

## Slide 21: Hadronic Background and Time Stamping
Simulation example of heavy Higgs doublet H0A0 at ~1.1 TeV mass (supersymmetry K’ point)
e+e-  H0A0  bbbb
Signal + full standard model background + γγ=>hadron background
CLIC-ILD detector: Mokka+Marlin simulation, reconstruction + kinematic fit.
Zero bunch crossings
MA mass resol. 3.8 GeV
20 bunch crossings
MA mass resol. 5.6 GeV
40 bunch crossings
MA mass resol. 8.2 GeV
Marco Battaglia

## Slide 22: MDI Working Group Priorities
Highest priority for the work until end 2010 are those subjects linked to the “CLIC critical feasibility items”, nota bene:
  Choice of the magnet technology for the FF magnets
  Integration of these magnets into the detectors, and their alignment
  Feasibility study of sub-nm active stabilization of these magnets
  Luminosity instrumentation
  Spent beam disposal
  Beam background backsplash from the post-collision collimators and dumps into the detector
  Intrapulse-Beam feedback systems in the interface region
22
L. Gatignon et al.

## Slide 23: Other Items to be Addressed in MDI:
Issues where the beam delivery system (BDS) influences the beam/background conditions for the detector
Issues where the BDS physically impacts on the detector
Beam background and its impact on the forward (det.+accel.) elements, including backsplash of background particles from one hardware element to the surrounding elements
Beam pipe, beam vacuum and vacuum infrastructure in the interface region
Radiation environment and radiation shielding in the interface region
Cryogenic operational safety issues in the interface region
Magnetic environment in the interface region (shielding of FF quadrupole, correction coils, anti(-DID), stray fields from the detector, etc.)
Overall mechanical integration (including the routing of services) in the interface region
Pull-push elements and scenarios (detector-to-detector interface)
Cavern layout and services (handled principally under CES WG)
23
From the CLIC MDI working group mandate

## Slide 26: QD0 Design
Magnet design needs to allow for spent beam extraction
Hybrid design is tunable by 10-20%
Can achieve the required field strength
M. Modena et al.

## Slide 27
QD0 Integration Concept: First Ideas
Courtesy A.Hervé

## Slide 28: Quadrupole Support Garage Position
Yoke + muon det.
HCAL + ECAL end-cap
QD0
“plugs”
K. Elsener

## Slide 29
Support Table
Support Tube
Support
QD0 Coils
(independent of yoke)
Cooling pipes with laminar flow
A. Herve
A. Herve

## Slide 30: Achieved Performance
CERN TMC active table for isolation
The two first resonances entirely rejected
Achieved integrated rms of 0.13nm at 5Hz
LAPP active system for resonance rejection
L.Brunetti et al (EPAC/Genova 2008)

## Slide 31: Current Work
Replace big stabilisation table by a compact passive+active stabilisation system
Instrumentation study (sensors and actuators)
Active system
Passive system
Courtesy A.Jeremie

## Slide 32: Current Work
Ex : force (actuator) applied to a point
Feedback development
Simulations
Different strategies studied:
A knowledge only at strategic points
A local model for the disturbances amplified by eigenfrequencies.
A complete model
Evgeny Solodko
FF magnet design
Courtesy A.Jeremie

## Slide 33
Cavern Layout
Courtesy J.Osborne
Based on ILC design

## Slide 34
A. Hervé – H. Gerwig – A. Gaddi / CERN
Cavern Layout

## Slide 35
Detector moving
Air-pads at CMS – move 2000T
Concept of the platform, A.Herve, H.Gerwig
J.Amann

## Slide 36
Summary and Conclusions
Basic choices have been made for the MDI
  crossing angle
  forward region openings
  vertex detector radius
  position of first quadrupole
  time stamping
They will be critically reviewed based on detailed technical work
Items that will be addressed include
  QD0
  QD0 integration and stabilisation
  Solenoid and anti-solenoids
  Intra-pulse feedback
  Backgrounds
  Vacuum
  Civil engeneering and infrastructure

## Slide 37: CLIC Forward Region Detectors
    Maintain very forward calorimetry functionalities, adapt to accelerator requirements (stability!), minimise back-scattering of background