## Slide 1: RCS design
Valeri Lebedev
AAC Meeting
November 16-17, 2009

## Slide 2: Outline
Objectives for RCS design
Logic behind parameter choices
Technical description

## Slide 3: Objectives & Challenges
Objectives
  Beam acceleration from 2 to 8 GeV
  Support
    2 MW in MI at 60 to 120 GeV (140 – 280 kW)
    8 GeV program with fast extracted beam (≥100 kW)
  Look for a solution being less expensive than pulsed SC linac
  Look into possible future upgrades
Challenges
  Beam current is ~5 times of Booster  Space charge, instabilities, RF, ep
Booster problems to be avoided
  No transition crossing
  No laminations seen by beam  smaller Z||, Z
  Zero Disp. in cavities  No SB resonance

## Slide 4: RCS Design Choices
Circumference, C = CMI/6
  6 injections to fill MI
High periodicity FODO
Racetrack
  Two long straights
  Dispersion zeroing with missed dipole
Acceptance matches MI acceptance
  10% allowance for e growth
2 harmonics RF system
  Space charge mitigation
  Beam stability
High injection energy helps with Space Charge and Instabilities
  Small size of vacuum chamber
† KV-like distribution, BF=2.2
Energy, min/max, GeV | 2/8
Repetition rate, Hz | 10
Circumference, m (MI/6) | 553.2
Tunes | 18.43
Transition energy, GeV | 13.36
Beam current at injection, A | 2.2
Harmonic number | 98
Max. RF voltage, (V98/V196) MV | 1.6/0.7
95% n. emittance, mm mrad | 22
Space charge tune shift, inj. | 0.07†
Norm. acceptance, mm mrad | 40
Injection time for 1 mA, ms | 4.3
Linac energy cor. at inject. | 1.2%
RF bucket size, eV s | 0.38

## Slide 5: Optics
b-functions are blown-up in injection region – reduction of foil heating
  6 half cells are used for injection region
Two types of quadrupoles with the same integral strength
  Large aperture quads for injection & extraction
Twiss parameters for the first half of the ring

## Slide 6: Optics (continue)
Straight line assignments
  Injection, extraction, scraping
  RF
Vacuum chamber radius, a = 21.3 mm (internal)
  7 mm allowance for orbit correction
Beam envelopes; acceptance - en=40 mm mrad, Ek = 2 GeV, Dp/p = 5 x 10-3.

## Slide 7: Vacuum Chamber
Competing effects are
  Shielding and distortion of dipole bending field by eddy currents excited in the vacuum chamber
  Vacuum chamber stability under atmospheric pressure
  Vacuum chamber heating by eddy currents
  Transverse impedance due to wall resistivity
  Ring acceptance
The compromise resulted in
  Round stainless steel vacuum chamber with radius of a=22 mm and wall thickness of d = 0.7 mm
  Inside quads of injection and extraction regions: a=43 mm d = 1 mm
  No limitations on the chamber thickness outside dipoles and quads
Ring acceptances and beam emittance:
  85 mm mrad - limited by vacuum chamber size
  40 mm mrad – limited by scrapers
  22 mm mrad – 95% norm. beam emittance

## Slide 8: Limitations on Vacuum Chamber Design
Shielding and distortion of the dipole bending field by eddy currents excited in the vacuum chamber
  Dipoles: |DB/B|max=8.5 x 10-4 @16 ms
  Quads – approximately half of the dipole effect
  Delayed quad wave form by ~70 ms
Vacuum chamber stability under atmospheric pressure
  Compression: 3.1 N/mm2
  Bend for Da/a=0.02: 8.9 N/mm2
  Yield stress : 200 N/mm2
Vacuum chamber heating by eddy currents (~a3)
  dP/dz=10 W/m
  DT=15 K for convective air cooling with heat transfer of 10-3 W/cm2/K

## Slide 9: Vacuum Chamber Impedance
Transverse impedance due to wall resistivity (~a-3)
  Z and dP/dz are related inversely proportional
    No dependence on vacuum chamber parameters

## Slide 10: Dipoles
Small aperture  Compact dipole
Sagitta – 1.7 cm

## Slide 11: Quadrupoles
Large and small quads have the same field integral
Large quads
  4 in injection region
  4 in extraction region

## Slide 12: Resonance Driving of Dipoles and Quads
Dipoles and quads of each cell have a resonance circuit compensating their inductive impedance
  50 standard + 2 special cells (one for each straight line)
    each is tuned to 10 Hz
  Total power ~1.5 MW
  Maximum voltage to ground 600 V
Similar to the Booster

## Slide 13: Beam Acceleration

## Slide 14: RF System
Dual Harmonic RF system,
  At injection V2=0.5 V1
10 Bunches extraction gap
  Set by required length of MI extraction gap
Beam loading is serious issue
  1.6 MV beam induced voltage (at resonance)
Longitudinal emittance is blown up to ~0.6 eV s to match to MI RF bucket
  Can be excited by quadrupole damper (same as in Booster)

## Slide 15: Injection-Extraction Straight
Doublet focusing for injection straight
  It takes space of 6 FODO half cells
Increased aperture for 8 quads
  4 in injection
  4 in extraction

## Slide 16: Injection
Strip injection through 600 mg/cm2 graphite foil
Small linac current (1 mA)  2200 turn injection (11 for Booster, 1000 for SNS)
B2 – small field to avoid H- stripping (2 kG)
B3 – Large field to strip H- to H0 (-8.3 kG)
Stripped electrons carry ~100 W beam power and have to be directed to the electron dump

## Slide 17: Transverse Painting
Transverse painting objectives
  Paint K-V like distribution
  Minimize number of secondary passages through foil
Major parameters
  Linac emittance – 0.5 mm mrad (rms, norm.)
  RCS beam emittance – 22 mm mrad (95%, norm.)
  Linac a- and b- functions are 0.345 of RCS ones
X-Y painting by CO displacement
  Closed 4 corrector bumps in each plane
    Independent control for X & q on foil

## Slide 18: Simulation Results for Transverse Painting
Final distribution is close to the KV-distribution
50 secondary passages per particle
  2.2 mm-2 per particle
420 mg/cm2 foil is tilted by 45 deg. to increase cooling due to black body radiation
  Tmax = 1500 K
  d-electrons remove ~25% of heating

## Slide 19: Injection Loss
Total injection loss ~4%
  ~2% miss the foil
  ~0.5% are not completely stripped in the foil
  0.15% are single scattered in the foil
  ~1% are outside of 40 mm mrad RCS acceptance
In normal operating conditions it results in the heat load
  injection beam dump ~3 kW
  collimation system ~1.5 kW
Prudent design (confirmed by SNS experience) would have both the injection waste beam absorber and the collimation system designed to handle 10% or 8.5 kW

## Slide 20: Injection Dump
Injection dump is located in the tunnel
It requires considerable radiation shielding

## Slide 21: Longitudinal Painting
Longitudinal painting is performed by momentum offset of linac beam
  sp=5·10-4,
  Dp/p=7·10-4,
  Tinj=14.6 ns (73%)
Additionally, Linac has to compensate the RCS energy variation during injection (4.3 ms)
  DE/E =1.2%
 Bunching factor = 2.2

## Slide 22: Extraction
Two kickers of 2.3 mrad each (±25kV, filling time 90 ns)
Quads displacements make vertical closed bump
  Q11 = -4.8 mm, Q12 = -6.39 mm, Q14 = 9.84 mm

## Slide 23: RCS versus Pulsed Linac
RCS
  Less expensive
  Injection at smaller energy  Easier to manage injection loss
  Limited upgrade potential
    Up to ~1 MW @15 Hz & 2-3 ns (MC) feasible with increased acceptance
Linac
  Easier to upgrade
    to 4 MW power proton driver for MC
    + to ~20 GeV recirculator for neutrino factory
  Many injections per cycle if foil strip-injection is used (10 Hz)
    Requires Recycler  8 GeV final energy
  An upgrade will require beam current increase: 1  ≥20 mA 2 GeV program discontinue or building another 2 GeV frontend!!!

## Slide 24: Conclusions
RCS looks as a good choice to accelerate from 2 to 8 GeV
  Less expensive than pulsed SC linac
    ~287 M$ versus ~355 M$ (no escalations)
It has considerable upgrade potential but cannot meet 4 MW required by Muon Collider
Choice between RCS and Pulsed linac need to be done. It will be driven by
  Cost & Upgradability

## Slide 25: Backup Viewgraphs

## Slide 26: Vacuum
Vacuum chamber
  10-7 Torr or better (beam loss, ep instabolity)
    No baking
  Secondary emission suppression (TiN or carbon film)

## Slide 27: Optics and Orbit Correction
Corrector pack near each quad: S and D coils
  Dipole corrector near each quad (h – F, v – D)
    4 fast correctors in each plane for injection painting
  Two families of sextupoles
    Partial chromaticity correction: from -25 to -(10 ÷ 15 )
    No dynamic aperture limitation
Optics correction
  Additional coils in all quads for optics correction
  F and D families (±0.25 tune correction ) (∫GdL=1.1 kG) + 36 separate optics correction quads (∫GdL=2.2 kG)
  12 Skew-quads (coupling & vertical dispersion)

## Slide 28: Optics Cell

## Slide 29: Collimation and Instrumentation
Collimators
  Two stage
  Located in the injection-extraction straight line
    Positioning in the other line is also discussed
      Choice is determined by loss scenario
Instrumentation
  Standard set of FNAL instrumentation (BPMs, BLMs, … )
  Instrumentation for the injection region
    Will be based on SNS experience

## Slide 30: Stripping on Carbon Foil