## Slide 1: Review of Jan’10 High Pressurizing Hydrogen gas filled RF cavity run and Status of beam test
K. Yonehara
APC, Fermilab
Muons, Inc.

## Slide 2: Goal of HPRF project
Study hydrogen plasma physics
Demonstrate High Pressure RF cavity under high radiation condition
Investigate RF breakdown from different aspect

## Slide 3: New optical system for Jan10 run
Gap = 3 cm
PMT
Trigger
We have higher intensity trigger light than in
previous measurement

## Slide 4: Improvement from previous test
Isolate trigger light from spectrometer light
  More spectroscopic light (factor 3)
Put trigger fiber near plasma region
  Expect more sensitivity
Debug averaging measurement method with digital oscilloscope
  Found this debug during the test
  Occasionally DAQ was triggered by second peak of optical trigger signal
  It was solved by setting DAQ timing window properly

## Slide 5: HPRF spectrum
540 psi (gas BD)
930 psi (gas BD)
1500 psi (metallic BD)
1310 psi (metallic BD)
1120 psi (metallic BD)
Calibrated by PMT response for wavelength
Intensity = Integrated spectrum signal/Integrated trig signal
H-α (656 nm)
H-β (486 nm)
Cu lines (510 ~ 525 nm)
Neutral Cu line (~325 nm)

## Slide 6: Summary in spectroscopic measurement
Clearly see H-α and H-β lines
Trigger PMT works and increase spectrometer light intensity (× 3)
Pressure dependent broadband background
Background level seems to be saturated at metallic breakdown region
We do not see clear Cu lines

## Slide 7: Precursor light in Trigger PMT
Spectrometer PMT (λ=656 nm)
Trigger PMT (take white light)
Magnetic field pick up coil
Breakdown!
Trigger PMT starts detecting
some light before breakdown
This is first time we captured
precursor light
Trigger PMT locates closer to
hydrogen plasma region
We have higher light intensity
than before
Spectrometer PMT has slow
response because of low
light intensity

## Slide 8: Preparation for beam test
Collimator design
  Start making engineering drawing
Diagnostic system
  Search available beam profile monitor by using luminescence screen
Circulator
  Will be delivered around end of April
DAQ & trigger system
  Trigger signal from Linac RF to synchronize Klystron
  Beam trigger byBPM
Hydrogen & Radiation Safety
  Wait output from radiation safety committee
  Obtain permission from DoE