CC p0 Analysis
J. Català (IFIC - U. Valencia/CSIC)
SciBooNE Collaboration Meeting - 2010-05-25

---
Outline:
- Event sample selection.
  - Reminder of gamma candidates selection.
- Reconstructed particles plots.
- CCPi0/CCinc x-section ratio.

---
Event sample selection
- Framework filters applied to Reconstruction:
  - MRDMatchFilter (CC definition filter).
  --- 2nd reconstruction ---
  - MuonMultiplicityFilter: 1 and only 1 muon in the event.
  - TrackOnMuonTime: non-muon tracks in 20 ns around muon time.
---ExtendedTacks---
  - EndPointFilter:	+-135 cm for XY, 10-171 for Z
  - MuCL:	>0.005
  - Disconnection:	>12cm
  - EC cluster energy in view 0 >= 15MeV
---MakeGammaCandidates---
  - >=2 GammaCandidates
---MakPi0Candidates---
- 1 Pi0Candidate
- GammaOpeningCosine < .96
Combined to reject tracks, not events

---
EndPointFilter
EndPoint of the track is always considered the farther edge from the event vertex (InitEdge of the muon), no matter the ‘real’ direction of the track.
EndPoint filter set at (-135, 135) cm for XY (10 cm from the edge of SciBar) and (10, 171) for Z.
SciBar contained even is not accurate given that it is allowed for the tracks to exit SciBar in the downstream direction.
Red track will be rejected even if it’s an in-coming track (from DIRT, for instance).
Magenta and green tracks will be accepted, cause they exit from the downstream edge of SciBar, towards the EC.

---
GammaCandidates
b) type GC.
a) type GC.
c) type GC.
GammaCandidate can be made from
a) 1 SciBar extended track;
b) 1 SciBar extended track + associated clusters;
c) set of clusters without a SciBar associated track.
The 2 GC sample contains mostly events with 3, 4 and 5 extended tracks
For type a) and b), Gamma edges and direction are taken from the SciBar Track.
MuCL rejection: scibar tracks with MuCL < 0.005 are not GammaCandidates.
SciBar tracks with distance to vertex <12 cm are not GammaCandidates.
Tracks leaking out from SciBar in any direction but the EC are also rejected
In gamma candidate type c) only unmatched clusters are considered.
At the current status, type c) are only made when only exists one non-matched cluster per view.
Event vertex (muon init edge) is taken as init edge of the gamma and the cluster possition defines the end edge.
Cluster energy >= 15MeV in view 0.

---
Gamma candidates Type c)
NEW
Other trks
Photon trks
Primary photon
Cluster energy per view for GC type c) (gamma conversion in EC).
Create a GC Type c) if exists only one free cluster per view.
Require 15 MeV minimum energy in the clusters in view 0 to consider it for a gamma candidate.
Need to think how to manage events with more than one free cluster per view.
Other trks
Photon trks
Primary photon

---
GammaOpeningAngle
GammaCandidates coming from the same photon have very small opening angle between them. We can remove the low-mass tail by cutting on the GammaOpeningAngle.
2 goodreco photons
2 good photons from the same true gamma
1 goodreco photon
0 goodreco photons
Before cut
Accept
After cut
Cut set at gamma_opening_cos <.96 using Eff*Pur maximization.
Plots of the signal contribution in terms of reco goodness.

---
Signal definition change
Found events that reaches the limit of the MC stored information, set at 200 MCparticles.
If the limit is reached, no other particle truth information is stored in the event whilst all the tracking and energy depositions are correct for all particles.
Given the high track multiplicity and the presence of EM showers in my selected events, turns out that a large amount of such events reaches the limit of 200 MCparticles.
My previous signal definition implied the existence of a muon and a pi0 in DetSimParticle list with the initial position coinciding with the DetSimVertex position. And sometimes the info of those particles is not stored because the limit.
As a workaround, I’m using in the following plots and tables the MC information at a generator level, defining my signal as a muon and a neutral pion staying alive at the end of the NEUT processing.
In previous meetings I’ve presented the plots with the background divided on background that contains pi0’s and background without pi0’s. In the following, the background is everything is not signal, and includes events with secondary pi0’s.
Only way to fully correct it is to re-process the MC (central value detector simulation + framework jobs) removing the limit.

---
Cut summary table:
Slight CCPi0 data deficit alleviated by using POT normalization for MC rather than mrdmatch normalization.

---
Plot approval:
- I propose the following particle reconstruction plots for approval (Slides 11 to 14).
  - The analysis has improved significantly, almost doubling the statistics.
  - After the correction of the MC issue I expect minor changes if any on the cuts
    - may change the signal/bkg contents, but not the DATA points and not the MC shape/total normalization.

---
Muon reconstruction
MRDmatch normalized
Small DIRT background contribution. MRDEC and COSMIC backgrounds barely visible.
Momentum bump at 1.2GeV due to muons escaping from MRD.
DATA/MC deficit concentrated in forward muon direction.
Shape agreement for muon momentum and vertex position distributions.
DATA
Signal
SB Bkg
DIRT
MRDEC
COSMIC

---
Photon reconstruction
MRDmatch normalized
148 MeV mean photon energy
True - Reco energy for correctly matched photons: 76 MeV (152 RMS)
Notice photon high purity because photons are found also in background events.
SCIBAR only
SCIBAR+EC
EC only
In addition to gamma candidates in scibar only and scibar+ec, i’m also adding gamma candidates in EC only.
Other trks
Photon trks (Scibar + EC)
Photon trks
(no leakage)

---
Pi0 reconstruction
MRDmatch normalized
Events with small opening angle between gammas are rejected. Use to be the same photon reconstructed as 2GC.
Pi0 produced mostly forward and at all angles.
DATA
Signal
SB Bkg
DIRT
MRDEC
COSMIC
Accept
DATA
Signal
SB Bkg
DIRT
MRDEC
COSMIC
Good agreement between DATA and MC.

---
Pi0 reconstruction
MRDmatch normalized
Good agreement in shape for the reconstructed quantities.
DATA
Signal
SB Bkg
DIRT
MRDEC
COSMIC
DATA
Signal
SB Bkg
DIRT
MRDEC
COSMIC
Visible peak near pi0 mass in the reconstructed invariant mass plot.
Notice that the background also peaks near pi0 mass. This is caused by secondary Pi0’s.

---
CCPi0/CCinc x-section ratio
{%sigma_{CC-%pi^0}} over {%sigma_{CC-inc}}={{ N_{CC-%pi^0 (DATA)}-N_{CC-%pi^0(normalized backgrounds)} }over{%varepsilon_{CC-%pi^0(signal)}}}over{{N_{CC-inc (DATA)}-N_{CC-inc (normalized backgrounds)}}over{%varepsilon_{CC-inc(signal)}}}
CCPi0/CCinc x-section ratio using mrdmatch normalization for the background subtraction:
0.053±0.008(stat.)
CCPi0/CCinc x-section ratio using POT normalization for the background subtraction:
0.060±0.008(stat.)
To compare with TrueMC x-sec ratio:
#CCpi0 events/#CCinc events=0.083

---
Summary
With respect to previous collaboration meeting
Track based event selection now mature.
New cut to reject poorly reconstructed signal events.
Added ECMRD and COSMIC backgrounds.
Clear signal found in data, good agreement with MC in all kinematic distributions except for forward muons. Causing an overall DATA/MC deficit.
Ratio of CCpi0/CCinc cross section measured using mrdmatch normalization for background subtraction
CCPi0/CCinc=0.053±0.008(stat.)
to be compared with a MC expectation of 0.083
Bug found in storing MC particle truth information in Detector Simulation. Will require new MC production to handle properly.

---
Looking forward
Perform a new MC production and see how it affects my analysis.
Try to verify with DATA
Background estimation for CC pi0 sample.
Signal efficiency estimation for CCpi0 sample.
Compare results with past experiments (ANL, BNL, K2K, etc).
Deal with events that contains more than one Pi0Candidate.

---
Backup Slides

---
sbtcat
The T in sbtcat comes from applying sbcat in the transversal direction in order to be able to reconstruct high angle tracks.
The main idea is to switch layers and channels in the sbcat. That means that the clusters will be constructed in the Z direction (in channel lines) and will be connected in X (Y). That should allow us to reconstruct large angle tracks.
Cluster
Cluster
Z
X

---
2nd reconstruction: sbcat + sbtcat
In order to increase the number of multi-track events, particularily the >= 3 track events, I’ve been developing and applying a ‘2nd reconstruction’.
2nd reconstruction consists in to run sequentially sbcat and sbtcat over the MRDMatched events. The way to implement it is to seek for hits that has not been used for the 3DTrack reconstruction in the default processing and run sbcat again using only such hits. Then, we look for hits still not being used for the 3DTracks from the default reconstruction nor for the 2DTracks in the 2nd sbcat processing. And then we run sbtcat over them.
Eventually, the 2nd sbcat will produce one or more new projections, and also sbtcat if there are more unused hits. We run again Match2DTracks over the new created projections in order to get new 3DTracks that comes from projections created either by 2nd sbcat run or sbtcat.
Default reco
2nd processing

---
EndPointFilter
- Is a containment requirement that uses the EndEdge of the track to reject particles scaping from a given FiducialVolume SciBar.
  - All tracks are considered for the filter.
  - Filter not rejecting tracks heading the EC.
  - Helps to improve the energy reconstruction.
  Values for the FV are chosen in accordance of the ExtendedTrack radius (explained in the next slide).

---
EndPointFilter
All plots are SciBar-MC MRDmatch normalized
Set to assure containment and to remove DIRT events.
Init edge of the track is set to the closest edge to the event vertex (InitEdge of the muon).
Cut set at (-135, 135) cm for XY and (10, 171) for Z.

---
ExtendedTrack tuning parameters
- ExtendedTrack rcp have the following parameters:
  - Rcproj_lenght_threshold (parameter not changed)
  - Radius: distance from the track to look for hits to add to the track.
    Standard value 20cm, chosen value: 10 cm
  - Chi^2 max of the fit for the new extendedtrack.
    standard value 50, chosen value: 10
  - Time difference between tracks (not change observed)
  - MuCL (not significant change observed)
  - Pe threshold (not significant change observed)

---
Muon reconstruction
MRDmatch normalized
Muon bump at 1.2GeV due to muons
escaping the MRD.
DATA
Signal
Bkg
DIRT
MRDEC
COSMIC