## Slide 1: Discussion of HL-LHC Project
Eric Prebys
Fermilab APC
Program Director, LARP

## Slide 2: Object of discussion
As we summarize the HL-LHC project, we should discuss three things
  How LARP activities align with the HL-LHC structure
  How LARP activities could be modified to better align with the structure
  What opportunities (if any) does this present for bringing US resources to bear which are outside of LARP?

## Slide 3: New Project Structure at CERN
High Luminosity LHC Projects: L. Rossi
prepare for operation at 5 1034 cm-2 sec-1
prepare for integrated luminosity of 3000 fb-1
 Implementation by 2018 - 2020
LHC Injector Upgrade Project: R. Garoby
remove bottlenecks in the PS and SPS
investigate options for PSB upgrade (energy)
LHC Consolidation Project: S. Baird
have to consolidate existing injector complex for at least 15+ years
3
CM15, CA, November 2010
Linear Collider Project: Steinar Stapnes

## Slide 4: HL-LHC Planning
Upgrade planning will utilize EuCARD*,
  Centrally managed from CERN (Lucio Rossi)
  Non-CERN funds provided by EU
  Non-EU partners (KEK, LARP, etc) will be coordinated by EuCARD, but receive no money.
Work Packages:
  WP1: Management
  WP2: Beam Physics and Layout
  WP3: Magnet Design
  WP4: Crab Cavity Design
  WP5: Collimation and Beam Losses
  WP6: Machine Protection
  WP7: Machine/Experiment Interface
  WP8: Environment & Safety
*European Coordination for Accelerator R&D
Significant LARP and other US Involvement

## Slide 5: HL-LHC Work Package 2:
5
Tentative Task List:
1) Communication & management:
2) Optics & Layout:
  NbTi solutions with and without local CC; L*; round and flat beams; 2-in-1
  Nb3Sn solutions with and without local CC; L*; round and flat beams; 2-in-1
  Novel solutions for correction of chromatic aberrations (a la SF & PR)
  IR4 layout and solution with global CC
   magnet parameters (aperture and length)
3) Single particle studies and tools:
  DA studies and FQ specifications
  Correction strategy and corrector specifications
   magnet parameters (FQ and corrector elements)
CM15, CA, November 2010

## Slide 6: HL-LHC Work Package 2 Brainstorming
6
Tentative Task List:
4) Collective Effects:
  Impedance estimates for new layout (collimator and aperture dependent)
  IBS estimates for different beam configurations
   beam separation; optimum configuration (flat beams vs round beams)
5) Beam-Beam Effects:
  BB long range compensation schemes
  BB limit for round and flat beams and coupling tolerances for flat beams
  Head-on BB compensation schemes and options
6) Beam Parameters and Luminosity optimization:
  L reduction and leveling (CC and poor man leveling via x-ing angle)
  Evaluation of operation experience of first 2 year LHC operation
  Options for beam parameter variation for L optimization during run (e.g. Q)
   beam parameter set (en, Nb, ss etc.)
CM15, CA, November 2010

## Slide 7: LHC Injector Upgrade Project:
7
Areas for USLARP involvement:
Turn by turn profile monitor for PSB
Space charge studies for the PSB and PS
Wide bandwidth feedback system for the SPS
Impedance calculations and measurements
Instability studies and estimates
e-cloud mitigation
CM15, CA, November 2010

## Slide 8: WP3 (magnets) TASK LIST
  1. Communication and management
  2. Nb3Sn quadrupoles
  3. Separation dipoles
  4. Cooling
  5. Miscellaneous
LARP
APUL?

## Slide 9: TASK 2 – Nb3Sn quadrupoles
Task Objectives
  Analyze the performance of existing Nb3Sn models, in particular LARP HQ quadrupoles
  Conceptual design studies of a very large aperture option (150 mm)
  Finalize the requirements for the HL-LHC inner triplet Nb3Sn quadrupole
Task description
This task is intended to give a final assessment of the possibility of using Nb3Sn quadrupoles for the LHC inner triplet and the performance parameters that can be achieved. A tentative layout with a 120 mm aperture quadrupole is given from WP2, and the necessary full list of requirements (field quality, radiation resistance, integration in the machine) should be worked out. A comparison with the present performance of the 120 mm aperture short model (HQ) magnets of LARP should be done, and iterations on the design if needed should be carried out. In particular we plan to analyze the following issues: (i) radiation resistance of all components (ii) magnet field quality and the possibility to apply corrections using magnetic shims (iii) option of splitting the magnet into two coils, with a related estimate of the loss in performance, possibly complemented by a hardware test, (iv) design of a helium containment vessel compatible with a magnet structure based on aluminum shrinking cylinder (v) magnet protection).
This task will be mainly driven by LARP collaboration (BNL, FNAL and LBL). LASA will lead the quench protection study.

## Slide 10: TASK 2 – Nb3Sn quadrupoles
Deliverables
  M48 Report on design study of the Nb3Sn inner triplet
Milestones
  M12 Requirements for Nb3Sn inner triplet and comparison with present status of the art
  M24 Study of magnetic shimming in HQ
  M36 Study of minimal distance between two coils in a cold mass
Relation to other WP
  Inputs from WP2. Moreover, this task feeds directly back to WP2 (e.g. required space for eventual absorber inserts at regions with higher losses etc which have an impact on the detailed IR layout).
Task leader: G. Luca Sabbi

## Slide 11: TASK 3 – SEPARATION DIPOLES
Task Objectives
  Conceptual design of separation dipoles according to the specifications given by WP2 using either Nb3Al or Nb-Ti. If a model is built, specify and follow-up the tests needed for assessing the design.
  Explore the possibility of using separation dipoles to create doglegs to increase the beam separation, thus allowing the installation of non-compact crab cavities.

## Slide 12: TASK 3 – SEPARATION DIPOLES
Deliverables
  M48 Report on design study of the separation dipoles
Milestones
  M12 Requirements for separation dipoles
  M24 Conceptual design of Nb3Al and Nb-Ti separation dipoles
  M36 Conceptual design of a crab cavity dogleg
Relation to other WP
  Inputs from WP2 and WP4. The task results feed also back to WP: the final length for the dipole magnets will impact the space available for local Crab Cavity installations and potential installations for the compensation of long-range beam-beam interactions.
Task leader: T. Nakamoto

## Slide 13: WP4 (crabs): Prelim. Tasks List (2nd draft)
Task 4.1: Coordination and Communication Coordination and scheduling of the WP tasks Monitoring the work, informing the project management and participants within the JRA WP budget follow-up | CERN, LARP, ULANC
Task 4.2: Support studies Tunnel preparation SPS and LHC Local IR layout and spatial integration Effect of phase noise , LLRF system conceptual design RF power system specification Operational aspects (how to commission/make invisible) Interlocks and fast Feedback | CERN, KEK, LARP
Task 4.3: Compact Crab Cavity design Complete cavity and cryomodule specifications Design optimisation for novel schemes Conceptual design of SOM, HOM and LOM couplers Conceptual design of helium tank and cryostat Multipacting simulations on cavity & couplers FEM simulations: mechanical & thermal aspects Initial down-selection of the CC options Completion of a full technical design on the initial down-selected options, with mechanical drawings and specification. Design of tooling, dies and cavity fabrication equipment | ULANC, LARP, CERN, JLAB

## Slide 14: WP4: Prelim Tasks List (2nd draft)
Task 4.4: Elliptical Crab Cavity Technical design Coupler development and testing Tuner design and mock up on copper models Study of mechanical effects: resonances, microphonics. Cavity performance with couplers and horizontal cryostat Performance difference between 2 K & 4 K Cryostat and He Tank Design Complete the full technical design | CERN, CEA, CNRS, KEK
Task 4.5: Compact Crab Cavity Prototyping and Test Procurement /fabrication of tooling, dies and equipment. Construction of models to refine manufacturing techniques and tooling. Fabrication of prototype niobium cavity Cleaning and electro-polishing on the bare niobium cavity. (i.e. no couplers, antennas or other accessories), including cavity surface inspection. Development and procurement of all test equipment and instrumentation. Low power tests and measurements on the bare cavity in a test cryostat to test for compliance with design gradient and cavity performance specs. Make the final CC design down-selection | CERN, CEA, CNRS, ULANC, STFC, LARP

## Slide 15: WP5 (Collimation) Structure I
WP 5.1: Coordination and Communication
WP 5.2: IR Simulations of Halo Loss
  Collimation Sixtrack: CERN ABP, Valencia
  Collimation Merlin: Uni Manchester
  Collimation Geant: Royal Holloway
WP 5.3: IR Simulations of Energy Deposition
  Mars: FNAL
  FLUKA: CERN STI, Uni Manchester
  Geant: Royal Holloway

## Slide 16: WP5 Structure II
WP 5.4: Design of IR Collimation
  CERN ABP
  Uni Valencia
  SLAC