## Slide 1: LHC Collimation Project - HL-LHC Design Study: WP5
R. Assmann
LARP CM15, 1.11.2010

## Slide 2: LHC Collimation Works Well…
With already very high LHC beam intensity we see unavoidable beam losses constantly (see example for lifetime > 75 hours).
We can characterize losses. E.g. losses for beam 1 mostly in momentum cleaning  had a few RF cavity trips. Losses for beam 2 mostly in betatron cleaning  no RF trips for beam 2.
Essentially all losses intercepted at primary collimators in betatron and momentum cleaning insertions!
Small leakage to outside cleaning insertions. High efficiency!
Some local losses occur in the experimental insertions (visible on logarithmic scale): luminosity-driven losses, p-p collisions.
In addition: rare beam dumps due to tiny, fast losses in middle of arc (10 events so far  rare dust particles?). Not discussed here…

## Slide 3: Phase I in Tunnel (Radiation-Optimized)
BEAM PIPES
COLLIMATOR
TRANSPORT ZONE
COLLIMATOR CABLE TRAYS
RADIATION-HARD CABLE PATH
WATER FEEDS
PHASE I/II
WATER
DISTRIBUTION
Implemented 2002 – 2009
LHC Collimation Project
Notes: 3

## Slide 4: Tunnel: 3 Primary Betatron Collimators
Implemented 2002 – 2009
LHC Collimation Project

## Slide 5: Losses Around the Ring (3.5 TeV, End Record Fill 26.9.2010, t > 75 h)
ATLAS
ALICE
CMS
LHC-b
0 – 27 km
Momentum
Collimation
Betatron Collimation
Beam 1
Beam 2
Essentially all losses at collimators  No quench!
3.5
3.0
2.5
2.0
1.5
1.0
0.5
0.0

## Slide 6: Losses Around the Ring (3.5 TeV, End Record Fill 26.9.2010, t > 75 h)
ATLAS
ALICE
CMS
LHC-b
0 – 27 km
Momentum
Collimation
Betatron Collimation
Beam 1
Beam 2
Details can be seen in logarithmic scale!
Dump
Logarithmic scale!

## Slide 7: Measured Cleaning at 3.5 TeV (beam1, vertical beam loss, intermediate settings)
factor 1,000
factor 4,000
Betatron Cleaning
IR8
factor 600,000
Cleaning efficiency: > 99.975%

## Slide 8: Meas. & Sim. Cleaning at 3.5 TeV (beam1, vertical beam loss, intermediate settings)
IR8
IR7
Confirms expected limiting losses in SC dispersion suppressor

## Slide 9: Status LHC Stored Energy

## Slide 10: LHC Status Energy Density

## Slide 11: Collimation is Designed for Upgrades!
EMPTY PHASE II TCSM SLOT (30 IN TOTAL)
PHASE I TCSG SLOT

## Slide 12: LHC Collimation Upgrade Work
Work is defined in three stages:
  2010 – 2013: Upgrade part 1
  2013 – 2017: Upgrade part 2
  2020: Upgrade part 3.

## Slide 13: Collimation Upgrade Part 1 (2010 – 2013)
Start date of work: 1.7.2010
End date of work: 31.12.2013
Deliverables:
  Improve collimation efficiency by factor 5-10.
  Implement flexibility in loss location (IR3 or IR7).

## Slide 14: Collimation Upgrade Part 2 (2013 - 2017) – to be approved in 2011
Start date of project: 1.1.2013
End date of project: 31.12.2017
Deliverables:
  Improve collimation efficiency by factor 2-3.
  Reduce setup time by factor 100.
  Implement radiation handling for highest intensities.

## Slide 15: Collimation Upgrade Part 3 (2020)  WP5 in FP7 HL-LHC Design Study
Deliverables:
  Same or better loss situation than before the IR upgrade (lower beta* with the same or better intensity reach).
  Adapt IR collimation to the new IR layout and optics.
  Design report, build hardware, implement modified IR collimation.
WP5

## Slide 16: WP Structure I
WP 5.1: Coordination and Communication
WP 5.2: IR Simulations of Halo Loss
  Collimation Sixtrack: CERN ABP, Valencia
  Collimation Merlin: Uni Manchester
  Collimation Geant: Royal Holloway
WP 5.3: IR Simulations of Energy Deposition
  Mars: FNAL
  FLUKA: CERN STI, Uni Manchester
  Geant: Royal Holloway

## Slide 17: WP Structure II
WP 5.4: Design of IR Collimation
  CERN ABP
  Uni Valencia
  SLAC

## Slide 18: Objectives I
WP 5.1: Coordination & Communication
  To coordinate and schedule work package tasks
  To monitor work progress and inform the project management and work package participants
  To follow up the WP budget and use of resources
  To prepare internal and deliverable reports
WP 5.2: IR Simulations of Halo Loss
  Assess locations and magnitudes of beam loss in the experimental IR’s for various upgrade scenarios.
  Study impact of imperfections on beam loss.
  Explore interplay of IR beam losses with machine parameters (beta*, crossing angle).
  Specify operational tolerances related to collimation and the IR upgrade.
  Define beam impact scenarios for energy depositions studies and collimator design.
  Prepare input for energy deposition studies.

## Slide 19: Objectives II
WP 5.3: IR Simulations of Energy Deposition
  Assess locations and magnitude of energy deposition in the IR’s for various upgrade scenarios including imperfections.
  Investigate any possibly required shielding requirements.
  Provide input to collimator design.
  Prepare input for background simulations.
WP 5.4: Design of IR Collimation
  Study required collimation to keep losses at the same level or below before the IR upgrade.
  Specification of collimator requirements.
  Integration of collimators, new layout and optics.
  Feed forward to simulation WP’s.

## Slide 20: Milestones (After Start of Design Study)
M12: Set up of models and implementation of upgrade optics.
M24: Assessment of beam halo losses in various upgrade scenarios.
M36: Definition of new IR collimation solution.
M42: Verification of new IR collimation solution in simulations. Possible iteration in design.
M48: Final report.

## Slide 21: Conclusion
LHC collimation delivers promised performance, allowing LHC to already reach 28 MJ in stored energy.
Performance reach will be reviewed in the Chamonix workshop, January 2011.
The first phase of the LHC upgrade is ongoing in full speed.
Two more phases have been defined up to 2020.
The upgrade of IR collimation is foreseen for 2020 and is WP5 of the HL-LHC FP7 design study.