## Slide 1: Data Link Projects - Minnesota
Roger Rusack The University of Minnesota

## Slide 2: Projects
Past Projects
  11,000 channels of 0.8 Gbs for the CMS crystal calorimeter readout.
  1,500 channels of the same for the LHC beam loss monitors.
  Power distribution by optical fibres.
Current Projects
  Investigating 5 GbS CWDM signal transmission and reception in a radiation environment.
  CMS HCAL upgrade to the readout and trigger.

## Slide 3: ECAL Link System
12
Rx module
12
1
GOH
12
1
96
Distributed Patch Panel
Back-end Patch Panel
Off Detector
Front End
Pigtail fiber
Ruggedized ribbon
Dense multi-ribbon cable
GOL
Laser diode
In-Line Patch Panel
CMS
PIN photo-diode array
Digital amp. ASIC
12
Digital
Receiver: NGK
GOL:
CERN MIC
GOL Opto-Hybrid (GOH): We design, prototype, qualify, define manufacturing specifications, procure the manufacture, burn in, perform final acceptance test.
12-channel NGK Rx: Off-the-shelf component: We qualify, procure, test samples during production.
Fiber, connectors and adaptors: We use Tracker components and contract options.
Laser diode:
ST Microelectronics

## Slide 4: System Requirements and Specifications - 2
Some requirements and specifications, in numbers:
Link System Requirement | Minimum Link Specification | Actual Link Specification
Clean Rx eye diagram | HIPPI-6400 mask standard | same
Low jitter (GOH to Rx) | 100 ps | < 50 ps
Low Bit Error Rate | < 10-12 (99% conf.) | < 10-12 to < 10-13 (99% conf.)
GOH temperature | -10°C to ~+40°C (FE card) | -20°C to +60°C (FE card)
Rx module temperature | +20°C to +50°C (case) | +18°C to +80°C (case)
Magnetic field | 4 T | same
Hadronic fluence | 3×1014/cm2 | same
Gamma dose | 1.5×105 Gy | same
Operating life | 10 years | same
<
~

## Slide 5: Components: Fiber and Connectors
Sub-components of the fiber system:
12
12
1
96
MU-sMU adapter (Sumitomo)
MFS adapter (Diamond)
MFS-MPO multi-ribbon cable (Ericsson, Diamond)
sMU-MFS fanout (Ericsson, Sumitomo, Diamond)
CMS
Distributed Patch Panel
Back-end Patch Panel
In-Line Patch Panel

## Slide 6: Components: Receiver
Rx module
12
PIN photo-diode array
Digital amp. ASIC
12
Off-the-shelf component: Our tasks are to qualify, procure, test samples during production.
The receiver of the Data Link is the 12-channel digital Rx manufactured by NGK.
Accepts single-mode fiber
Operating wavelength 1310 nm
Speed: up to 1.25 Gb/s
Sensitivity: -18 dBm (typically <19 dBm)
Saturation: -5 dBm
Jitter: < 42 ps
Temperature: 0°C to 80°C
Some characteristics and specifications of the Rx:
NGK Rx QA:
All channels tested by NGK (pass/fail mask test at 1.25 Gb/s, input power -20dBm, case temperature 80°C; simultaneously jitter must be < 42 ps)
We will test samples during production (see later slides).

## Slide 7: Irradiation Test Setup
Ten GOH were irradiated in 60 MeV proton beam at PSI, 27-29 Feb.
PC running LabVIEW control program
GIII Tx
GOH eval board
GIII Rx
I2C controller
data, clock, I2C
“Sender” card
clock
GOH
GOH
“Sandwich” GOH (clock, I2C only)
GOH
GOH
BERT GOH (data, clock, I2C)
data
data
beam area
control room
beam
Rx eval board
deser eval board
~30 m
data
One BERT GOH to observe any data errors.
Nine “sandwich” GOH to observe evolution of eye diagram vs. dose and also have some statistics in case of GOL or laser failure.
Mother test card
scope

## Slide 8: Some photos
In the control room
Serious cabling
Closeup of the GOH stack
Setup in the beam area

## Slide 9: Minnesota Contributions
The complete data link - 11,000 channels:
  System qualification and specifications.
  Manufacture
  Qualification
  Installation
Test modules:
  3 BERT systems. PC based, irradiator and stand alone.
  3 GOH testers - QA at manufacturer and for reception. Eye diagram test.
  Cable tester.
  Various devices for component checking during construction.
Extended production to manufacture ~ 1500 rad hard data links for the LHC Beam Monitors.

## Slide 10: Current Projects
Investigating the use of Wavelength Division Multiplexing for future HEP data systems.
Produced μTCA boards with SFP+ transmitter/receivers SNAP12 driven by a Virtex 5 FPGA.
Used to test CWDM for a control link.
Context upgrade of the readout of the hadron calorimeter.
Possible application in the electromagnetic calorimeter upgrade for HI-LHC.

## Slide 11: SFP+ Tests
Two miniCTR2 boards used to send and receive data 6.25 Gbs – separate clocks.

## Slide 12: CCWDM Tests
Tests done with four wavelengths 1470nm, 1490nm, 1510nm, and 1530nm SFP+ 4.8 GbS.

## Slide 13: CWDM Tests

## Slide 15: Future Plans
Radiation Test of WDM components.
Test with XFP.
Test with Mach-Zehnder
Radiation tests with M-Z

## Slide 16: XFP Test

## Slide 17: Test With Mach-Zehnder
Use Mach-Zehnder with a CW laser and overlay 10 GbS signal generated from FPGA through a SER-DES

## Slide 18: Summary
Minnesota group has long experience with production and testing of large scale fibre-optic systems.
Currently exploring the SNAP12 and CDW solutions.
Doing this in the context of CMS HCAL upgrade and general R&D towards high density readout systems.