## Slide 1: Fast Serial Links activities at the University of Chicago
Jean-Francois Genat
and
Mircea Bogdan, Anton Kapliy
Yann Peschanski, Fukun Tang
Fermilab, Aug 19th 2010

## Slide 2
- ATLAS Silicon Fast Tracker
- ATLAS Tile Calorimeter
J-PARC
PET

## Slide 3: ATLAS Fast TracKer (FTK)
LHC@ 10^34: 25 overlapping pp collisions
3 10^34 75 “
FTK: Early rejection of background events, provides global track reconstruction just after the start of Level 2 processing, on L1 accepts
Massively parallel processing for fast online track reconstruction
Silicon
Strips and pixels
DAQ ROBs
FTK system
L2
L1 100 kHz
RODs
S-links at 1.3 Gb/s
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 4: ATLAS Fast TracKer (FTK)
HOLA card: 250 units fan to DAQ and FTK detector data on two S-links at 1.3 Gb/s (805nm)
External SerDes (not FPGA embedded)
Successfully used at CDF for the Level 2 system
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 5: ATLAS Fast TracKer Plans
- Integrate SerDes in the FPGA
Cyclone III allows up to 2Gb/s serial I/Os
Keep the Agilent optical interfaces
HOLA performance sufficient up to 2020
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 6: ATLAS Tile Calorimeter
- 10,000 PMT channels
- Present readout is level1-triggered using G-link at 320 Mb/s
Upgrade: Digitize and send all on the fly at 12-bit 40 MHz
Requires 12.3 Gb/s on 1000 channels (total 12Tb/s !)
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 7: Dataflow for the sLHC upgrade
256 Drawers: 4 Motherboards/drawer
Motherboards: 12 3-1 cards = 12 PMT channels
3-1 card:
2-gains: 2 channels to be sampled (12 bits) at 40 MHz
Integrator = 20 bits/ Motherboard
12 PMT channels
Assuming 12- bit words, data rate is:
[12 x 2 x 12- bits + 20- bits)] x 40 MHz = 12.3 GBit/s per Motherboard
Present is 320 MBit/s Use 3 GBT devices at 4.8 Gb/s
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 8: ATLAS Tile Calorimeter
10,000 Photomultipliers channels
On-detector front-end electronics including ADCs
Level 1 triggered readout at 600Mb/s using G-link
Fukun Tang, Fermilab, Aug 19th 2010

## Slide 9: 40 Gb/s ribbon fiber evaluation kit (Avago)
Single Board compatible with Transmitter and Receiver
Up to 3.5 Gb/s per test channel
Independent connection to all channels
24 SMA connectors (differential)
DC coupled high-speed signals
Control Pins for all I/O
3.3V Power Supply
Evaluation boards at 12 x 3.25 Gb/s
(Avago, Reflex Photonics)
Jean-Francois Genat, Fermilab, Aug 19th 2010
Notes: 9

## Slide 10: Tests at 2 Gb/s
First test using:
- Two Avago test cards (12 x 3.5 Gb/s)
A Cyclone III device on an evaluation card from Altera
First tests of one channel at 2 Gb/s ok (no opto device, just FPGA), .
Then, set the Avago opto test cards in the path
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 11
FPGA
USB
Test Data
2.5 Gb/s
30m
30Gb/s
1 link tested @ 2.5Gb/s
Error Counter
RJ45
RJ45
Optical interface
RX/TX
Fiber
850 nm
SMA
Cyclone IV GX
Transceiver Starter Kit
1 channel @ 2.5 Gb/s
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 12: Test card under development
Test of a channel with a Stratix IV device at 6.25 Gb/s
for BER and radiation hardness (150 kRad)
Altera FPGA devices available:
Cyclone IV 3.125 Gb/s
Stratix IV 6.25 Gb/s
Stratix IV GT 10 Gb/s
Stratix V GT 12.5 Gb/s (28 Gb/s on 4 channels)
FPGA
USB Interface
Ribbon
Fiber
Custom PCB
Rx
Tx
Implement in the FPGA:
- SerDes at 6.25 Gb/s
Pseudo random sequences
CERN GBT code
Fast XORs
- Error Counters
Laptop
USB
Jean-Francois Genat, Fermilab, Aug 19th 2010
- Layout between opto devices and FPGA critical:
Use of a dedicated software (Hyperlynx) for
the crosstalk evaluation at 10 GB/s
Avago SFPs
Notes: 12

## Slide 13: BER tests at 3.25 Gb/s
Agilent 10.6 Gbs Bit Error Rate tester
FPGA
Ribbon
fibers
Custom PCB
Rx
Tx
Laptop
USB
BER tests @ 3.25 Gb/s (Avago evaluation board limited)
FPGA used only for SerDes function on the path
Evaluation
board
Jean-Francois Genat, Fermilab, Aug 19th 2010
Stratix IV GT evaluation kit ordered
Notes: 13

## Slide 14: J-PARC
- PMT channels, 16-channel regular VME modules
- Digitization on the fly at 125 MHz (upgrade at 500 MHz)
- Energy sums in parallel through 805nm multi-mode fibers (100m)
- Trigger and data on two optical channels
- Regular VME cards with 2.5 GB/s links on the front panel
- TI SerDes + Avago optical modules at 2.5 Gb/s
- Interconnected as a parallel structure:
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 15: ATCA
- Just started, have in view a data acquisition system for a PET camera
a few hundred channels at a 100 kHz-1 MHz event rate
MicroTCA foreseen
Jean-Francois Genat, Fermilab, Aug 19th 2010

## Slide 16: Conclusion
> 10Gb/s serial transmission links available today, with bunched fibers
- Thanks to Silicon-Germanium and Gallium Arsenide technologies
- Radiation hardness to be checked
- Ok for most of the present detectors needs
We are open to work with other teams, as adequate specific parts are developed and get available
Jean-Francois Genat, Fermilab, Aug 19th 2010